## Slide 1
Project: P802.15 Working Group for Wireless Specialty Networks
Submission Title: Overview of FEC proposals for 15.6ma
Date Submitted: November 15th, 2022
Source: Marco Hernandez1,3, Ryuji Kohno1,2, Takumi Kobayashi1,2, Minsoo Kim1
Company: 1Yokosuka Research Park International Alliance Institute (YRP-IAI), Japan; 2Yokohama National University (YNU), Japan. 3CWC, Oulu Univ. Finland.
Address: 3-4 Hikarino-oka, Yokosuka, 239-0847, Japan.
E-Mail: Marco.Hernandez@ieee.org; kohno@ynu.ac.jp; Kobayashi-Takumi-ch@ynu.ac.jp; Minsoo@minsookim.com;
Abstract: Technical contributions.
Purpose: In response to the call for technical contributions.
Notice: This document has been prepared to assist P802.15.6ma. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.6ma.

## Slide 2: FEC harmonization

## Slide 3: HARQ based on decomposable CC 15-22-0561
It looks promising. However, some improvements and clarifications must be addressed to be considered in the Std:
  Simulation parameters must be changed to the ones suggested by the Technical Requirements Document and Channel Model Document.
  For compatibility with 4ab BCC, increase K=7 and try other coding rates including ½ for the proposed punctured CC.
  Performance degradation is better shown as PER vs Eb/N0 or SNR as a function of several retransmissions.
  Missing results of latency versus Eb/No or SNR as a function of retransmissions to show compliance with the TRD.

## Slide 4: Use of Super Orthogonal Convolutional Code 15-22-0562
Missing characteristics/construction of the SOCC.
A well-know disadvantage of SOC constructions is a significant increment in complexity and latency due to the resulting low coding rate construction.
A very low coding rate does not seem to comply with 6ma requirements in terms of latency.
  Performance degradation is better shown as PER vs Eb/No or SNR.
  Missing results in terms of latency versus Eb/No or SNR to show compliance with the TRD.
  The SOCC does not seem to perform better (PER and latency) than the considered LDPC code.