## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [An updated PHY Header Proposal]
Date Submitted: [17th November 2022]
Source: [Billy Verso, Jarek Niewczas, Carl Murray (Qorvo)]
Address [ ]
E-Mail:[billy.verso (at) qorvo.com]
Re: [Proposals for TG4ab next generation UWB project]
Abstract: [A proposed PHR for the 4ab HRP UWB PHY enhanced data rates supporting dynamic data rate selection.]
Purpose: [To promote further discussion and convergence on the content for the IEEE 802.15.4ab amendment.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
Document 15-22-0467 proposed an efficient way of supporting dynamic data rate by introducing an initial rate header (PHR1) sent at a low rate and a main header (PHR2) transmitted at the payload modulation rate (or slower depending on the required strength vs. the payload coding).
This submission is an evolution of that idea that incorporates a number of considerations from 15-22-0475-01 and focuses upon the modulation rates specified by the consensus document 15-22-0517 and the PHY header modulation rates that this implies.
Additionally, based on discussions with interested parties, we present some parameter choices that we would like TG4ab to consider and decide upon as part of a group consensus.

## Slide 3: A two-stage approach to PHR for dynamic data rates:
PHR is split into two parts
  First comes a “short” rate header, PHR1, sent at a low rate to robustly and efficiently select from the full set of supported modulation and coding combinations
  Then PHR2, sent at the highest rate consistent with the target modulation indicated by PHR1, includes everything else we need to indicate in the PHR
To ease the transition between the different modulation rates of PHR1 and PHR2 we can include a fixed short gap between them.
  We leave this as a TBD (expect to be ≤ ~1 µs), if the group agrees a gap is needed

## Slide 4: PHR1: short, efficient & robust selection of rate/code
PHR1 consists of 3 bits to select data rate and 1 bit to select BCC vs LDPC code for the PSDU
Encoding this PHR1 with BCC ½ rate K=7 code with 6 tail symbols, makes it 10 symbols long…
Choices:
  (a) In 15-22-0467-01 we proposed a 3.9 Mbps symbol rate so that PHR1 was ~2.5 µs in duration
  (b) Deeming (a) not strong enough we have revised this to 1.95 Mbps making it ~5 µs
  (c) If the group agrees that this needs to be stronger then let’s make it 0.975 Mbps which would be ~10 µs long
One more possibility:
  (d) Treat (b) as 20 uncoded bits and map the combinations of data rate + LDPC across these in a way that makes the hamming distance sufficiently strengthen the combinations that need the most robustness. We believe this can give strength of (c), for those rates that need it, at the ~5 µs cost of (b).

## Slide 5: PHR2 rate consistent with PSDU modulation
PHR2 is sent using the K=7 code (with 6 tail bits) at the highest rate consistent with the target modulation indicated by PHR1 and chosen for the correct level of robustness.
When using the BCC K=7 code for the PSDU, we send PHR2 at the same rate as the PSDU, i.e., with 1 symbol for each bit.
When using the LPDC code we tailor the strength of PHR2 (mapping each bit across 2, 3 or 4 symbols), depending on the necessary robustness
  This is a TBD that the group should converge on based on simulation results.
  Note that this mapping does not necessarily need to be the same for all rates.

## Slide 6: PHR2 content
With PHR2 being sent at the highest rate consistent with the data modulation, it is not very expensive to include additional content.
  So, for example, could include version bits inexpensively
This submission is not proposing specific PHR2 content.
  This can be agreed later.

## Slide 7: How to incorporate into 802.15.4z
Dynamic data rate selection is already partially covered by the 802.15.4 text (from 4a days)
Once it is agreed it is relatively easy to add text to define the 4ab dynamic PHR format.
Can then have configurations to support 4z type PHR at the data rate for the new 4ab data rates and a configuration to enable the dynamic PHR format, i.e., update table 15-10b to add the dynamic mode and expand to five static rates as follows:
  Replace the two rates DRHM_LR, DRHM_HR with five easier to understand rate definitions:
    DRHM_1p95, DRHM_7p8, DRHM_31p2, DRHM_62p4 and DRHM_124p8
  Add (pre-existing) DRMDR into the table to enable the 4ab dynamic PHR operating mode.
Table 11-2—PHY PIB attributes

## Slide 8: A note on SYNC length
The SYNC length to be used when employing the dynamic data rate needs to be fixed in the transmitter depending on the needs of the remote receiver.
The transmitter also needs to know what data rates the remote receiver supports.
We envisage this information is communicated either via OOB means or via an in-band IE exchange at an initial low rate, perhaps with a default setting so that this exchange is not needed for some agreed common use case.

## Slide 9: Conclusion
This submission builds upon 15-22-0467, 15-22-0475 and 15-22-0517 to propose and efficient way of dynamically supporting all the new HPRF mode data rates proposed for 4ab.
The data rate can be dynamically selected across the whole proposed range of 1.95 Mb/s to 124.8 Mb/s via an initial rate header (PHR1) which determines both the main (PHR2) header modulation rate and the coding and modulation rate for the PHY Payload.

## Slide 10
THE END.