## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [An updated PHY Header Proposal]
Date Submitted: [16th January 2023]
Source: [Billy Verso, Jarek Niewczas, Carl Murray (Qorvo)]
Address [ ]
E-Mail:[billy.verso (at) qorvo.com]
Re: [Proposals for TG4ab next generation UWB project]
Abstract: [A proposed PHR for the 4ab HRP UWB PHY enhanced data rates supporting dynamic data rate selection.]
Purpose: [To promote further discussion and convergence on the content for the IEEE 802.15.4ab amendment.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
Document 15-22-0467 proposed an efficient way of supporting dynamic data rate by introducing an initial rate header (PHR1) sent at a low rate and a main header (PHR2) transmitted at the payload modulation rate (or slower depending on the required strength vs. the payload coding).
This submission is an evolution of that idea that incorporates a number of considerations from 15-22-0475-01 and focuses upon the modulation rates specified by the consensus document 15-22-0517 and the PHY header modulation rates that this implies.
Additionally, based on discussions with interested parties, and further development of the ideas of earlier revision(s) we update this submission to examine encoded mapping of PHR1 in more detail.

## Slide 3: A two-stage approach to PHR for dynamic data rates:
PHR is split into two parts
  First comes a “short” rate header, PHR1, sent at a low rate to robustly and efficiently select from the full set of supported modulation and coding combinations
  Then PHR2, sent at the highest rate consistent with the target modulation indicated by PHR1, includes everything else we need to indicate in the PHR
To ease the transition between the different modulation rates of PHR1 and PHR2 we can include a fixed short gap between them.
  We leave this as a TBD (expect to be ≤ ~1 µs), if the group agrees a gap is needed

## Slide 4: PHR1: short, efficient & robust selection of rate/code
PHR1 consists of 3 bits to select data rate and 1 bit to select BCC vs LDPC code for the PSDU
Encoding this PHR1 with BCC ½ rate K=7 code with 6 tail symbols, makes it 10 symbols long…
Let’s look more closely at PHR1 and mapping it as uncoded bits. We can map the combinations of data rate + LDPC across these in a way that makes the hamming distance sufficiently strengthen the combinations that need the most robustness

## Slide 5: PHR1: variable distance mapping
PHR1 will indicate data-rate and coding used in PHR2 and the data mode/coding
This PHR1 needs to be at least as strong as the weaker of the two.
With 22-bit PHR2, the Es/No requirement for 1% PER is approx. +1.9dB (at the decoder input), however using 2 repetitions can improve the performance by 3dB. If CCK7 was used for PHR1, without any repetition, Es/No is -0.3dB, which is too weak to match PHR2 with 2x repetition.
Choices:
  (a) send PHR1 using CCK7 and with 2x repetition which would increase duration from 5 µs to 10 µs
  (b) Use alternative coding in PHR1 to strengten PHR1 options which require high performance (like 1.9Mbps with LDPC). The mapping would make the Hamming distance higher for the combinations that need the most robustness and lower the Hamming distances for combinations which require higher SNR to operate (like 31Mbps or faster modes). Sufficient performance can be obtained with PHR1 shorter than 5 µs.

## Slide 6: PHR1: variable distance mapping
Example PHR1 encoded bit-sequences (20-bits long) are shown here
Bit-sequence encoding PHR1 index 1, which could correspond to LDPC-coded 1.9Mbps, has an increased Hamming distance to all the other indexes.
Es/No performance of such enhanced PHR1 coding is improved from -0.3dB (CCK7 coding) to -1.8dB, which is better than PHR2 with 2x repetition.
The price to pay is the reduced Hamming distance between the remaining options, which translated to Es/No performance of +2.2dB. However, this is still sufficient for all the remaining data-mode options.
Alternative mappings can be used, for example prioritizing not one but 2 or 3 indexes with variable strengths, depending on requirements
Shorter sequences than 20-bits could be sufficient.

## Slide 7: PHR2 rate consistent with PSDU modulation
PHR2 is sent using the K=7 code (with 6 tail bits) at the highest rate consistent with the target modulation indicated by PHR1 and chosen for the correct level of robustness.
When using the BCC K=7 code for the PSDU, we send PHR2 at the same rate as the PSDU, i.e., with 1 symbol for each bit.
When using the LPDC code we tailor the strength of PHR2 (mapping each bit across 2, 3 or 4 symbols), depending on the necessary robustness
  This is a TBD that the group should converge on based on simulation results.
  Note that this mapping does not necessarily need to be the same for all rates.

## Slide 8: PHR2 content
With PHR2 being sent at the highest rate consistent with the data modulation, it is not very expensive to include additional content.
  So, for example, could include version bits inexpensively
This submission is not proposing specific PHR2 content.
  This can be agreed later.

## Slide 9: How to incorporate into 802.15.4z
Dynamic data rate selection is already partially covered by the 802.15.4 text (from 4a days)
Once it is agreed it is relatively easy to add text to define the 4ab dynamic PHR format.
Can then have configurations to support 4z type PHR at the data rate for the new 4ab data rates and a configuration to enable the dynamic PHR format, i.e., update table 15-10b to add the dynamic mode and expand to five static rates as follows:
  Replace the two rates DRHM_LR, DRHM_HR with five easier to understand rate definitions:
    DRHM_1p95, DRHM_7p8, DRHM_31p2, DRHM_62p4 and DRHM_124p8
  Add (pre-existing) DRMDR into the table to enable the 4ab dynamic PHR operating mode.
Table 11-2—PHY PIB attributes

## Slide 10: A note on SYNC length
The SYNC length to be used when employing the dynamic data rate needs to be fixed in the transmitter depending on the needs of the remote receiver.
The transmitter also needs to know what data rates the remote receiver supports.
We envisage this information is communicated either via OOB means or via an in-band IE exchange at an initial low rate, perhaps with a default setting so that this exchange is not needed for some agreed common use case.

## Slide 11: Conclusion
This submission builds upon 15-22-0467, 15-22-0475 and 15-22-0517 to propose and efficient way of dynamically supporting all the new HPRF mode data rates proposed for 4ab.
The data rate can be dynamically selected across the whole proposed range of 1.95 Mb/s to 124.8 Mb/s via an initial rate header (PHR1) which determines both the main (PHR2) header modulation rate and the coding and modulation rate for the PHY Payload.

## Slide 12
THE END.