## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Propagation Characteristics of UWB Communication Applications for Human BAN (HBAN) Use Cases
Date Submitted: January 14th, 2023
Source: Daisuke Anzai, Nagoya Institute of Technology
Address Gokiso-cho, Showa-ku, Nagoya, 466-8555, Japan
Voice: +81-52-735-5389, FAX: +81-52-735-5389, E-Mail: anzai@nitech.ac.jp
Re: In response to call for technical contributions
Abstract: This provides of fundamental propagation characteristics including path loss characteristics for UWB communication applications for BCI use case.
Purpose: Material for discussion in P802.15.6a TG corresponding to comments in EC Meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Propagation Characteristics of UWB Communication Applications for Human BAN (HBAN) Use Cases
Daisuke Anzai and Sho Asano
Nagoya Institute of Technology

## Slide 3: UWB communication applications
Brain-computer interface (BCI) model[1]
Passengers bus model[1]
Human BAN (HBAN)
Vehicle BAN (VBAN)
[1]IEEE 802.15-22-0344-02-006a

## Slide 4: UWB antenna at 3.1 - 10.6 GHz band
18 mm
20 mm
Frequency: 3.1 – 10.6 GHz
Planar elliptical dipole antenna
Element size: 20 mm x 18 mm x 1 mm
Interval between each element: 0.5 mm
|S11| [dB]
Frequency [GHz]

## Slide 5: Simulation model
Transmitted signal waveform
UWB antenna
(transmit antenna)
Frequency: 3.4 – 4.8 GHz
Frequency-dependent finite-different time-domain (FDTD) method
Multi-size voxel model (min. size: 0.5 mm)
Homogeneous human model (Japanese male developed by NICT, Japan)

## Slide 6: Dielectric constants of human model
Relative permittivity
Conductivity

## Slide 7: Simulation model for BCI case (Forward antenna direction)

## Slide 8: Simulation setup (Human head model)

## Slide 9: Path loss characteristics (Sensor #10)

## Slide 10: Path loss characteristics (Sensor #22)

## Slide 11: Distance characteristics (Human head, BCI)
mm
Directions | PL0 [dB] | n | [dB]
x | 24.84 | 3.84 | 9.52
y | 3.78 | 6.80 | 7.27
z | 3.73 | 6.03 | 9.31
Directions | PL0 [dB] | n | 
x | 24.84 | 3.84 | 9.52
y | 3.78 | 6.80 | 7.27
z | 3.73 | 6.03 | 9.31

## Slide 12: Log-normal distribution (Human head, BCI)
-direction
-direction
-direction

## Slide 13: Power delay profile (Human head, BCI)

## Slide 14: Simulation model (On-body model)
28 receivers were place on the body surface including head, arm, and chest

## Slide 15: Path loss characteristics (Sensor #7)

## Slide 16: Path loss characteristics (Sensor #18)

## Slide 17: Path loss characteristics (Sensor #28)

## Slide 18: Distance characteristics (Arm, BCI)
mm
Directions | PL0 [dB] | n | [dB]
x | 23.70 | 9.76 | 0.74
y | 102.62 | 0.57 | 8.15
z | 104.27 | 0.59 | 4.98
Directions | PL0 [dB] | n | 
x | 23.70 | 9.76 | 0.74
y | 102.62 | 0.57 | 8.15
z | 104.27 | 0.59 | 4.98

## Slide 19: Log-normal distribution (Front torso, BCI)
-direction
-direction
-direction

## Slide 20: Power delay profile (Front torso, BCI)

## Slide 21: Simulation model (Off-body model)
Top view
50 receivers (#29-#78) were placed at a height of 30 mm above the transmitting antenna (the top of the human head)
The interval of each receiver was set to 5 mm

## Slide 22: Path loss characteristics (Sensor #29)

## Slide 23: Path loss characteristics (Sensor #78)

## Slide 24: Distance characteristics (Off-body, BCI)
mm
Directions | PL0 [dB] | n | [dB]
x | 48.47 | 1.45 | 9.63
y | 19.13 | 2.67 | 2.72
z | 22.81 | 2.69 | 7.55
Directions | PL0 [dB] | n | 
x | 48.47 | 1.45 | 9.63
y | 19.13 | 2.67 | 2.72
z | 22.81 | 2.69 | 7.55

## Slide 25: Log-normal distribution (Off-body, BCI)
-direction
-direction
-direction

## Slide 26: Simulation model for BMI case (Forward antenna direction)
BMI: Brain Machine Interface

## Slide 27: Path loss characteristics (Sensor #10)

## Slide 28: Path loss characteristics (Sensor #22)

## Slide 29: Distance characteristics (Human head, BMI)
mm
Directions | PL0 [dB] | n | [dB]
x | 32.21 | 2.55 | 12.94
y | 10.72 | 5.63 | 8.02
z | 13.00 | 4.62 | 8.86
Directions | PL0 [dB] | n | 
x | 32.21 | 2.55 | 12.94
y | 10.72 | 5.63 | 8.02
z | 13.00 | 4.62 | 8.86

## Slide 30: Log-normal distribution (Human head, BMI)
-direction
-direction
-direction

## Slide 31: Power delay profile (Human head, BMI)

## Slide 32: Simulation model (On-body model, BMI)
28 receivers were place on the body surface including head, arm, and chest

## Slide 33: Path loss characteristics (Sensor #7)

## Slide 34: Path loss characteristics (Sensor #18)

## Slide 35: Path loss characteristics (Sensor #28)

## Slide 36: Distance characteristics (Arm, BMI)
mm
Directions | PL0 [dB] | n | [dB]
x | 60.60 | 2.01 | 1.10
y | 90.00 | 0.66 | 10.08
z | 87.49 | 0.45 | 5.35
Directions | PL0 [dB] | n | 
x | 60.60 | 2.01 | 1.10
y | 90.00 | 0.66 | 10.08
z | 87.49 | 0.45 | 5.35

## Slide 37: Log-normal distribution (Front torso, BMI)
-direction
-direction
-direction

## Slide 38: Power delay profile (Front torso, BMI)

## Slide 39: Simulation model for BCI case (Sideways antenna direction)

## Slide 40: Simulation model for BMI case (Sideways antenna direction)
BMI: Brain Machine Interface

## Slide 41: Summary of channel parameters
Antenna direction | Case | Receiving direction | Receiving antenna position |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Whole head (d0 = 10 mm) |  |  | Scalp (d0 = 10 mm) |  |  | Arm (d0 = 100 mm) |  |  | Torso (front) (d0 = 100 mm) |  |  | Off-body (d0 = 10 mm) |  | 
 |  |  | PL0 [dB] | n | σs [dB] | PL0 [dB] | n | σs [dB] | PL0 [dB] | n | σs [dB] | PL0 [dB] | n | σs [dB] | PL0 [dB] | n | σs [dB]
Forward | BCI | X | 24.84 | 3.84 | 9.52 | 27.13 | 3.36 | 10.18 | 23.70 | 9.76 | 0.74 | 69.31 | 3.85 | 3.02 | 48.47 | 1.45 | 9.63
 |  | Y | 3.78 | 6.80 | 7.27 | 11.44 | 5.32 | 6.96 | 102.62 | 0.57 | 8.15 | 50.24 | 2.76 | 0.65 | 19.13 | 2.67 | 2.72
 |  | Z | 3.73 | 6.03 | 9.31 | 17.58 | 3.31 | 7.52 | 104.27 | 0.59 | 4.98 | 27.52 | 8.61 | 1.98 | 22.81 | 2.69 | 7.55
 | BMI | X | 32.21 | 2.55 | 12.94 | 33.07 | 2.40 | 14.17 | 60.60 | 2.01 | 1.10 | 70.72 | 5.04 | 2.69 | 40.26 | 1.65 | 6.19
 |  | Y | 10.72 | 5.63 | 8.02 | 14.08 | 4.89 | 7.88 | 90.00 | 0.66 | 10.08 | 59.62 | 3.02 | 0.61 | 23.09 | 2.25 | 3.85
 |  | Z | 13.00 | 4.62 | 8.86 | 18.04 | 3.52 | 8.75 | 87.49 | 0.45 | 5.35 | 32.56 | 9.25 | 1.61 | 22.12 | 2.66 | 5.81
Sideways | BCI | X | 20.37 | 3.80 | 7.47 | 10.97 | 5.63 | 6.89 | 51.42 | 3.14 | 1.13 | 16.68 | 10.59 | 2.42 | 0.05 | 4.95 | 2.66
 |  | Y | 19.60 | 4.96 | 7.59 | 25.39 | 3.86 | 7.31 | 80.65 | 1.99 | 11.42 | 67.02 | 3.72 | 1.80 | 34.94 | 2.74 | 5.65
 |  | Z | 13.36 | 4.54 | 7.09 | 19.77 | 3.34 | 7.03 | 76.35 | 1.85 | 5.12 | 62.07 | 6.87 | 2.61 | 44.11 | 0.56 | 5.84
 | BMI | X | 17.71 | 4.01 | 7.33 | 14.01 | 4.84 | 7.51 | 51.22 | 3.28 | 1.09 | 15.68 | 11.30 | 2.58 | -3.03 | 5.25 | 4.76
 |  | Y | 26.20 | 4.19 | 12.94 | 33.17 | 2.65 | 12.88 | 78.08 | 2.63 | 12.69 | 56.25 | 4.89 | 1.52 | 45.33 | 1.24 | 6.31
 |  | Z | 20.14 | 4.09 | 8.89 | 23.42 | 3.39 | 9.35 | 77.09 | 1.87 | 5.07 | 36.17 | 10.07 | 1.61 | 42.50 | 0.80 | 4.96

## Slide 42: Summary and future works
The path loss characteristics were evaluated in HBAN use cases, assuming the receivers were placed on the human head, arm, chest and off the human body
Future works include time-domain analyses such as multipath delay power profile and multipath delay spread

## Slide 43: References
D. Anzai, I. Balasingham, G. Fischer, J. Wang, “Reliable and High-Speed Implant Ultra-Wideband Communications with Transmit–Receive Diversity,” EAI/Springer Innovations in Communication and Computing, pp. 27-32, March 2020.
Y. Shimizu, D. Anzai, R. C-Santiago, P. A. Floor, I. Balasingham, and J. Wang, “Performance evaluation of an ultra-wideband transmit diversity in a living animal experiment” IEEE Trans. Microw. Theory Tech., vol. 65, no. 7, pp. 2596-2606, July 2017.
D. Anzai, K. Katsu, R. Chavez-Santiago, Q. Wang, D. Plettemeier, J. Wang, and I. Balasingham, “Experimental evaluation of implant UWB-IR transmission with living animal for body area networks,” IEEE Trans. Microw. Theory Tech., vol. 62, no. 1, pp. 183-192, Jan. 2014.
J. Shi, D. Anzai, and J. Wang, “Channel modeling and performance analysis of diversity reception for implant UWB wireless link,” IEICE Trans. Commun., no. E95-B, vol. 10, pp. 3197-3205, Oct. 2012.