## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Comparison of Ipatov sequences of different lengths]
Date Submitted: [Jan, 2023]
Source: [Chenchen Liu, Bin Qian, Lei Huang, David Xun Yang] Company [Huawei Technologies]
Address [Huawei Bantian Base, Longgang District, Shenzhen, 518129 China]
E-Mail:[liuchenchen1@Huawei.com]
Re: [Task Group 4ab: UWB Next Generation]
Abstract: [Compared the performance of Ipatov sequences of lengths 91,121 and 127]
Purpose: [ ]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Related Submissions
15-21-0377-00-04ab-preamble-codes-for-data-communications (Carlos Aldana)
15-22-0507-00-04ab-simulation-evaluation-of-preamble-sequences-for-4ab (Chenchen Liu)

## Slide 3: Background
Ipatov sequence can be a good candidate for both synchronization and sensing
There are serval different candidate lengths, such as 91, 121and 127
The performance of different Ipatov sequence will be analyzed in this contribution

## Slide 4: Cardinality of Ipatov Sequence
The cardinality of Ipatov sequences that can not be transformed into each other by cyclic shifts or multiplication by a constant (half of them are the reverse of the other half) is shown below[1]
A subset of sequences can be selected to have low cross correlations with each other[2]
With increasing number of UWB devices, the cardinality of the selected Ipatov sequences is expected to be large in order to reduce the interference
 | Len=91 | Len=121 | Len=127
Cardinality | 24 | 22 | ?
Cardinality(with low cross correlation) | 8 | 22 | 16

## Slide 5: Cardinality of Ipatov Sequence
The Probability that two uncoordinated UWB devices choose the same sequence for different cardinality
Only one channel available according to MIIT China regulations[3] will make the situation worse

## Slide 6: PRF Problem
The number of non-zero elements and its PRF with SF=1 is shown in the table below
The final mean PRF can be adjusted by changing the SF. The transmit energy is determined by the mean PRF and number of symbol repetitions
The limit on SF is the channel PDP (CM6 and CM8:900ns, Others: < 330ns[4]) and sequence length.
By setting the SF and number of repetitions, sequence of different length can have similar mean PRF and energy (e.g., length 91 with SF=4 have the same mean PRF as length 121 with SF=3)
 | Len=91 | Len=121 | Len=127
No. of non-zeros | 81 | 81 | 64
PRF (SF=1) | 0.89*BW | 0.67*BW | 0.5*BW

## Slide 7: Auto-correlation
Ipatov sequences are selected for use because of their perfect periodic autocorrelation properties, which can improved sensing and channel estimation performance.
With CFO, the auto-correlation performance may degrade. The detailed results will be shown with SF=4 and center frequency being 8GHz
The normalized Peak-to-Sidelobe Level (PSL) metric is used
PSL=
, where

## Slide 8: Auto-correlation
The PSL for CFO=0.1ppm and 40ppm
Auto-correlation performance can be further improved by accumulation across multiple symbols and advanced signal processing algorithm
PSR(dB) Len=91 | Seq25 | Seq26 | Seq27 | Seq28 | Seq29 | Seq30 | Seq31 | Seq32
CFO=0.1 | -72.5 | -72.8 | -72.1 | -73.5 | -72.2 | -72.8 | -72.4 | -72.9
CFO=40 | -20.2 | -20.3 | -19.7 | -21.1 | -20.1 | -20.5 | -19.9 | -20.7
PSR(dB) Len=127 | Seq9 | Seq10 | Seq11 | Seq12 | Seq13 | Seq14 | Seq15 | Seq16 | Seq17 | Seq18 | Seq19 | Seq20 | Seq21 | Seq22 | Seq23 | Seq24
CFO=0.1 | -69.7 | -69.5 | -68.6 | -67 | -69.1 | -69.4 | -70.7 | -69.5 | -69.7 | -69.5 | -68.6 | -67 | -69.1 | -69.4 | -70.7 | -69.5
CFO=40 | -17 | -17.2 | -16.3 | -14.4 | -16.3 | -17 | -17.8 | -17 | -17 | -17.2 | -16.3 | -14.4 | -16.3 | -17 | -17.8 | -17
PSR(dB) Len=121 | s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s17 | s18 | s19 | s20 | s21 | s22
CFO=0.1 | -69.6 | -70.2 | -69.6 | -70.2 | -71.2 | -71.2 | -69.2 | -69.2 | -69.5 | -69.5 | -68.1 | -68.1 | -69.8 | -69.8 | -70.2 | -69.2 | -69.2 | -70.2 | -70.3 | -70.2 | -70.3 | -70.2
CFO=40 | -17 | -17.5 | -17 | -17.5 | -18.6 | -18.6 | -16.6 | -16.6 | -16.9 | -16.9 | -15.7 | -15.7 | -17.4 | -17.4 | -17.7 | -16.9 | -16.9 | -17.7 | -17.6 | -17.7 | -17.6 | -17.7

## Slide 9: Cross-correlation
Low cross-correlation can reduce the interference and help the coexistence with legacy UWB devices
The cross-correlation is evaluated with the normalized cross-correlation peak (NCP):
In general, the CFO will lower the cross-correlation peak, so the cross-correlation with CFO=0 can be regarded as the worst case, especially when accumulated through multiple symbols
, where

## Slide 10: Cross-correlation
NCP for Ipatov sequence of length 91
NCP(𝒙,𝒚) (dB) | Seq25 | Seq26 | Seq27 | Seq28 | Seq29 | Seq30 | Seq31 | Seq32
Seq25 | 0 | -14.6 | -10.2 | -10.6 | -10.6 | -13.6 | -9.5 | -13.1
Seq26 | -14.6 | 0 | -10.6 | -13.6 | -10.2 | -10.6 | -10.6 | -10.9
Seq27 | -10.2 | -10.6 | 0 | -14.6 | -13.6 | -10.6 | -10.2 | -10.6
Seq28 | -10.6 | -13.6 | -14.6 | 0 | -10.6 | -10.2 | -12.1 | -9.5
Seq29 | -10.6 | -10.2 | -13.6 | -10.6 | 0 | -14.6 | -13.1 | -12.1
Seq30 | -13.6 | -10.6 | -10.6 | -10.2 | -14.6 | 0 | -10.9 | -10.2
Seq31 | -9.5 | -10.6 | -10.2 | -12.1 | -13.1 | -10.9 | 0 | -10.6
Seq32 | -13.1 | -10.9 | -10.6 | -9.5 | -12.1 | -10.2 | -10.6 | 0

## Slide 11: Cross-correlation
NCP for Ipatov sequence of length 127
NCP(𝒙,𝒚) (dB) | Seq9 | Seq10 | Seq11 | Seq12 | Seq13 | Seq14 | Seq15 | Seq16 | Seq17 | Seq18 | Seq19 | Seq20 | Seq21 | Seq22 | Seq23 | Seq24
Seq9 | 0 | -18.1 | -18.1 | -18.1 | -14.5 | -14.5 | -14.5 | -12 | -7.5 | -10.1 | -14.5 | -10.1 | -14.5 | -14.5 | -10.1 | -18.1
Seq10 | -18.1 | 0 | -18.1 | -18.1 | -14.5 | -14.5 | -14.5 | -14.5 | -10.1 | -13.2 | -10.1 | -9.3 | -10.1 | -12 | -14.5 | -10.1
Seq11 | -18.1 | -18.1 | 0 | -18.1 | -14.5 | -14.5 | -18.1 | -14.5 | -14.5 | -10.1 | -13.2 | -16.1 | -10.1 | -18.1 | -14.5 | -10.1
Seq12 | -18.1 | -18.1 | -18.1 | 0 | -14.5 | -14.5 | -14.5 | -14.5 | -10.1 | -9.3 | -16.1 | -16.1 | -18.1 | -10.1 | -9.3 | -12
Seq13 | -14.5 | -14.5 | -14.5 | -14.5 | 0 | -14.5 | -18.1 | -18.1 | -14.5 | -10.1 | -10.1 | -18.1 | -13.2 | -14.5 | -9.3 | -10.1
Seq14 | -14.5 | -14.5 | -14.5 | -14.5 | -14.5 | 0 | -14.5 | -18.1 | -14.5 | -12 | -18.1 | -10.1 | -14.5 | -16.1 | -14.5 | -16.1
Seq15 | -14.5 | -14.5 | -18.1 | -14.5 | -18.1 | -14.5 | 0 | -13.2 | -10.1 | -14.5 | -14.5 | -9.3 | -9.3 | -14.5 | -7.5 | -18.1
Seq16 | -12 | -14.5 | -14.5 | -14.5 | -18.1 | -18.1 | -13.2 | 0 | -18.1 | -10.1 | -10.1 | -12 | -10.1 | -16.1 | -18.1 | -13.2
Seq17 | -7.5 | -10.1 | -14.5 | -10.1 | -14.5 | -14.5 | -10.1 | -18.1 | 0 | -18.1 | -18.1 | -18.1 | -14.5 | -14.5 | -14.5 | -12
Seq18 | -10.1 | -13.2 | -10.1 | -9.3 | -10.1 | -12 | -14.5 | -10.1 | -18.1 | 0 | -18.1 | -18.1 | -14.5 | -14.5 | -14.5 | -14.5
Seq19 | -14.5 | -10.1 | -13.2 | -16.1 | -10.1 | -18.1 | -14.5 | -10.1 | -18.1 | -18.1 | 0 | -18.1 | -14.5 | -14.5 | -18.1 | -14.5
Seq20 | -10.1 | -9.3 | -16.1 | -16.1 | -18.1 | -10.1 | -9.3 | -12 | -18.1 | -18.1 | -18.1 | 0 | -14.5 | -14.5 | -14.5 | -14.5
Seq21 | -14.5 | -10.1 | -10.1 | -18.1 | -13.2 | -14.5 | -9.3 | -10.1 | -14.5 | -14.5 | -14.5 | -14.5 | 0 | -14.5 | -18.1 | -18.1
Seq22 | -14.5 | -12 | -18.1 | -10.1 | -14.5 | -16.1 | -14.5 | -16.1 | -14.5 | -14.5 | -14.5 | -14.5 | -14.5 | 0 | -14.5 | -18.1
Seq23 | -10.1 | -14.5 | -14.5 | -9.3 | -9.3 | -14.5 | -7.5 | -18.1 | -14.5 | -14.5 | -18.1 | -14.5 | -18.1 | -14.5 | 0 | -13.2
Seq24 | -18.1 | -10.1 | -10.1 | -12 | -10.1 | -16.1 | -18.1 | -13.2 | -12 | -14.5 | -14.5 | -14.5 | -18.1 | -18.1 | -13.2 | 0

## Slide 12: Cross-correlation
NCP for Ipatov sequence of length 121
(dB) | s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s17 | s18 | s19 | s20 | s21 | s22
s1 | 0 | -19.1 | -14.6 | -19.1 | -13.1 | -13.1 | -14.6 | -19.1 | -11.7 | -11.7 | -13.1 | -13.1 | -11.7 | -13.1 | -13.1 | -19.1 | -19.1 | -11.7 | -19.1 | -11.7 | -14.6 | -11.7
s2 | -19.1 | 0 | -19.1 | -14.6 | -13.1 | -13.1 | -11.7 | -11.7 | -19.1 | -19.1 | -11.7 | -13.1 | -14.6 | -19.1 | -13.1 | -11.7 | -11.7 | -13.1 | -13.1 | -19.1 | -11.7 | -14.6
s3 | -14.6 | -19.1 | 0 | -19.1 | -13.1 | -13.1 | -19.1 | -14.6 | -11.7 | -11.7 | -13.1 | -13.1 | -13.1 | -11.7 | -11.7 | -19.1 | -19.1 | -13.1 | -14.6 | -11.7 | -19.1 | -11.7
s4 | -19.1 | -14.6 | -19.1 | 0 | -13.1 | -13.1 | -11.7 | -11.7 | -19.1 | -19.1 | -13.1 | -11.7 | -19.1 | -14.6 | -13.1 | -11.7 | -11.7 | -13.1 | -11.7 | -14.6 | -13.1 | -19.1
s5 | -13.1 | -13.1 | -13.1 | -13.1 | 0 | -14.6 | -19.1 | -14.6 | -13.1 | -11.7 | -19.1 | -19.1 | -11.7 | -11.7 | -19.1 | -11.7 | -13.1 | -19.1 | -11.7 | -19.1 | -11.7 | -14.6
s6 | -13.1 | -13.1 | -13.1 | -13.1 | -14.6 | 0 | -14.6 | -19.1 | -11.7 | -13.1 | -19.1 | -19.1 | -11.7 | -11.7 | -19.1 | -13.1 | -11.7 | -19.1 | -11.7 | -14.6 | -11.7 | -19.1
s7 | -14.6 | -11.7 | -19.1 | -11.7 | -19.1 | -14.6 | 0 | -14.6 | -19.1 | -19.1 | -11.7 | -11.7 | -19.1 | -19.1 | -11.7 | -11.7 | -13.1 | -13.1 | -13.1 | -13.1 | -13.1 | -13.1
s8 | -19.1 | -11.7 | -14.6 | -11.7 | -14.6 | -19.1 | -14.6 | 0 | -19.1 | -19.1 | -11.7 | -11.7 | -19.1 | -19.1 | -13.1 | -13.1 | -11.7 | -11.7 | -13.1 | -13.1 | -13.1 | -13.1
s9 | -11.7 | -19.1 | -11.7 | -19.1 | -13.1 | -11.7 | -19.1 | -19.1 | 0 | -14.6 | -14.6 | -19.1 | -11.7 | -11.7 | -13.1 | -14.6 | -19.1 | -13.1 | -13.1 | -13.1 | -13.1 | -11.7
s10 | -11.7 | -19.1 | -11.7 | -19.1 | -11.7 | -13.1 | -19.1 | -19.1 | -14.6 | 0 | -19.1 | -14.6 | -11.7 | -11.7 | -13.1 | -19.1 | -14.6 | -13.1 | -13.1 | -11.7 | -13.1 | -13.1
s11 | -13.1 | -11.7 | -13.1 | -13.1 | -19.1 | -19.1 | -11.7 | -11.7 | -14.6 | -19.1 | 0 | -14.6 | -19.1 | -19.1 | -11.7 | -13.1 | -13.1 | -11.7 | -14.6 | -11.7 | -19.1 | -13.1
s12 | -13.1 | -13.1 | -13.1 | -11.7 | -19.1 | -19.1 | -11.7 | -11.7 | -19.1 | -14.6 | -14.6 | 0 | -19.1 | -19.1 | -11.7 | -13.1 | -13.1 | -11.7 | -19.1 | -13.1 | -14.6 | -11.7
s13 | -11.7 | -14.6 | -13.1 | -19.1 | -11.7 | -11.7 | -19.1 | -19.1 | -11.7 | -11.7 | -19.1 | -19.1 | 0 | -14.6 | -14.6 | -13.1 | -13.1 | -19.1 | -11.7 | -13.1 | -13.1 | -13.1
s14 | -13.1 | -19.1 | -11.7 | -14.6 | -11.7 | -11.7 | -19.1 | -19.1 | -11.7 | -11.7 | -19.1 | -19.1 | -14.6 | 0 | -19.1 | -13.1 | -13.1 | -14.6 | -13.1 | -13.1 | -11.7 | -13.1
s15 | -13.1 | -13.1 | -11.7 | -13.1 | -19.1 | -19.1 | -11.7 | -13.1 | -13.1 | -13.1 | -11.7 | -11.7 | -14.6 | -19.1 | 0 | -19.1 | -14.6 | -14.6 | -19.1 | -11.7 | -19.1 | -11.7
s16 | -19.1 | -11.7 | -19.1 | -11.7 | -11.7 | -13.1 | -11.7 | -13.1 | -14.6 | -19.1 | -13.1 | -13.1 | -13.1 | -13.1 | -19.1 | 0 | -14.6 | -14.6 | -11.7 | -19.1 | -11.7 | -19.1
s17 | -19.1 | -11.7 | -19.1 | -11.7 | -13.1 | -11.7 | -13.1 | -11.7 | -19.1 | -14.6 | -13.1 | -13.1 | -13.1 | -13.1 | -14.6 | -14.6 | 0 | -19.1 | -11.7 | -19.1 | -11.7 | -19.1
s18 | -11.7 | -13.1 | -13.1 | -13.1 | -19.1 | -19.1 | -13.1 | -11.7 | -13.1 | -13.1 | -11.7 | -11.7 | -19.1 | -14.6 | -14.6 | -14.6 | -19.1 | 0 | -19.1 | -11.7 | -19.1 | -11.7
s19 | -19.1 | -13.1 | -14.6 | -11.7 | -11.7 | -11.7 | -13.1 | -13.1 | -13.1 | -13.1 | -14.6 | -19.1 | -11.7 | -13.1 | -19.1 | -11.7 | -11.7 | -19.1 | 0 | -19.1 | -14.6 | -19.1
s20 | -11.7 | -19.1 | -11.7 | -14.6 | -19.1 | -14.6 | -13.1 | -13.1 | -13.1 | -11.7 | -11.7 | -13.1 | -13.1 | -13.1 | -11.7 | -19.1 | -19.1 | -11.7 | -19.1 | 0 | -19.1 | -14.6
s21 | -14.6 | -11.7 | -19.1 | -13.1 | -11.7 | -11.7 | -13.1 | -13.1 | -13.1 | -13.1 | -19.1 | -14.6 | -13.1 | -11.7 | -19.1 | -11.7 | -11.7 | -19.1 | -14.6 | -19.1 | 0 | -19.1
s22 | -11.7 | -14.6 | -11.7 | -19.1 | -14.6 | -19.1 | -13.1 | -13.1 | -11.7 | -13.1 | -13.1 | -11.7 | -13.1 | -13.1 | -11.7 | -19.1 | -19.1 | -11.7 | -19.1 | -14.6 | -19.1 | 0

## Slide 13: Cross-correlation
The PDF of NCP for Ipatov sequence of different lengths

## Slide 14: Cross-correlation
length 91 vs length 121(card=8)
Length 121 has better cross-correlation in the sense of worst case, best case and median case
NCP (dB) 91 | Seq25 | Seq26 | Seq27 | Seq28 | Seq29 | Seq30 | Seq31 | Seq32
Seq25 | 0 | -14.6 | -10.2 | -10.6 | -10.6 | -13.6 | -9.5 | -13.1
Seq26 | -14.6 | 0 | -10.6 | -13.6 | -10.2 | -10.6 | -10.6 | -10.9
Seq27 | -10.2 | -10.6 | 0 | -14.6 | -13.6 | -10.6 | -10.2 | -10.6
Seq28 | -10.6 | -13.6 | -14.6 | 0 | -10.6 | -10.2 | -12.1 | -9.5
Seq29 | -10.6 | -10.2 | -13.6 | -10.6 | 0 | -14.6 | -13.1 | -12.1
Seq30 | -13.6 | -10.6 | -10.6 | -10.2 | -14.6 | 0 | -10.9 | -10.2
Seq31 | -9.5 | -10.6 | -10.2 | -12.1 | -13.1 | -10.9 | 0 | -10.6
Seq32 | -13.1 | -10.9 | -10.6 | -9.5 | -12.1 | -10.2 | -10.6 | 0
NCP (dB) 121 | s1 | s2 | s3 | s4 | s7 | s8 | s9 | s10
s1 | 0 | -19.1 | -14.6 | -19.1 | -14.6 | -19.1 | -11.7 | -11.7
s2 | -19.1 | 0 | -19.1 | -14.6 | -11.7 | -11.7 | -19.1 | -19.1
s3 | -14.6 | -19.1 | 0 | -19.1 | -19.1 | -14.6 | -11.7 | -11.7
s4 | -19.1 | -14.6 | -19.1 | 0 | -11.7 | -11.7 | -19.1 | -19.1
s7 | -14.6 | -11.7 | -19.1 | -11.7 | 0 | -14.6 | -19.1 | -19.1
s8 | -19.1 | -11.7 | -14.6 | -11.7 | -14.6 | 0 | -19.1 | -19.1
s9 | -11.7 | -19.1 | -11.7 | -19.1 | -19.1 | -19.1 | 0 | -14.6
s10 | -11.7 | -19.1 | -11.7 | -19.1 | -19.1 | -19.1 | -14.6 | 0

## Slide 15: Summary
Consider the future increasing of UWB devices and the new regulations of MIIT, the cardinality of the selected Ipatov sequences shall be large
Different length Ipatov sequence can have similar mean PRF and energy by setting the SF and repetition properly
All the Ipatov sequences have very good autocorrelation even if the CFO is as larger as 40ppm
The Ipatov sequence of length 121 have good cross correlation between each other

## Slide 16: References
[1] V. P. Ipatov, “Ternary sequences with ideal autocorrelation properties” Radio Eng. Electron. Phys., vol. 24, pp. 75−79, Oct. 1979.
[2] 15-18-0590-00-004z-hrp-uwb-phy-enhanced-mode-converged-consensus (Billy Verso)
[3] 15-23-0023-02-04ab-china-miit-s-consultation-on-uwb(Bin Qian)
[4] 15-21-0377-00-04ab-preamble-codes-for-data-communications (Carlos Aldana)
[5] 15-22-0616-00-04ab-interference-analysis-of-initial-synchronization-sequence.pptx (Chenchen Liu)
[6] 15-22-0507-00-04ab-simulation-evaluation-of-preamble-sequences-for-4ab(Chenchen Liu)
[7] D. Shedd and D. Sarwate, "Construction of sequences with good correlation properties (Corresp.)," in IEEE Transactions on Information Theory, vol. 25, no. 1, pp. 94-97, January 1979
[8] T. Hoholdt and J. Justesen, "Ternary sequences with perfect periodic autocorrelation (Corresp.)," in IEEE Transactions on Information Theory, vol. 29, no. 4, pp. 597-600, July 1983
[9] P802.15.4z, Draft Standard for Low-Rate Wireless Networks

## Slide 17: Appendix Ipatov sequences of length 121
Sequence | Code sequence
s1 | 1 0 0 0 -1 1 0 0 -1 0 1 0 -1 -1 1 1 -1 1 0 -1 0 0 1 -1 -1 0 1 0 1 -1 1 1 1 0 0 -1 -1 1 0 -1 1 0 1 -1 0 1 1 0 -1 1 -1 1 -1 0 0 0 0 -1 0 0 0 -1 -1 0 0 -1 1 -1 0 -1 0 0 -1 -1 -1 0 -1 1 1 -1 -1 0 -1 0 1 -1 -1 -1 1 0 1 1 0 1 1 -1 1 1 -1 0 0 -1 0 -1 0 -1 -1 -1 -1 -1 1 1 1 1 0 -1 -1 -1 1 -1 1
s2 | 1 0 -1 0 -1 1 -1 1 -1 0 0 1 -1 1 1 1 1 0 -1 0 1 1 0 1 -1 -1 -1 0 0 0 0 -1 0 1 0 0 -1 -1 -1 1 -1 -1 1 -1 1 1 0 1 1 -1 0 0 0 -1 -1 1 1 0 -1 1 1 0 0 1 0 0 0 -1 1 1 -1 0 -1 0 0 -1 1 0 -1 1 -1 0 -1 1 0 1 1 0 0 -1 0 -1 0 -1 -1 -1 0 -1 0 1 -1 0 0 -1 -1 0 1 1 -1 1 0 -1 -1 -1 -1 -1 1 1 -1 -1 -1
s3 | 1 -1 1 -1 -1 -1 0 1 1 1 1 -1 -1 -1 -1 -1 0 -1 0 -1 0 0 -1 1 1 -1 1 1 0 1 1 0 1 -1 -1 -1 1 0 -1 0 -1 -1 1 1 -1 0 -1 -1 -1 0 0 -1 0 -1 1 -1 0 0 -1 -1 0 0 0 -1 0 0 0 0 -1 1 -1 1 -1 0 1 1 0 -1 1 0 1 -1 0 1 -1 -1 0 0 1 1 1 -1 1 0 1 0 -1 -1 1 0 0 -1 0 1 -1 1 1 -1 -1 0 1 0 -1 0 0 1 -1 0 0 0 1
s4 | -1 -1 -1 1 1 -1 -1 -1 -1 -1 0 1 -1 1 1 0 -1 -1 0 0 -1 1 0 -1 0 -1 -1 -1 0 -1 0 -1 0 0 1 1 0 1 -1 0 -1 1 -1 0 1 -1 0 0 -1 0 -1 1 1 -1 0 0 0 1 0 0 1 1 -1 0 1 1 -1 -1 0 0 0 -1 1 1 0 1 1 -1 1 -1 -1 1 -1 -1 -1 0 0 1 0 -1 0 0 0 0 -1 -1 -1 1 0 1 1 0 -1 0 1 1 1 1 -1 1 0 0 -1 1 -1 1 -1 0 -1 0 1
s5 | 1 -1 0 -1 -1 -1 0 -1 1 -1 -1 1 -1 1 -1 -1 -1 0 0 -1 1 -1 0 -1 1 1 1 -1 -1 -1 -1 -1 0 1 0 0 -1 -1 -1 1 0 0 -1 1 1 -1 0 1 -1 1 -1 0 0 -1 0 1 1 -1 -1 1 1 0 0 -1 0 0 0 0 -1 -1 1 0 1 0 0 1 1 0 1 1 0 -1 -1 -1 -1 1 -1 -1 0 1 -1 -1 0 -1 0 1 0 1 0 1 -1 0 0 0 1 0 1 1 -1 1 0 -1 0 1 -1 0 1 1 0 0 0

## Slide 18: Appendix Ipatov sequences of length 121
Sequence | Code sequence
s6 | 0 0 0 1 1 0 -1 1 0 -1 0 1 -1 1 1 0 1 0 0 0 -1 1 0 1 0 1 0 -1 0 -1 -1 1 0 -1 -1 1 -1 -1 -1 -1 0 1 1 0 1 1 0 0 1 0 1 -1 -1 0 0 0 0 -1 0 0 1 1 -1 -1 1 1 0 -1 0 0 -1 1 -1 1 0 -1 1 1 -1 0 0 1 -1 -1 -1 0 0 1 0 -1 -1 -1 -1 -1 1 1 1 -1 0 -1 1 -1 0 0 -1 -1 -1 1 -1 1 -1 -1 1 -1 0 -1 -1 -1 0 -1 1
s7 | 1 -1 -1 -1 1 1 -1 0 0 -1 -1 1 1 0 1 1 0 1 -1 1 -1 0 0 0 0 -1 -1 -1 -1 1 -1 0 1 1 1 0 1 0 -1 0 1 -1 1 0 1 1 1 -1 0 -1 1 1 0 -1 -1 1 -1 1 -1 -1 -1 -1 -1 0 1 -1 0 -1 0 0 -1 1 0 0 -1 -1 0 0 -1 0 -1 -1 1 0 -1 0 0 1 0 -1 -1 0 1 0 1 0 1 -1 0 1 -1 -1 1 -1 -1 0 0 0 1 0 0 0 1 -1 -1 -1 0 0 1 -1 1
s8 | 1 -1 1 0 0 -1 -1 -1 1 0 0 0 1 0 0 0 -1 -1 1 -1 -1 1 0 -1 1 0 1 0 1 0 -1 -1 0 1 0 0 -1 0 1 -1 -1 0 -1 0 0 -1 -1 0 0 1 -1 0 0 -1 0 -1 1 0 -1 -1 -1 -1 -1 1 -1 1 -1 -1 0 1 1 -1 0 -1 1 1 1 0 1 -1 1 0 -1 0 1 0 1 1 1 0 -1 1 -1 -1 -1 -1 0 0 0 0 -1 1 -1 1 0 1 1 0 1 1 -1 -1 0 0 -1 1 1 -1 -1 -1 1'
s9 | 1 -1 -1 -1 -1 0 -1 1 1 -1 1 0 -1 -1 0 0 0 0 -1 -1 -1 1 1 0 1 0 0 -1 1 -1 1 0 0 0 1 -1 -1 0 1 -1 -1 -1 0 1 0 0 0 -1 0 0 -1 0 -1 1 -1 0 -1 -1 1 -1 -1 0 0 1 1 0 1 1 1 0 0 1 1 -1 0 0 -1 1 0 -1 1 -1 -1 1 1 -1 0 -1 1 0 1 0 1 0 -1 1 0 0 -1 0 1 0 1 1 0 -1 -1 -1 -1 -1 1 0 -1 0 1 1 -1 -1 -1 1 -1
s10 | -1 1 -1 -1 -1 1 1 0 -1 0 1 -1 -1 -1 -1 -1 0 1 1 0 1 0 -1 0 0 1 -1 0 1 0 1 0 1 -1 0 -1 1 1 -1 -1 1 -1 0 1 -1 0 0 -1 1 1 0 0 1 1 1 0 1 1 0 0 -1 -1 1 -1 -1 0 -1 1 -1 0 -1 0 0 -1 0 0 0 1 0 -1 -1 -1 1 0 -1 -1 1 0 0 0 1 -1 1 -1 0 0 1 0 1 1 -1 -1 -1 0 0 0 0 -1 -1 0 1 -1 1 1 -1 0 -1 -1 -1 -1 1

## Slide 19: Appendix Ipatov sequences of length 121
Sequence | Code sequence
s11 | 1 1 0 1 0 -1 0 -1 1 1 1 1 0 0 -1 -1 1 0 0 0 -1 -1 0 1 1 -1 -1 1 1 0 1 -1 0 1 1 1 0 -1 0 0 0 0 -1 1 1 -1 0 -1 1 -1 0 0 1 0 0 1 -1 0 0 -1 -1 -1 -1 -1 1 -1 0 -1 -1 1 -1 1 1 1 -1 -1 -1 0 -1 -1 -1 1 0 -1 1 0 1 0 0 -1 1 -1 1 -1 0 1 0 -1 1 1 0 -1 1 -1 -1 1 -1 -1 0 0 0 -1 0 -1 0 -1 -1 0 0 -1 0
s12 | 0 -1 0 0 -1 -1 0 -1 0 -1 0 0 0 -1 -1 1 -1 -1 1 -1 0 1 1 -1 0 1 0 -1 1 -1 1 -1 0 0 1 0 1 -1 0 1 -1 -1 -1 0 -1 -1 -1 1 1 1 -1 1 -1 -1 0 -1 1 -1 -1 -1 -1 -1 0 0 -1 1 0 0 1 0 0 -1 1 -1 0 -1 1 1 -1 0 0 0 0 -1 0 1 1 1 0 -1 1 0 1 1 -1 -1 1 1 0 -1 -1 0 0 0 1 -1 -1 0 0 1 1 1 1 -1 0 -1 0 1 0 1 1
s13 | 1 -1 1 -1 0 -1 1 1 0 -1 -1 0 0 -1 -1 -1 1 1 1 -1 1 1 1 1 0 1 0 -1 -1 -1 -1 -1 1 0 0 -1 0 -1 0 -1 -1 1 -1 0 0 -1 1 1 1 0 -1 1 -1 0 1 0 1 -1 0 1 1 -1 -1 1 0 -1 1 0 1 1 1 0 0 -1 -1 1 0 1 0 0 0 -1 0 1 -1 -1 1 -1 1 1 -1 -1 0 -1 -1 0 1 0 -1 0 0 -1 0 0 1 -1 0 0 0 -1 1 -1 -1 0 0 0 0 -1 -1 0 -1
s14 | -1 0 -1 -1 0 0 0 0 -1 -1 1 -1 0 0 0 -1 1 0 0 -1 0 0 -1 0 1 0 -1 -1 0 -1 -1 1 1 -1 1 -1 -1 1 0 -1 0 0 0 1 0 1 -1 -1 0 0 1 1 1 0 1 -1 0 1 -1 -1 1 1 0 -1 1 0 1 0 -1 1 -1 0 1 1 1 -1 0 0 -1 1 -1 -1 0 -1 0 -1 0 0 1 -1 -1 -1 -1 -1 0 1 0 1 1 1 1 -1 1 1 1 -1 -1 -1 0 0 -1 -1 0 1 1 -1 0 -1 1 -1 1
s15 | 1 0 1 0 1 -1 1 1 0 0 0 1 1 1 -1 -1 1 -1 1 -1 -1 1 0 1 0 0 -1 0 0 -1 0 1 -1 1 -1 0 1 1 -1 1 0 1 -1 0 1 -1 -1 -1 1 -1 -1 -1 0 -1 1 1 -1 -1 -1 -1 -1 0 0 1 -1 0 0 -1 1 1 0 -1 0 0 0 0 -1 0 -1 -1 -1 0 1 1 0 1 1 -1 0 0 0 1 -1 1 0 0 -1 -1 0 1 -1 0 -1 -1 0 0 -1 -1 1 1 0 1 0 -1 -1 -1 -1 1 0 -1 0

## Slide 20: Appendix Ipatov sequences of length 121
Sequence | Code sequence
s16 | -1 0 -1 0 0 0 0 -1 -1 1 1 0 -1 0 0 -1 -1 0 0 1 0 0 -1 -1 -1 -1 -1 1 0 1 -1 -1 1 1 1 0 -1 -1 -1 0 0 0 -1 1 0 -1 1 -1 -1 0 -1 1 -1 0 1 1 0 -1 1 1 1 1 0 1 1 0 1 0 -1 -1 1 -1 1 1 -1 0 0 -1 0 1 -1 0 0 1 -1 -1 0 0 -1 1 -1 1 -1 0 -1 -1 -1 1 1 -1 1 1 1 -1 1 0 0 0 -1 0 -1 0 -1 -1 1 0 -1 0 1 0 1
s17 | 1 0 1 0 -1 0 1 -1 -1 0 -1 0 -1 0 0 0 1 -1 1 1 1 -1 1 1 -1 -1 -1 0 -1 1 -1 1 -1 0 0 -1 -1 1 0 0 -1 1 0 -1 0 0 -1 1 1 -1 1 -1 -1 0 1 0 1 1 0 1 1 1 1 -1 0 1 1 0 -1 1 -1 0 -1 -1 1 -1 0 1 -1 0 0 0 -1 -1 -1 0 1 1 1 -1 -1 1 0 1 -1 -1 -1 -1 -1 0 0 1 0 0 -1 -1 0 0 -1 0 1 1 -1 -1 0 0 0 0 -1 0 -1
s18 | 0 -1 0 1 -1 -1 -1 -1 0 1 0 1 1 -1 -1 0 0 -1 -1 0 -1 1 0 -1 -1 0 0 1 -1 1 0 0 0 -1 1 1 0 1 1 0 -1 -1 -1 0 -1 0 0 0 0 -1 0 1 1 -1 0 0 -1 1 0 0 -1 -1 -1 -1 -1 1 1 -1 0 -1 -1 -1 1 -1 -1 -1 1 0 -1 1 0 1 -1 1 1 0 -1 1 -1 1 0 -1 0 0 -1 0 0 1 0 1 -1 -1 1 -1 1 -1 -1 1 1 1 0 0 0 1 1 -1 1 0 1 0 1
s19 | 1 1 1 1 0 0 1 -1 1 1 -1 0 0 -1 0 0 -1 -1 1 -1 0 -1 1 -1 1 -1 0 1 -1 -1 -1 0 -1 0 1 0 0 0 -1 -1 -1 1 0 1 0 0 -1 0 -1 0 -1 -1 0 -1 1 0 0 -1 -1 0 0 0 0 -1 1 0 1 1 -1 -1 -1 1 1 0 0 -1 1 1 0 1 1 1 0 -1 -1 -1 -1 -1 1 -1 -1 0 1 0 -1 1 -1 0 0 0 -1 0 1 1 -1 0 1 1 0 -1 1 0 -1 0 -1 1 1 -1 -1 1 -1
s20 | 1 1 0 1 1 -1 0 0 -1 1 0 1 1 0 -1 -1 -1 1 0 -1 -1 0 0 -1 -1 -1 0 1 0 -1 0 0 1 1 -1 -1 1 0 1 0 1 0 -1 -1 1 -1 1 -1 -1 0 -1 1 -1 1 0 1 -1 -1 1 -1 -1 1 1 0 -1 1 0 -1 0 -1 -1 -1 -1 -1 1 -1 0 0 0 0 -1 1 1 0 0 0 -1 -1 0 -1 0 0 -1 0 1 -1 1 0 -1 1 1 1 -1 -1 -1 -1 0 0 1 0 0 0 1 0 1 -1 0 0 1 -1 1

## Slide 21: Appendix Ipatov sequences of length 121
Sequence | Code sequence
s21 | -1 1 -1 -1 1 1 -1 0 -1 0 1 -1 0 1 1 0 -1 1 1 0 -1 0 0 0 -1 1 -1 0 1 0 -1 -1 1 -1 -1 -1 -1 -1 0 1 1 1 0 1 1 -1 0 0 1 1 -1 -1 -1 1 1 0 1 -1 0 0 0 0 -1 -1 0 0 1 -1 0 -1 -1 0 -1 0 -1 0 0 1 0 1 -1 -1 -1 0 0 0 1 0 -1 0 -1 -1 -1 1 0 -1 1 -1 1 -1 0 -1 1 -1 -1 0 0 -1 0 0 -1 1 1 -1 1 0 0 1 1 1 1
s22 | 1 -1 1 0 0 -1 1 0 1 0 0 0 1 0 0 -1 -1 -1 -1 1 1 1 -1 0 1 -1 1 0 -1 0 0 -1 0 -1 -1 0 0 0 1 1 -1 0 0 0 0 -1 1 -1 -1 -1 -1 -1 0 -1 0 1 -1 0 1 1 -1 -1 1 -1 -1 1 0 1 -1 1 -1 0 -1 -1 1 -1 1 -1 -1 0 1 0 1 0 1 -1 -1 1 1 0 0 -1 0 1 0 -1 -1 -1 0 0 -1 -1 0 1 -1 -1 -1 0 1 1 0 1 -1 0 0 -1 1 1 0 1 1