## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Ultra-Wideband Swarm Ranging Protocol for Dynamic and Dense Networks
Source: Feng Shan, Haodong Huo, Chunyi Li (Southeast University, China)
Address : [2 Sipailou, Nanjing, 210012 China]
E-Mail: [shanfeng@seu.edu.cn]
Re: 141st IEEE 802.15 WSN Meeting, WNG
Abstract: [UWB, swarm ranging, two way ranging]
Purpose:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Ultra-Wideband Swarm Ranging Protocol for
Dynamic and Dense Networks
Feng Shan, Haodong Huo, Jiaxin Zeng, Zengbao Li, Weiwei Wu, and Junzhou Luo, “Ultra-Wideband Swarm Ranging Protocol for Dynamic and Dense Networks,” IEEE/ACM Transactions on Networking (ToN), vol. 30, no. 6 (2022): 2834-2848. (Open Access at DOI: 10.1109/TNET.2022.3186071)

## Slide 3
I am Feng SHAN, an Associate Professor at School of Computer Science and Engineering, Southeast University (SEU), Nanjing, China.
I received the Ph.D. degree in Computer Science from Southeast University in 2015, supervised by Professor Junzhou Luo.
I was a Visiting Scholar at the School of Computing and Engineering, University of Missouri-Kansas City, Kansas City, MO, USA, from 2010 to 2012.
My research interests are in the areas of wireless communication, unmanned system swarm cooperation, algorithm design and analysis.
Who am I?

## Slide 4
SEU-NetSI Research Group Introduction
NetSI group conducts research in the area of Internet of Things and Swarm Intelligence. More specially, the focus is on the wireless networking for a swarm of moving things and study how to coordinate their collaboration.
NetSI group research goal is to provide theoretically sound analysis as well as build practically working systems.

## Slide 5
Outline
Introduction
Preliminary
Protocol Design
Experiment
Conclusion

## Slide 6
Outline
Introduction
Preliminary
Protocol Design
Experiment
Conclusion

## Slide 7
Swarm of robots and devices
Aerial / ground robots, wearable / portable devices are
becoming smaller, lighter, and cheaper.
Crazyflie 2.1
Robo Master EP
SPOT
Hundreds of them may form a swarm to participate in
complicated cooperative tasks.
An army of legged robot dogs battle in a deep forest.
A team of drones search for given targets.
A swarm of small robots explore and map unknown environments.
Mobile phone

## Slide 8
Dynamic and dense swarm network
Dynamic and dense swarm
Large number.
High mobility.
Short distance.
Requirements
Real-time internal distance ranging
for localization.
Low latency ad hoc networking
and communication.

## Slide 9
Ultra-wideband swarm ranging protocol
Ultra-wideband (UWB) wireless technology support simultaneously ranging and communication.
Our target is to design a UWB ranging protocol for a dynamic and dense networks of robots and devices.

## Slide 10
Challenges to design such a ranging protocol
Design a simple yet efficient protocol
  A large number share the same UWB channel.
  Inappropriate cause conflicting and high computation cost.
Design a adaptive and robust protocol
  High mobility requires high frequency ranging.
  Ranging frequency should be reduced whenever necessary.
  Also cause wireless channel unstable and packet lose.
Design a scalable and compatible protocol
  Message has limitation space for dense neighbor.
  Support existing networking and localization protocols.

## Slide 11
Outline
Introduction
Preliminary
Protocol Design
Experiment
Conclusion

## Slide 12: Double-sided two-way ranging (DS-TWR)
Double-sided two-way ranging (DS-TWR)
  An existing ranging protocol from IEEE Standard 802.15.4-2011 is later improved by industry giant Decawave.
Distance calculated after exchanging four messages
  poll, response, final, and report messages.
A
B
poll
response
final
report
time
time
reply
time
round
time
reply
time
round
time
(carry , ,
time stamps)

## Slide 13: Double-sided two-way ranging (DS-TWR)
Recorded timestamps :
Calculate the round and reply time:
Time of flight:
Conclusion: ranging if has
A
B
poll
response
final
report
time
time
reply
time
round
time
reply
time
round
time
(carry , ,
time stamps)
B side |  |  |  | 
A side |  |  |  | 
B side |  |  |  | 
A side |  |  |  | 

## Slide 14
IEEE 802.15.4z-2020
Enhanced MAC and PHY layer to achieve higher ranging accuracy.
Detailed specification for many-to-many DS-TWR.
Pre-allocated time slots, unable to handle dynamic join and leave devices.
Too complicated to implement on low-end devices.
"IEEE Standard for Low-Rate Wireless Networks--Amendment 1: Enhanced Ultra Wideband (UWB) Physical Layers (PHYs) and Associated Ranging Techniques," in IEEE Std 802.15.4z-2020 (Amendment to IEEE Std 802.15.4-2020) , vol., no., pp.1-174, 25 Aug. 2020

## Slide 15
DS-TWR
Token
A
B
C
A practical implementation – Token Ring
Maintain a global token to control the ranging process. Token owner initializes ranging process with all its neighbors, one by one. Then, pass the token to the next in the ring.
Token Ring method can avoid channel collision.
Broecker B, Tuyls K, Butterworth J. Distance-based multi-robot coordination on pocket drones[C]//2018 IEEE International Conference on Robotics and Automation (ICRA). IEEE, 2018: 6389-6394.

## Slide 16
A practical implementation – Token Ring
Inefficient: messages heard by all neighbors, but are mostly ignored.
Unstable: when the global token is lost, the entire ranging process crashes.
DS-TWR
Token
A
B
C

## Slide 17
The basic idea of swarm ranging
Define one single message named ranging message
Each side periodically broadcasts the ranging message
ranging message
Broadcast ranging message
A
B
C
A
C
A
B
B
C

## Slide 18
The basic idea of swarm ranging
To deal with the challenges of the dynamic and dense swarm, the following questions must be answered.
  Q1: How to design the ranging message so that sufﬁcient timestamps are carried?
  Q2: Does the enlarged transmit period affect accuracy?
  Q3: How does high mobility affect the ranging accuracy?
  Q4: How often should the ranging message be broadcasted?
  Q5: What if message lost or ranging frequency mismatched?
  Q6: How to handle dense neighbors?
  Q7: Does the swarm ranging protocol supports or compatible with other higher level protocols?

## Slide 19
Outline
Introduction
Preliminary
Protocol Design
Experiment
Conclusion

## Slide 20: Ranging message and ranging table
Each ranging message includes
  The last transmit timestamp
  All receive timestamps since last transmit
Ranging table keeps only few timestamps
A
Y
Y side |  |  |  | 
A side |  |  |  | 
Y side |  |  |  | 
A side |  |  |  | 

## Slide 21
Each ranging message includes
  The last transmit timestamp
  All receive timestamps since last transmit
Ranging table keeps only few timestamps
Q1 (ranging message design) is answered
Ranging message and ranging table

## Slide 22: How mobility affect ranging accuracy
A
Y
time
time
distance
A
Y
Distance computed:

## Slide 23: How mobility affect ranging accuracy
A
Y
time
time
distance
A
Y
Distance computed:
Q3 (mobility affects accuracy) is answered

## Slide 24: Design of adaptive ranging protocol
Calculation occurs at receiving , the actual ToF:
Bound the error:
Then:
Consider , Finally:
As a conclusion
  When two sides are close, use short ranging period;
  When two sides move fast, use short ranging period.
Q4 (broadcast frequency) is answered

## Slide 25: Packet loss and ranging period mismatch
We summary four cases.
  Case 1, side receives more than it transmits.
  Case 2, one message from side is lost.
  Case 3, side transmits more than it receives.
  Case 4, one message from side is lost.
A
Y
A
Y
A
Y
A
Y
Case 1
Case 2
Case 3
Case 4

## Slide 26: Handle mismatch and loss
Handle Case 1 and Case 2
Y side |  |  |  | 
A side |  |  | or | 
Y side |  |  |  | 
A side |  |  |  | 
Y side |  |  |  | 
A side |  |  |  | 
Y side |  |  |  | 
A side |  |  |  | 
A
Y
A
Y
Case 1
Case 2
Notes:   Case 1, 𝐴 side receives more than it transmits.
  Case 2, one message from 𝐴 side is lost.
  for both cases, after updating the ranging table normally, we will found a missing timestamp here, so we discard some timestamp to prepare for the next round

## Slide 27: Handle mismatch and loss
Handle Case 4
Y side |  |  |  | 
A side |  |  |  | 
Y side |  |  |  | 
A side |  |  |  | 
Y side |  |  |  | 
A side |  |  |  | 
Y side |  |  |  | 
A side |  |  |  | 
Q5 (packet loss and mismatched frequency) is answered
A
Y
Case 4
Notes: Case 4, one message from 𝑌 side is lost.
after updating the ranging table normally, we will found mismatched timestamps, so we discard some timestamp to prepare for the next round

## Slide 28: Handle dense neighbors
When the neighbors are dense, ranging message capacity will not be enough to carry all timestamps for every neighbor.
Our solution:
  Allow neighbors to have different ranging periods.
  Carry neighbors’ information only when necessary.
  Expire neighbors’ information after a certain time.
Upgrade the ranging table by adding new elements
  : the newest ranging period for A and Y
  : the next (expected) delivery time for neighbor Y
  : the expiration time for neighbor Y
Y side |  |  |  |  | 
A side |  |  |  |  | 
Y side |  |  |  |  | 
A side |  |  |  |  | 

## Slide 29: Handle dense neighbors
Selectively include known neighbors’ timestamp information in every ranging message M according tountil reach the maximum size limitation. Update each included neighbors’to T (local clock time of A) + P.
Time
T1
M1={A, B, C, D}
T2
T3
Time Interval
M2={D, A, B, E}
M3={C, D, B, A}
T4
M4={E, C, B, D}
Q6 (dense neighbor) is answered
Notes: Now I will show you how the new ranging table works:
Assume that device A received a ranging message MY from Y：
If Y is a new neighbor, A will initialize a corresponding ranging table for it.
Then, A will record the reception time of message MY , extract ranging related timestamps from it and then fill these timestamps into corresponding cells of table TY .
After that, A will try to compute the distance between A and Y if there are sufficient timestamps in table TY .
Finally, the ranging period between A and Y will be updated according to the distance and velocity between them, the expiration time of TY will be refreshed.
点击鼠标
As I just introduced in the last slide, when neighbors are dense, ranging message capacity will not be enough to carry all timestamps for every neighbor with respect to the payload size limitation of MAC layer.
Since we allow different neighbors to have different ranging periods, starvation will occur.
To guarantee the fairness of ranging resource allocation, we proposed the following allocation approach:
点击鼠标，播放动画
Assume that at the beginning there are only four known neighbors, A B C and D.
There next expected delivery time are annotated as 〖 𝒕〗_𝑨𝟏 〖 𝒕〗_𝑩𝟏 〖 𝒕〗_𝑪𝟏 〖 𝒕〗_𝑫𝟏 respectively.
点击鼠标，展示 T1
At time T1 , ranging related timestamps of neighbor A will be included in the current ranging message, and its next expected delivery time will be updated to T1 plus P, where T1 is the local clock time and P is the ranging period P in ranging table TA .
Similarly, B, C and D will also be included in message M1.
Here we assume that the message capacity is set to 4.
点击鼠标，展示 T2 和 〖 𝒕〗_𝑬𝟏
At time T2 , here is a new neighbor E and its next expected delivery time is earlier than C, so in this round, C will not be included in ranging message M2.
点击鼠标，展示之后的所有动画：
In this way, our ranging protocol guaranteed the fairness in the dense neighbor scenarios, its performance in real-world experiments will be presented later.
Now, Q6 is answered.

## Slide 30: Support higher level protocols/algorithms
Maintains neighbor list for higher level protocol, e. g., OLSR.
Support for localization by providing the fundamental distance information
Applications
Fundamental
Technologies
Hardware
...
Drones
Robots
Mobile phones
Wearable devices
Ad Hoc
Networking
Network
Localization
Swarm Ranging
Source Seeking
Exploration
Battling
Mapping
...
Q7 (support higher level protocols) is answered

## Slide 31
Outline
Introduction
Preliminary
Protocol Design
Experiment
Conclusion

## Slide 32
Hardware
Crazyradio PA
Crazyflie 2.1
Flow deck
Lighthouse deck
DW1000/3000
UWB deck
Slide 32

## Slide 33: Ranging period and accuracy
The impact of ranging period on ranging accuracy
Slide 33

## Slide 34: Velocity, ranging period and accuracy
The ranging results are delayed compare to the ground truth.
The larger P, the bigger delay.
Velocity also affects the delay .
moving towards
moving away
Impact of ranging period
Slide 34

## Slide 35
Adaptive ranging period
Adaptive to velocity
Adaptive to distance
Slide 35

## Slide 36: Protocol performance
Performance for mismatched ranging period
Comparison with ranging based on token ring.
Slide 36

## Slide 37
Handle dense neighbors
Balances the allocation of ranging resources.
Guarantees fair chances for each drone to ranging.
Slide 37

## Slide 38
Scalability
Close to the optimal performance.
Even when there are 29 neighbors to respond to, our protocol can still guarantee that all the neighbors’ latest distances are measured every second.
Slide 38

## Slide 39: Demo Video
Slide 39

## Slide 40
Outline
Introduction
Preliminary
Protocol Design
Experiment
Conclusion

## Slide 41: Conclusion
We proposed a UWB swarm ranging protocol, designed specially for dynamic and dense networks.
It is simple yet efficient. All messages are unified in one, i.e., ranging message, which is broadcasted periodically.
It is adaptive and robust. The ranging period adapts to the ranging pair’s velocity and distance. Packet loss is handled appropriately.
It is scalable and compatible. A rotation scheme is designed to handle dense neighbors. Higher level networking and localization protocols and algorithms are supported.
Real-world experiment is conducted. The protocol is implemented on Crazyflie drones, that are powered by STM32 microcontrollers and have only 192KB memory.

## Slide 42: Comparison
Swarm Ranging Protocol
802.15.4z Many-to-Many DS-TWR
  Multiple roles and message types are involved.
  Pre-allocated time slots, not suitable for dynamic join and leave devices (time-scheduling mode).
  Contend control requires additional control information (contend mode).
  Require higher-level packet loss and ranging starvation handling.
  Suitable for application scenarios with low mobility and sparse devices.
  Only one message type is involved (Ranging Message), easy to implement.
  No additional ranging control overhead (i.e. RCP and RCUP).
  Packet loss is carefully considered and handled.
  Alleviate ranging starvation by utilizing local information.
  Designed for dynamic and dense swarm applications.
Open source code: https://github.com/SEU-NetSI/crazyflie-firmware

## Slide 43
Q&A