## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Round hopping and block assignment in hyper blocks
Date Submitted: March, 2023
Source: Rojan Chitrakar, Lei Huang, Kuan Wu, David Xun Yang (Huawei Technologies)
Email: rojan.chitrakar@huawei.com
Abstract: Considerations for round hopping and block assignment in hyper blocks
Purpose: Resolve issues with round hopping and block assignment in hyper blocks.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | Round hopping and block assignment issues in hyper block-based mode are resolved.
Infrastructure synchronization mechanisms | 

## Slide 3
Background: Hyper block
Hyper block concept that supports NBA-MMS-UWB ranging is introduced in [1].
A hyper block is a group of blocks.
Hyper block mode uses the time structure that is periodic
  Each hyper block consists of a whole number of blocks.
  different blocks may have different configuration for block duration, Round duration, and slot duration
[1] DCN 23-0059r0 (Jan 2023) “Hyper block concept for use of NBA-MMS”
Round
0
Round
1
Round
0
Round
1
Round
2
Round 5
Block 0
Block 1
Block 2
Hyper Block K
Round
0
……
Block 0
Block 1
Hyper Block K-1
Block 2
Block 0
Block 1
Hyper Block K
Block 2
Block 0
Block 1
Hyper Block K+1
Block 2
……
POLL
RESPONSE
1
1
REPORT
[NB] :
[UWB] :
One Ranging Round
POLL
RESPONSE
1
1
REPORT
2
2
3
3
4
4
POLL
RESPONSE
1
1
REPORT
2
2
3
3
4
4
POLL
RESPONSE
1
1
REPORT
POLL
RESPONSE
1
1
REPORT
2
2
3
3
4
4
5
5
6
6
One Ranging Round
One Ranging
Round
POLL
RESPONSE
1
1
REPORT
2
2
3
3
4
4
One Ranging Round
POLL
RESPONSE
1
1
REPORT
POLL
RESPONSE
1
1
REPORT
One Ranging
Round
One Ranging
Round

## Slide 4
Background: Round Hopping in 802.15.4z
The controller may decide to “hop” to a different ranging round in the next ranging block (i.e., if participating ERDEVs are using ranging round j in ranging block N, they will use ranging round k in ranging block N + 1, where k != j).
It is assumed that the devices participating in the ranging exchange have either (a) pre-negotiated a hopping sequence that is known to all devices, or (b) have exchanged all the information necessary such that each device can generate the hopping sequence so that they know which ranging round in each ranging block is to be used if hopping is triggered.
The Hopping Mode field (in the RR IE) specifies the hop mode for the ranging block, where zero means no hopping and one means hopping.

## Slide 5
Discussion
Round hopping algorithm itself is not standardized in 802.15.4z but it assumes that such algorithm exist and all devices participating in ranging know which ranging round in each ranging block is to be used if hopping is triggered. It is also assumed that a round will be allocated for each device in each block.
In addition the round hopping functions would assumed a fixed Number of Rounds per block.

## Slide 6
Problem
One or more blocks (in a hyper block) may not be suitable for a device (e.g., due to insufficient slot or round duration, block assigned for a different application etc.), so controller may not allocate a round for a device in every block.
  => However a device may not be aware of this and still needs to check every block whether it is allocated a round in the block, leading to power wastage.
If the Hopping function assumes a fixed value for the Number of Rounds per block N_Round (e.g., 2) that is smaller than the maximum possible value (e.g., 6), only a subset of rounds may be selected in the blocks with more rounds (e.g., block 1).
Insufficient # of slots (or round duration)
slots are never chosen
Block assigned for a different application

## Slide 7
Proposal
In the first and each subsequent allocated rounds, the Initiator informs the next assigned block and the Number of Rounds in the assigned block.
  Note: The controller may dynamically assign any block in a hyper block to devices or a network based on factors, such as but not limited to:
          Required slot numbers/durations, or application type (one-to-one, one-to-many ranging etc.), or transaction frequency requirements etc.

## Slide 8
Proposal
Once the next assigned block and the number of rounds in the block is known, devices (initiator(s) and responder(s)) can determine the allocated round in the next assigned block.
  If round hopping is not enabled, the allocated round is the same as in the previous block (unless a new round is explicitly assigned).
  If round hopping is enabled, the allocated round is calculated based on the block index and the Number of Rounds.
A new IE, Enhanced Ranging Round IE (ERR IE) may be defined.
  The ERR IE may be included in any message sent by the Initiator to the Responder in the current round (for example in the RCM or in the measurement report).
Octets: 1 | 1 | Bits: 0 | 1 - 15 | Octets: 2 | 0 or 1
Hyper Block Index | Relative Block Index | Hopping Mode | Round Index | Transmission Offset | Number of Rounds
ERR IE
Index of the hyper block in which the next assigned block is located
Relative Index of the next assigned block in the hyper block (first block = 0 etc.)
Number of Rounds in the block indicated by the Relative Block Index
Same meaning as in RR IE but applies to the next assigned block.

## Slide 9
Summary
We discussed the issue of block assignment and round hopping in hyper blocks.
We proposed that in the first and each subsequent allocated rounds, the Initiator informs the next assigned block and the Number of Rounds in the assigned block.