## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Updates for Multiple Transmission
Date Submitted: May 18, 2023
Source: [Taeyoung Ha, Mingyu Lee, Youngwan So, Aniruddh Rao Kabbinale, Ankur Bansal, Clint Chaplin] Company [Samsung Electronics]
E-Mail: ty1115.ha@samsung.com
Abstract: Updates for Multiple RSF Transmissions in a Slot Scenario
Purpose: Increase air time efficiency by allowing the multiple MMRS transmission in a slot.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
        doc.: 15-23-0236-00-04ab

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | Transmit RSF in a slot to reduce air-time
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Concerns on Multiple transmission
Power control
If body blocking occurs, significant signal attenuations can occur
If significant signal attenuations occurs, a weak signal may not be detected through the correlator
Implementation Complexity
In order to achieve multiple transmission scheme, a implementation complexity will increase

## Slide 4: RSSI Value Experimental Results
Below figure shows the probability that the RSSI difference between Responder 1 and Responder 2 exceeds the 30 dB
  The worst case is that 1) the antenna of Initiator is located at the lower left and not blocked 2) Responder 1 is blocked by hand and Responder 2 is not blocked (i.e., yellow bar at the CASE 3)
  In this case, the probability that the RSSI difference between Responder 1 and Responder 2 exceeds the 30 dB is about 0.006

## Slide 5: Ranging Experimental Environment
In order to check the feasibility of the Multiple Transmission scenario in the VR scenario additional experiments were conducted
  Responder 1 (Right Transmitter) and Responder 2 (Left Transmitter) use different preamble code (Ipatov sequence, Length = 128)
  Responder 1 and Responder 2 transmit a packet to the Initiator simultaneously
  Initiator (Receiver) tries to detect the Responder 1’s preamble
  Ranging is proceeded through SS-TWR manner

## Slide 6: Ranging Experimental Environment
In order to check the feasibility of the Multiple Transmission scenario in the VR scenario additional experiments were conducted
  Experiments were proceeded according to the distance between Initiator and Responder 2 (i.e., Left Transmitter)
  The distance between Initiator and Responder 1 (i.e., Right Transmitter) is fixed as 90 cm
  Reference case means that there is only Responder 1 (i.e., Responder 2 do not transmit any signals)

## Slide 7: Ranging Experimental Results
Below figure shows the probability that the Initiator successfully receives the packet of Responder 1 (i.e., Right Transmitter)
  For Reference case (i.e., no Responder 2), the probability of successfully receiving is 1.0 (i.e., No packet drop)
  As the distance between the Initiator and Responder 2 (i.e., Left Transmitter) decrease, the probability of successfully receiving packet decrease (Probability is about 0.95 when the distance between the Initiator and Responder 2 is 10 cm)

## Slide 8: Ranging Experimental Results
Below figure shows the average measured distance between the Initiator and Responder 1 (i.e., Right Transmitter)
  The exact distance between the Initiator and Responder 1 (i.e., Right Transmitter) is 90 cm
  As the distance between the Initiator and Responder 2 (i.e., Left Transmitter) decrease, the average measured distance increase (Average measured distance is about 95.6 cm when the distance between the Initiator and Responder 2 is 10 cm)

## Slide 9: Implementation Complexity
Current UWB chipsets in smartphones have multiple antenna and each antenna has its own correlator to measure AoA and etc.
If these antenna and correlator sets are used for detecting different RSFs, multiple transmission scheme can be achieved
Additional software updates or hardware may be needed

## Slide 10: Summary
Power control
If body blocking occurs, significant signal attenuations can occur
If significant signal attenuations occurs, a weak signal may not be detected through the correlator
Based on the experimental results for VR scenario, the probability of significant signal attenuation is somewhat low
Receiving packet ratio and measurement results show proper performance even with the current Ipatov sequences
Implementation Complexity
In order to achieve multiple transmission scheme, a implementation complexity will increase
 Current multiple antenna and correlator sets can be used
 Additional hardware/software to implement new feature is inevitable