## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: Considerations on CIR scaling and quantization
Source: Bin Qian, Chenchen Liu, Rojan Chitrakar, Xiaohui Peng, Lei Huang, David Xun Yang (Huawei Technologies)
Address : [Huawei Bantian Base, Longgang District, Shenzhen, 518129 China]
E-Mail: [qianbin14@huawei.com]
Re: Task Group 4ab: UWB Next Generation for 802.15.4
Abstract: [UWB, sensing, CIR]
Purpose:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | Adaptive CIR scaling and quantization to reach a better performance in terms of SQNR
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Reference
[1] IEEE 802.15-23-0079-01-04ab-latest-consensus-on-uwb-sensing-for-802.15.4ab
[2] IEEE 802.15-23-0120-00-04ab-cir-report-size
[3] IEEE 802.15-23-0121-00-04ab-cir-scaling-and-quantization

## Slide 4: Recap
In [1], the group agreed that encoding signed I/Q values each with 16 bits is mandatory, and other bit-width values could be optional
In [2], it is shown that the CIR report size could be as large as thousands bytes, which leads to a transmission duration of several milliseconds.
To reduce the overhead of CIR report, [3] proposed a power-of-two scaling and quantization method of the I/Q values in the CIR report
  The proposed method followed the idea of CSI scaling and quantization in 11bf
One concern is that the CSI is in the frequency domain while the CIR is in the time domain. Whether the scaling and quantization method in 11bf could be directly applied to UWB needs more investigation

## Slide 5: Real Data Testing
Indoor environment
  The distance between the sensing initiator and the sensing responder is about 5m. A person is walking towards the sensing responder
Both the CIR data and CSI data are collected
  The sampling rate of CIR data is 1GHz. 14 sensing packets are tested with bitmap length 64. The time offset from the reference tap is 3 taps.
  The CSI data is 20MHz with 52 effective subcarriers. 18 OFDM symbols are tested.

## Slide 6: Real Data Histogram
The Histogram of absolute I/Q values of CIR and CSI are analyzed
The energy of the CIR data is dominated by limited paths. The energy of most paths is weak
The energy of the CSI data is distributed more evenly
The different distribution of CIR and CSI may lead to scaling and quantization performance loss

## Slide 7: Adaptive Power-of-Two Scaling and Quantization
The proposed method takes into account the property that the energy of the CIR data is dominated by limited paths
The proposed method
  Let denote the CIR values, where and are the real component and imaginary component of the CIR values, respectively.
  Each and could be quantized as
  where and are the mantissas, and and are the exponents
  The mantissa consists of the significant digits of and
  The exponent is 0 when the leftmost bit is taken as mantissa, and exponent value is incremented by 1 for each right shift of the mantissa

## Slide 8: Adaptive Power-of-Two Scaling and Quantization (cont.)
and could use the common exponent, i.e., , which could be determined by the maximum absolute value of and
Assume and bits are used for mantissas, bits are used for the common exponent, the number of bits per CIR tap is
+ +
Example
  , the number of bits per CIR tap is 16
  , the number of bits per CIR tap is 20
  , the number of bits per CIR tap is 32

## Slide 9: Illustrative Example: Power-of-two Scaling in [3]
I-component
Q-component
Assumption
  The internal processing bit-width is 16 bits
  The scaling factor is , i.e., the 6 rightmost bits will be removed
Quantized I/Q data
Total number of bits per CIR tap is 16

## Slide 10: Illustrative Example: Adaptive Power-of-two Scaling
I-component
Q-component
Assumption
  The internal processing bit-width is 16 bits per I/Q-component
Quantized I/Q data
Total number of bits per CIR tap is 16

## Slide 11: CIR Tap 16-bit Simulations
We set in [3], and in the proposed method.
  The overall overhead for both methods is same
The probabilities that the SQNR of the adaptive power-of-two scaling, real-value scaling, and power-of-two scaling is larger than 35dB are 0.55, 0.3, and 0.18, respectively
CCDF is complementary cumulative distribution function, which is defined as

## Slide 12: CIR Tap 20-bit Simulations
We set in [3], and in the proposed method
  The overall overhead for both methods is same
The probabilities that the SQNR of the adaptive power-of-two scaling, real-value scaling, and power-of-two scaling is larger than 35dB are 1, 0.83, and 0.65, respectively
CCDF is complementary cumulative distribution function, which is defined as

## Slide 13: Summary
Compared with the method in [3], our proposed method has better performance in terms of SQNR.
  All the multiplications and divisions could be converted to left or right bit shifts
  Both methods have the same complexity and overhead
The proposed CIR reporting method is recommended to be included in the sensing TFD

## Slide 14: Appendix

## Slide 15: CIR Tap 16-bit Simulations
We set in [3], and in the proposed method.
  The overall overhead for both methods is same

## Slide 16: CIR Tap 20-bit Simulations
We set in [3], and in the proposed method
  The overall overhead for both methods is same

## Slide 17: Thank You