## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: Channel Modeling Activities of TG6ma for Human and Vehicle Body Area Networks
Date Submitted: May 16th, 2023
Source: Takumi Kobayashi, Daisuke Anzai, Minsoo Kim, Marco Hernandez, Ryuji Kohno
Company: (1) Nagoya Institute of Technology, (2) YRP International Alliance Institute, (3) CWC Oulu Univ. Finland, (4) Yokohama National University
Address: YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan
Voice:[+81-90-5408-0611] E-Mail:[kobayashi@nitech.ac.jp, Anzai@nitech.ac.jp, minsoo@minsookim.com, marco.hernandez@ieee.org, kohno@ynu.ac.jp, Kohno@yrp-iai.jp]
Re: In response to call for technical contributions
Abstract: This provides draft of channel and environmental model and its classification for vehicle body area network(VBAN) of amendment of IEEE802.15.6-2012 for wireless body area network(BAN) with enhanced dependability.
Purpose: Material for discussion in P802.15.6ma TG corresponding to comments in EC Meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Channel Modeling Activities of TG6ma for Human and Vehicle Body Area Networks
Takumi Kobayashi, Daisuke Anzai, Marco Hernandez , Minsoo Kim , Ryuji Kohno
(1) Nagoya Institute of Technology, Japan (2)YRP-International Ariane Institute, Japan (3) CWC, University of Oulu, Finland (4) Yokohama National University, Japan

## Slide 3: Background
IEEE std. IEEE802.15.6 -2012
IEEE802.15.6 for dependable body area networks (BAN) has been published in 2012.
Narrow band (NB) PHY,
Ultra wide band (UWB) PHY,
Human body communication (HBC) PHY
IEEE802.15 TG6ma
Task group for revision of 802.15.6-2012
In order to achieve more enhanced dependability, Task group 6ma (TG6ma) is in active.
By focusing on UWB PHY for more wider applications required higher dependability.
10 years…

## Slide 4: Channel models
IEEE802.15.6 – 2012 defined “Channel models document”[1] to define the channel models that can be used to performance analysis of expected use cases.
Original IEEE802,15,6 mainly focused Medical applications as the applications requires dependability.
Channel models of IEEE802.15.6 also defines the channel models in / on / around the human body.
[1] IEEE P802.15-08-0780-12-0006-TG6

## Slide 5: Channel models and scenarios in IEEE802.15.6-2012
IEEE 802.15.6-2012 channel models considered
Fading ( Small scale/ large scale)
Path loss
Shadowing
Power delay profile
In-body (implant)
On-body (body surface)
CM1, 2, 3, 4
Scenario 1, to Scenario 7. (S1 – S7)
IEEE P802.15-08-0780-12-0006-TG6
No definition of UWB channel models for implant devices

## Slide 6: Extend more wider applications
TG6ma, revision of IEEE802.15.6 is considering extend to more wider application by using UWB-PHY
Vehicle Body Area Network
Brain-Computer/Machine Interfaces
coordinator
Engine Compartment
Cabin Room
Gastrointestinal tract
capsule endoscopy
Transceiver on body surface
Capsule endoscopy

## Slide 7: New application of enhanced dependable BANs
Recently, brain computer interface (BCI) and brain machine interface (BMI) technologies are dramatically advanced. However, most of these researches use wired connection due to difficulties to keep dependability on wireless communication.
Enhanced dependable BAN is highly expected to be used for the BMI and BCI sensing and controlling systems.
On-body device
In-head device
External
Device
On-body (head) transmitter device

## Slide 8: New application of enhanced dependable BANs
5
1
2
3
4
6
Engine/motor diagnostic sensor and controller
Air pressure sensor, wheel health sensor and controller
Transmission monitoring sensor and controller
Cabin environment sensor (temperature, brightness, humidity etc.)
Sheet sensor, health care sensors for driver
Sheet sensor, health care sensors for passenger
Engine/Motor room environment model
Cabin room environment model
https://media.istockphoto.com/photos/transparent-car-design-wire-model3d-illustration-my-own-car-design-picture-id594040008?k=6&m=594040008&s=612x612&w=0&h=XE8LiBjpM51aB4pH2CFt6-MT6IvALRPnlxPcac0RXhg=
Note:
Various type of car/vehicles
Bus, Bulldozer, Heavy construction equipment needed each different sensors.

## Slide 9: Engine/Motor Room Environment
Many metallic components
Components existing in densely
Ignition noise, motor noise
Larger path-loss than free propagation
A lot of reflection of RF signal
Electro-magnetic interference, EMI issues
Ignition coil
Electric motor
High current battery and cable
Spark plug
Electric generator
https://www.as-web.jp/car/575374/attachment/03a_sub_dsc01273
Especially EV

## Slide 10: VBAN Use cases
Failure and/or deterioration detection of vehicle components.
  - Nodes are in engine compartment / coordinator is in engine compartment
Sensing for safety driving support / Collision avoidance
  - Nodes are on outside surface of vehicle / coordinator is in engine compartment
Entertainment for passengers
  - Nodes are in cabin / coordinator is in cabin.
Key-less entry system - Node is around user outside of vehicle / coordinator is in engine compartment
Communication between user on pedestrian and vehicle
  - Node is around user outside of vehicle / coordinator is on outside surface of vehicle (vehicle moves at walking speed (<5km/h))
Vehicle controlling / Wireless herness
  - Coordinator and nodes are in between cabin and chassis of vehicle.
Driver’s health problem detection
  - Coordinator in engine compartment / nodes are on human (driver) body.
Driver’s and passenger’s healthcare application
  - Nodes and coordinator are on human body.

## Slide 11: Classification of Channel and Environment Models for Human and Vehicle Body Area Networks (HBAN&VBAN)
Note:
HBAN-model:
-Environment with co-existing systems is not considered.
VBAN model:
Key-less entry system
Localization in-body, on-body
Most dominant model should be defined and separatory defined as Mandatory and Optional.
Channel model
HBAN model
VBAN model
In-body (Implant)
On-body
Around body
Outdoor
Indoor
Home
Office
Medical (e.g. Hospital)
In-vehicle
On-vehicle
Around vehicle
Engine compartment
Cabin
Through Engine compartment and cabin
Roof
Side Right/Left/Front/back
Bottom
Static vehicle
Moving vehicle
※Covered by IEEE 802.15.6-2012
※Around means;
Desk, WiFi AP in the room etc.
Channel model
With environment
※
※
※
※
※
Implanted BCI model
※not covered in 2012
On skull BCI model
capsule endoscopy

## Slide 12: Channel and Environmental Models
Path loss
Reflection
Multipath
Fading
LOS / NLOS model
White Gaussian noise
Interference from co-existing wireless systems e.g. Bluetooth, IEEE 802.11, IEEE 802.15.4 etc.
Interference from the other BANs.
Interference from the other electric systems, devices and components (Electro-magnetic interference; EMI from electric motors, spark plugs in vehicles, etc.
Electro-magnetic compatibility; EMC. Possibility to affect to the other systems and human body.
VBAN  HBAN interference
VBAN and HBAN  Vehicle control and human body impacts.
Colored noise (Impulse noise, spike noise, ignition noise etc.)
Time-varying channel and interference modeling (Statistic, non-static, pseudo static model)
※optional
or
?
Environment model
Channel model
Channel model
EMI EMC
Colored noise
Other wireless systems
Environment model
Time-varying modeling
※mandatory
※mandatory
※mandatory
※mandatory
※optional
※optional
※optional
※IEEE802.15.6-2012
※will be defined in this amendment
※mandatory
or
?
※mandatory
※Comments in May 2021.

## Slide 13
RF
ANT
Propagation Model （based on S-V Model）
Interference from the other BAN
Interference from the other UWB (not BAN)
+
EMI from vehicle system
Colored noise
EV Switching noise
Ignition noise
etc…
RF
ANT
Channel model
Distance dependent function
Distance dependent function
Standard antenna
Standard antenna
Environmental model
Interference from the other Wireless systems
We propose to define environmental models including antenna effect. Parameter measurements will be performed by using standard antennas which will be defined separately.

## Slide 14: Channel models and scenarios in IEEE802.15.6ma
Path loss (Mandatory)
Optional;
  Fading ( Small scale/ large scale)
  Shadowing
  Power delay profile
Scenario | Description | Frequency Band | Channel Model
S1 | Implant to Implant | 402-405 MHz, | CM1
S2 | Implant to Body Surface | 402-405 MHz, | CM2
S2.1 | Implant (upper body) to Body Surface | 3.1-10.6 GHz UWB | CM2.1
S2.2 | Implant (head) to Body Surface | 3.1-10.6 GHz UWB | CM2.2
S3 | Implant to External | 402-405 MHz, 3.1-10.6 GHz UWB | CM2
S4 | Body Surface to Body Surface (LOS) | 400, 600, 900 MHz 2.4, 3.1-10.6 GHz | CM3
S4.1 | Body Surface to Body Surface (LOS) | 3.1-10.6 GHz CM4.1 | CM4.1
S5 | Body Surface to Body Surface (NLOS) | 400, 600, 900 MHz 2.4, 3.1-10.6 GHz | CM3
S6 | Body Surface to External (LOS) | 900 MHz 2.4, 3.1-10.6 GHz | CM4
S6.1 | Body Surface (head) to External (LOS) | 3.1-10.6 GHz | CM6.1
S6.2 | BAN Coordinator to BAN coordinator | 3.1-10.6 GHz | CM6.2
S7 | Body Surface to External (NLOS) | 900 MHz 2.4, 3.1-10.6 GHz | CM7
Specific use cases
Implant to Body Surface for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy

## Slide 15: Channel models and scenarios for capsule endoscopy S.2.1
Gastrointestinal tract
Implant to Body Surface for Capsule Endoscopy
capsule endoscopy
Transceiver on body surface
Specific use cases
Implant(head) to on-body for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy

## Slide 16: Channel models for BMI and BCI S2.2 implant(head) to on-body
Specific use cases
Implant(head) to on-body for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy

## Slide 17: Channel models for BMI and BCI S2.3 implant(head) to external
Specific use cases
Implant(head) to on-body for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy

## Slide 18: Channel models for BMI and BCI S4.1 ― on-body(head) to on-body
Specific use cases
Implant(head) to on-body for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy
Receiver
Device
On-body (head) transmitter device

## Slide 19: Channel models for BMI and BCI S6.1 ― on-body(head) to external
Specific use cases
Implant(head) to on-body for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy
Receiver
Device
On-body (head) transmitter device

## Slide 20
HBAN coordinator to HBAN coordinator
Body surface to body surface
Cannot be considered as similar
Body surface to body surface
Body surface to ANOTHER body surface
Need to consider SAR issues
S6.2&CM6.2

## Slide 21: Channel models for BMI and BCI S6.2 ― HBAN to HBAN

## Slide 22: Environment models that can be applicable against different type of vehicles
Engine
Cabin
Engine
Cabin
Policy:
IEEE 802.15.6ma defines several common environment models against most dominant use cases as mandatory models.
Categories:
Categorize several type of vehicle like “for passengers”, “bus”, “small cargo”, “middle cargo”, “Large cargo” and “special purpose vehicles” such as a construction machines and build models for various categories.
Different
Size;
Structure;...etc.
https://nohat.cc/f/heavy-truck-illustration-isolated-on-a-white-background/comvecteezy328938-201908251309.html

## Slide 23
Symmetric scenario
Coordinator
Node
In channel model (without EMC/EMI and Interference issues), two direction of propagation should be considered as equal:
Channel reciprocity.
Channel models of “Coordinator to node” and “Node to coordinator” without noise source should be the same.
Coordinator
Node
Asymmetric scenario
Coordinator
Node
Coordinator
Node
Noise and/or interference source
In case of environmental model including EMC/EMI . colored noise and interference issues, two direction between source and sink is not same meaning.
Environmental model of two different direction should be defined separately.
Environmental models of “Coordinator to node” and “Node to coordinator” should be different.

## Slide 24: Engine/Motor Room Environment
Many metallic components
Components existing in densely
Ignition noise, motor noise
Larger path-loss than free propagation
A lot of reflection of RF signal
Electro-magnetic interference, EMI issues
Ignition coil
Electric motor
High current battery and cable
Spark plug
Electric generator
https://www.as-web.jp/car/575374/attachment/03a_sub_dsc01273
Especially EV

## Slide 25: Models between VBAN and HBAN
VBAN
coordinator
VBAN
node
VBAN
node
HBAN
coordinator
HBAN
coordinator
HBAN
node
HBAN
node
HBAN
node
HBAN
node
Channel and Environmental models for VBAN.
Channel and Environmental models for HBAN.
VBAN
coordinator
HBAN
coordinator
HBAN
coordinator
HBAN
node
Channel and Environmental models between VBAN coordinator and HBAN coordinators.
Channel and Environmental models between VBAN coordinator and VBAN coordinators.

## Slide 26: Channel and Environmental models of VBAN Scenario 8.1 & CM8.1 “In-vehicle to In-vehicle (functional compartment)”
S8: In-vehicle to In-vehicle (sedan)
coordinator
Engine Compartment
Cabin Room
S8.2: In-vehicle to In-vehicle (functional compartment)

## Slide 27: Channel models and scenarios in IEEE802.15.6ma
S11: On-vehicle to on-vehicle (LOS)
S8: In-vehicle to In-vehicle (sedan)
S13: On-vehicle to external (LOS)
S9: In-vehicle to On-vehicle
S14: On-vehicle to external (NLOS)
S12: On-vehicle to on-vehicle (NLOS)
S10: In vehicle to External

## Slide 28: Channel and Environmental models of VBAN
S11: On-vehicle to on-vehicle (LOS)
S8: In-vehicle to In-vehicle (sedan)
S13: On-vehicle to external (LOS)
S9: In-vehicle to On-vehicle
S14: On-vehicle to external (NLOS)
S12: On-vehicle to on-vehicle (NLOS)
S10: In vehicle to External

## Slide 29: Scenario 8
Nodes and coordinator are in cabin room
Entertainment for passengers
  Nodes are in cabin room / coordinator is in cabin room.
  Symmetric environmental model
  EMI from engine and electric system are negligible. => channel model
Use case
Geometrical configuration
 | Use case | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
8 | Entertainment for passengers | Case 8 |  | Case 8.1 | Same as 8.1 | ---
S8: In-vehicle to In-vehicle (sedan)
Coordinator or node
Common channel model to IEEE 802.15.4a

## Slide 30: Channel models for BUS
Nodes and coordinator, VBAN and HBAN are in cabin room
Geometrical configuration
coordinator
Noise source
VBAN Coordinator
HBAN Coordinator
Entertainment for passengers
  Nodes are in cabin room / coordinator is in cabin room.
Use case
scenario |  | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
8.1vv | VBAN coordinator and VBAN coordinator | Case 3.1a |  | Case 3.1a | Same as 3.1a | ---
8.1vh | VBAN coordinator and HBAN coordinator | Case 3.1b |  |  |  | ---

## Slide 31: Scenario 8.1 for BUS
Nodes and coordinator are in cabin room
Geometrical configuration
S8.1: In-vehicle to In-vehicle (bus)

## Slide 32: Scenario 10
Key-less entry system
  Node is around user outside of vehicle / coordinator is in Engine compartment
  Asymmetric environment. Two direction model should be defined separatory.
Use case
Geometrical configuration
In-body / External
scenario | Use case | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
10 | Key-less entry system | Case 4.1 V-H | Case 4.2 V-H | Case 4.3 V-H |  | ---
 |  | Case 4.1 H-V | Case 4.2 H-V | Case 4.3 H-V |  | ---
Noise source
VBAN Coordinator
HBAN Coordinator
Common channel model to IEEE 802.15.4a

## Slide 33: Channel and Environmental models of VBAN Scenario 8.1 & CM8.1 “In-vehicle to In-vehicle (functional compartment)”
S8: In-vehicle to In-vehicle (sedan)
coordinator
Engine Compartment
Cabin Room
S8.2: In-vehicle to In-vehicle (functional compartment)

## Slide 34
 |  |  |  | STATUS | PL | PDP | Matlab | Modeling & Documentation | Reference
Scenario | Description | Frequency Band | Channel Model |  |  |  |  |  | 
S1 | Implant to Implant | 402 - 405 MHz | CM1 | OK | COPY of ORIGINAL | COPY of ORIGINAL | COPY of ORIGINAL | done | Original CMD of IEEE 802.15.6-2012
S2 | Implant to Body Surface | 402-405 MHz | CM2 | OK | COPY of ORIGINAL | COPY of ORIGINAL | COPY of ORIGINAL | done | Original CMD of IEEE 802.15.6-2012
S2.1 | Implant (upper body) to Body Surface ※Capsule endoscopy | 3.1-10.6 GHz | CM2.1 | OK(PL) | Done | TBD (0%) | Done(PL option2) | Done(PL) | Kamran's Contribution, [DCN15-22-0401-01-006a], Daisuke's contribution [DCN15-23-0145-00-006a],
S2.2 | Implant (head) to Body Surface ※BCI | 3.1-10.6 GHz | CM2.2 | OK(PL) | Done | Done | Done(PL) | Done(PL) | Daisuke's contribution [DCN15-23-0145-00-006a],
S2.3 | Implant (head) to external ※BCI | 3.1-10.6 GHz | CM2.3 | OK(PL) | Done | Done | Done(PL) | Done(PL) | Daisuke's contribution [DCN15-23-0145-00-006a],
S3 | Implant to External | 402-405MHz | CM3.1 | OK | COPY of ORIGINAL | COPY of ORIGINAL | COPY of ORIGINAL | done | Original CMD of IEEE 802.15.6-2012
S3.1 | Implant (upper body) to External ※Capsule endoscopy | 3.1-10.6GHz | CM3.1 | OK(PL) | Done (Will be enhanced?),(antenna gain) |  |  | 90% | Daisuke's contribution New doc. May.
S4 | Body Surface to Body Surface (LOS) | 400, 600, 900 MHz | CM4 | OK | COPY of ORIGINAL | COPY of ORIGINAL | COPY of ORIGINAL | done | Original CMD of IEEE 802.15.6-2012
 |  | 2.4, |  | OK | COPY of ORIGINAL | COPY of ORIGINAL | COPY of ORIGINAL | done | Original CMD of IEEE 802.15.6-2012
 |  | 3.1-10.6 GHz |  | OK | COPY of ORIGINAL | COPY of ORIGINAL | COPY of ORIGINAL | done | Original CMD of IEEE 802.15.6-2012
S5 | Body Surface to Body Surface (NLOS) | 2.4 GHz | CM5 | OK | COPY of ORIGINAL | COPY of ORIGINAL | COPY of ORIGINAL | done | Original CMD of IEEE 802.15.6-2013
 |  | 3.1-10.6 GHz |  | OK | COPY of ORIGINAL | COPY of ORIGINAL | COPY of ORIGINAL | done | Original CMD of IEEE 802.15.6-2014
S6 | Body Surface to External (LOS) | 3.1-10.6 GHz | CM6 | OK | COPY of ORIGINAL | COPY of ORIGINAL | COPY of ORIGINAL | done | Original CMD of IEEE 802.15.6-2015
S6.1 | Body Surface (head) to External (LOS) | 3.1-10.6 GHz | CM6.1 | OK(PL) | Done | Done | Done(PL) | Done(PL) | Daisuke's contribution [DCN15-23-0145-00-006a],
S6.2 | BAN coordinator to BAN coordinator | 3.1-10.6 GHz | CM6.2 | OK(PL) | Done | T.B.D (0%) | Done(PL) | 80% | Daisuke's contribution New doc. May.
S7 | Body Surface to External (NLOS) | 3.1-10.6 GHz | CM7 | OK | COPY of ORIGINAL | COPY of ORIGINAL | COPY of ORIGINAL | Editing (COPY of ORIGINAL) | Original CMD of IEEE 802.15.6-2012

## Slide 35
 |  |  |  | STATUS | PL | PDP | Matlab | Modeling & Documentation | Reference
Scenario | Description | Frequency Band | Channel Model |  |  |  |  |  | 
S8 | In-vehicle to In-vehicle (sedan) | 2.4 GHz | CM8 | CFP |  |  |  |  | Car industry documents
 |  | 3.1-10.6 GHz |  | OK(PL) | Done | TBD (20%) simulation running | TBD (1%) ready to start | 100% (for PL) | Daisuke's contribution P802.15-23-0146-00-006a
S8.1 | In-vehicle to In-vehicle (passenger bus) | 2.4 GHz | CM8.1 | CFP |  |  |  |  | Car industry documents
 |  | 3.1-10.6 GHz |  | OK(PL) | Done | TBD (50%) simulation running | TBD (1%) ready to start | 100% (for PL) | Daisuke's contribution P802.15-23-0146-00-006a
S8.2 | In-vehicle to In-vehicle (functional compartment) | 2.4 GHz | CM8.2 | CFP |  |  |  |  | Car industry documents
 |  | 3.1-10.6 GHz |  | OK(PL) | Done | TBD (70%) simulations done | TBD (1%) ready to start | 100% (for PL) | Daisuke's contribution P802.15-23-0146-00-006a
S9 | In-vehicle to On-vehicle | 2.4 GHz | CM9 | CFP |  |  |  |  | Car industry documents
 |  | 3.1-10.6 GHz |  | OK(PL) | Done | 10% | T.B.D (1%) | 100% (for PL) | Daisuke's contribution P802.15-23-0146-00-006a + New doc. at May.
S10 | In vehicle to External | 2.4 GHz | CM10 | CFP |  |  |  |  | Car industry documents
 |  | 3.1-10.6 GHz |  | OK(PL) | Done | 10% | T.B.D (1%) | 100% (for PL) | Daisuke's contribution P802.15-23-0146-00-006a + New doc. at May.
S11 | On-vehicle to on-vehicle (LOS) | 2.4 GHz | CM11 | CFP |  |  |  |  | Car industry documents
 |  | 3.1-10.6 GHz |  | OK(PL) | Done | 10% | T.B.D (1%) | 100% (for PL) | Daisuke's contribution P802.15-23-0146-00-006a + New doc. at May.
S12 | On-vehicle to on-vehicle (NLOS) | 2.4 GHz | CM12 | CFP |  |  |  |  | Car industry documents
 |  | 3.1-10.6 GHz |  | OK(PL) | Done | 10% | T.B.D (1%) | 100% (for PL) | Daisuke's contribution P802.15-23-0146-00-006a + New doc. at May.
S13 | On-vehicle to external (LOS) | 2.4 GHz | CM13 | CFP |  |  |  |  | Car industry documents
 |  | 3.1-10.6 GHz |  | OK(PL) | Done | 10% | T.B.D (1%) | 100% (for PL) | Daisuke's contribution P802.15-23-0146-00-006a + New doc. at May.
S14 | On-vehicle to external (NLOS) | 2.4 GHz | CM14 | CFP |  |  |  |  | Car industry documents
 |  | 3.1-10.6 GHz |  | OK(PL) | Done | 10% | T.B.D (1%) | 100% (for PL) | Daisuke's contribution P802.15-23-0146-00-006a + New doc. at May.

## Slide 36: Summary
IEEE 802.15 TG6ma is now active to revision for IEEE802.15.6-2012
Channel models document has been defined with new channel models and scenarios for new applications.
In this TG activity, we define new scenarios for HBAN and 8 scenarios for VBAN.
Scenario S2.1 is for the application of capsule endoscopy
Scenarios S2.2 S4.1 and S6.1 are for the BCI/BMI application
Scenarios S6.2 is for communication between coordinator to coordinator.
Some of VBAN channel and environment models are defined by the original contributions.

## Slide 37: References
“802.15.6-2012 - IEEE Standard for Local and metropolitan area networks –Part 15.6: Wireless Body Area Networks,” IEEE, NY, Feb., 2012. DOI:10.1109/IEEESTD.2012.6161600
Kamya Yekeh Yazdandoost and Kamran Sayrafian-Pour, “Channel
Model for Body Area Network,” IEEE P802.15-08-0780-
11-0006, Sept., 2010.
Yan T, Suzuki K, Kameda S, Maeda M, Mihara T, Hirata M , “Electrocorticographic effects of acute ketamine on non-human primate brains,” J Neural Eng. 2022, 19(2): 026434
Kaiju T, Inoue M, Hirata M, Suzuki T, “High-density mapping of primate digit representations with a 1152-channel µECoG array,” J Neural Eng. 17 March 2021 Volume 18, Number 3
Takumi Kobayashi, Daisuke Anzai, Minsoo Kim, Marco Hernandez, Ryuji Kohno, “Summary of Channel and Environmental Modeling Activities for BANs on TG15.6a,” IEEE P802.15-22-0091-05-006a, Jan., 2023.
Takumi Kobayashi, Minsoo Kim, Marco Hernandez, Ryuji Kohno, “Channel Model for Wearable and Implant BAN in use case of BMI and BCI,” IEEE P802.15-22-0069-04-006a, Sept., 2022.
Takumi Kobayashi, Minsoo Kim, Marco Hernandez, Ryuji Kohno, “TG6ma Channel Model Document for Enhanced Dependability,” IEEE P802.15-22-0519-00-006a, Sept., 2022.
Takumi Kobayashi, Minsoo Kim, Marco Hernandez, Ryuji Kohno, “Chanel and Environmental Models Classification for Vehicle Body Area Network (VBAN) on TG15.6a,” IEEE P802.15-21-0560-01-006a, Nov. 2021.

## Slide 38: Thank you for your attention

## Slide 39: ↓ Supplementary ↓

## Slide 40: Channel and Environmental models of VBAN Scenario 8.1 & CM8.1 “In-vehicle to In-vehicle (functional compartment)”
S8: In-vehicle to In-vehicle (sedan)
coordinator
Cargo space
Cabin Room
S8.2: In-vehicle to In-vehicle (functional compartment)

## Slide 41: Scenario 13
Outside surface of vehicle / coordinator is on vehicle
Communication between user on pedestrian and vehicle
  Node is around user outside of vehicle / coordinator is on outside surface of vehicle (vehicle moves in walking speed (<5km/h))
  Asymmetric environmental model
Use case
Geometrical configuration
Moving at walking speed (<5km/h)
S | Use case | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
13 | Communication between user on pedestrian and vehicle | Case 5.1 V-H |  | Case 5.3 V-H |  | ---
 |  | Case 5.1 H-V |  | Case 5.3 H-V |  | ---
Noise source
VBAN Coordinator
HBAN Coordinator
Common channel model to IEEE 802.15.4a

## Slide 42: Dynamic Channel Models Situations
Channel between a user on pedestrian and a vehicle.
Users in a vehicle are slightly moving due to vibration and acceleration.
Walking and/or standing users on a bus and train.
Between a tractor and trailer tail.
Moving at walking speed (<5km/h)
Noise source
VBAN Coordinator
HBAN Coordinator
LOS
NLOS
LOS

## Slide 43: Classification of Channel and Environment Models for Human and Vehicle Body Area Networks (HBAN&VBAN)
Note:
HBAN-model:
-Environment with co-existing systems is not considered.
VBAN model:
Key-less entry system
Localization in-body, on-body
Most dominant model should be defined and separatory defined as Mandatory and Optional.
Channel model
HBAN model
VBAN model
In-body (Implant)
On-body
Around body
Outdoor
Indoor
Home
Office
Medical (e.g. Hospital)
In-vehicle
On-vehicle
Around vehicle
Engine compartment
Cabin
Through Engine compartment and cabin
Roof
Side Right/Left/Front/back
Bottom
Static vehicle
Moving vehicle
※Covered by IEEE 802.15.6-2012
※Around means;
Desk, WiFi AP in the room etc.
Channel model
With environment
※
※
※
※
※
Implanted BCI model
※not covered in 2012
On skull BCI model
capsule endoscopy

## Slide 44: Channel models and scenarios in IEEE802.15.6-2012
IEEE 802.15.6-2012 channel models considered
Fading ( Small scale/ large scale)
Path loss
Shadowing
Power delay profile
In-body (implant)
On-body (body surface)
CM1, 2, 3, 4
Scenario 1, to Scenario 7. (S1 – S7)
IEEE P802.15-08-0780-12-0006-TG6

## Slide 45: Channel models and scenarios in IEEE802.15.6ma
Path loss (Mandatory)
Optional;
  Fading ( Small scale/ large scale)
  Shadowing
  Power delay profile
Scenario | Description | Frequency Band | Channel Model
S2 | Implant to Body Surface | 402-405 MHz, | CM2
S2.1 | Implant (upper body) to Body Surface | 3.1-10.6 GHz UWB | CM2.1
S2.2 | Implant (head) to Body Surface | 3.1-10.6 GHz UWB | CM2.2
S3 | Implant to External | 402-405 MHz, 3.1-10.6 GHz UWB | CM2
S4 | Body Surface to Body Surface (LOS) | 400, 600, 900 MHz 2.4, 3.1-10.6 GHz | CM3
S4.1 | Body Surface to Body Surface (LOS) | 3.1-10.6 GHz CM4.1 | CM4.1
S5 | Body Surface to Body Surface (NLOS) | 400, 600, 900 MHz 2.4, 3.1-10.6 GHz | CM3
S6 | Body Surface to External (LOS) | 900 MHz 2.4, 3.1-10.6 GHz | CM4
S6.1 | Body Surface (head) to External (LOS) | 3.1-10.6 GHz | CM6.1
S7 | Body Surface to External (NLOS) | 900 MHz 2.4, 3.1-10.6 GHz | CM4
Specific use cases
Implant to Body Surface for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy

## Slide 46: Channel models and scenarios in use case of BMI and BCI
Implant to Body Surface for BCI
Body Surface to External on-body surface for BCI
Implant to External for BCI
Body Surface to Body Surface for BCI
We will define what is BCI and BMI.
Specific use cases
Implant to Body Surface for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy
Future
Future
Arm
Wired connection
electrode

## Slide 47: Suggestion from Prof. Hirata
Implant to implant model for next Gen.
Future
Arm
Wired connection
electrode

## Slide 48: 1.5 Gen.
Transmitter Device
Brain
Skull bone
Skin
Skull bone
electrodes
Receiver
Device
<10mm
Receiver can be placed any where on body like on arm, wrist, neck etc.

## Slide 49: Channel models for BMI and BCI S2.2 (A) implant(head) to on-body
Specific use cases
Implant(head) to on-body for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy

## Slide 50: Channel models for BMI and BCI S2.2 (B,C) implant(head) to on-body
Specific use cases
Implant(head) to on-body for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy
Skin tissues
Skull bone
<10mm
Receiver
Tx antenna
electrodes
Brain
Skin tissues
<10mm
Receiver
Tx antenna
electrodes
Brain
Skull bone
Skull bone
transmitter

## Slide 51: Channel models for BMI and BCI S4.1 ― on-body(head) to on-body
Specific use cases
Implant(head) to on-body for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy
Receiver
Device
On-body (head) transmitter device

## Slide 52: Channel models for BMI and BCI S6.1 ― on-body(head) to external
Specific use cases
Implant(head) to on-body for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy
Receiver
Device
On-body (head) transmitter device

## Slide 53: Future generation
Brain
Skin
Skull bone
Transmitter
electrodes
<10mm
Receiver
Future

## Slide 54: Channel models and scenarios for capsule endoscopy S.2.1
Gastrointestinal tract
Implant to Body Surface for Capsule Endoscopy
capsule endoscopy
Transceiver on body surface
Specific use cases
Implant(head) to on-body for BCI
Implant to External for BCI
Body surface to body surface for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy

## Slide 55: Titanium courted implanted device
RF
RF
Ant.
RF
Ant.
Ant.
Metal e.g. Titanium
Metal e.g. Titanium
Metal e.g. Titanium
Non-metallic material
Whole body of an implanted device is covered by metallic material.
Partially non-metallic window is on the surface of the implant devices.
Antenna is outside of metallic chassis

## Slide 56: Whole-body voxel human models for numerical simulation
Development of whole-body voxel human models
https://emc.nict.go.jp/bio/model/model01_1_e.html
Whole-body voxel human models for numerical simulation is ready to use to develop and analyze channel and environmental model around human brain numerically.

## Slide 57: Environment Model in Vehicle
5
1
2
3
4
6
Engine/motor diagnostic sensor and controller
Air pressure sensor, wheel health sensor and controller
Transmission monitoring sensor and controller
Cabin environment sensor (temperature, brightness, humidity etc.)
Sheet sensor, health care sensors for driver
Sheet sensor, health care sensors for passenger
Engine/Motor room environment model
Cabin room environment model
https://media.istockphoto.com/photos/transparent-car-design-wire-model3d-illustration-my-own-car-design-picture-id594040008?k=6&m=594040008&s=612x612&w=0&h=XE8LiBjpM51aB4pH2CFt6-MT6IvALRPnlxPcac0RXhg=
Note:
Various type of car/vehicles
Bus, Bulldozer, Heavy construction equipment needed each different sensors.

## Slide 58
Channel model
Large scale fading
Small scale fading
HBAN
Channel model
VBAN
Channel model
Path loss
Shadowing
In-body
On-body
Surrounding body
In-vehicle
On-vehicle
Surrounding vehicle
From 15.6-2012
with new contribution
From 15.4a
UWB Channel model
Simulation methodology
HBAN
Channel model
In-body
On-body
Surrounding body
VBAN
Channel model
In-vehicle
On-vehicle
Surrounding vehicle
15.4 Indoor residential
15.4 outdoor
New contributions
From 15.8
NEW contribution

## Slide 59: Use cases
 | Use case | Sedan/RV / SUV with combustion internal engine | Sedan/RV / SUV EV | Bus | Cargo / pickup | Special purpose
1 | Failure and/or deterioration detection of vehicle components | Case 1.1 | Case 1.2 | Case 1.3 |  | Case 1.5
2 | Sensing for safety driving support / Collision avoidance | Case 2.1 C-N | Case 2.2 C-N | Case 2.3 C-N |  | Case 2.5 C-N
 |  | Case 2.1 N-C | Case 2.2 N-C | Case 2.3 N-C |  | Case 2.5 N-C
3 | Entertainment for passengers | Case 3.1 |  | Case 3.3 | Same as 3.1 | ---
4 | Key-less entry system | Case 4.1 C-N | Case 4.2 C-N | Case 4.3 C-N |  | ---
 |  | Case 4.1 N-C | Case 4.2 N-C | Case 4.3 N-C |  | ---
5 | Communication between user on pedestrian and vehicle | Case 5.1 C-N |  | Case 5.3 C-N |  | ---
 |  | Case 5.1 N-C |  | Case 5.3 N-C |  | ---
6 | Vehicle controlling / Wireless herness | Case 6.1 C-N |  | Case 6.3 C-N |  | Case 6.5 C-N
 |  | Case 6.1 N-C |  | Case 6.3 N-C |  | Case 6.5 N-C
7 | Driver’s health problem detection | Case 7.1 C-N |  | Case 7.3 C-N |  | Case 7.5 C-N
 |  | Case 7.1 N-C |  | Case 7.3 N-C |  | Case 7.5 N-C
8 | Driver’s and passenger’s healthcare application | IEEE 802.15.6 – 2012 Channel models can be applied |  |  |  |