## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ NB Assisted Data Communications]
Date Submitted: [May 15, 2023]
Source: [Mingyu Lee, Taeyoung Ha, Youngwan So, Aniruddh Rao Kabbinale, Clint Chaplin] Company [Samsung Electronics]
Address: [34, Seongchon-gil, Seocho-gu, Seoul, Korea]
E-Mail: [mg0218.lee@samsung.com]
Abstract: [Explain the need to offload UWB communications to NB, and propose an operation to support UWB ranging triggered NB]
Purpose: [ ]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the authoring individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The authors(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | Offload UWB data communications to NB
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | Support frequent UWB Ranging by offloading data communications to NB
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Contents
Motivation
NB Assisted Data Communications
Conclusions

## Slide 4: Motivation (1/2)
Recently, UWB ranging based applications are being developed
As one of example, UWB payment system utilizes the UWB contention based ranging to select the nearest user among the users nearby
The selected user can provide the payment information by using UWB data communications between the user device and the UWB payment system
However, since the devices perform ranging and data communication with each other on the same UWB channel, the UWB channel becomes more congested as the number of device increases
Especially, time resources are very limited to support both UWB ranging and UWB data communication on the same UWB channel as the number of device increases
Notes: [1] 15-22-0282-00-04ab-the-advantages-of-uwb-wakeup

## Slide 5: Motivation (2/2)
As one of UWB payment system, UWB gate application in subway can be provided
Every gate has to find the nearest user by using UWB contention based ranging
A gate performs payment procedure for the selected user who is passing through
The gate may continue UWB ranging to track the user
To meet the delay requirement (e.g., 1 sec / user), UWB time resource may not be enough to support the large number of UWB gates
Gate
Gate
= 1
Contending Devices
Successful Devices
Gate 1
Access Zone with = 1
(, distance from the center of gate entrance)
Gate
Gate
= 1
Gate 2
…
Gate
Gate
= 1
Gate N
Candidate Devices for Contention
Departing Devices
Each gate requires contention based ranging and data communications by using non-overlapped time resource with other gates to minimize interference
Notes: [1] 15-22-0282-00-04ab-the-advantages-of-uwb-wakeup

## Slide 6: NB Assisted Data Communications
Initiator can allocate NB channel/time to responders
The requirements / conditions may vary according the applications
  In UWB gate system, each gates may have their own NB channel(s) which can be allocated to the nearest user selected by using the UWB result
  Time resources saved by NB offloading can be used for more frequent ranging OR the increase of the number of gates
A method for NB resource allocation is required (e.g., IE for NB Allocation )
[ NB assisted]
UWB
(e.g., Gate 1 ~ N)
NB CH. 1
(e.g,. Gate 1)
NB CH. 2
(e.g,. Gate 2)
NB CH. N
(e.g,. Gate N)
…
[ UWB only]
UWB (e.g., Gate 1 ~ N)
Data
Data
Data
…
Ranging
Data
…
Ranging
Ranging
Ranging
Ranging
Ranging
Data
…
Block # N
Block # N+1
Offloading Data Communications
Ranging result based
NB resource allocations

## Slide 7: IE for NB Resource Allocation
Initiator may provide an allocation packet with an IE for NB resource allocation to responders
  IE may include NB channel #, offset to start of NB communications, duration of NB communications, interval of NB communications
  IE may utilize the block structure (e.g., block duration, round duration, especially slot duration) to indicate the start timing (i.e., offset to start of NB communications, the duration of NB communications, interval of NB communications
  IE (similar to RDM IE in 4z or Scheduling IE) in 4ab may be defined if initiator and responder wants to allocate NB resources
Initiator may send the allocation packet after ranging phase
  Initiator may send the allocation packet based on the ranging results
  For example, if a responder approaches to initiator enough, the initiator send NB allocation information

## Slide 8: Simple IE for NB Resource Allocation
Initiator may transmit an allocation packet during measurement report phase with some minimized information for NB resource allocation to responder(s) after ranging
  Address Size field specifies the size of the address used in NB Allocation IE
  Address field identifies the participating device. The size of the Address field is specified by the Address Size field
  NB Channel field is used to assign a NB channel index to device identified by the address field
  NB PHY specifies the NB PHY configuration index (i.e., O-QPSK PHY #1 - #10 in section 1.2.3. [1] )
  Transmission Offset field specifies the time offset between the start of allocation packet and the start of NB packet in the channel specified by NB Channel field
Bits : 2 | 6 | Octets : 2/3/8 | Octets : 2 | 1 | 4
Address Size | Reserved | Address | NB Channel | NB PHY | Transmission Offset
NB CH. 1
NB
Ranging
Phase
NB CH. 2
NB CH. N
…
UWB CH
Allocation Packet
…
time

## Slide 9: Possible fields for NB Resource Allocation
Initiator may transmit an allocation packet during measurement report phase with some more additional field for NB resource allocation to responder(s)
  NB Channel set field indicates the set of used and unused channel
  NB Channel Seed field specified the value for the seed of hopping function if NB hopping is used (e.g., value is non-zero)
  Transmission Window field specifies the duration of NB transmissions in the channel specified by NB Channel field
  Transmission Interval field indicates the remaining time until the start of the next connection window relative to the start of the current connection window
Bits : 6 | 2 | Octets : 2/3/8 | 2 | 2 | 1 | 1 | 4 | 4 | 3
Version | Address Size | Address | NB Channel Set | NB Channel | NB Channel Seed | NB PHY | Transmission Offset | Transmission Window | Transmission interval
NB CH. 1
NB
Ranging
Phase
NB CH. 2
NB CH. N
…
UWB CH
Allocation Packet
≈
NB
…
time

## Slide 10: Conclusion
Congestion in UWB channel can be mitigated by offloading it to NB
In this contribution, NB assisted data communication is considered
  NB is treated as data channel(s) which can offload data communications from UWB
On-demand scheduling based NB resource usage is provided
  In NB-MMS-UWB, strict rule and detailed role for NB resource usage are provided to maximize the efficiency and performance
  In this contribution, initiator can use NB resources freely regardless of the use of NB-MMS-UWB
Time resources saved by NB offloading can be used to improve ranging frequency or system performance in UWB

## Slide 11: Thank You

## Slide 12: References
[1] X. Luo (Apple Inc), F. Leong (NXP), M. Lee (Samsung Electronics), et al., “NBA-UWB Technical Framework Proposal”, 15-22-0262-01-04ab.