## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ UWB based NB Resource Allocation]
Date Submitted: [July 11, 2023]
Source: [Mingyu Lee, Taeyoung Ha, Youngwan So, Aniruddh Rao Kabbinale, Clint Chaplin] Company [Samsung Electronics]
Address: [34, Seongchon-gil, Seocho-gu, Seoul, Korea]
E-Mail: [mg0218.lee@samsung.com]
Abstract: [Explain the need to offload UWB communications to NB, and propose an operation to support UWB ranging triggered NB]
Purpose: [ ]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the authoring individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The authors(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | Offload UWB data communications to NB
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | Support frequent UWB Ranging by offloading data communications to NB
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Contents
Recap : Offloading UWB Data Communications to NB
Comments / Resolutions
TFD Contents

## Slide 4: Recap: Offloading UWB Data Communications to NB
Initiator may transmit a NB allocation packet during measurement report phase with a minimized information for NB resource allocation to responder(s) after ranging
  Address Size field specifies the size of the address used in NB Allocation IE
  Address field identifies the participating device. The size of the Address field is specified by the Address Size field
  NB Channel field is used to assign a NB channel index to device identified by the address field
  NB PHY specifies the NB PHY configuration index (i.e., O-QPSK PHY #1 - #10 in section 1.2.3. [1] )
  Transmission Offset field specifies the remaining time until the start(or end) of NB packet in the channel specified by NB Channel field relative to the start of allocation packet (or end of round / block)
Bits : 2 | 6 | Octets : 2/3/8 | Octets : 1 | 1 | 4
Address Size | Reserved | Address | NB Channel | NB PHY | Transmission Offset
NB CH. 1
NB
Ranging
Phase
NB CH. 2
NB CH. N
…
UWB CH
NB Allocation Packet
…
time
Offset to start of NB Data Communications

## Slide 5: Comments / Resolutions (1/2)
UWB is faster than NB, why do we need to use NB for data transmission ?
  UWB is faster than NB. However, since the number of NB channels is much greater than the number of UWB channels, NB channels can be used by multiple devices simultaneously
  In gate payment case, except for the gate doing ranging / data communications, other gates have to wait for their turn even if data communication with specific device is required
  If NB offloading is used, other gates can have NB data communication while a gate is ranging in UWB channel => Number of gates can be increased and delay performance can be enhanced !
[ UWB Triggered NB]
UWB
(e.g., Gate 1 ~ N)
NB CH. 1
(e.g,. Gate 1)
NB CH. 2
(e.g,. Gate 2)
NB CH. 3
(e.g,. Gate 3)
…
[ UWB only]
UWB (e.g., Gate 1 ~ 3 )
Data
Data
Data
Ranging
…
Block # N
Block # N+1
Offloading Data Communications
Ranging result based NB resource
allocations
Data
Ranging
Data
Ranging
Data
Ranging
Data
Ranging
Data
Ranging
Data
Gate 1
Gate 2
Gate 3
Gate 1
Gate 2
Gate 3
Ranging
…
Ranging
Ranging
Ranging
Ranging
Ranging
Ranging
Ranging
Ranging
Ranging
Ranging
Ranging
Gate 1
Gate 2
Gate 5
Gate 6
Gate 3
Gate 4
Gate 1
Gate 2
Gate 5
Gate 6
Gate 3
Gate 4
…
Number of Gates 2
Notes: [1] 15-22-0282-00-04ab-the-advantages-of-uwb-wakeup

## Slide 6: Comments / Resolutions (2/2)
NB data transmission may interfere with Wi-Fi
  Time sensitive applications (e.g., gate payment) can use this feature for supporting the large number of devices simultaneously
  In general, a large scale network to support the large number of users (e.g., gate payment system) is deployed by well-designed network plan
  By the network plan, the interference between NB and Wi-Fi can be minimized (e.g., Wi-Fi AP may use non-NB channels)
Notes: [1] 15-22-0282-00-04ab-the-advantages-of-uwb-wakeup

## Slide 7: TFD
3 Message Format
1.3.1 NB Allocation IE
The NB Allocation IE is used by an initiator to send the NB resource allocation information to a responder (in a unicast frame). The content field of the NB Allocation IE shall be formatted as shown in Figure 2.
Figure 2 Control Field of the Scheduling IE
Address Size field specifies the size of the address used in NB Allocation IE.
Address field identifies the participating device. The size of the Address field is specified by the Address Size field
NB Channel field is used to assign a NB channel index to device identified by the address field
NB PHY specifies the NB PHY configuration index.
Transmission Offset field specifies the remaining until the start of NB packet in the channel specified by NB Channel field relative to the end of NB allocation packet.
  2 Basic Operation
  Initiator may transmit a NB allocation packet during measurement report phase followed by ranging phase. The NB allocation packet shall include NB Allocation IE to responder(s). After ranging phase, ERDEVs are scheduled in the measurement phase to exchange the required information for NB data communications. In the example Figure 1, the initiator send NB allocation packet including NB Allocation IE with NB channel and offset to responder for starting NB data communication during measurement phase.
Figure 1 NB Data Communication Triggered by NB Allocation Packet
At the end of time offset, initiator shall transmit NB packet on the allocated NB channel. The responder may listen for incoming NB packet. Once the responder has received NB packet, it may transmit NB packet.
Bits : 2 | 6 | Octets : 2/3/8 | Octets : 2 | 1 | 4
Address Size | Reserved | Address | NB Channel | NB PHY | Transmission Offset

## Slide 8: Thank You