## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: NB message format for Multiple Transmission
Date Submitted: June 13, 2023
Source: [Taeyoung Ha, Mingyu Lee, Youngwan So, Aniruddh Rao Kabbinale, Ankur Bansal, Clint Chaplin] Company [Samsung Electronics]
E-Mail: ty1115.ha@samsung.com
Abstract: Updates for Multiple RSF Transmissions in a Slot Scenario
Purpose: Increase air time efficiency by allowing the multiple MMRS transmission in a slot.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Multiple RSF Transmission

## Slide 3: Packet Format for NB
Control Packet
ID: Message ID
RPA: Resolvable Private Address RPA_hash: AES-128-ECB(key=IdentityResolvingKey, data=RPA_prand]) % 2^24 RPA_prand: Static during one ranging block, at least

## Slide 4: Packet Format for NB
Control Packet
MessageControl | MessageContents [Length]
0x00 | {Number of Responder [1], List of {Responder Address [3], Slot index [1], UWB PHY CONFIG[3]}
0x01 | {Number of Responder [1], List of {Responder Address [3], Slot index [1]}
0x02 | {Number of Responder [1], List of {Responder Address [3], UWB PHY CONFIG[3]}

## Slide 5: Packet Format for NB
MessageContents Description
MessageContents[Length in octets] | Description
Number of Responder [1] | Number of responders in this Ranging session
Responder Address [3] | Address of Responder, RPA_Hash or Public random address
Slot index [1] | Allocated slot index of the Responder (if poll packet is transmitted, the slot of poll message becomes 0, if only Control packet is transmitted, the slot of control message becomes 0)
UWB PHY CONFIG [3] | RSF의 PHY Configuration Bits 0-5: Preamble Code Indexes {9, …, 48} if (9 <= Preamble Code Index <= 32) { Bits 6-12: Reserved } elseif (33 <= Preamble Code Index <= 48) { Bits 6-12: MMRS complementary set zeros {0, …, 64} } Bits 13-15: Number of MSR {32, 40, 48, 64, 128, 256} Bits 16-19: UWB channel 1-16 Bits 20-23: Reserved

## Slide 6: Packet Format for NB
Control Packet
MessageControl | MessageContents [Length]
0x03 | {same as MessageControl = 0x00}, but Poll Message will not be transmitted
0x04 | {same as MessageControl = 0x01}, but Poll Message will not be transmitted
0x05 | {same as MessageControl = 0x02}, but Poll Message will not be transmitted
0x06 | {0x00}, but Poll Message will not be transmitted

## Slide 7: Packet Format for NB
Control Packet
MessageControl | MessageContents [Length]
0x10 | {same as MessageControl = 0x00}, but only Initiator send the measurement report
0x11 | {same as MessageControl = 0x01}, but only Initiator send the measurement report
0x12 | {same as MessageControl = 0x02}, but only Initiator send the measurement report
0x13 | {same as MessageControl = 0x00}, but Poll Message will not be transmitted, and only Initiator send the measurement report
0x14 | {same as MessageControl = 0x01}, but Poll Message will not be transmitted, and only Initiator send the measurement report
0x15 | {same as MessageControl = 0x02}, but Poll Message will not be transmitted, and only Initiator send the measurement report
0x16 | {0x00}, but Poll Message will not be transmitted, and only Initiator send the measurement report

## Slide 8: Packet Format for NB
Control Packet
MessageControl | MessageContents [Length]
0x20 | {same as MessageControl = 0x00}, but only Responder send the measurement report
0x21 | {same as MessageControl = 0x01}, but only Responder send the measurement report
0x22 | {same as MessageControl = 0x02}, but only Responder send the measurement report
0x23 | {same as MessageControl = 0x00}, but Poll Message will not be transmitted, and only Responder send the measurement report
0x24 | {same as MessageControl = 0x01}, but Poll Message will not be transmitted, and only Responder send the measurement report
0x25 | {same as MessageControl = 0x02}, but Poll Message will not be transmitted, and only Responder send the measurement report
0x26 | {0x00}, but Poll Message will not be transmitted, and only Responder send the measurement report

## Slide 9: Packet Format for NB
Control Packet
MessageControl | MessageContents [Length]
0x30 | {same as MessageControl = 0x00}, but Initiator and Responder send the measurement report
0x31 | {same as MessageControl = 0x01}, but Initiator and Responder send the measurement report
0x32 | {same as MessageControl = 0x02}, but Initiator and Responder send the measurement report
0x33 | {same as MessageControl = 0x00}, but Poll Message will not be transmitted, and Initiator and Responder send the measurement report
0x34 | {same as MessageControl = 0x01}, but Poll Message will not be transmitted, and Initiator and Responder send the measurement report
0x35 | {same as MessageControl = 0x02}, but Poll Message will not be transmitted, and Initiator and Responder send the measurement report
0x36 | {0x00}, but Poll Message will not be transmitted, and Initiator and Responder send the measurement report

## Slide 10: Packet Format for NB
Poll Packet
ID: Message ID
RPA: Resolvable Private Address RPA_hash: AES-128-ECB(key=IdentityResolvingKey, data=RPA_prand]) % 2^24

## Slide 11: Packet Format for NB
Poll Packet
MessageControl | MessageContents [Length]
0x00 | {0x00}
0x01 | {Number of Responder [1], List of {Responder Address [3], UWB PHY CONFIG[3]}