## Slide 1
Project: P802.15 Working Group for Wireless Specialty Networks
Submission Title: Overview of 15.6-2012 Std and P15.6ma in the 802 Architecture
Date Submitted: July 3rd, 2023
Source: Marco Hernandez1,2, Ryuji Kohno1,3, Takumi Kobayashi1,4, Daisuke Anzai4, Minsoo Kim1
Company: 1YRP-IAI, Japan; 2CWC, Oulu Univ. Finland, 3YNU, Japan; 4Nagoya I.T., Japan.
Address: 3-4 Hikarino-oka, Yokosuka, 239-0847, Japan.
E-Mail: Marco.Hernandez@ieee.org; kohno@ynu.ac.jp; Kobayashi-Takumi-ch@ynu.ac.jp; Minsoo@minsookim.com;
Abstract: Joint meeting 802.1 and 802.15.
Purpose: Material for discussion.
Notice: This document has been prepared to assist P802.15.6ma. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.6ma.

## Slide 2: 802.15.6 in a nutshell
15.6 Body Area Networks define a simple star topology of devices or wearables around the human body
For medical and non-medical applications

## Slide 3: Star topology
Devices: sensor/actuator + radio interface
  may be placed on-body or in-body (implant or digestible)
A coordinator controls the access to the medium.
Those define a self-contained human wireless network
  Up to the link layer
  Connection to the outside (Internet) at a higher layer.

## Slide 4: 15.6ma
The TG 15.6ma works on a revision of the 15.6-2012 Std
  Increase dependability in dense scenarios & other wireless systems (operation in unlicensed band)
  Add support to vehicles (cars, bus) VBAN
  Interoperability between HBAN and VBAN
  Guarantee of delivery of data to infrastructure (throughput & latency) in L2
The latter is the TG6ma interest in TSN.

## Slide 5: Context of 15.6 and 15.6ma in the 802 Architecture
Outline:
  Use of the LLC,
  MAC address format,
  QoS mechanism and
  MSDU formats.

## Slide 6: Use of LLC in 15.6-2012
The MAC Services of the 15.6 Std implicitly support the LLC sublayer entity.
The Std does not mention explicitly the exchange of MSDUs via the LLC client or provider.
  The spec only mentions “the MAC provides its service to the MAC client (higher layer) through the MAC service access point (SAP) located immediately above the MAC sublayer”.
  The underline assumption is that a 15.6 ad hoc network (a coordinator and associated nodes) does not interact with another entity in L2; and neither what happens above the MAC layer.
  In addition, the 15.6 Std has a clause for cyber-security based on a Key Encapsulation Mechanism (KEM).

## Slide 7: LLC in 15.6ma
The revision 15.6ma aims to interact with another 15.6ma entity in L2 (C2C) and with other entities in L2 (bridge) to connect to other networks (Wi-Fi, 5G, Ethernet)
  1) The revision 15.6ma will explicitly describe the support of LLC Protocol Discrimination (LDP) and Ethertype Protocol Discrimination (EPD).
  2) Support of IEEE 802.1Q bridge ports to use the 15.6ma MAC service for the exchange MSDUs.

## Slide 8: MAC address format
The MAC Services and protocols in the15.6-2012 Std and planned revision P15.6ma use 48-bit MAC addresses
  Hence, compatibility with the 802.1 family of Stds
Support of multicast addressing has not been considered (at least at the moment)

## Slide 9: Support of QoS via Traffic Type in 15.6-2012
  “UP values, when referenced in prioritizing medium access of data and management type frames, shall be determined based on the designation of frame payloads (traffic) contained in the frames according to Table 18. The traffic designation for background (BK), best effort (BE), excellent effort (EE), video (VI), voice (VO), and network control is based on some traffic types defined in Annex G.1 of IEEE Std 802.1D™-2004”

## Slide 10: Traffic type for the UWB PHY in 15.6
The UWB PHY clause defines high QoS mode to traffic type 6, and default mode any other traffic type (~7).
This was necessary to discriminate between two UWB technologies
  Default mode: IR-UWB and optional FM-UWB
  High QoS mode: only IR-UWB
  The TG will discuss if FM-UWB will be deprecated.

## Slide 11: Planned QoS in P15.6ma
TG6ma has plans to revise Table 18, but nothing concrete yet.
Nevertheless, TG 15.6ma will support compatibility with 802.1 traffic classification.

## Slide 12: MSDU format in 15.6-2012
The usual: MAC header + MAC payload + MAC footer

## Slide 13: 15.6ma MAC
Due to the historic background of 15.6, the MSDU format supports several MAC mechanisms (polling, CSMA, slotted Aloha, LBT), and it is up to vendors what specifically to implement.
  However, the result was that the MAC spec is difficult to understand
The revision 15.6ma plans to simplify the MAC mechanism under a UWB PHY:
  LBT & slotted Aloha (CAP) and TDMA (CFP)
  (maybe the support of an Ethertype field)
  Hence, the MSDU Header will change.

## Slide 14: Next steps
Plan next actions: