## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Preliminary Performance Evaluation of Channel Coding in TG6ma
Date Submitted: Sept. 14th, 2023
Source: Daisuke Anzai1, Sho Asano1, Takumi Kobayashi1, Marco Hernandez2, Kento Takabayashi3
Company: 1Nagoya Institute of Technology (NIT), Japan; 2YRP International Alliance Institute (YRP-IAI), Japan; 3Toyo University, Japan
Address: Gokiso-cho, Showa-ku, Nagoya, 466-8555, Japan
Voice: +81-52-735-5389, FAX: +81-52-735-5389, E-Mail: anzai@nitech.ac.jp
Re: In response to call for technical contributions
Abstract: This provides a preliminary investigation of channel coding proposed in TG6ma, and some simulation results are discussed.
Purpose: Material for discussion in P802.15.6a TG corresponding to comments in EC Meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Preliminary Performance Evaluation of Channel Coding in TG6ma
Daisuke Anzai1, Sho Asano1, Takumi Kobayashi1, Marco Hernandez2, and Kento Takabayashi3
1Nagoya Institute of Technology (NIT)
2YRP International Alliance Institute (YRP-IAI)
3Toyo University

## Slide 3: Channel coding in TG6ma
User priority | Traffic designation | Frame type | Inner code | Outer code
0 | Background | Data | 15.4ab LDPC code (R=1/2) | -
1 | Best effort | Data | 15.4ab LDPC code (R=1/2) | -
2 | Excellent effort | Data | 15.4ab LDPC code (R=1/2) | -
3 | Video | Data | 15.4ab LDPC code (R=1/2) | -
4 | Voice | Data | 15.4ab LDPC code (R=1/2) | (54,46) shortened RS code
5 | Medical data or network control | Data or management | 15.4ab LDPC code (R=1/2) | (54,38) shortened RS code
6 | High-priority medical data or network control | Data or management | 15.4ab LDPC code (R=1/2) | (54,28) shortened RS code
7 | Emergency or medical implant event report | Data | 15.4ab LDPC code (R=1/2) | (54,14) shortened RS code

## Slide 4: Preliminary evaluation results
・ Outer code
Shortened RS code with a code length of 324 bits
・ Inner code
LDPC code with a code length of 1296 bits
Burst error channel and AWGN assumed
IR-UWB modulation
Data rate: 50 MHz
Center Frequency: 7987.2 MHz
Bandwidth: 499.2 MHz
PRF: 4 MHz

## Slide 5: Preliminary evaluation results
BCC and LDPC codes with a code length of 1296 bits
AWGN channel assumed
IR-UWB modulation
Data rate: 50 MHz
Center Frequency: 7987.2 MHz
Bandwidth: 499.2 MHz
PRF: 4 MHz

## Slide 6: Preliminary evaluation results
・ Outer code
Shortened RS code with a code length of 324 bits
・ Inner code
BCC code with a code length of 1296 bits
AWGN channel assumed
IR-UWB modulation
Data rate: 50 MHz
Center Frequency : 7987.2 MHz
Bandwidth: 499.2 MHz
PRF : 4 MHz

## Slide 7: References
D. Anzai, I. Balasingham, G. Fischer, J. Wang, “Reliable and High-Speed Implant Ultra-Wideband Communications with Transmit–Receive Diversity,” EAI/Springer Innovations in Communication and Computing, pp. 27-32, March 2020.
Y. Shimizu, D. Anzai, R. C-Santiago, P. A. Floor, I. Balasingham, and J. Wang, “Performance evaluation of an ultra-wideband transmit diversity in a living animal experiment” IEEE Trans. Microw. Theory Tech., vol. 65, no. 7, pp. 2596-2606, July 2017.
D. Anzai, K. Katsu, R. Chavez-Santiago, Q. Wang, D. Plettemeier, J. Wang, and I. Balasingham, “Experimental evaluation of implant UWB-IR transmission with living animal for body area networks,” IEEE Trans. Microw. Theory Tech., vol. 62, no. 1, pp. 183-192, Jan. 2014.
J. Shi, D. Anzai, and J. Wang, “Channel modeling and performance analysis of diversity reception for implant UWB wireless link,” IEICE Trans. Commun., no. E95-B, vol. 10, pp. 3197-3205, Oct. 2012.