## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Performance Evaluation of Channel Coding Based on TG6ma Channel Model for Some Classes of Coexistence
Date Submitted: Jan. 17th, 2024
Source: Daisuke Anzai, Shunsuke Ishiguro, Takumi Kobayashi
Company: Nagoya Institute of Technology (NIT), Japan
Address: Gokiso-cho, Showa-ku, Nagoya, 466-8555, Japan
Voice: +81-52-735-5389, FAX: +81-52-735-5389, E-Mail: anzai@nitech.ac.jp
Re: In response to call for technical contributions
Abstract: This provides a preliminary investigation of the effect of interference cancellation on UWB ranging accuracy under multiple BAN coexistence situations, and some simulation results are discussed.
Purpose: Material for discussion in P802.15.6a TG corresponding to comments in EC Meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Performance Evaluation of Channel Coding Based on TG6ma Channel Model for Some Classes of Coexistence
Daisuke Anzai, Sho Asano, Kento Takabayashi,
Takumi Kobayashi, Marco Hernandez, Ryuji Kohno
Nagoya Institute of Technology (NIT)
Toyo University, YNU, YRP-IAI, CWC Oulu Univeristy

## Slide 3: Importance of QoS control
User priority | Traffic designation | Frame type
0 | Background (BK) | Data
1 | Best effort (BE) | Data
2 | Excellent effort (EE) | Data
3 | Video (VI) | Data
4 | Voice (VO) | Data
5 | Medical data or network control | Data or management
6 | High-priority medical data or network control | Data or management
7 | Emergency or medical implant event report | Data
In WBAN systems, a wearable vital sign sensor node can include various types of sensors with different data rates, the allowable communication error ratio and delay
IEEE 802.15.6 based WBAN may deal with 8 levels of user priority data
Those data have a wide range of quality of service (QoS)
Therefore, optimal error control for input data is an important feature in sensor data transmission procedures

## Slide 4: Error control in current IEEE 802.15.6
IEEE 802.15.6 shall use a (63, 51) BCH code as an error correcting code in narrowband, UWB and HBC PHY
Only user priority 6 data in UWB-PHY may use a hybrid ARQ with a (126, 63) shortened BCH code
However, the error control scheme of the current IEEE 802.15.6 cannot deal with the QoS because of lack of flexibility
In IEEE 802.15.6ma, we indicate a concept of channel coding technique to deal with various types of QoS data as shown in a next figure

## Slide 5: Forward error correcting codes in TG6ma
As an outer code, shortened Reed-Solomon (RS) codes with N=54 (original code length N=63) will be selected to correct burst errors due to interference from other WBANs and the coding rates are changed according to each QoS and channel condition
As an inner code, 15.4ab LDPC (K=324, 648, 972, R=1/2) or BCC will be selected for the coexistence of 15.6ma and 15.4ab
This updated concept table is considered as the first priority
User priority | Inner code | Outer code | HARQ
0 | 15.4ab LDPC or BCC (R=1/2) |  | -
1 | 15.4ab LDPC or BCC (R=1/2) |  | -
2 | 15.4ab LDPC or BCC (R=1/2) |  | -
3 | 15.4ab LDPC or BCC (R=1/2) |  | -
4 | 15.4ab LDPC or BCC (R=1/2) | (54, 46) shortened RS code | -
5 | 15.4ab LDPC or BCC (R=1/2) | (54, 38) shortened RS code | -
6 | 15.4ab LDPC or BCC (R=1/2) | (54, 28) shortened RS code | -
7 | 15.4ab LDPC or BCC (R=1/2) | (54, 14) shortened RS code | -

## Slide 6: Evaluations (Only RS)
Bit error ratio of (54,46), (54,38), (54,28), (54,14) shortened RS codes and no encoding were evaluated under an
AWGN channel and BPSK modulation
Performances can be improved as the coding rate decreases

## Slide 7: Evaluations (LDPC and RS)
Inner code: N=1296-bit (R=1/2) LDPC code
Outer code: (54,46), (54,38), (54,28), (54,14) shortened RS codes and no encoding
Performances can be controlled by changing the code rate of the RS code
Low coding rate cases can correct a lot of errors and erasures
AWGN channel and BPSK modulation
Burst erasure occurs at 32.5% of the code length of the LDPC code (70 consecutive 6-bit erasures)

## Slide 8: FEC performance evaluation under TG6ma channel model
PDF of log-normal distribution ()
The PDF of shadowing in path-loss is as follows:
From the above, the voltage amplitude ratio follows a log-normal distribution, and the PDF is as follows:
: mean of shadowing [dB]
: standard deviation of shadowing [dB]
: mean of logarithmic amplitude ratio
: standard deviation of logarithmic amplitude ratio

## Slide 9: Evaluation results in shadow fading
BPSK modulation
AWGN and Shadowing
・w/o coding
・Only RS
・Only LDPC
RS parameter
Code length: 324 bits
LDPC parameter
Code length: 1296 bits
Fading parameter
Variance: 2.69 [dB]

## Slide 10: Evaluation results in shadow fading
BPSK modulation
AWGN and Shadowing
・LDPC
・Outer: RS, Inner: LDPC
RS parameter
Code length: 324 bits
LDPC parameter
Code length: 1296 bits
Fading parameter
Variance: 2.69 [dB]

## Slide 11: References
D. Anzai, I. Balasingham, G. Fischer, J. Wang, “Reliable and High-Speed Implant Ultra-Wideband Communications with Transmit–Receive Diversity,” EAI/Springer Innovations in Communication and Computing, pp. 27-32, March 2020.
Y. Shimizu, D. Anzai, R. C-Santiago, P. A. Floor, I. Balasingham, and J. Wang, “Performance evaluation of an ultra-wideband transmit diversity in a living animal experiment” IEEE Trans. Microw. Theory Tech., vol. 65, no. 7, pp. 2596-2606, July 2017.
D. Anzai, K. Katsu, R. Chavez-Santiago, Q. Wang, D. Plettemeier, J. Wang, and I. Balasingham, “Experimental evaluation of implant UWB-IR transmission with living animal for body area networks,” IEEE Trans. Microw. Theory Tech., vol. 62, no. 1, pp. 183-192, Jan. 2014.
J. Shi, D. Anzai, and J. Wang, “Channel modeling and performance analysis of diversity reception for implant UWB wireless link,” IEICE Trans. Commun., no. E95-B, vol. 10, pp. 3197-3205, Oct. 2012.