## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [DraftC comment resolution proposals]
Date Submitted: [November 15, 2022]
Source: [Alexander Krebs, (Apple)]
Email: krebs @ apple.com
Re: [Input to the Working Group]
Abstract: [Recommendation how to resolve some of the DraftC pre-ballot comments]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Reassignments
Bin Q: 154 360 361 362 381 518 519 637 741 742 755 756 787 809 810 905 906 22 355 751 790 796
Jinjing: 8 18 23 24 37 211 328 329 365 366 367 368 370 372 373 374 379 687 758 759 760 761 762 763 764 765 766 767 768 769 770 775 776 781 782 783 785 786 788 789
Rojan: 168 627 13 77 169 170 343 634 640 641 642 643 644 651 652 653 654 655 709 730 824 826 828 830 832 834
Youngwan: 25 26 27 50 89 212 327 332 333 336 337 604 623 624 626 900 901 902 39 182 183 386 387 388 389 393 816 817 818 823
Hongwon: 87 151 166 510 38 511 534 535 536 537 538 539 540 545 546 649 650 699 704 801 811
Vinod+Xiliang: 92 93 215 216 217 218 839 840 841 843
Carl: 29 80 81 90 91 212 332 624 729 901
Alex: add all but the above from MSS category

## Slide 3: Accept
Name | Index # | Category | Page | Sub-clause | Line # | Comment | Proposed Change | Category | Assignee | Comment Alex
Benjamin Rolfe | 129 | Technical | 17 | 7.3.7.3 | 5 | Missing requirement. Should include a normative statement that the field shall be set to one of the valid non reserved ID values in Table 1. | Change to: The Compact Frame ID field identifies the Compact frame and what is contained in Content field. The Compact Frame ID field shall be set to a non-reserved value defined in Table 1. | NEWFR | Alex | Accept
Pooria Pakrooh | 74 | Technical | 42 | 10.38.1 | 24 | Z=2ms. | Replace Z with 2ms in Figure 21. | MSS |  | Accept
Benjamin Rolfe | 148 | Technical | 43 | 10.38.2 | 8 | The cross reference doesn't track with the base standard (Rev E D01). I think the correct xref is 10.31.3.3 (for now). | Change to 10.31.3.3 | MSS |  | Accept
Benjamin Rolfe | 147 | Technical | 43 | 10.38.2 | 9 | Use of "shall not" is not good specification practice as it is unverifiable, imprecise and readily misunderstood. Positive statements are always better. In this case we are specifying a specific transmission offset (zero) to be used when round hopping is used. So that's what we should say. | Change to: The round hopping, specified in 10.29.3.3 may be optionally be used with UWB MMS ranging. To ease carrier coherence between UWB MMS phases, when round hopping is used, the transmission offset shall be zero. | MSS |  | Accept
Benjamin Rolfe | 154 | Technical | 45 | 10.38.3.3 | 28 | Incomplete specification: suggests a course of action to select "one" or "two or more" of a set without specifying which one or more are selected. If this decision is implementation dependent (out of scope of this standard) then we should be clear. | Add after last sentence: The method for selecting responders for this purpose is out of scope of this standard. | MSS |  | Accept
Li-Hsiang Sun | 12 | Technical | 50 | 10.38.4.1 | 12 | ranging control slots' are not defined, only used once in draft and 2 ranging control slots durations can be different | change to "includes (macMmsRcpPollNSlots + macMmsRcpRespNSlots) ranging slots | NBMSS | Alex | Accept
Benjamin Rolfe | 150 | Technical | 51 | 10.38.4.2 | 18 | "shall not" (incorrect use of normative language). Easily stated as a positive (verifiable) requirement. | Change to: When the UWB MMS ranging round is terminated before its completion, the involved device shall cease transmission for the remainder of the ranging round. | NBMSS | Alex | Accept
Billy Verso | 208 | Technical | 57 | 10.38.8.2 | 11 | For clarity the designation "802.15.4 2.5 MHz NB Channels" at the left of Figure 34 should probably just be "O-QPSK PHY Channels" | Change the designation to "O-QPSK PHY Channels", and insert the words "2.5 MHz spaced" before the "O-QPSK" on line 9 (above the figure). | NBF | Alex | Accept
Li-Hsiang Sun | 15 | Technical | 58 | 10.38.8.3 | 1 | In Fig 35 'ranging slot' is used. 'ranging slot' is defined in p68L2, but in Table 9 duration of macMmsRcpPollNSlots, macMmsRcpRespNSlots, macMms1stReportNSlots, macMms2ndReportNSlots are not the same as a ranging slot | In Fig 35 change 'Ranging slot' to 'initiator ranging slot(s)' and 'responder ranging slot(s)' | NBF | Alex | Accept
Carl Murray | 707 | Technical | 58 | 10.38.8.3 | 1 | In Figure 35 is "Ranging slot" the correct term? This would mean that the maximum packet would be 95% of a ranging slot but the POLL slot for example can be multiple ranging slots |  | NBF | Alex | dup #15
Benjamin Rolfe | 155 | Technical | 58 | 10.38.8.4.2 A | 21 | Incorrect use of "may". May defines an optional behavior within the scope of this standard. Here we are clearly describing something outside the scope of this standard (upper layer decision based on what other radios it is using) | Change to: For example, an initiator device that is equipped with an IEEE 802.11 radio and engaged in concurrent radio transmissions with other devices on known WLAN channels can choose to exclude the conflicting channels. | NBF | Alex | Accept
Rojan Chitrakar | 621 | Technical | 60 | 10.38.9.1 | 6 | ranging initiation message should be One-to-many Poll Compact frame. Figures 37 and 38 should also be updated accordingly. | as in comment | NBF | Alex | Accept
Rojan Chitrakar | 629 | Technical | 64 | 10.38.10.2.1 | 22 | What is reference [2] and is it a normative reference? If so should be listed in clause 2 (Normative references). AES is widely used in IEEE, please check if the normative reference FIPS Pub 197 included in 802.15.4-2020 already covers the AES-128-ECB. | Please check if the normative reference FIPS Pub 197 already covers the AES-128-ECB, else add the relevant reference in the subclause 2. | NBF | Alex | Accept
Rojan Chitrakar | 628 | Technical | 64 | 10.38.10.2.1 | 25 | "and the RPA_prand communicated by the initiator." The initiator's RPA_prand shall be the RPA_prand carried in the most recetly received frame, else the RPA_hash resolution will fail. | Rephrase as: " … and the most recent RPA_prand communicated by the initiator." | NBF | Alex | Accept
Carl Murray | 716 | Technical | 66 | 10.38.10.3.7 | 18 | typo? | Change with indexes 43 to 49 to with indexes 44 to 49 | NBF | Alex | Accept
Rojan Chitrakar | 633 | Technical | 69 | 10.38.10.3.13 | 28 | ADV_CONF Compact frame should be Advertising Poll Compact frame. The field is also used in the Public Advertising Poll Compact frame. | as in comment | NBF | Alex | Accept
Carl Murray | 749 | Technical | 77 | 10.38.10.8 | 13 | Incorrect statement | Change … and may also convey short term operating parameters to … and may also convey short term operating parameter request(s) | NBF | Alex | Accept
Carl Murray | 838 | Technical | 103 | 10.38.11.1 | 1 | A"ranging slot" is a measurement unit. | Replace "Number of slots" by "Number of ranging slots" in descriptions for macMmsRcpPollNSlots, macMmsRcpRespNSlots and macMmsRpDuration. | NBF | Alex | Accept