## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSNs)
Submission Title: Future Directions of Next Generation OCC Standard
Date Submitted: January 17, 2024
Source: Nguyen Ngoc Huy, Yeong Min Jang [Kookmin University]
Address: Kookmin University, 77 Jeongneung-Ro, Seongbuk-Gu, Seoul, 02707, Republic of Korea
Voice: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract: Present the future directions for NG-OCC
Purpose: Presentation for contribution on NG-OCC
Notice: This document has been prepared to assist the NG-OCC. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by NG-OCC.

## Slide 2: Contents
NG-OCC Characteristics
  AI Integration in NG-OCC
  Channel Model to Support High Mobility Under Adverse Condition
Future Applications of NG-OCC
  OCC-based Drone Networks
  Indoor/Outdoor Positioning Using OCC and LiDAR
  Deep Learning based OCC to Support High Mobility Vehicle
Conclusion

## Slide 3: AI Integration in NG-OCC
Status of current standard: The most recent standardization of NG-OCC incorporates the use of deep learning(DL) for light source tracking, region of interest (RoI) creation, and enhancement of the decoder side.
Target and Necessity of NG standard: To meet the specifications and requirements of NG-OCC, the implementation of AI is essential for achieving increased stability, higher data rates, and improved mobility.
Novelty of NG standard: Within NG-OCC, AI deployment involves integrating various AI technologies into the system through the implementation of lightweight AI for each technology.
Commercialization point of view: The integration of AI in NG-OCC occupations aims to enhance operational efficiency, decision-making process and enable automation while necessitating continuous learning and ethical considerations on the usage of AI.

## Slide 4: Channel Modeling for NG-OCC
Conventional Channel Estimation
Least Square (LS) Estimation
Least Minimum Mean Squared Error (LMMSE)
Maximum Likelihood (ML) Estimation
Machine Learning Based Channel Estimation
Deep learning-based
Conventional Neural Network -based
Deep Residual Learning-based
FFDNet-based
ResCBDNet-based

## Slide 5
Difference between conventional and machine learning base channel estimation
Using ML for channel estimation can offer advantages in scenarios where traditional methods may struggle to adapt to changing and complex channel conditions like (atmospheric turbulence or mobility of optical sources).
DRL algorithms have the capability to learn and adapt to non-linear and non-stationary channel conditions, which may be difficult for traditional estimation techniques such as Least Squares Estimation, Maximum Likelihood Estimation (MLE) that assume linearity and stationarity.
Traditional estimation methods may assume Gaussian noise(electronic and thermal noise). which may not accurately represent real-world noise characteristics in FSO/OCC systems. ML can learn to handle non-Gaussian noise distributions(Atmospheric turbulence).
Traditional methods often rely on assumptions about the channel, noise, or environmental conditions.
ML, being a model-free approach, can learn directly from data without making strong assumptions.
Channel Modeling for NG-OCC

## Slide 6
Currently, the RF spectrum faces limitations, including restricted availability, electromagnetic interference (EMI), multipath reflections leading to fading and degraded signal transmission quality, and strict regulatory operations with high risks in communications security.
Spectrum-optic-based technologies such as OCC can be a solution to address spectrum scarcity, providing a broad range of frequencies, no regulations, no EMI, and no multipath reflections.
Additionally, OCC, as an OWC subsystem network, can be applied as backhaul networks supporting the demands of upcoming 5G/6G generation technologies.
These demands are characterized by ultra-high security, massive user connectivity, ultra-high capacity, low latency, and ultra-low power consumption.
In practical application, of OCC encompassing fields such as IoT, underwater communication, joint communication, sensing, and localization (V2V, M2M, Drone/UAV, etc.).
Therefore, future research is needed to guide the implementation of OCC across various fields to maximize its potential in each application.
Future Application of NG-OCC

## Slide 7
Status of current standard: Non-existent
Target and Necessity of NG standard: To meet the specifications and requirements of NG-OCC-enabled drone/UAV networks. OCC utilization in drone networks can improve security, immunity to RF interference, low latency, and higher bandwidth.
Novelty of NG standard: Integration of NG-OCC-enabled network for drone network applications, which can be applied to various tasks such as surveillance, monitoring, data collection, delivery services, and more.
Commercialization point of view: The integration of NG-OCC in drone networks aims to enhance operational efficiency, improved security, immunity to RF interference, lower latency, and higher bandwidth.
OCC-based Drone Networks

## Slide 8
Status of current standard: Non-existent
Target of NG standard: Standardize the extended usage of OCC for aiding indoor/outdoor positioning systems.
Necessity of NG standard: Due to the increase usage of indoor/outdoor positioning systems, the usage of OCC for providing indoor/outdoor positioning systems is deemed important since several studies has proven that incorporation of OCC can improve the accuracy of indoor/outdoor positioning.
Novelty of NG standard: The indoor/outdoor positioning systems based on OCC as the main or supporting technology to provide flexible technology integration with other existing state-of-the-art technology for indoor/outdoor positioning systems.
Commercialization point of view: The indoor/outdoor positioning systems is one of the hot topic to discuss nowadays, by promoting this standards, it is expected that the it can attract industry interests.
Indoor/Outdoor Positioning using OCC and LiDAR

## Slide 9
Status of current standard: It is based on IEEE 802.15.7-202x (Right now SA Ballot stage), utilizing RS-OFDM modulation and MIMO C-OOK to achieve mobility of approximately 10 km/h.
Target of NG standard: To enhance the recognition accuracy of LEDs under high-mobility conditions and to improve the selection of the Region of Interest (RoI).
Necessity of NG standard: The OCC system offers numerous benefits but faces significant challenges, particularly in high-mobility and noisy environments, which affect the accuracy of LED detection and communication performance. Issues also arise from external light sources like the sun and streetlights, complicating the real-time processing of OCC signal detection and analysis.
Novelty of NG standard: This contribution aims to present an Optical Camera Communication (OCC) system that integrates YOLOv8 for the detection and tracking of LEDs on the receiver side.
Commercialization point of view: The system operates in real-time on simple embedded devices and has been tested to show high effectiveness up to 10 meters in low-mobility settings.
DL based OCC to Support High Mobility Vehicle

## Slide 10: Comparison table of IEEE 802.15.7a and NG-OCC
Feature | IEEE 802.15.7a TG | NG Standard
Data rate | Up to 100 Mbps | Up to 200 Mbps
Communication distance | Up to 200 meters | Up to 1 kilometer
Modulation and coding | OFDM, Hybrid, etc. Convolution, Hamming, RS codes | Massive MIMO OFDM, etc. Turbo, Polar, LDPC codes
Use of AI model | AI that is related to image processing | Integration of various and lightweight AI technologies is possible
Joint communication and sensing | Non-support | Joint communications and sensing (LiDAR, RADAR, IMU, GPS, etc.) using AI.
Mobility support | Up to 350 km/h | Up to 350 km/h
MAC protocol | Haft duplex operation Unslotted ALOHA and CSMA/CA | Full duplex operation New MAC protocol based on AI
Communication mode | Unidirectional | Bidirectional
Type of light sources | Ordinary IR/VL/UV Light | IR/VL/UV Tunable Laser
Applications | 2D communications (V2V, IoT, etc.) | 3D communications and Localization (Drone/UAV, etc.)

## Slide 11
Current OCC
The implementation of OCC focuses on DL and RoI for tracking LEDs during data delivery, involving unidirectional communication and heavy computational load.
The channel estimation system lacks consideration, causing the OCC to struggle in adapting to complex channel conditions.
Latency and accuracy in the OCC system has not been considered, leading to a lack of real-time data transmission and causing delays in response and decision-making.
The application of OCC in transportation has faced challenges in accessing RF networks due to its high mobility and isolation from open air, compounded by poor channel quality.
Future OCC
The future OCC will involve the integration of lightweight capabilities of multiple AI algorithms technologies to enhance OCC system.
Future OCC applications need to consider channel characteristics to enhance data quality, especially in underwater communication and complex weather conditions.
The integration of OCC into 5G/6G networks in the future is necessary to reduce latency and enable real-time communication.
In the future implementation, OCC will support high-mobility communication with Edge and Cloud, enabling efficient data storage and improving communication efficiency.
OCC will be capable of providing position determination, joint communication and sensing, vehicle information forwarding, and a hybrid RF/FSO/OCC network.
Conclusions

## Slide 12
IEEE 802.15 IG NG-OCC
Starting from January 2024
Need active contributions from OWC or OCC experts.
IEEE 802.15.7-2028(?)
Conclusions

## Slide 13
Camera specification
Preferred Camera Types for OCC
Shutter type | Rolling shutter (preferred), Global shutter
Resolution | Min: 720 × 540 (single-link) Max: 3840 x 2160 (multi-link)
Frame rate | Min: 30 FPS Preferred: >120 FPS
Spectrum | Mono, color
Light sources | VL, UV, IR

## Slide 14
Device examples:
Web camera: Logitech, Samsung, Microsoft, Intel
Machine vision camera: FLIR, Basler, Allied Vision, Toshiba
DSLR/Mirrorless: Nikon, Canon, FujiFilm, Panasonic, Sony
CCTV: Panasonic, HikVision, Samsung
360 camera: Ricoh, GoPro, DJI
Smartphone: Apple, Samsung, Huawei, Xiaomi, LGE
Gimbal attached camera (support mobility): DJI
LiDAR: Velodyne, Ouster, RoboSense
RADAR: Continental, NanoRadar
LED: LG Display, LG Innotek, Samsung Display
Invited Device Manufacturers for OCC

## Slide 15
R&D Institute, Companies and Universities:
ETRI – Korea
KIEL Research Institute - Korea
Nagoya University - Japan
Keio University – Japan
University of Science and Technology of China – China
Boston University – USA
RPI – USA
Signify – Netherland
Panasonic Lighting – Japan
OSRAM – Germany
Casio – Japan
GE Lighting – USA
EU Universities and Companies (COST)
Invited R&D Institutes, Companies and Universities for OCC Standard

## Slide 16
newfocus COST:
Aalto University(FI), Aristotle University in Thessaloniki(GR), and University of Strathclyde (UK)
Collaborators:
• Cluster 1: Universidade de Aveiro (Portugal), Scuola Superiore Sant’Anna(Italy)
• Cluster 2: KTH(Sweden); Ericsson(Sweden); KU Leuven(Belgium); University of
Edinburgh(UK)
• Cluster 3: Kadir Has University(Turkey); University of Sarajevo & BH Telecom (Bosnia and Herzegovina); Northumbria University(UK); Czech Technical University at Prague(Czech Republic)
• Cluster 4: DLR(Germany); University of Versailles Saint-Quentin(France); Fraunhofer HHI(Germany)
• Cluster 5: Ozyegin University(Turkey); UNS-FTN (Serbia); Inria (France)
• Cluster 6: Roma Tre University(Italy); Universidad de La Laguna(Spain); Universidad Carlos III de Madrid(Spain); Alex Ekwueme Federal University(Nigeria); Centrale Marseille & Institut Fresnel(France)
Invited R&D Institutes, Companies and Universities for OCC Standard

## Slide 17
R&D Institute, Companies and Universities (Paper Optical Camera Communication based on google scholar 2021-2024)
Kookmin University , Yeungnam University , Changwon National University , Pukyong National University, Ulsan National Institute of Science and Technology (UNIST) - South Korea
Ritsumeikan University , Okayama University of Science, Chiba Institute of Technology, Nagoya University - Japan
South China University of Technology, Soochow University, Jilin University, Wuhan University of Technology, The Hong Kong Polytechnic University, Nanjing University of Posts and Telecommunications, Harbin Engineering University – China
Invited R&D Institutes, Companies and Universities for OCC Standard

## Slide 18
R&D Institute, Companies and Universities (Paper Optical Camera Communication based on google scholar 2021-2024)
Xidian University, Sichuan University, Southwest Jiaotong University, Feng Chia University – China.
National Yang Ming Chiao Tung University, National Chiao Tung University, Industrial Technology Research Institute – Taiwan.
Quy Nhon University - Vietnam
Northumbria University, University of Strathclyde, University of Southampton – UK
University of Aveiro (Universidade de Aveiro) – Portugal.
University of Las Palmas de Gran Canaria (ULPGC) – Spain.
Czech Technical University in Prague - Czech Republic.
Eastern Institute of Technology - New Zealand.
Politehnica University of Bucharest – Romania.
Invited R&D Institutes, Companies and Universities for OCC Standard

## Slide 19
R&D Institute, Companies and Universities (Paper Optical Camera Communication based on IEEE (Journal) 2021-2024)
The Chinese University of Hong Kong - China
KUET, Noakhali Science and Technology University - Bangladesh
University of Essex - UK
Nanyang Technological University - Singapore
Michigan State University - USA
i2CAT Foundation - Spain
RMIT University - Australia
IDeTIC-ULPGC – Spanyol
State University of Campinas (UNICAMP) - Brazil
Nagaoka University of Technology – Japan
TU Dortmund University - Germany
Invited R&D Institutes, Companies and Universities for OCC Standard

## Slide 20
R&D Institute, Companies and Universities (Paper Optical Camera Communication based on IEEE (conference) 2021-2024)
National Formosa University - Taiwan
RMIT University – Australia
Universidad Nacional de Colombia – Colombia
Tokyo University of Agriculture and Technology – Japan
Fuzhou University – China
Defence Science and Technology Laboratory - UK
Research Technology SEW-EURODRIVE GmbH & Co.KG - Germany
Perm State National Research University - Russia
Universidade de Aveiro – Portugal
Michigan State University - USA
Tokyo University of Agriculture and Technology - Japan.
Universidad Autónoma de San Luis Potosí – Mexico.
Invited R&D Institutes, Companies and Universities for OCC Standard

## Slide 21
Webcam Manufacturers
Lenovo Group Ltd. - China
Razer Inc. - USA
Dell - USA
Obsbot - China
Elgato – Germany
Ausdom Global – China
Vivitar Corporation - USA
Creative Technology Ltd. – Singapore
Shenzhen Teng Wei Video Technology Co. Ltd. – China
A4Tech Co. Ltd. – Taiwan
KYE Systems Corp. (Genius) – Taiwan
Invited R&D Institutes, Companies and Universities for OCC Standard

## Slide 22
CCTV Manufacturers
Bosch – Germany
Dahua – China
Axis – Sweden
Hanwha Techwin - South Korea
CP Plus – India
Lorex – Canada
Honeywell - USA
Vmukti Solutions – India
Digital Watchdog - USA
Vivotek – Taiwan
Arecont - United States
Invited R&D Institutes, Companies and Universities for OCC Standard

## Slide 23
360 Camera Manufacturers
Nikon – Japan
LG Electronics - South Korea
Samsung - South Korea
Insta360 – China
Eastman Kodak Company - USA
Rylo Inc. - United States
Xiaomi Technology – China
Immervision – Canada
Digital Domain Productions - USA
YI Technology – China
Leica Camera AG – Germany
EZVIZ Inc. – China
Invited R&D Institutes, Companies and Universities for OCC Standard

## Slide 24
Drone companies
DJI - China
Parrot - France
Ehang - China
3D Robotics - United States
Insitu - United States
Aeryon - Canada
Yuneec - China
SenseFly - Switzerland
Lily Robotics - United States
DroneDeploy - United States
Invited R&D Institutes, Companies and Universities for OCC Standard

## Slide 25
Invited university for drone networks and OCC
Osaka University – Japan
Tokyo University of Agriculture and Technology - Japan
Tokyo Institute of Technology – Japan
The University of Western Australia – Australia
National University of Singapore – Singapore
The University of Edinburgh - UK
New Jersey Institute of Technology - United States
King Abdullah University of Science and Technology - Saudi Arabia
University of Waterloo – Canada
Shanghai Jiaotong University - China
Invited R&D Institutes, Companies and Universities for OCC Standard