## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Performance Evaluation of Channel Coding with Interleaver Based on TG6ma Channel Model for Some Classes of Coexistence
Date Submitted: September 11th, 2024
Source: Daisuke Anzai, Sho Asano, Kento Takabayashi, Takumi Kobayashi, Marco Hernadez, Ryuji Kohno
Company: Nagoya Institute of Technology (NIT), Japan
Address: Gokiso-cho, Showa-ku, Nagoya, 466-8555, Japan
Voice: +81-52-735-5389, FAX: +81-52-735-5389, E-Mail: anzai@nitech.ac.jp
Re: In response to call for technical contributions
Abstract: This provides a preliminary investigation of the effect of interleaving on channel coding defined in TG6ma under multiple BAN coexistence situations, and some simulation results are discussed.
Purpose: Material for discussion in P802.15.6a TG corresponding to comments in EC Meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Performance Evaluation of Channel Coding with Interleaver Based on TG6ma Channel Model for Some Classes of Coexistence
Daisuke Anzai, Sho Asano, Takumi Kobayashi, Kento Takabayashi, Marco Hernandez, Ryuji Kohno
Nagoya Institute of Technology (NIT)
Toyo University, YNU, YRP-IAI, CWC Oulu Univeristy

## Slide 3: Importance of QoS control
User priority | Traffic designation | Frame type
0 | Background (BK) | Data
1 | Best effort (BE) | Data
2 | Excellent effort (EE) | Data
3 | Video (VI) | Data
4 | Voice (VO) | Data
5 | Medical data or network control | Data or management
6 | High-priority medical data or network control | Data or management
7 | Emergency or medical implant event report | Data
In WBAN systems, a wearable vital sign sensor node can include various types of sensors with different data rates, the allowable communication error ratio and delay
IEEE 802.15.6 based WBAN may deal with 8 levels of user priority data
Those data have a wide range of quality of service (QoS)
Therefore, optimal error control for input data is an important feature in sensor data transmission procedures

## Slide 4: Error control in current IEEE 802.15.6
IEEE 802.15.6 shall use a (63, 51) BCH code as an error correcting code in narrowband, UWB and HBC PHY
Only user priority 6 data in UWB-PHY may use a hybrid ARQ with a (126, 63) shortened BCH code
However, the error control scheme of the current IEEE 802.15.6 cannot deal with the QoS because of lack of flexibility
In IEEE 802.15.6ma, we indicate a concept of channel coding technique to deal with various types of QoS data as shown in a next figure

## Slide 5: Forward error correcting codes in TG6ma
As an outer code, shortened Reed-Solomon (RS) codes with N=54 (original code length N=63) will be selected to correct burst errors due to interference from other WBANs and the coding rates are changed according to each QoS and channel condition
As an inner code, 15.4ab LDPC (K=324, 648, 972, R=1/2) or BCC will be selected for the coexistence of 15.6ma and 15.4ab
This updated concept table is considered as the first priority
User priority | Inner code | Outer code | HARQ
0 | 15.4ab LDPC or BCC (R=1/2) |  | -
1 | 15.4ab LDPC or BCC (R=1/2) |  | -
2 | 15.4ab LDPC or BCC (R=1/2) |  | -
3 | 15.4ab LDPC or BCC (R=1/2) |  | -
4 | 15.4ab LDPC or BCC (R=1/2) | (54, 46) shortened RS code | -
5 | 15.4ab LDPC or BCC (R=1/2) | (54, 38) shortened RS code | -
6 | 15.4ab LDPC or BCC (R=1/2) | (54, 28) shortened RS code | -
7 | 15.4ab LDPC or BCC (R=1/2) | (54, 14) shortened RS code | -

## Slide 6: Simulation settings

## Slide 7: Effect of interleaving on BER performance
Modulation: BPSK
Interleaver type: Random
Channel: AWGN + burst erasure channel
w/o Interleaving
w/ Interleaving

## Slide 8: Effect of interleaving on BER performance
Modulation: BPSK
Interleaver type: Random
Channel: AWGN + burst erasure channel
Burst erasure: 65 bits, 30%
Burst erasure: 289 bits, 30%

## Slide 9: Effect of interleaving on BER performance
w/o Interleaving
w/ Interleaving
Modulation: BPSK
RS(54, 28) + LDPC(R=1/2)
Channel: AWGN + burst erasure channel

## Slide 10: Burst erasure channel (65 bit, 30%)
w/o Interleaving

## Slide 11: Burst erasure channel (65 bit, 30%)
w/ Interleaving

## Slide 12: References
D. Anzai, I. Balasingham, G. Fischer, J. Wang, “Reliable and High-Speed Implant Ultra-Wideband Communications with Transmit–Receive Diversity,” EAI/Springer Innovations in Communication and Computing, pp. 27-32, March 2020.
Y. Shimizu, D. Anzai, R. C-Santiago, P. A. Floor, I. Balasingham, and J. Wang, “Performance evaluation of an ultra-wideband transmit diversity in a living animal experiment” IEEE Trans. Microw. Theory Tech., vol. 65, no. 7, pp. 2596-2606, July 2017.
D. Anzai, K. Katsu, R. Chavez-Santiago, Q. Wang, D. Plettemeier, J. Wang, and I. Balasingham, “Experimental evaluation of implant UWB-IR transmission with living animal for body area networks,” IEEE Trans. Microw. Theory Tech., vol. 62, no. 1, pp. 183-192, Jan. 2014.
J. Shi, D. Anzai, and J. Wang, “Channel modeling and performance analysis of diversity reception for implant UWB wireless link,” IEICE Trans. Commun., no. E95-B, vol. 10, pp. 3197-3205, Oct. 2012.