## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Channel model proposal for IEEE 802.15.4ad]
Date Submitted: 14 May 2024
Source: Hiroshi Harada (Kyoto University)
Address Yoshidahonmachi. Sakyo, Kyoto, 606-8501, Japan
Voice: +81-75-753-5317 , E-Mail: hiroshi.harada@i.kyoto-u.ac.jp
Re: [Wireless Next Generation, Long Range extension enhancements to 802.15.4-2020]
Abstract: Propose channel models to evaluate proposed systems for IEEE 802.15.4ad. A part of this contribution was supported from the commissioned research (No.05101) by National Institute of Information and Communications Technology (NICT) , Japan.
Purpose: Propose channel models to evaluate proposed systems for IEEE 802.15.4ad.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Channel model proposal for IEEE 802.15.4ad
May 15, 2023
Hiroshi Harada, Ph.D.
May 2024

## Slide 3: Background
Group needs to specify a channel model to evaluate the proposed methods.
The channel model should be internationally standardized.
The channel model should be as simple as possible, if MIMO is not currently used in the group.
Delay spread depends on use case or frequency used.
  The delay spread is 1-2 us in urban micro in sub 1 GHz band.
  The delay spread is 7-10 us in rural area in VHF band
This presentation presents candidate channel models.
May 2024

## Slide 4: Expected use cases of IEEE 802.15.4 SUN
H. Harada, K. Mizutani, J. Fujiwara, K. Mochizuki, K. Obata, and R. Okumura, “IEEE 802.15.4g based Wi-SUN Communication Systems,” IEICE Transactions on Communications, E100-B, No. 07, pp. 1032–1043, Jul. 2017.
May 2024

## Slide 5: Channel Model in Urban Area
If the environment is Typical urban, it is important to consider maximum delayed wave with around 5 us at sub 1 GHz
One possible channel model is COST207 GSM Typical urban model
There is a MATLAB code if you need
COST207, “Digital land mobile communications,” Mar. 1989．
May 2024

## Slide 6: Channel Model in Rural Area
Based on Doc. 15-24-287, the delay spread could be 10us if VHF band is used. In this case, a possible model for such a model is IEEE 802.22 Type A.
Used in IEEE 802.22 community
May 2024

## Slide 7: 3GPP-based channel model
TR38.901 is a candidate
Supports carrier frequencies above 500 MHz
  Not compatible with VHF band, but for VHF band, use 500 MHz if the group agreed
TDL and CDL are available, but TDL in Section 7.7.2 is preferred since it does not perform MIMO and is mainly sub1GHz
The RMS delay spread values of both CDL and TDL models are normalized and they can be scaled in delay so that a desired RMS delay spread can be achieved. The scaled delays can be obtained according to the equation in Section 7.7.3 (TR38.901)
  The delay wave may not always be in good agreement with measured values in reality
There is a MATLAB code if you need