## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: Theoretical Analysis of System Performance in a Multi-BAN Coexistence Environment (Class 1)
Date Submitted: 14 November 2024
Source: Kento Takabayashi1, Ryuji Kohno2,3
Company: (1) Toyo University (2)Yokohama National University (3) YRP International Alliance Institute
Address: (1) 2100 Kujirai, Kawagoe, Saitama, Japan 351-8585, (3)79-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan,
(4) YRP1 Blg., 3-4 Hikarinooka, Yokosuka-City, Kanagawa, 239-0847 Japan
Voice:[(1) +81-866-94-2104 , (3) +81-90-5408-0611] E-Mail:[takabayashi.kento.xp@gmail.com, kohno@ynu.ac.jp, kohno@yrp-iai.jp]
Re: In response to call for technical contributions
Abstract:
Purpose: Material for discussion in P802.15.6ma TG corresponding to comments in EC Meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Theoretical Analysis of System Performance in a Multi-BAN Coexistence Environment (Class 1)
November 2024,
Hybrid Session,
Hyatt Regency - Vancouver, BC
Kento Takabayashi (1), Ryuji Kohno(2,3)
(1) Toyo University (2)Yokohama National University (3) YRP International Alliance Institute

## Slide 3: Coexistence environment level
  Coexistence environment class is divided into 8 categories
  This presentation introduces a simple PER performance analysis in class 1
    These results can be useful for cross-layer evaluation of physical and MAC layers in multiple WBANs environment
Coexistence environment class | Environment
0 | 6ma BAN only
1 [1a] | Multiple 6ma BANs 1a
2 [1b] | Multiple 15.6 & 6ma BANs
3 | Multiple 6ma BANs & non-UWB systems (Wi-Fi & Unlicensed 3GPP)
4 [2a] | Multiple 6ma BANs & 802.15 UWB systems
5 [2b] | Multiple 6ma BANs, non-802.15 UWB systems (ETSI UWB systems)
6 [2c] | Multiple 6ma BANs & 802.15 UWB & non-802.15 UWB systems (ETSI UWB)
7 | Multiple 6ma BANs & non-UWB systems (Wi-Fi & Unlicensed 3GPP) & 802.15 UWB & non-802.15 UWB systems (ETSI UWB)

## Slide 4: Assumed environment
Several asynchronous (not managed) WBANs interfere a managed WBANs group
The entire transmitted packet is affected by interference
Notes: This figure shows the assumed environment

## Slide 5: Mathematical expression
(Packet error ratio, : PSDU length (bit))
(Bit error probability, BPSK)
  : Received power, : Noise spectral density, B: Bandwidth, : Number of interferences, : Each received interference power
(dBm)
  : Transmission spectral density, : Path loss in CM3, : sensor to hub distance (mm)
= (dBm)
  : Path loss in HBAN to HBAN LOS case, : Hub to hub distance (mm)

## Slide 6: Evaluation
Channel model | AWGN
Path loss model (objective WBAN) | IEEE model CM3 (S4 and S5 in 15.6ma)
Path loss model (HBAN to HBAN) | S6.2 in 15.6ma channel model
Bandwidth () | 499.2 MHz
Modulation | BPSK
Transmission spectral density, | -41.3 dBm/MHz
PSDU length () | 1296 bits
Distance from hub to sensor in WBAN, | 40 cm
Noise spectral density, | -203.86 dBm/Hz
Number of interference WBAN, | 1~5
Channel model | AWGN
Path loss model (objective WBAN) | IEEE model CM3 (S4 and S5 in 15.6ma)
Path loss model (HBAN to HBAN) | S6.2 in 15.6ma channel model
 | 499.2 MHz
Modulation | BPSK
 | -41.3 dBm/MHz
 | 1296 bits
 | 40 cm
 | -203.86 dBm/Hz
 | 1~5
For simple analysis, error correcting and retransmission is not considered
Packet collision within a managed WBAN and from other managed WBANs is also not considered

## Slide 7: Results
Example of SINR of managed WBAN vs distance between managed WBAN and interfering WBAN ,
The number of not managed WBAN,
Notes: These lines mean the number of unmanaged WBANs
In the case of LDPC and ARQ, PER improved as 𝑟_𝑚𝑎𝑥 increased, and no error floor occurred

## Slide 8: Results
Example of PER of managed WBAN vs distance between managed WBAN and interfering WBAN ,
The number of not managed WBAN,

## Slide 9: Conclusion
Sufficient SINR and PER performance was obtained without error correction when the number of not managed WBAN was small or distance from interfering WBAN was far enough
  For example, when , PER can be achieved for if is more than 2.0 m away
  In normal use cases, interference from a distance of 3.0 m or more does not significantly affect a managed WBAN
  Interference from a distance of 5.0 m or more can be almost ignored
  When interference from very close ranges increases, error controlling and interference mitigation are required

## Slide 10
Thank you for your attention ! ! !