## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSNs)
Submission Title: Q-Learning-based MAC layer resource allocation and optimization for CSMA/CA-based OWC MAC
Date Submitted: Sep 11, 2024
Source: Muhammad Adnan, Nguyen Ngoc Huy, Yeong Min Jang (Kookmin University)
Address: Room #603 Mirae Building, Kookmin University, 77 Jeongneung-Ro, Seongbuk-Gu, Seoul, 136702, Republic of Korea
Voice: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract: Present the Q-Learning-based MAC layer resource allocation and optimization for CSMA/CA-based OWC MAC
Purpose: Presentation for contribution on IG NG-OWC
Notice: This document has been prepared to assist the IG NG-OWC. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by IG NG-OWC.

## Slide 2
Q-Learning-based MAC layer resource allocation and optimization for CSMA/CA-based OWC MAC Sept 11, 2024

## Slide 3: Contents
Background
    OWC
    Medium Access Control (MAC) Protocols
    CSMA/CA
    Resource allocation and optimization for CSMA/CA-based OWC MAC
Q-Learning-based MAC layer resource allocation and optimization for CSMA/CA-based OWC MAC
Conclusion

## Slide 4: Background: OWC, MAC, CSMA/CA
OWC:
OWC refers to optical wireless communication, which is a technology that utilizes light for transmitting data wirelessly.
Unlike traditional radio frequency (RF) communication, OWC relies on line-of-sight transmission for data transfer.
Key components of OWC include a transmitter, typically an LED or laser that emits light carrying the data, and a receiver, usually a photodetector that converts received light into electrical signals.
MAC Protocols
MAC protocols serve a crucial role in controlling and organizing access to wireless networks.
These protocols are designed to prevent simultaneous transmissions from multiple devices, which could result in data collisions and loss.
By allowing only one device to transmit at a time, MAC protocols effectively minimize interference and enhance overall network efficiency [1].
CSMA/CA:
This protocol involves devices monitoring the channel, utilizing random waiting periods, and employing confirmation messages to regulate data transmission and minimize interference.
Working Mechanism of CSMA/CA:
  Carrier Sense:
  Listening to the Channel:
  Prior to data transmission, a device monitors the communication channel to determine if it's available or in use.
  When the channel is free, the device can proceed to the next phase and initiate transmission.
  If the channel is occupied, the device delays and rechecks later.

## Slide 5: Background: OWC, MAC, CSMA/CA
Working Mechanism of CSMA/CA:
  2. Random Backoff:
  In case of a busy channel, the device waits for an unpredictable duration, called the backoff interval, before attempting again.
  This strategy helps prevent collisions when multiple devices are queued for transmission.
  The backoff duration is typically calculated using a random value within a Contention Window (CW), which expands exponentially after successive collisions (referred to as binary exponential backoff).
  3. Transmission:
  Following the random backoff, the device reassesses the channel.
  If the channel remains unoccupied, the device sends its data.
  Should the channel become busy during the delay, the device waits for another chance, repeating the monitoring and delay process.
  4. Acknowledgment (ACK):
  After sending data, the transmitter awaits a confirmation (ACK) from the recipient.
  This ACK verifies successful data reception.
  If the transmitter doesn't receive an ACK within a specified timeframe, it assumes transmission failure (due to collision or interference) and restarts the process with a new random backoff time.

## Slide 6: Background: OWC, MAC, CSMA/CA
Resource allocation and optimization for CSMA/CA-based OWC MAC
In CSMA/CA, collision avoidance relies on adjusting backoff times.
Deep Reinforcement Learning (DRL) can adaptively modify these times based on the network's current state, leading to fewer collisions and increased throughput.
Similarly, the Q-learning agent is designed to optimize Contention Window (CW) selection, reducing collisions and increasing packet transmission success, thereby improving overall network efficiency.
The DQN aims to enhance channel access decisions by minimizing collision probability and maximizing successful transmissions.
The DQN algorithm is proposed for CSMA/CA-based OWC-MAC to optimize network performance by balancing various Quality of Service (QoS) metrics, including maximizing throughput, minimizing latency, and maximizing Packet Delivery Ratio (PDR).

## Slide 7: Q-Learning-based MAC layer resource allocation and optimization for CSMA/CA-based OWC MAC
The design of the DQN environment for OWC-MAC, align MAC layer elements with the Q-learning model and configure the connections between transmitter, receiver, and coordinator to enable dynamic decision-making based on DQN predictions.
The process involves the following steps:
Step 1: Design the DQN Environment
Initially, we develop the CSMA/CA mechanism for OWC-MAC and frame the channel access mechanism (MAC layer) as a reinforcement learning (RL) challenge solveable through DQN.
  1. State: The current system status needs to be represented, potentially including:
    Channel Status (occupied or free)
    Packet Queue Length (quantity of packets awaiting transmission)
    Contention Window Dimensions (for adaptive backoff management)
    Collision count (for identifying and preventing collisions)
  2. Actions: The DQN agent would choose from several options:
    Send: Try to transmit a packet.
    Defer / Wait: Refrain from sending and wait for an idle channel.
    Modify Contention Window: Adaptively alter the contention window size (optional).
  3. Rewards: This indicates the effectiveness of each action in a given state:
    +1: Packet transmitted successfully (without collision).
    0: Postpone or delay.
    -1: Packet collision or transmission failure.
  4. Next State: The system moves to a new state after an action is taken, which the DQN will utilize for continuous learning and improvement.

## Slide 8: Continue...
Step-2: DQN Agent
The DQN agent will engage with the CSMA/CA environment to develop an optimal strategy through iterative learning.
Step-3: Q-Learning-based CSMA/CA mechanism for OWC-MAC
We can implement a Q-Learning-based CSMA/CA mechanism utilizing the DQN agent's decision-making process for OWC-MAC, replacing the conventional static channel access behavior of CSMA/CA.
The DQN can determine whether to initiate transmission, delay, or modify the backoff window.
The DQN agent collaborates with the transmitter, receiver, and coordinator to acquire the most effective approach for reducing collisions and enhancing transmission success rates.
Transmitter:
The transmitter's role is to dispatch packets via the optical communication link.
Traditionally, it employs the CSMA/CA protocol to evaluate the channel and determine transmission timing.
In this case, the DQN agent will assume control and decide:
  When to send data.
  When to wait.
Receiver:
The receiver's duty is to accept transmitted packets and relay feedback to the coordinator and transmitter regarding the success or failure of the transmission.
Coordinator:
The coordinator functions as the central entity, operating the DQN agent and managing communication between transmitters and receivers.
It obtains state information from the transmitter, inputs it into the DQN, and returns the selected action.

## Slide 9
Conclusion
The Q-Learning-based OWC-MAC approach is designed to efficiently allocate and optimize resources by dynamically adjusting the Contention Window (CW) size according to network conditions.
This adaptation aims to reduce collisions and facilitate rapid channel access, ultimately enhancing overall network performance.
By implementing Q-Learning-based OWC-MAC, various Quality of Service (QoS) metrics can be balanced, such as maximizing throughput, minimizing latency, and increasing Packet Delivery Ratio (PDR), to optimize network efficiency.
In this system, the agent monitors the communication environment's state, makes decisions based on its observations, and learns from the results of its actions.
This process contributes to the optimization of the MAC layer, reduction of collisions, and improvement of overall throughput in OWC-MAC systems.

## Slide 10
References
[1] Esfahani, Mohammad Salah, et al. "Visible light communication networks MAC layer solutions: open issues and trends." Photonic Network Communications 43.2 (2022): 116-134.