## Slide 1
IG NG-OWC
Submission Title: Enhancing Efficiency with AI-based Multi Object Tracking Integration for NG-OWC in Building Management System
Date Submitted: September 11, 2024
Source: Khairi Hindriyandhito, Nguyen Ngoc Huy, Yeong Min Jang, Kookmin University
Address: Room #603 Mirae Building, Kookmin University, 77 Jeongneung-Ro, Seongbuk-Gu, Seoul, 136702, Republic of Korea
Voice: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract: Present the utilization of AI-based multi object tracking in NG-OWC in a building management system
Purpose: Presentation for contribution on IG NG-OWC
Notice: This document has been prepared to assist the IG NG-OWC. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by IG NG-OWC.

## Slide 2
Enhancing Efficiency with AI-based Multi Object Tracking Integration for NG-OWC in Building Management System September 11, 2024

## Slide 3: Contents
Background
NG-OWC for Building Management System
NG-OWC with AI-based Multi Object Tracking
Conclusion

## Slide 4: Background
The Building Management System (BMS) is essential in current urban environments, especially for office employees who spend extensive periods indoors. It includes multiple systems essential for building functionality, such as HVAC, lighting, security, and Indoor Air Quality (IAQ).
A study indicated that building operations make up 30% of energy usage in the European Union, mostly due to HVAC systems. Consequently, an innovative approach for minimizing energy usage through the implementation of an efficient system is essential.
Optical Camera Communication (OCC) is an advanced technology that facilitates data communication via light signals detected by camera sensors. Recent advances have considerably enhanced the data rate, dependability, and integration capabilities of OCC, rendering it a viable communication protocol for BMS.
By utilizing the current CCTV infrastructure, OCC may convert surveillance cameras into multifunctional devices, concurrently facilitating security monitoring and data transmission.

## Slide 5: NG-OWC for Building Management System​
The input image will be processed using multi-object tracking to classify LEDs and humans.
The LED classification would then be utilized to acquire OCC data and save it within the BMS system.
The acquired human classification will be utilized for human occupancy detection, which will subsequently be employed in the BMS system.

## Slide 6: NG-OWC with AI-based Multi Object Tracking
The sensors would be connected to an OCC transmitter (LED array). The CCTV would then capture it collectively with the surrounding image.
The image would then be analyzed using AI-based multi-object tracking to recognize humans and read OCC data from the observed LED.
The data collected would then be utilized to forecast temperature, humidity, and CO2 levels based on additional human occupancy detection, as they have significant correlations.
The BMS system would then regulate the HVAC depending on the forecasted data.

## Slide 7: Conclusion
The implementation of Optical Camera Communication (OCC) in Building Management Systems (BMS) will substantially enhance efficiency by leveraging current CCTV systems.
The incorporation of AI-driven multi-object tracking into BMS enables the utilization of CCTV imagery for human occupancy detection and OCC data communication via LED classification.
The proposed approach would minimize the necessary communication components and simultaneously improve HVAC management using human occupancy detection, therefore enhancing energy efficiency in BMS

## Slide 8
Reference
Vandenbogaerde, L., Verbeke, S., & Audenaert, A. (2023). Optimizing building energy consumption in office buildings: A review of building automation and control systems and factors influencing energy savings. Journal of Building Engineering, 107233.
Ahmed, M. F., Hasan, M. K., Chowdhury, M. Z., Hoan, N. C., & Jang, Y. M. (2021). Continuous status monitoring of industrial valve using OCC-enabled wireless sensor network. IEEE Transactions on Instrumentation and Measurement, 71, 1-10.
Van Hoa, N., Nguyen, H., Nguyen, C. H., & Jang, Y. M. (2020, October). Occ technology-based developing iot network. In 2020 International Conference on Information and Communication Technology Convergence (ICTC) (pp. 670-673). IEEE.