## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Non-interleaved MMS comment resolution
Date Submitted: September 12, 2024
Source: Riku Pirhonen (NXP)
Abstract: Current UWB Multi-millisecond (MMS) operation supports interleaved transmission of initiator and responder ranging packets. This proposals introduces minimal changes to allow also non-interleaved operation to support traditional SS-TWR and DS-TWR.
Purpose: Propose non-interleaved option for MMS by introducing ExtendedRpDuration.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
        DCN 15-24-0532-00-04ab

## Slide 2: This presentation
Graphical presentation of
  Non-Interleaved SS- and DS-TWR for UWB Driven Mode
  Non-Interleaved SS- and DS-TWR for NBA-MMS
  Non-Interleaved SS- and DS-TWR for UWB Driven Mode with SP0 control packet
Recap of the key comments presented in DCN 15-24-0409-01-04ab
  ExtendedRpDuration in Draft 1 “Management MAC Configuration Field”
  macMmsExtendedRpDuration to MAC PIB attributes
  Stylized proposal how to edit the figures in 10.38.5
  Some minor text edits in 10.38.5

## Slide 3: Non-Interleaved SS- and DS-TWR for UWB Driven Mode
RpDuration
2 x RpDuration
3 x RpDuration
Report content:
Responder Treply1
Initiator Treply2
Reporting phase
Initiator
Responder
Note that RpDuration can be longer than, e.g., exact 5 ms
ExtendedRpDuration defines number of MMS packets
1 ms slot
UWB SYNC+SFD
UWB RSF/RIF

## Slide 4: Non-Interleaved SS- and DS-TWR for NBA-MMS
RpDuration
2 x RpDuration
3 x RpDuration
Report content:
Responder Treply1
Initiator Treply2
Reporting phase
Initiator
Responder
1 ms slot
UWB SYNC+SFD
UWB RSF/RIF
NB packet
Initiator NB slots length is defined by macMmsRcpPollNSlots
Responder NB slot length is defined be macMmsRcpRespNSlots
ExtendedRpDuration defines number of MMS packets

## Slide 5: Non-Interleaved SS- and DS-TWR for UWB Driven Mode with SP0 control packet
Initiator
Responder
ExtendedRpDuration defines number of MMS packets
1 ms slot
UWB SYNC+SFD
UWB RSF/RIF
RpDuration
UWB SP0 CNTRL
2 x RpDuration
3 x RpDuration
Reporting phase

## Slide 6: 10.38.9.3.12 The Management MAC Configuration field
44-45
46-47
ExtendedRpDuration
Add ExtendedRpDuration bits (955)

## Slide 7: 10.38.9.3.12 The Management MAC Configuration field
Page 86, line 33 The ExtendedRpDuration field enables non-interleaved MMS packets by extending the ranging phase to double or triple of the RpDuration. By default, bits are 00, which means interleaved initiator and responder transmissions. Bit values 01 mean double RpDuration and non-interleaved transmission by initiator and responder as shown in Figure XX [in chapter 10.38.5], and bits set to 10 mean triple RpDuration and non-interleaved transmissions by initiator – responder – initiator, as shown in figure XX [in chapter 10.38.5]. Bit combination 11 is reserved.
Add description below the Figure (956)

## Slide 8: 10.38.10.1 MMS specific MAC PIB attributes
macMmsExtendedRpDuration | Integer | 0 – 3 | 0 = Interleaved ranging phase 1 = Non-interleaved ranging phase of double RpDuration 2 = Non-interleaved ranging phase of triple RpDuration 3 = reserved | 0
Add MAC PIB attribute
Page 125, line 1, table 20 (959)

## Slide 9: 10.38.5 UWB MMS ranging phase
Add Figures to illustrate non-interleaved response possible with ExtendedRpDuration
Figure XX – Example non-interleaved UWB MMS ranging phase with 2xRpDuration (macMmsExtendedRpDuration = 1)
Figure XX – Example non-interleaved UWB MMS ranging phase with 3xRpDuration (macMmsExtendedRpDuration = 2)
Example with ExtendedRpDuration value 1 (2xRpDuration) and 2 (3xRpDuration) (97)

## Slide 10: Other text edits throughout the document
10.38.5 UWB MMS ranging phase (952) p 69, line 7. In non-interleaved mode responder shall start transmission of MMS packet after one RpDuration from the start of the ranging phase, and when DS-TWR is desired, initiator may transmit a second MMS packet after two RpDurations from the start of the ranging phase.
10.38.5 UWB MMS ranging phase (953) p 69, line 12. After macMmsRpDuration, or in case of non-interleaved mode after double or triple macMmsRpDuration as defined by the ExtendedRpDuration, and transmission and reception of all the fragments…

## Slide 11: Summary of comments 952, 953, 97, 954, 955, 956, 959
Riku Pirhonen | 952 | 69 | 10.38.5 | 7 | In order to support traditional SS-TWR and DS-TWR, non-interleaved mode is proposed. It would delay sending responder MMS packet by RpDuration and, for DS-TWR, initiator can send another MMS packet after two RpDurations. | In non-interleaved mode responder shall start transmission of MMS packet after one RpDuration from the start of the ranging phase, and when DS-TWR is desired, initiator may transmit a second MMS packet after two RpDurations from the start of the ranging phase.
Riku Pirhonen | 953 | 69 | 10.38.5 | 12 | Add behavior in case of the proposed non-interleaved mode. | After macMmsRpDuration, or in case of non-interleaved mode after double or triple macMmsRpDuration as defined by the ExtendedRpDuration, and transmission and reception of all the fragments…
Frank Leong | 97 | 69 | 10.38.5 | 15 | The example only represents interleaved MMS operation. A non-interleaved example should be added. | Add two similar figures, one showing non-interleaved SS-TWR MMS operation (2*RpDuration), and another showing non-interleaved DS-TWR MMS operation (3*RpDuration).
Riku Pirhonen | 954 | 69 | 10.38.5 | 16 | Add picture of the proposed non-interleaved mode | Add picture that shows non-interleaved mode with double and triple RpDuration.
Riku Pirhonen | 955 | 86 | 10.38.9.3.12 | 1 | Add ExtendedRpDuration field to the Managemetn MAC Configuration field figure | Add ExtendedRpDuration field between RpDuration and Reserved, and use bits 44 and 45 for this
Riku Pirhonen | 956 | 86 | 10.38.9.3.12 | 33 | Add description for ExtendedRpDuration field | The ExtendedRpDuration field enables non-interleaved MMS packets by extending the ranging phase to double or triple of the RpDuration. By default, bits are 00, which means interleaved initiator and responder transmissions. Bit values 01 meand double RpDuration and non-interleaved transmission by initiator and responder as shown in Figure XX [in chapter 10.38.5], and bits set to 10 mean triple RpDuration and non-interleaved transmissions by initiator – responder – initiator, as shown in figure XX [in chapter 10.38.5]. Bit combination 11 is reserved.
Riku Pirhonen | 959 | 125 | 10.38.10.1 | 1 | Add MAC PIB attribute macMmsExtendedRpDuration to Table 20 on the row after MacMmsRpDuration | macMmsExtendedRpDuration, Integer, 0 - 3, 0 = Interleaved ranging phase, 1 = Non-interleaved ranging phase of double RpDuration, 2 = Non-interleaved ranging phase of triple RpDuration, 3 = reserved, Default 0

## Slide 12: DS-TWR for MMS – reference from IEEE802.15.4