## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Items that should be evaluated by the proposers of the 802.15.4ad PHY]
Date Submitted: 12 November 2024
Source: Hiroshi Harada (Kyoto University)
Address Yoshidahonmachi. Sakyo, Kyoto, 606-8501, Japan
Voice: +81-75-753-5317 , E-Mail: hiroshi.harada@i.kyoto-u.ac.jp
Re: [Wireless Next Generation, Long Range extension enhancements to 802.15.4-2020]
Abstract: Clarify items that should be evaluated by the proposer of the 802.15.4ad PHY. A part of this contribution supported from the commissioned research (No. JPJ012368C05101) by National Institute of Information and Communications Technology (NICT) , Japan is included.
Purpose: Clarify items that should be evaluated by the proposer of the 802.15.4ad PHY.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Items that should be evaluated by the proposers of the 802.15.4ad PHY
Nov. 13, 2024
Hiroshi Harada, Ph.D.

## Slide 3: Background
In the 802.15.4ad TG, the propagation channel and interference model for computer simulations have been discussed and summarized, but the evaluation items and simulation parameters have not been clarified.
This contribution document clarifies parameters used for the computer simulations and items that should be evaluated by computer simulation by the proposer of the 802.15.4ad PHY

## Slide 4: Packet format and evaluation items
When proposing their own PHY, the proposers need to propose the packet format clearly.
The proposer shall show the packet synchronization error rate (SER) and packet error rate (PER) in an AWGN/multipath fading environments and interference environment defined by the technical guidance document for the proposed system using computer simulation.
When performing computer simulations, the packet length should be 250 bytes for transmission rates faster than the current 802.15.4-2020 SUN-defined transmission rate, and 64 and 20 bytes for slower transmission rates than 50 kbit/s.
Following on the previous discussion on 802.15.4 SUN standardization group, the required PER should be 1% when transmitting 64 and 20 bytes for slower transmission rates than 50 kbit/s and 10% when transmitting 250 bytes for the rest of the transmission rates.

## Slide 5: Doppler Frequency
It is desirable to determine one Doppler frequency for the frequency of 500 MHz or more and below 500 MHz, respectively.
The author proposes the 200MHz band as a representative of less than 500MHz, and the 900MHz band as a representative of 500MHz or more.
The group is defining the speed of the radio at 3km/h in the technical guidance document.
Using the above parameters, the author proposes that the Doppler frequency should be 2.5 Hz for 500 MHz or more, and 0.6 Hz for less than 500 MHz.