## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Partial proposal on adding SUN FSK to two Japanese VHF bands]
Date Submitted: [6th Jan. 2025]
Source: [Shugo Kajita1, Shoichi Kitazawa2, Tetsushi Ikegami3, Susumu Ishihara4, Arata Kato1, Takashi Matsuda5, Ryu Miura5, Masakatsu Ogawa6, Mineo Takai7, Masanori Uno8 ]
Company [1Space-Time Engineering Japan, Inc., 2Muroran IT, 3Meiji University, 4Shizuoka University, 5National Institute of Information and Communications Technology, 6Sophia University, 7Space-Time Engineering, LLC., 8e-trees.Japan Inc. ]
Address []
Voice:[], FAX: [], E-Mail:[skajita@spacetime-eng.com, kitazawa@muroran-it.ac.jp, ikegami@meiji.ac.jp, ishihara.susumu@shizuoka.ac.jp, akato@spacetime-eng.com, matsuda@nict.go.jp, ryu@nict.go.jp, m-ogawa@sophia.ac.jp, mineo@spacetime-eng.com, uno@e-trees.jp ]
Re: [Response to TG 802.15.4ad Call for Proposals (IEEE P802.15-24-0488-01-04ad)]
Abstract: [This document includes a partial proposal on adding SUN FSK to two Japanese VHF bands.]
Purpose: [Partial proposal on adding SUN FSK to two Japanese VHF bands]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Background
Japanese VHF-High Band
  The Ministry of Internal Affairs and Communications (MIC) is in the process of initial round of rule-making to introduce Narrowband IoT Communication Systems in the Japanese VHF-High band (170 – 177.5 and 217.5 – 222 MHz). One of their primary use cases is public safety applications including disaster response and recovery operations.
  SUN FSK and SUN OFDM already defined in other frequency bands are being considered as the foundation for the initial rules. However, it is anticipated that standards tailored specifically for the VHF-High Band will be developed before the second round of rule-making begins.
Japanese Unmanned Mobile Image Transmission System (UMITS) Band
  The MIC is also exploring the possibility of implementing narrowband channelization in the UMITS band (169.05–169.3575 MHz and 169.8075–170 MHz) to improve spectrum utilization for command and control (C2) links used in unmanned aerial vehicle (UAV) operations.
  Currently, no specific channel spacing or channel plan exists for narrowband channels in the rules governing this licensed band. However, a standardized channel plan with defined channel spacing is being considered to facilitate better spectrum management.
S. Kajita (STE Japan, Inc.), S. Kitazawa (Muroran IT)

## Slide 3: Purpose and Scope of this proposal
This partial proposal aims to add a set of operating modes to the SUN PHY for the Japanese VHF-High Band and UMITS Band, aligning with the rules currently being considered or investigated.
This proposal focuses exclusively on SUN FSK for the following reasons:
  The proposed operating modes should be compatible with off-the-shelf IEEE 802.15.4 radio modules to reduce device manufacturing time and costs.
  Off-the-shelf IEEE 802.15.4 radio modules designed for Wireless M-Bus (N mode) in the 169 MHz (VHF) band are available, offering some programmability in operating frequencies, modulation, and channel parameters.
  Adopting a constant envelope modulation scheme like FSK is both energy-efficient and cost-effective for high-power transmission radios, as it significantly reduces the performance requirements for power amplifiers compared to non-constant envelope modulation schemes.
This proposal is partial and can be merged with other proposals for the same frequency bands, if applicable.
S. Kajita (STE Japan, Inc.), S. Kitazawa (Muroran IT)

## Slide 4: Proposed Changes to the Existing SUN FSK
This proposal aims to preserve the existing SUN FSK standard with minimal modifications, except for the following changes:
  Support for Higher Data Rates: The symbol period used for MAC and PHY timing parameters is adjusted to 20 µs, replacing the symbol period of operating mode #1 currently specified in the standard.
  Energy Detection (ED) for Coexistence: To enable coexistence among different channel bandwidth operations, narrower channel operations may perform ED over a bandwidth wider than their operational bandwidth. The specific bandwidth for ED, as well as the necessity of performing ED, is determined by the regulatory requirements for the corresponding band.
S. Kajita (STE Japan, Inc.), S. Kitazawa (Muroran IT)

## Slide 5: Proposed Modulation and Channel Parameters for the VHF-High Band
Frequency band (MHz) | Parameter | Operating mode |  |  |  |  |  | 
 |  | #1 | #2 | #3 | #5 | #7 | #9 | #11
170-177.5, 217.5-222 | Data rate (kb/s) | 5 | 10 | 20 | 40 | 80 | 160 | 320
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 2-FSK | 2-FSK | 2-FSK | 2-FSK
 | Modulation index | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
 | Channel spacing (kHz) | 12.5 | 12.5 | 25 | 50 | 100 | 200 | 400
 |  |  |  | #4 | #6 | #8 | #10 | #12
 | Data rate (kb/s) |  |  | 28 | 55 | 110 | 220 | 440
 | Modulation |  |  | 4-FSK | 4-FSK | 4-FSK | 4-FSK | 4-FSK
 | Modulation index |  |  | 0.33 | 0.33 | 0.33 | 0.33 | 0.33
 | Channel spacing (kHz) |  |  | 25 | 50 | 100 | 200 | 400
S. Kajita (STE Japan, Inc.), S. Kitazawa (Muroran IT)

## Slide 6: Proposed Modulation and Channel Parameters for the UMITS Band
Frequency band (MHz) | Parameter | Operation mode |  |  |  |  | 
 |  | #1 | #3 | #5 | #7 | #9 | #11
169.05 – 169.3575, 169.8075 – 170 | Data rate (kb/s) | 5 | 10 | 20 | 40 | 80 | 120
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 2-FSK | 2-FSK | 2-FSK
 | Modulation index | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
 | Channel spacing (kHz) | 12.5 | 25 | 50 | 100 | 200 | 300
 |  | #2 | #4 | #6 | #8 | #10 | #12
 | Data rate (kb/s) | 8 | 16 | 32 | 64 | 128 | 192
 | Modulation | 4-FSK | 4-FSK | 4-FSK | 4-FSK | 4-FSK | 4-FSK
 | Modulation index | 0.33 | 0.33 | 0.33 | 0.33 | 0.33 | 0.33
 | Channel spacing (kHz) | 12.5 | 25 | 50 | 100 | 200 | 300
S. Kajita (STE Japan, Inc.), S. Kitazawa (Muroran IT)