## Slide 1
Uncompressed 4K video transmission at 300GHz
Transmitter
Receiver
300 GHz signal
Baseband signal
Eye pattern
4K video signals with the HDMI format from a PC were converted to SDI-formatted signals.
A 300 GHz carrier signal was modulated with the amplitude shift keying (ASK) signal of the SDI using a subharmonic mixer (SHM).
300 GHz-band wireless signals were transmitted over 20 cm.
The transmission distance of roughly 6 m was confirmed for the maximum.
The received 4K video signal was sent to a 4K monitor.
Since the 4K video signal was uncompressed, it was received with no latency.
Overview of the system
The center frequency and bandwidth of the transmitted signal were 300 GHz and 12 GHz, respectively.
The bitrate of the SDI signal was 5.9 Gbps, and the bandwidth of the baseband signal was 5.9 GHz.
The eye pattern of the received signal was clearly opened.
Specifications
10 GHz
5 GHz
Transmitter
Receiver
6m
DISCLAIMER
The use of any particular/specific brands of components, equipment, or instruments as a part of the demonstration and presentation does not constitute an endorsement of those brands by IEEE, IEEE SA, or the IEEE LMSC.