## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Initial 802.15.4ad Proposal]
Date Submitted: [12 January, 2025]
Source: [Joerg ROBERT] Company [FAU Erlangen-Nürnberg/Fraunhofer IIS]
Address [Am Wolfsmantel 33, Erlangen, 91058, Germany]
E-Mail:[joerg.robert@ieee.org]
Abstract: []
Purpose: [Presentation in TG15.4ad]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Goals of the Proposal
Make IEEE 802.15.4 future proof for the next years
Maximize the spectral efficiency while keeping an eye on the complexity
Focus on the low-hanging fruits
Avoid complex and fancy stuff
Only allow useful combinations of parameters
Proposals are indicated by underlined page title

## Slide 3: Keep in Mind the dB Scaling
3dB improvement means halving the received signal energy by factor 2
 Doubling the battery lifetime under optimal conditions
10dB improvement means reducing the received signal energy by factor 10
Increasing the battery lifetime by a factor of 10 under optimal conditions
And... reducing the channel usage time and the robustness against interference

## Slide 4: Contents
SUN O-QPSK Proposal
SUN FSK Proposal
SUN OFDM Proposal
SUN LR-OFDM Proposal

## Slide 5: SUN O-QPSK

## Slide 6: It this Useful?

## Slide 7: Analysis of SUN O-QPSK
The SUN O-QPSK mode uses a spreading modulation
A low data-rate is blown up to a significantly higher bandwidth using Direct Sequence Spread Spectrum (DSSS) methods
BUT:
The license-exempt spectrum is a very scarce resource and we should really spend it wisely
DSSS is a linear method, hence not providing any actual coding gain that always requires non-linear decoding (e.g. Viterbi)
All devices use the same DSSS sequence, limiting the capacity
FSK/OFDM modes offer a significantly better alternative

## Slide 8: Proposal for SUN O-QPSK
Remove all sub-GHz frequencies from SUN O-QPSK
Keep O-QPSK for 2.4 GHz as it offers some benefits with respect to crystal frequency tolerances
Goal: Avoid the introduction of new services as O-QPSK will block spectrum today that we will require for new applications tomorrow

## Slide 9: SUN FSK

## Slide 10: Analysis of SUN FSK
The FSK modes are currently the currently most commonly used SUN modes
Potential areas of improvement
  Number of modes
  Modulation
  Synchronization / Preamble
  Forward Error Correction

## Slide 11: Proposal: Data Whitening
Make data whitening mandatory
Data whitening is practically always useful
The complexity increase is negligible
Reducing the number of potential modes reduces the testing complexity

## Slide 12: Modulation
Currently supported modulates schemes are
  Classical FSK (modulation index 1.0)
  Minimum Shift Keying (MSK) (FSK with modulation index 0.5)
  4-GFSK
Spectral shaping is not defined
Some modes may lack significant performance penalties (details on next slides)
Potentially higher bandwidth than actually required

## Slide 13: General MSK Issue
2-FSK with modulation index 0.5 (alias MSK) is a linear modulation that is able to achieve the theoretically optimal performance [1]
BUT
Achieving the full performance requires a correlation receiver with precise timing and phase estimation and pre-coding
Using a classical non-coherent demodulation causes a loss of typically 6dB due to missing orthogonality and differential demodulation [1]!
Using 2-FSK with modulation index 1.0 only leads to a loss of typically 3dB!

## Slide 14: What to do with MSK in SUN?
Generating MSK is very simple
  Every simple FSK modulation is able to generate perfect MSK signals
The problem of MSK is the higher complexity to achieve a better performance than classical 2-FSK
  Precise channel sounding and channel estimation ( LoRa FHSS issue)
  Coherent decoding
  Use of MSK pre-coding
Reserve MSK for modes with mandatory FEC
Add MSK-precoding (follow 802.15.4me 24.4.9)
Create new preamble for MSK modes
Potentially add additional reference signals (pilots) for long packets

## Slide 15: High Performance & Simple FSK?
We should offer a mode simple non-coherent mode with better performance than 2-FSK
4-FSK is already defined in SUN FSK and offers a significantly improved performance compared to classical 2-FSK [1]
4-FSK is already supported by many state-of-the art chips
Addition of 4-FSK in modulation for bands where not defined yet
Potential optimization of modulation index
Optimization of preamble for 4-FSK

## Slide 16: FSK Spectral Shaping
The hard switching between adjacent symbols causes a high spectral bandwidth of classical FSK [1]
In order to optimize spectral usage the spectral bandwidth should be reduced
Make Gaussian FSK with BT = 1 mandatory (follow 24.4.4.2 in 802.15.4me for 2-FSK, define similar scheme for 4-FSK)
Already supported by all state-of-the art chips
No impact on demodulation

## Slide 17: Proposal for FSK Modulation
Mandatory use of Gaussian Shaping with BT = 1 (follow 24.4.4.2 in 802.15.4me for 2-FSK, define similar scheme for 4-FSK)
Generally reduce allowed tolerances to allow for optimized decoding in future receivers (details tbd.)
MSK (2-FSK with modulation index 0.5) only with pre-coding (25.4.9 in 802.15.4me) and forward error correction
Define new preamble and potential pilots for MSK modes that meet coherent demodulator requirements
Addition of 4-FSK modes to bands where not defined yet
Modulation index and new preambles tbd.
New bandwidths and channels tbd.

## Slide 18: Analysis: FSK Forward Error Correction
The SUN FSK convolutional code only offers a constraint length of 4
  Comparability low performance in AWGN channels
  Very low performance in case of interference and fading for lower rates
  Very high performance loss for long packets [2]
Time interleaver is very short and not optimized for interference
  Low robustness in case of interference, especially loss of header
  Distribution of the errors not optimized for erasure-decoding in interference channels
No separate error check for header
  No early detection of false positives
  Higher power consumption and longer off-air times

## Slide 19: FEC System Considerations
A good FEC requires a good demodulator
  Reliable Log-Likelihood (LLR) values (“Soft Bits”)
  Precise detection of fades / interference
  State-of-the-art codes (e.g. LDPC, Turbo, Polar) are very sensitive against wrong LLRs
Classical non-coherent FSK demodulator do not provide precise LLR values
  Limited gain of coding in AWGN channel
  State-the-art codes practically not usable
  Still good performance for interference (for proper interleaver)
Optimal performance with coherent demodulation (MSK)
  Operation close to the theoretical limits (AWGN, interference)
  State-of-the art codes can be used

## Slide 20: Suitable FEC Codes
No convolutional code
  Only for modes intended for non-coherent decoding
Convolutional codes
  Use constraint length 7 codes (already used in SUN OFDM, LECIM) with rate 1/2 and rate 1/3
  High performance gain with coherent decoding
  Good performance in case of interference
Turbo / LDPC / Polar codes
  Only useful in case of coherent decoding (MSK)
  Precise LLR requirements demand sophisticated receivers
   We should not do this ...

## Slide 21: Some Thoughts on the CRC
The cyclic redundancy check (CRC) is used to detect errors
The CRC cannot correct any errors
BUT:
Interference typically leads to burst errors
Convolutional codes lead to burst errors in case of decoding failures (which are likely to happen for long codes)
Why not replacing the CRC with a Reed Solomon (RS) Code?
Comparable complexity to a CRC if only used for error-detection (simple RX)
A 4 byte RS(255,...) code can correct up to 4 byte errors
RS codes are ideal for removing remaining decoding errors (already used in standards like ISDB-T, DVB-T)

## Slide 22: Header CRC
A bis issue of the synchronization is the detection of false positives
  A packet is detected out of the noise
  The receiver starts to decode the packet, requiring much energy and the system is in the wrong state to detect actual packets  important for low rates
A CRC in the header offers the possibility to quickly detect false positives
A simple receiver design would simply ignore the header CRC
The header CRC is already part of SUN OFDM

## Slide 23: Issues with Current Interleaver
The current SUN FSK interleaver is too short to provide good robustness against interference (interleaver length of only 16 symbols)
Especially the slower symbol rates are more vulnerable to interference due to their long on-air time
Significantly increased interleaver depth required with low impact on memory consumption
Optimized design required to optimize for erasure decoding
The LECIM time interleaver with minor modifications could the required characteristics (802.15.4me 24.4.7)

## Slide 24: Proposal for FEC
Use constraint length 7 convolutional codes (already used in SUN OFDM, LECIM) with rate 1/2 and rate 1/3
Make FEC mandatory for coherent modes (i.e. MSK)
Add 8bit header CRC
Use Reed Solomon Code instead of CRC
Add interleaver as defined in LECIM (802.15.4me 24.4.7) with minor modifications
Make interleaver mandatory for FEC modes

## Slide 25: Issues with Current Preamble
Preambles not optimal, especially for coherent detection
Potential problems with existing SUN FSK modes
Design of new FSK preambles that meet the actual requirements and are different from existing systems to avoid issues with existing SUN devices

## Slide 26: Proposal for Preamble
New preambles for all FSK modes with modifications compared to existing SUN FSK
Details of the preamble are tbd.

## Slide 27: SUN OFDM

## Slide 28: Analysis of SUN OFDM
Use of OFDM is ramping up
Complexity significantly higher compared to FSK
Potential areas of improvement
  Number of modes
  Modulation
  Synchronization / Preamble
  Forward Error Correction
  More communalities with SUN FSK

## Slide 29: OFDM Modulation
Sub-carrier spacing of approx. 10kHz and cyclic prefix of 1/4 meets market demands
Bandwidth flexibility by adjusting the number of used sub-carriers
Pilot density that meets channel estimation requirements
Filter to minimize out-of-band emissions is shown in the block diagram, but not defined

## Slide 30: Proposal for OFDM Modulation
Specify pulse shaping filter as in TVWS-OFDM modulation (802.15.4me, 27.3.13)
Add additional bandwidths if required

## Slide 31: QAM Mappings
The current specification offers a variety of QAM modes
Coherent demodulation is assumed, requiring channel estimation using the preamble / pilot signals
The BPSK modes with repetition are not really useful
  The robustness of these modes does not match the synchronization capabilities of the preamble
  It is very unlikely that the current pilot schemes are able to offer any kind of usable channel estimates at negative SNR values
  BPSK does not itself provide any gains compared to QPSK for coherent demodulation
  Repetition codes are linear codes and hence bad codes by default [2]
  Convolutional codes provide better performance in case of interference
64QAM is currently not defined

## Slide 32: Does this Work?

## Slide 33: Some Question Related to BPSK Modes
What was the intention behind BPSK modes, especially the modes with repetition?
A proper receiver design achieving the theoretical robustness is practically impossible
  An extremely long preamble would be required
  The channel estimation with the current pilot schemes would require a very sophisticated receiver with an adaptive Wiener filter
  Due to the spreading nature of OFDM there is not real gain for impulsive noise
Lower reception levels could be achieved by lower bandwidth  LR OFDM

## Slide 34: Proposal for QAM Mappings
Remove repetition modes of BPSK
Add 64QAM
Add symbol interleaver as defined in ETSI EN 300 744 for optimizing the QAM mapping
But: Be clear that 64-QAM will required a very good channel with high SNR, and you have to implement a sophisticated channel estimation inside the receiver

## Slide 35: Suitable FEC Codes
Uncoded is no option for OFDM systems
Convolutional codes
  Keep the constraint length 7 codes with rate 1/2 and add the rate 1/3 code (already used in LECIM)
  Coherent decoding is anyhow required with OFDM
  Good performance in case of interference
Turbo / LDPC / Polar codes
  Would offer significant performance improvement, especially with 64QAM
  Would mean drastic complexity increase
  Require very precise estimation of LLR

## Slide 36: Issues with Current Interleaver
The current SUN OFDM interleaver is too short to provide good robustness against interference
Especially impulsive noise – destroying complete OFDM symbols – cannot be handled effectively
Significantly increased interleaver depth required with low impact on memory consumption
Optimized design required to optimize for erasure decoding
The LECIM time interleaver with minor modifications could the required characteristics (802.15.4me 24.4.7)

## Slide 37: Proposal for FEC
Use constraint length 7 convolutional codes (already used in SUN OFDM, LECIM) with rate 1/2 and rate 1/3
State-of-the art FEC tbd.
Make FEC always mandatory
Use Reed Solomon Code instead of CRC
Add interleaver as defined in LECIM (802.15.4me 24.4.7) with minor modifications
Make interleaver mandatory

## Slide 38: Issues with Current Preamble
Preambles length does not meet actual requirement of the modulation
Adjustment of the preamble length to meet the actual requirements
Use of different pattern to avoid detection of current SUN OFDM receivers

## Slide 39: Proposal for Preamble
Keep current preamble structure
Adjust the length of the preamble to meet SNR requirement
Adjust modulation of the preamble to avoid coexistence issues with current SUN OFDM receivers
Details of the preamble are tbd.

## Slide 40: LR OFDM

## Slide 41: LR OFDM Concept
Generally, we support the TI LR-OFDM proposal [3]
The proposal is a good approach to address long-range with low reception power  makes the SUN OFDM BPSK modes obsolete
BUT: The TI proposal has some issues that should be improved
The synchronization using a narrow-band signal is not very robust and limits the capacity
The proposed modulation causes a loss of approx. 6dB

## Slide 42: Issues with the TI Synchronization
Using a narrow-band signal is generally not a good idea
  No diversity in case of frequency selective fading
  Issues with (narrow-band) interference, e.g. blocking and false positives
  High probability of collisions between different users accessing the channel
A proper synchronization has to support multiple layers
  Different devices may access the channel at the same time
A proper synchronization has to support frequency and time diversity

## Slide 43: Proposed Synchronization (I / II)
Time- / frequency diagram of the proposed synchronization
OFDM Symbols
OFDM Subcarriers
Sync-Burst

## Slide 44: Proposed Synchronization (II / II)
The synchronization consists of multiple sync bursts
Each sync burst uses 6 consecutive OFDM symbols
The sync. follows a staircase structure, always two OFDM symbols use the same carrier
The positions of the sync bursts can be varied to allow for different parallel networks
The synchronization is able to use the classical OFDM receiver  will be presented in a later meeting

## Slide 45: Issues with TI Modulation
The TI proposal always uses two adjacent OFDM symbols that use the same OFDM subcarrier
The first of the two OFDM symbol is a reference symbol
The second symbol carriers the BPSK payload information
3dB loss as only 50% of the transmit signal is used for payload
~3dB loss as the data is encoded differentially
Total loss of ~6dB compared to pilot-based decoding (as used in current SUN OFDM)

## Slide 46: Proposed Modulation
Group the data into bursts, the burst structure is shown above
Only a single carrier is used at a time
Each burst has 8 payload and 4 pilot symbols
Different bursts are distributed over the available bandwidth
The pilot structure follows the classical SUN OFDM structure
The modulation structure fulfills the 500kHz FCC requirement
Payload Data
Pilot
OFDM Symbols
OFDM Subcarriers

## Slide 47: Out-of-Band Emissions
Spectrum of a single OFDM sub-carrier
OFDM is not really narrow-band, sidelobes go only down by 40dB
Causing interference in case of many LR OFDM devices

## Slide 48: Proposal for LR-OFDM Modulation
Specification of shaping filter to reduce out-of-band emissions
Specification of strict spectral mask
Details tbd.

## Slide 49: Proposal for FEC
Same modes as proposed for new SUN OFDM on earlier slides

## Slide 50: Summary
I really presented many details
In order to not bore you too much ... details and simulation results will be presented in the following sessions
The goal is to maximize performance by keeping the complexity low

## Slide 51: Literature
[1] Proakis, J. G.; Salehi, M. (2008); “Digital communications.” McGraw-Hill (2008)
[2] Dolinar, S.; Divsalar, D.; Fabrizio, F.; "Code performance as a function of block size." TMO progress report 42.133 (1998) https://citeseerx.ist.psu.edu/document?repid=rep1&type=pdf&doi=133435497ecbd8c685b186d8b073387fb8721877
[3] Almholt, T.; DCN 15-24-0651-00, https://mentor.ieee.org/802.15/dcn/24/15-24-0651-00-04ad-tg-sun-phy-next-gen-ofdm-lr-contribution.pptx

## Slide 52: Thanks!