## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Summary of security related work in the WG15]
Date Submitted: [2025-02-17]
Name: [Tero Kivinen] Affiliation: [Wi-SUN Alliance] E-Mail: [kivinen@iki.fi]
Abstract:
[This document provides summary of the security related task groups in the 802.15 working group.

## Slide 2: Summary of security task groups
There is currently 3 task groups working on the security
  TG4ac working on the privacy enhancements
    In letter ballot
  TG4ae adding ASCON cipher to the IEEE Std 802.15.4
    Should be getting ready for letter ballot
  TG9a adding EDHOC key management protocol to IEEE Std 802.15.9
    Should be going to letter ballot after this session

## Slide 3: TG9a: EDHOC
This will be quite short amendment to the IEEE Std 802.15.9
It will add one new annex describing how to use IETF EDHOC (RFC9528) in IEEE Std 802.15.9.
  EDHOC = Ephemeral Diffie-Hellman Over COSE
  COSE = CBOR Object Signing and Encryption
  CBOR = Concise Binary Object Representation
There will be two versions of the EDHOC that are supported:
  Raw EDHOC
  EDHOC over CoAP

## Slide 4: TG9a: Why EDHOC
EDHOC enables a low complexity implementation with few and short messages
In one example, of a three-message public key based EDHOC session including cryptographic agility and extensibility, each protocol message is smaller than 46 bytes, and the session consists of 101 bytes in total.
EDHOC allows different methods for performing mutual authentication, for example using digital signatures or static Diffie-Hellman keys, with the authentication credentials passed by value or by reference.

## Slide 5: TG4ae: ASCON
This amendment adds ASCON cryptographic cipher to IEEE Std 802.15.4.
This also defines better how to use generic AEAD ciphers in the IEEE Std 802.15.4, the current text is specific to the AES-CCM and AES-CCM* ciphers.
Specifies how the 13-octet nonce from IEEE Std 802.15.4 is expanded to 16-octet nonce for ASCON use case.
  Uses same construct as current AES-CCM, i.e., generate flags byte as first byte of nonce.
  ASCON does not need internal counter, thus L in flags will be set to zero, and nonce will be zero padded to 16-octets.
Most of the document will be the test vectors for ASCON.

## Slide 6: TG4ae: Why ASCON
NIST selected ASCON as Lightweight Cryptography Standards for Constrained Devices.
ASCON provides:
  Authenticated encryption (AEAD cipher)
  Hash (could be used to replace SHA2/3)
  Extendable Output Functions (key derivation, PRF etc)
Simplicity Ascon is natively defined on 64-bit words using only the bitwise Boolean functions and, xor, not, and rot (bitwise rotation).
Lightweight and Flexible in Hardware Current implementation results show that Ascon provides excellent implementation characteristics in terms of size and speed.
  Several times faster than AES-GCM both in software and hardware
  Smaller code size than AES-GCM

## Slide 7: TG4ac: Privacy
IEEE Std 802.15.4 do include optional security that provides confidentiality and authentication of the frames, but there has not been need for privacy.
  Most of the IEEE Std 802.15.4 devices have been either fixed in location, or not connected to the persons.
  This is now changing as some mobile phones start to include IEEE Std 802.15.4 radios.
  IEEE Std 802.15.4 devices has used fixed 64-bit extended addresses or 16-bit short addresses, and there has not been a way to change either of them.
  This amendment learns from the work done earlier, and takes very 802.15.4 way of solving problem, i.e., everything is done in next higher layer.
  This amendment provides MLME primitives to provide the tools next higher layer needs to achieve suitable level of privacy.

## Slide 8: TG4ac: Primitives
Address list management (MLME-PRIV-ADDR-LIST, MLME-PRIV-ADDR-LIST-CONFIRM, MLME-PRIV-REQ-ADDR)
Short address management (MLME-PRIV-ADDR-ASSIGN, MLME-PRIV-ADDR-ASSIGN-CONFIRM)
Key identifier management (MLME-PRIV-UPDATE-KEY-ID, MLME-PRIV-UPDATE-KEY-ID-CONFIRM)
Network discovery and device discovery (MLME-PRIV-NET-VERIFIER-GENERATE, MLME-PRIV-NET-VERIFIER-VERIFY)

## Slide 9: TG4ac: Identifiers
Uses IEEE Std 802c Administratively Assigned Identifiers (AAI-64)
  i.e., XYZ bits are set to one, zero, zero.
  Adds two more bits (S, T) to indicate what type of identifiers it is uses to keep the different types of identifiers distinct.
Types of identifiers:
  Extended privacy address
  Device identifier (DI)
  Network ID
  Short addresses
  Short address nonce generation prefix (SANGP)

## Slide 10: TG4ac: Extended privacy address
Extended address used in the MAC header, this shall replace the static 64-bit extended address in MAC header.
This is the only type of address that is sent over the air in clear (in MAC header).
Randomly generated.
Device may generate this whenever it needs or feels like.
Device may have multiple addresses in use at the same time in the same network.
Device should use different extended privacy address lists in different networks.
Device will send list of extended privacy address to its peers when it changes them (or it can use broadcast/multicast frames to update addresses).

## Slide 11: TG4ac: Device identifier (DI)
Device identifier is stable identifier for the device for the lifetime of the network.
Randomly generated.
When sent in any frames, the frames shall be encrypted.
Device may use different DIs in different networks.
It is used for example in the frames where device updates its list of extended privacy addresses to indicate originating device sending the update.

## Slide 12: TG4ac: Network ID
Network ID is used to identify network during the lifetime of the network.
Randomly generated when network is created by the creator of the network.
Never sent over the air.
Needs to be provided by the provision system to allow device to join network (provision system is out of scope).
Different networks use different network ID, and there is one owner of the network identified by the network ID.

## Slide 13: TG4ac: Short addresses
16-bit addresses that can be used in the IEEE Std 802.15.4 MAC header as source or destination address.
  In IEEE Std 802.15.4 there can be only one short address at one time.
  Privacy enhancements allows multiple.
Not stable, they are provided by the some entity in the network to the device when it joins.
Normally they do not change while device is connected.
The entity providing addresses needs to make sure they are unique at that time.
Same short address may be given to another device later when the first device has disassociated from the network.
Each short address is associated to one 16-bit PAN ID.

## Slide 14: TG4ac: Short address nonce generation prefix (SANGP)
48-bit prefix used to generate extended addresses used in the IEEE Std 802.15.4 security layer when using short addresses.
Security layer requires extended address to generate nonce even when using short addresses. This extended address needs to be unique over the lifetime of the key used in the network.
  Generate 64-bit extended address for nonce generation use by combining the 48-bit SANGP and 16-bit short address.
Device assigning short addresses also assign SANGP associated with the list of short addresses.
Can be randomly generated in small networks (up to few thousands).
In larger networks needs to make sure they are unique, thus using counter is acceptable way of making sure each are unique (they do not need to be random).

## Slide 15: TG4ac: Address list sequence number
In case device uses multiple extended privacy addresses at the same time (simultaneously, not sequently).
It is used to provide ordering for the address lists received.
If only one extended privacy address or one short address is used, then replay prevention mechanism provided by the security layer prevents replays and no sequence number is needed.

## Slide 16: TG4ac: Frame counters
In IEEE Std 802.15.4 there is one frame counter for a device or one per key.
Privacy enhancements adds separate frame counters for each address.
Frame counters are initialized to random value when they are taken in to use.

## Slide 17: TG4ac: Sending list of addresses

## Slide 18: TG4ac: Sending address list retry

## Slide 19: TG4ac: Requesting address list

## Slide 20: TG4ac: Assigning addresses

## Slide 21: TG4ac: Updating key identifiers 1

## Slide 22: TG4ac: Updating key identifiers 2

## Slide 23: TG4ac: Network announcement detect

## Slide 24: TG4ac: Network announcement address list 1

## Slide 25: TG4ac: Network announcement address list 2

## Slide 26: TG4ac: Network request start