## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSNs)
Submission Title: Current Status of Existing FSO Technologies
Date Submitted: March 11, 2025
Source: Mohammad Mahdi Biswas Rimu, Yeong Min Jang (Kookmin University)
Address: Room #603 Mirae Building, Kookmin University, 77 Jeongneung-Ro, Seongbuk-Gu, Seoul, 136702, Republic of Korea
Voice: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract: Current Status of Existing FSO Technologies
Purpose: Presentation for contribution in FSO Technologies
Notice: This document has been prepared to assist the IG NG-OWC. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by IG NG-OWC.

## Slide 2
Current Status of Existing FSO Technologies March 11, 2025

## Slide 3: Contents
Background
Current Status
Existing Issues
Mitigation Strategies
Future Research Directions
Conclusion
References

## Slide 4: Background
Free-Space Optical (FSO) communication is a wireless technology that uses light to transmit data through the air, similar to fiber optics but without physical cables. It relies on laser beams to send information between two points, typically using infrared or visible light.
Use Cases: Satellite Communication, 5G Backhaul, Hybrid RF-FSO Network, 6G Network, UAV Communication and last-mile connectivity.
Key advantages: High Bandwidth, Low Latency, Low Implementation Cost and Immunity to Electromagnetic Interference.
Challenges: Pointing-Acquisition-Tracking (PAT), Atmospheric Conditions like Fog, Rain, and Turbulence.

## Slide 5: Existing FSO Technologies
Proposed Scheme | Mobility | Modulation | BER | Data Rate | Link Distance
High Speed 60Gbps RGB Laser Based-FSOC Link by Incorporating Hybrid PDM-MIMO Scheme for Indoor Applications | Stationary | OOK | 4.36 × 10⁻¹⁰ With a 4×4 MIMO configuration | 60 Gbps (max). | up to 500 meters using MIMO
Experimental Demonstration of FSO Under 2 km Urban Atmosphere Using Adaptive Fiber Coupling | Stationary | OOK | Up to 3.80 × 10^-8 in closed-loop operation | 10 Gbps (max) | 2km
FSO-Based Drone Assisted Mobile Access Network | Up to 20-100m | OOK | 10-9 (approximately | Up to 100Gbps | Up to 2km
Urban Low-Altitude long-range atmospheric links for FSO | Up to 12.7 km/h. | OOK | approximately 10-6 | 5 Gbps | 6.6 km and 12.7 km
Development of high-speed FSO transmission link for the implementation of 5G and Internet of Things | stationary | OOK | Not defined | Up to 160 Gbps | Up to 40 km

## Slide 6: Existing FSO Technologies
Proposed Scheme | Mobility | Modulation | BER | Data Rate | Link Distance
Performance Analysis of Indoor FSO Communication Systems Under Receiver Mobility | Stationary | OOK | Not fixed | Not defined | 8 × 4 × 3 m indoor room
A Location-Aware Resource Optimization for Maximizing Throughput of Emergency Outdoor–Indoor UAV Communication with FSO/RF | Robust optimization | OOK | Not fixed | >15Mbps | Up to 1km
High-Speed Trains Access Connectivity Through RIS-Assisted FSO Communications | Up to 500km/h | OOK | Around 10-9 | Increased by up to 45% and 63% respectively | Up to 5km
Design and Analysis of High-Speed FSO Communication System for Supporting Fifth Generation (5G) Data Services in Diverse Geographical Locations | stationary | OOK | Around 10-9 | Up to 160 Gbps | 10.75 km (max)
Provisioning internet Access Using FSO in High-Speed Rail networks | up to 270 km/h. | OOK | Not defined | 566 Mbps | 70 m

## Slide 7: Existing FSO Technologies
Proposed Scheme | Mobility | BER | Modulation | Data rate | Link distance
Beam Control for Indoor FSO and Dynamic Dual-Use VLC Lighting Systems | Robust optimization | Up to 10^-8 | OOK | 40 Mbps | 5m*5m*2m
All-Optical UAV-Based Triple-Hop FSO-FSO-VLC Cooperative System for High-Speed Broadband Internet Access in High-Speed Trains | Robust optimization | Not defined | OOK | Not defined | Up to 2.5 km
Blind Signal Detection Under Synchronization Errors for FSO Links With High Mobility | up to 360 km/h | below 10-6 | OOK | 1 Gbps | Several kilometers
Large Submillimeter High-Speed Photodetector for Large Aperture FSO Receiver | stationary | below 10-3 | OOK | 25 Gbps | 10 m
FSO communication system for high-speed trains under varying visibility conditions | 400 km/h | Not defined | OOK | 1.25 | 14.2 km (max)

## Slide 8
Existing Issues in Current FSO Technologies
Atmospheric Attenuation (Fog, Rain, Snow and Dust)
Turbulence-Induced Fading (Scintillation)
Beam Misalignment (Pointing and Tracking Errors)
Background Light Interference (Solar and Artificial Light Noise)
Limited Range and Line-of-Sight (LOS) Requirement

## Slide 9
Mitigation Strategies of Existing Issues
Deployment of hybrid RF-FSO systems to switch to RF links when FSO is degraded
Implementation of adaptive power control to increase laser intensity during attenuation.
Use of adaptive optics to compensate for wave front distortions.
Implementation of error correction coding (e.g., Reed-Solomon or LDPC) to recover lost data.
Deployment of relay nodes to extend coverage.
Implementation dynamic beam adjustment to avoid obstacles.

## Slide 10
Future Research Directions
Machine Learning for Channel Estimation
Hybrid RF-FSO Systems
Advanced Adaptive Optics
Quantum FSO Communication
Terahertz (THz) & Multi-Wavelength FSO
Satellite-Based FSO & Deep-Space Communication
MEMS and Beam Steering Technologies
Integrated Photonic Systems

## Slide 11
Conclusion
FSO is a High-Speed, Secure Alternative
Offers high bandwidth, low latency, and immunity to electromagnetic interference.
Challenges Still Exist
Atmospheric attenuation, beam misalignment, and turbulence limit performance.
Innovations Are Driving Progress
AI-based tracking, adaptive optics, and hybrid RF-FSO systems are improving reliability.
Expanding Applications
Future potential in 6G networks, satellite communication, deep-space missions, and quantum encryption.

## Slide 12
References
https://ieeexplore.ieee.org/abstract/document/8844114
https://scholar.google.com/scholar?hl=en&as_sdt=0%2C5&q=+High+speed+60Gbps+RGB+laser+based-FSOC+link+by++incorporating+hybrid+PDM-MIMO+scheme+for++indoor+applications&btnG=
https://scholar.google.com/scholar?hl=en&as_sdt=0%2C5&q=+Experimental+demonstration+of+free-space+optical+communication+under+2++km+urban+atmosphere+using+adaptive+fiber+coupling&btnG=
https://www.sciencedirect.com/science/article/pii/S0030401824008058
https://scholar.google.com/scholar?hl=en&as_sdt=0%2C5&q=+Development+of+high-speed+FSO+transmission+link++for+the+implementation+of+5G+and+Internet+of+Things&btnG=
https://scholar.google.com/scholar?hl=en&as_sdt=0%2C5&q=+Performance+Analysis+of+Indoor+FSO++Communication+Systems+Under+Receiver+Mobility&btnG=
https://scholar.google.com/scholar?hl=en&as_sdt=0%2C5&q=ALocationAware+Resource+Optimization+for+Maximizing++Throughput+of+Emergency+Outdoor%E2%80%93Indoor+UAV++Communication+with+FSO%2FR&btnG=
https://ieeexplore.ieee.org/abstract/document/9860053
https://scholar.google.com/scholar?hl=en&as_sdt=0%2C5&q=+Design+and+Analysis+of+High-Speed+Free+Space++Optical+%28FSO%29+Communication+System+for++Supporting+Fifth+Generation+%285G%29+Data+Services+in++Diverse+Geographical+Locations+of+India&btnG=
https://scholar.google.com/scholar?hl=en&as_sdt=0%2C5&q=+Provisioning+internet+Access+Using+Fso+in+HigH-sPeed+rAil+networks&btnG=
https://scholar.google.com/scholar?hl=en&as_sdt=0%2C5&q=Beam+control+for+indoor+FSO+and+dynamic++dual-use+VLC+lighting+systems&btnG=