## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Group Association for IEEE 802.15.4
Date Submitted: 10th March 2025
Source: Jianlin Guo, Pu (Perry) Wang, Takewa Tomoaki, Sanda Takayoshi, Kieran Parsons, Petros Boufounos, Philip Orlik, Yukimasa Nagai, Takenori Sumi, Benjiman Rolfe (Mitsubishi Electric)
E-Mail: guo@merl.com
Abstract: This document proposes a group association method for IEEE 802.15.4 to achieve fast association.
Purpose: Discuss fast association in IEEE 802.15.4 networks to meet the requirements of emerging applications that require fast and controlled access in large-scale and dense deployment environment.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
IEEE 802.11ai amended IEEE 802.11 standard for fast initial link setup (FILS) designed to improve dense environments, enabling a STA to achieve a secure link setup within 100ms,
  FILS association
  FILS authentication
For IEEE 802.15.4, the large-scale and dense deployment scenarios are emerging, and these deployments require fast access control
  For example, device manufactures are making IEEE 802.15.4ab-based UWB devices for large-scale and dense deployments
IEEE 802.15.4 association mechanisms can be divided into
  Regular association (IEEE 802.15.4-2020)
  UWB association (IEEE 802.15.4ab)
The regular association method provides an option for devices to request fast association, i.e., fast connection setup
However, the question is that what if all devices request for fast association?
Need of Group/Fast Association in IEEE 802.15.4

## Slide 3
Advanced UWB-Based access control and real-time location systems
In this deployment, the objective is to realize hands-free access control and real-time location using smart devices, e.g., smart phones and smart key tags, as the primary interfaces
  Explore solutions to make UWB technology more effective for enterprise applications
  Improve scalability for fast access control and real-time location systems
There are also other large-scale and dense deployment scenarios
  Campus, logistics hubs, and hospitals
Potential scales
  Thousands of access controllers and tens of thousands of users requesting access using smart devices
Expected key features
  Fast connection setup
  Zero manual operation
  Seamless background communications
Dense Deployment Scenarios and Expected Features

## Slide 4
IEEE 802.15.4 PAN coordinator divides devices that are requesting for association into groups
Instead of sending association response to individual device, PAN coordinator sends aggregated association command frame that contains the association responses to a group of devices
  Reduce network traffic
  Reduce association latency
  Reduce frame collision
In addition, to reduce association request and association response command frame collision, PAN coordinator specifies a silence period to prevent devices from sending the repeated association requests to same PAN coordinator
  Reduce frame collision
  Increase reliability
Accordingly, devices whose association request command frames acknowledged by MAC layer ACK do not send further association requests during silence period
Proposed Group Association Method for IEEE 802.15.4

## Slide 5
IEEE 802.15.4 Command Frame Format
IEEE 802.15.4 MAC Command Frame Format
Format of Frame Control Field
To be modified
To be modified
To be modified
To be modified

## Slide 6
Content Field of IEEE 802.15.4 Association Request Frame
Association Request Command Content Field Format
Association Request Command Capability Information Field format
1 = fast association request
No modification is needed for Association Request Frame

## Slide 7
Association Response Command Content Field format
Valid Values of the Association Status Field
Content Field of IEEE 802.15.4 Association Response Frame
Content field modification is needed for Association Response Frame

## Slide 8
Octets: 1 | 11 | 11 | … | 11 | 4
NoR | Association Response 1 | Association Response 2 | … | Association Response NoR | Association Request Transmission Silence Period
Octets:8 | 2 | 1
Extended Device ID | Short address | Association status
Group Association Response Command Frame Content Field format
Association Response Format
Proposed Content Field for IEEE 802.15.4 Association Response Frame
NoR = Number of Responses
If allocated

## Slide 9
Proposed Frame Control Field Change of IEEE 802.15.4 Association Response Frame
Format of Frame Control Field
AR = 0
Devices do not transmit immediate MAC layer ACK since AR = 0
Instead, devices transmit ACK in CAP period to PAN coordinator via CSMA mechanism or PAN coordinator guides ACK transmission
Short = 0b10

## Slide 10
Proposed Addressing Fields Change of IEEE 802.15.4 Association Response Frame
Destination address = Short broadcast address
How to distinguish regular Association Response Frame and group Association Response Frame?
  AR
  Destination Address Mode
  Destination Address

## Slide 11
Association Type Based Device Grouping
Grouping devices based on association types contained in association request frames with type 1 devices having high priority
IEEE 802.15.4 PAN coordinator
Type 1 devices
Type 0 devices

## Slide 12
Time Based Device Grouping
Grouping devices based on times association request frames received with earlier devices having high priority
IEEE 802.15.4 PAN coordinator
Group 1 devices
Group 2 devices
Group 3 devices

## Slide 13
Distance Based Device Grouping
Grouping devices based on distances to PAN coordinator with closer devices having high priority
Group 1 devices
Group 2 devices
Group 3 devices
IEEE 802.15.4 PAN coordinator

## Slide 14
Communication Channel Based Device Grouping
Grouping devices based on communication channels
PAN coordinator can respond simultaneously with multiple antennas or sequentially with one antenna via channel hoping
Channel 1 devices
Channel 2 devices
Channel 3 devices
Channel 1
Channel 2
Channel 3
Frequency
IEEE 802.15.4 PAN coordinator

## Slide 15
Beamforming Based Device Grouping
Grouping devices based on beamforming directions
PAN coordinator transmit beacons sequentially to different beamforming directions
Sector 1 devices receive beacon at time t1
Sector 3 devices receive beacon at time t3
Sector 2 devices receive beacon at time t2
Beamforming direction divider
IEEE 802.15.4 PAN coordinator

## Slide 16
This document presents a group association method for regular IEEE 802.15.4 association and its realization in IEEE 802.15.4 to achieve fast association in large-scale and dense deployment scenarios
A silence period is proposed to prevent devices to transmit repeated association requests to same IEEE 802.15.4 PAN coordinator
Document also provides five grouping methods for IEEE 802.15.4 PAN coordinator to group devices that are requesting for association
Next, will fit group association method into IEEE 802.15.4ab UWB association framework
Summary