## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: FECs table configuration
Date Submitted: March 13th, 2025
Source: Marco Hernandez1,2, Seong-Soon Joo3, Ryuji Kohno1, Takumi Kobayashi4, Anzai Daisuke4
Company: 1YRP-IAI, 2CWC Oulu Univ., 3KPST, 4Nagoya I. Tech.
Address: (1)79-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan,
(2) YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan
Voice:[] E-Mail:[Marco.Hernandez@ieee.org, ssjoo@etri.sci.kr, Kohno@yrp-iai.jp, kobayashi@nitech.ac.jp, anzai@nitech.ac.jp]
Re: In response to call for proposals
Purpose: Material for discussion in P802.15.6ma TG
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Coexistence Class | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
QoS Level |  |  |  |  |  |  |  | 
0 | LDPC/BCC | LDPC/BCC | LDPC/BCC | LDPC/RS | LDPC/RS | LDPC/BCC | LDPC/RS | LDPC/RS
1 | LDPC/BCC | LDPC/BCC | LDPC/BCC | LDPC/RS | LDPC/RS | LDPC/BCC | LDPC/RS | LDPC/RS
2 | LDPC/BCC | LDPC/BCC | LDPC/BCC | LDPS/RS | LDPS/RS | LDPC/BCC | LDPS/RS | LDPS/RS
3 | LDPS/BCC | LDPS/BCC | LDPS/BCC | LDPS/RS | LDPS/RS | LDPS/BCC | LDPS/RS | LDPS/RS
4 | LDPC/RS | LDPC/RS | CFP/HARQ | LDPC/RS | LDPC/RS | LDPS/BCC | LDPC/RS | LDPC/RS
5 | LDPC/RS | LDPC/RS | CFP/HARQ | CFP/HARQ | CFP/HARQ | LDPC/RS | CFP/HARQ | CFP/HARQ
6 | LDPS/RS | LDPS/RS | CFP/HARQ | CFP/HARQ | CFP/HARQ | LDPS/RS | CFP/HARQ | CFP/HARQ
7 | LDPS/RS | LDPS/RS | CFP/HARQ | CFP/HARQ | CFP/HARQ | LDPS/RS | CFP/HARQ | CFP/HARQ
Table 2 Specification of Error-Control Defined Corresponding 64 Combinations of 8 QoS Levels and 8 Coexistence Classes
FEC, ARQ), and HARQ have been investigated to satisfy technical requirement in various channel model, QoS levels of user packets, and classes of coexistence considering compatibility with IEEE802.15.6-2012 and another UWB PAN IEEE802.15.4ab, etc. Tabel 2 shows its summary in P802.15.6ma. LDPC/BCC and LDPC/RS mean concatinated codes with LDPC as inner code, Binary Convolutional Code(BCC) and Reed-Solomon(RS) code as outer code. CFP/HARQ means packets in Contention Free Period(CFP) are protected with Hybrid ARQ(HARQ).