IEEE P802.15
Wireless Specialty Networks

Title:	Alternate format to replace compact frames
Date Submitted:	2025-03-30
Name:	Tero Kivinen	Affiliation:	Wi-SUN Alliance	E-Mail	kivinen@iki.fi
Abstract:	Provide more secure, private format to replace compact frames

Change history of this document
Revision	Date	Description
15-25-0173-00	2025-03-30	Initial version
15-25-0173-01	2025-05-13	New version including modified Multipurpose frame

# Alternate format for compact frames
# General
The TG4ab draft D02 contains completely new frame format called compact frames, which has serious shortcomings.
- Not all of the frames can be secured
- When secured it requires upper layer coordination to be able to keep frame counters in sync and not to reuse frame counters.
- It adds new address format
- It does not include source and destination addresses, it only includes one address, and what address that is depends on the compact frame id
- It is not very compact even when it claims to be so.
This document provides and alternative way to do same thing but using existing IEEE Std 802.15.4 frame formats.
# Options
In IEEE Std 802.15.4 there is multiple ways to do same things, and depending on the properties required different options can be selected. Here is two options proposed in this document:
- MAC Command frames
- Multipurpose frames containing IEs
- Multipurpose frames with version number of 0b01 or 0b10.
  - Add new version of multipurpose frame which has one octet (version 0b01) or two octet (version 0b10) of sub-id field after the header before IEs.
Both use normal addressing formats, and can use the privacy addresses specified in the TG4ac. Different addressing schemes are used depending on the environment:
- SrcAddrMode of NONE meaning no addresses, when the source frame address is already known (i.e., it is coordinator or whoever is initiating the system), and DstAddrMode of SHORT or EXTENDED with or without PAN ID.
- SrcAddrMode of SHORT or EXTENDED with or without PAN ID and a DstAddrMode of NONE with macImplicitBroadcast set to true (i.e., when the message is to be sent to group of devices).
These methods allow 0/2/4/8/10 octet long addressing fields with full privacy if needed.
# Summary comparison of different formats
Lengths used:
- The base header for compact frames is on octet long
- FCS used in always two octets
- RPA Hash and RPA Prand are three octet long
- Message ID is one octet long
- Message Content is variable and not counted in any of the numbers below
- MAC Commands and Multipurpose frames both use short addresses, and only use one address, without PAN IDs. This will make Addressing fields two octets long. Depending on the compact frame type they use either source or destination address.
- MAC Command and Multipurpose frames do not use sequence numbers.
- For security we assume we use KeyIdMode 0x01 using 8-bit KeyIndex, meaning Auxiliary security header shall be six octets long for MAC Command and Multipurpose frames.
- Security level of two or five is used, i.e., MIC length will be four octets.

Frame type	Unsecured overhead				Secured overhead
	Compact frames	MAC Command	Multipurpose version 0b00	Multipurpose version 0b01	Compact frames	MAC Command	Multipurpose version 0b00	Multipurpose version 0b01
Advertising Poll Public Advertising Response Public Start of Ranging	10	6	9	5	N/A	6+6+4=16	9+6+4=19	5+6+4=15
Advertising Response Advertising Confirmation Start of Ranging Public Advertising Poll Public Advertising Confirmation Acquisition	7	6	9	5	N/A	6+6+4=16	9+6+4=19	5+6+4=15
One-to-one Poll One-to-many Poll	10	6	9	5	10+2+4=16	6+6+4=16	9+6+4=19	5+6+4=15
One-to-one Response One-to-one Initiator Report One-to-one Responder Report One-to-many Response One-to-many Initiator Report One-to-many Responder Report	7	6	9	5	7+2+4=13	6+6+4=16	9+6+4=19	5+6+4=15

In summary using MAC Command frames with short addresses is shorter than using compact frames. Using privacy addresses from TG4ac will offer much better privacy features than what is currently offered.
When using secured frames the MAC command frames are same length (Poll frames) or three octet longer (responses). This is because the normal security layer transmits the four octet frame counter with the frame to make sure there is no reuse of the frame counters. The secured compact frames trusts upper layer to properly make sure that the Slot Index, Round Index, and Block Index are properly increment and will never repeat. As some of those fields are transmitted inside the compact frames themselves, which causes chicken and egg problem as to be able to decrypt that frame the recipient needs to know the current Slot Index, Round Index and Block Index, how will the first secured communication reach the other end.
These calculations did assume that devices are using frequencies where there are other transmitters and recipients at the same time. If there are no other IEEE Std 802.15.4 devices transmitting on that frequency then even the one address could be removed (for example when there is pair-wise ranging between two devices), especially if security is used, as in that case the MIC will provide protection against other random transmitters on the channel.
# MAC Command frame format
# General format
This format uses MAC Command frames to send the compact frames. Each Compact frame type is allocated one MAC Command ID (17 command IDs), and as the addressing fields are already in the MHR PRA Hash and PRA Prand are not needed and are omitted from the compact frames.
The Content field of the MAC command contains the Message ID and Message Content from the Compact Frame.
Frames shall be formatted as illustrated in Figure 1.
Octets: 2	0/1	variable	variable	variable		1	1	variable	2/4
Frame Control	Sequence Number	Addressing fields	Auxiliary Security Header	IE		Command ID	Message ID	Message Content	FCS
				Header IEs	Payload IEs
MHR					MAC Payload				MFR

—MAC Command frames for compact frames
It would be possible to make the format one octet shorter, by combining the Compact frame type and Message ID, i.e., allocate one Command ID for each Compact frame type and Message ID pairs. This would allocate about 50 new command IDs.
# Multipurpose frame format version 0b00 with IEs.
# General format
 This format uses Multipurpose frames to send the compact frames. Each Compact frame type is allocated one IE payload (17 MLME Nested IEs), and as the addressing fields are already in the MHR PRA Hash and PRA Prand are not needed and are omitted from the compact frames. As there will not be any payload in Multipurpose frame no Payload Termination IE is needed.
The Content field of the Payload IE contains the Message ID and Message Content from the Compact Frame.
Frames shall be formatted as illustrated in Figure 2.
Octets: 1/2	0/1	variable	variable	variable		2	2	1	variable	2/4
MP Frame Control	Sequence Number	Addressing fields	Auxiliary Security Header	IE				Message ID	Message Content	FCS
				Header IEs	Payload IEs	MLME IE	Nested IE
MHR					MAC Payload					MFR

—MAC Command frames for compact frames
It would be possible to make the format one octet shorter, by combining the Compact frame type and Message ID, i.e., allocate one IE for each Compact frame type and Message ID pairs. This would allocate about 50 new IEs instead of 17.
# Multipurpose frame format version 0b01 or 0b10
# General format of version 0b01 or 0b10 frames
This format defines new version o the Multipurpose frames. The version 0b01 includes one octet sub-id field immediately after the Auxiliary Security Header. The version 0b10 includes two octet extended-sub-id field instead. The sub-id and extended-sub-id field values are using separate registries. The version 0b10 is for future extensions.
Each Compact frame type is allocated one sub-id value (17 sub-id values), and as the addressing fields are already in the MHR PRA Hash and PRA Prand are not needed and are omitted from the compact frames.
The Content field of the Payload IE contains the Message ID and Message Content from the Compact Frame.
Frames shall be formatted as illustrated in Figure 3.
Octets: 2	0/1	variable	variable	1/2	variable		1	variable	2/4
MP Frame Control	Sequence Number	Addressing fields	Auxiliary Security Header	Sub-id or extended-sub-id	IE		Message ID	Message Content	FCS
					Header IEs	Payload IEs
MHR						MAC Payload			MFR

—MAC Command frames for compact frames
It would be possible to make the format one octet shorter, by combining the Compact frame type and Message ID, i.e., allocate one IE for each Compact frame type and Message ID pairs. This would allocate about 50 new IEs instead of 17.