## Slide 1: Proposed Areas for the IEEE802.16 Revision
May 13, 2025
DCN 15-25-0242-00-16me

## Slide 2: Proposed Categories of Additions/Modifications
Overhead reduction in the DPP burst for short messages
Modify the gain adjustment and the preamble sequences to match the performance of repetition/combining
Add explicit spec of the DPP FEC to include both CTC and CC
Improve channel access
New Functionality
  Automatic selection of repetitions vs no repetitions for a given MCS
  Automatic channel selection when multiple channels are available
  Capability negotiation
  Filtering with and without authentication
DCN 15-25-0242-00-16me

## Slide 3: DPP Overhead Reduction
Add a low overhead mode for applications characterized by:
  Short messages
  Single message per burst
  Fixed MCS
Overhead can be reduced by
  Optimizing the gain adjustment and preamble sequences
  Remove the sender and receiver ID from the CTRL MSG
  Protect the entire burst with the HMAC if authentication enabled or with a single CRC if authentication is disabled.
  HMAC filed should be minimized subject to security strength considerations
DCN 15-25-0242-00-16me

## Slide 4: Gain adjustment and preamble sequences
The length of the gain adjustment and the preamble sequences are fixed in ieee802.16t as follows:
  Gain adjustment sequence: 54 bits
  Preamble sequence: 63 bits
When repetition/combining is applied, these sequences become the weakest link and they do not allow the full benefit of repetition combining.
The sequences need to be extended so that their SNR requirements is same or lower than the repetition factor they serve. For example, for repetition factor 8, the sequences were extended to 70 for gain adjustment and 127 bits for preamble.
To minimize the overhead, optimization of these sequences vs repetition factor is required.
DCN 15-25-0242-00-16me

## Slide 5: Improve Channel ACCESS
The objective is to minimize burst collisions when many DPP links are operating in range of each other.
Performance improvement may involve:
  Modifications in CSMA/CA strategy, e.g., persistent CSMA/CA
  Sophisticated deferral schemes:
    Utilize knowledge of the messages and their duration
    Utilize master slave relationship
  Delegate CSMA/CA function to a node with good coverage to avoid the hidden node problem
DCN 15-25-0242-00-16me

## Slide 6: Automatic selection of repetitions vs no repetitions for a given MCS
This will support the following scenario:
  The DPP terminals are configured with a fixed MCS and a fixed repetition factor.
  Operation with repetitions introduces significant overhead
  It is desired to operate most of the time with no repetitions and invoke repetitions only when a predefined condition is met, e.g., type of message or when no ack received when no repetition.
It is desired to have the receiver determine from the preamble whether the burst has repetitions. The feasibility and sequence selection needs to be explored.
DCN 15-25-0242-00-16me

## Slide 7: Automatic channel selection when multiple channels are available
It is desired to operate in TDD mode but when there are multiple channels, an automatic channel selection algorithm is required.
The algorithm should share the load across all channels. This can be done by:
  Statistical distributed means
  Using a central entity
DCN 15-25-0242-00-16me

## Slide 8: Capability Negotiation
The value of certain configurable parameters can be determined using capability negotiation during the association phase.
The parameters could be either standard, vendor specific or both.
Example of a standard parameter: MCS
Example of vendor specific parameter: DPP vs legacy air interface protocol
DCN 15-25-0242-00-16me

## Slide 9: Filtering with and without authentication
When authentication is enabled, filtering can be done based on HMAC. The sender and receiver ID can be removed.
When authentication is disabled, a sender ID will be added to be used for filtering by the receiver.
DCN 15-25-0242-00-16me