## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Overview of SRM function]
Date Submitted: [13 May, 2025]
Source: [KITAZAWA Shoichi] Company [Muroran IT]
Address [Muroran, Hokaido, JAPAN]
Voice:[ ], FAX: [ ], E-Mail:[kitazawa@muroran-it.ac.jp]
Re: [ ]
Abstract: [ Overview of SRM function]
Purpose: [ ]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Overview of SRM function
Muroran Institute of Technology
KITAZAWA Shoichi

## Slide 3: Abstract
In IG Access, we are discussing improving spectrum access techniques.
This document aims to provide information about SRM (Spectrum Resource Measurement) and TCP (Transmit power control)

## Slide 4: General use case
The Network Manager or a group of Network Managers control(s) PHY/MAC parameter based on spectrum resource usage.
802.15.4
Coordinator
802.15.4
Coordinator
802.15.4
Coordinator
Radio resource contention will be occur
between different piconet
Detecting spectrum resource usage and notifies to the management entity.
SRM specify MAC framework for exchanging spectrum resource related information.
Network manager(s)

## Slide 5: Spectrum resource measurement (SRM)
IEEE 802.15.4-2024 10.28
SRM specifies the following functions and procedures in order to effectively operate wireless systems that could have heavy interferences within or outside the network:
Spectrum resource measurements and network performance metrics, such as packet error ratio, delay, etc.
Information elements and data structures to capture these measurements, procedures for collecting and exchanging spectrum resource measurement information with higher layers or other devices and for Transmit Power Control (TPC).

## Slide 6: SRM performance metrics
Energy detection (ED)
Percentage of time of failed transmissions
Percentage of time of deferred transmissions
Retry histogram
Channel utilization
Received channel power indicator (RCPI)
Received signal noise indicator (RSNI)
Received signal strength indicator (RSSI)
Noise histogram
Average access delay
MAC performance metrics specific MAC PIB attributes

## Slide 7: SRM Functions
Attribute name
macED
MacTxFailTime
macTxDeferredTime
macRetryHistogram
macChannelUtilization
macRcpi
macRsni
macRssi
macNoiseHistogram
macFrameErrorCount
macCounterOctets
macRetryCount
macMultipleRetryCount
macTxFailCount
macTxSuccessCount
macFcsErrorCount
macSecurityFailure
Attribute name
macDuplicateFrameCount
macRxSuccessCount
macNackCount
macDeferredTxCount
macAverageBufferUtilization
macMaximumBufferUtilization
macTxFragmentCount
macRxFragmentCount
macTxMulticastCount
macRxMulticastCount
macAverageAccessDelay
macSrmChannelNumber
macSrmRxAddrMode
macSrmRxDeviceAddress
macSrmStartTime
Attribute name
macSrmDuration
macSRMmeasurementMode

## Slide 8: Transmit power control (TPC)
IEEE 802.15.4-2024 10.28.3.3
TPC is one of the effective means of enhancing the performance of WPANs. A careful setting of the operating transmit power by the wireless node offers several benefits; e.g., efficient spatial re-use of the radio spectrum and minimizes interference. At the time of joining the network, the maximum transmit power
that the device shall abide by is notified by the adjacent devices that are already in the network via the beacon frame or association response frame. After joining the network, the device can specify the transmit power for the following communication types:
Broadcast communication (e.g., in the scan process) by setting phyBroadcastTxPower.
Unicast communication with any device (e.g., when a specific communication quality is required for an individual communication or in order to reduce the interference to other devices) by setting phyUnicastTxPower.
Unicast communication with a specific peer device by setting phyPeersTxPower.

## Slide 9: TPC Functions
Attribute name
phyTxPower
phyUnicastTxPower
phyPeersTxPower

## Slide 10: SRM flow
Router
PNC#1
(Concentrator)
Leaf
Router
Router
Router
[SRM Request]
Timing: On demand
Request type:
- information get: PIB attributes
- information set: TPC
[SRM Information/Extended Beacon]
Timing: On demand or periodical
- Extended Beacon: before MAC join
- SRM Information: after MAC join
Information type: information set (TPC)
[SRM Response/Report]
Timing: - Response: in response to SRM request
- Report: periodical or event-driven
Information type:
- Response: PIB attributes
- Report: Status