## Slide 1: IEEE 802.16t Point to multipoint MAC performance analysis

## Slide 2: Analysis Goal
To analyze the 802.16t MAC layer in narrowband scenarios
To understand the tradeoffs between overhead, latency and throughput under diverse traffic
To inform potential MAC improvements, such as more efficient scheduling algorithms or reduced overhead in control frames

## Slide 3: Key analysis areas
MAC Efficiency: slot utilization; quantify scheduling overhead.
Diverse Traffic Testing: Simulate different traffic scenarios with different number of MSs with mixed demand.
Performance Measurement: Calculate average/max latency, deadline misses; slot usage and fairness
Frame-Level Scheduling Visualization: Track per frame allocations to locate source and reason for overhead and latencies

## Slide 4: Characteristics of railroad application traffic
Low data volume
  Most messages are short packets (20–500 bytes), but require timely and reliable delivery
Periodicity:
  Periodic telemetry (e.g., status, health) and event-driven alerts
  Long idle periods punctuated by bursts (e.g., fault reports, emergency commands, diagnostics)
Latency:
  Some messages are delay-tolerant, others safety-critical with strict latency (<100–200 ms)
Asymmetric:
  uplink usually higher than downlink

## Slide 5: MAC Controllable parameters and tradeoffs
BW Requests polling periodicity and scheduling cycle
  Polling too often consumes bandwidth; too infrequent leads to traffic starvation. Needs tuning per MS traffic class.
  CDMA based BW requests
Scheduling window: fixed / sliding; fixed size / adaptive size
Frame duration
Bulk vs. Request based
Prioritization and QoS enforcement
  Serving urgent traffic may starve low-priority MSs in tight bandwidth;
  Fairness mechanisms should be tuned for mission profile
MAPs vs dynamic allocations

## Slide 6: Analysis Tool
Non real time
  Time is simulated by slots
Runs on a single device
  Configurable PHY characteristics
  No real traffic communication

## Slide 7: Analysis Tool Inputs
PHY configuration
  Channel bandwidth, frame duration, UL/DL ratio
Number of MSs
Traffic profiles:
  Changing MCS profile
  Random error rate profile
  One or more Traffic Scenarios are defined to simulate realistic network activity
  A Traffic Scenario describes the transmission behavior of a group of MSs and consists of a mix of traffic patterns.
  Each Traffic Pattern is characterized by the following parameters:
    Traffic period and timing: interval between transmissions and the precise start time of the pattern.
    Data Packet size (fixed / random)
    Packet periodicity (fixed/random)
    QoS limitations

## Slide 8: Measurement outputs
Summary Measurements:
  Throughput
  Slots distribution: management (IR, PR, Req etc); data; unused
  Latency (average / max / restriction violations)
For deeper analysis:
  Frame by frame slots assignment visualization
Example of output for uplink scenario:
  Channel BW: 125 kHz; Frame duration 100 msec
  MS-1 to MS-4: 512 bytes every 500 msec, MCS 64QAM ¾
  MS-5 to MS-8: 67 bytes every 220-250 msec, MCS 16QAM ½
  MS-8 to MS-12: 75 bytes every 200 msec, MCS 64QAM ¾

## Slide 9: Example for Uplink Output
Average and Max Latency

## Slide 10: Per Frame Allocations
Frame |  | MS-1 |  |  |  | MS-2 |  |  |  | MS-3 |  |  |  | MS-4 |  |  |  | MS-5 |  |  |  | MS-6 |  | 
 |  | In | Data | Maint |  | In | Data | Maint |  | In | Data | Maint |  | In | Data | Maint |  | In | Data | Maint |  | In | Data | Maint
0 |  | 19 | 4 | 3 |  | 0 | 4 | 0 |  | 0 | 4 | 0 |  | 0 | 4 | 0 |  | 0 | 4 | 0 |  | 6 | 4 | 0
1 |  | 0 | 21 | 0 |  | 19 | 3 | 3 |  | 0 | 3 | 0 |  | 0 | 3 | 0 |  | 0 | 3 | 0 |  | 0 | 3 | 0
2 |  | 0 | 10 | 0 |  | 0 | 17 | 0 |  | 19 | 1 | 3 |  | 0 | 1 | 0 |  | 0 | 1 | 0 |  | 0 | 1 | 0
3 |  | 0 | 5 | 0 |  | 0 | 1 | 0 |  | 0 | 19 | 0 |  | 19 | 1 | 3 |  | 0 | 1 | 0 |  | 6 | 1 | 0
4 |  | 0 | 2 | 0 |  | 0 | 1 | 0 |  | 0 | 1 | 0 |  | 0 | 19 | 0 |  | 6 | 1 | 3 |  | 0 | 7 | 0
5 |  | 19 | 2 | 0 |  | 0 | 2 | 0 |  | 0 | 2 | 0 |  | 0 | 2 | 0 |  | 0 | 9 | 0 |  | 6 | 2 | 3
6 |  | 0 | 14 | 0 |  | 19 | 1 | 0 |  | 0 | 1 | 0 |  | 0 | 1 | 0 |  | 0 | 4 | 0 |  | 0 | 5 | 0
7 |  | 0 | 5 | 0 |  | 0 | 17 | 0 |  | 19 | 1 | 0 |  | 0 | 1 | 0 |  | 6 | 2 | 0 |  | 0 | 2 | 0
8 |  | 0 | 1 | 0 |  | 0 | 3 | 0 |  | 0 | 16 | 0 |  | 19 | 1 | 0 |  | 0 | 5 | 0 |  | 6 | 1 | 0
9 |  | 0 | 1 | 0 |  | 0 | 1 | 0 |  | 0 | 3 | 0 |  | 0 | 15 | 0 |  | 6 | 1 | 0 |  | 0 | 6 | 0