## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title : Proposals for Physical Layer (PHY) OQPSK extensions
Date Submitted : 2025-Sep-15
Source : Fabrice Portier, Guner Arslan, Mark Gorday (Silicon Labs), Thomas Almholt (TI)
[Email: portier@ieee.org]
[Email: talmholt@ti.com]
Abstract : Extensions to IEEE 802.15.4-2024 include not only waveform and range improvements but also a broader rationalization of bands and data rates in line with global regulations.
Purpose : Clarification and extension in range of OQPSK PHY
Notice : This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release : The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Outline
Introduction
OQPSK extensions – Bands vs Regulations (WW)
OQPSK extensions – Rates, BW, and Range
OQPSK extensions – Further opportunities
Conclusion

## Slide 3
Introduction
O-QPSK PHY in IEEE 802.15.4-2024 section 13
  Outdated bands and extra restrictions preventing from WW application
  PHY specifications interfering with local regulations – complex updates
  Non-flexible and complex combinations of datrarates, spreading, and regions
   simplify while extending range
OQPSK-LR
  Simple extension on the chip-rate to extend range with lower data rate
  Initially proposed by Henk, see previous presentations 15-24-0398-00-04ad-o-qpsk-lr-phy-for-sun, & evaluations in 15-25-0182, 15-25-0260…
   keep it simple with only 1 or 2 lower datarate
OQPSK shaping improvements ?
  Should we consider better shaping trade-offs (spectrum BW vs simple half-sine) for the extensions?

## Slide 4
OQPSK – Bands vs Regulations (WW)
Example limitations
  §13.2.2: for SubGHz OQPSK, Bitrate 250kbps is defined for NA (FCC bands) while 100kbps for Europe (ETSI)
  §13.3.1: The EU band is restricted to 868–868.6 MHz in the “requirements” section, which is outdated and unnecessarily narrow, as regulations now allow a wider range
Improvement opportunities: simplify ?
  If there is no strong rationale for including precise 'bands’ and ‘regions’ limitations directly in the “requirements” of IEEE PHY specifications
    Support Worldwide Operation of Existing PHYs/Spreading Configurations (including 250kbps and 100kbps)
    Remove restrictive band requirements from the core specification -- e.g. Could just define broad frequency application range (and could add an informative section in annex) and let regulatory bodies set limits (as is done in some LECIM sections) ?
    Propose simple combinations of chiprates, keeping the 2 current symbol-to-chip-mapping, avoiding regional restrictions

## Slide 5
Slide 5
OQPSK – Remove regulations
Below is a table form of what is in the current 802.15.4-2024 Section 13 specifications.
Proposal 1 is to simply remove regulation from this section entirely, this would leave 4 PHY’s. 2 data rates and 2 spreading factors.
Notes: Jul 12, 2010
Page 5

## Slide 6
OQPSK – Rates, BW, and Range
Option 2 is to add more scalability to the PHY.
Have a clear set of rates and spreading options to better align with the needs (regulation bandwidths, robustness, datarate…)
  We could consider datarates of {37.5,100,200,250} kbps using (16,4) and (32,4)-DSSS for each datarate across all bands
   Better use of defined bands/BW
   Higher flexibility and Range

## Slide 7
OQPSK – Further opportunities
Signal shaping
  Could we consider an optimization of the waveform if we define new rates ?
    shaping filter, trade-off between narrower “low-pass” filter & current “half-sine” shaping, e.g. α-half-sine (α≈1.5)
    with better OoB spectrum
    while keeping constant-envelope

## Slide 8
OQPSK – Explanation on FCC limits
  FCC limit is defined at -6dB down from peak when measured using 100KHz RBW on a spectrum analyzer.
  The spreadsheet is using a simple first order estimation of “Chip rate /1.23”, the exact BW measured using this technique is effected by additional filtering that may be present in an individual implementation.

## Slide 9
OQPSK – Explanation on ETSI limits
  ETSI limit is defined at 99% power bandwidth on a spectrum analyzer.
  The spreadsheet is using a simple first order estimation of “Chip rate * 1.19”, the exact BW measured using this technique is effected by additional filtering that may be present in an individual implementation.

## Slide 10
Current SUN-OQPSK table (backup)