## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Summary of Discussion on Merged baseline for SUN OFDM HR]
Date Submitted: 18 Sept 2025
Source: Hiroshi Harada (Kyoto University)
Address Yoshidahonmachi. Sakyo, Kyoto, 606-8501, Japan
Voice: +81-75-753-5317 , E-Mail: hiroshi.harada@i.kyoto-u.ac.jp
Re: [Wireless Next Generation, Long Range extension enhancements to 802.15.4-2020]
Abstract: The SUN OFDM HR (High Rate) proposed for 802.15.4ad in documents 15-25/0280r4 and 15-25/0392r0 has been organized. Based on these documents, the Next Step following the Hawaii meeting was discussed. At the Hawaii meeting, the proposal merging and the standard baseline were discussed among the proposers. This document is a summary of the discussion on SUN OFDM HR among these proposers. A part of this contribution supported from the commissioned research (No. JPJ012368C05101) by National Institute of Information and Communications Technology (NICT) , Japan is included.
Purpose:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary of Discussion on Merged Baseline for SUN OFDM High Rate (HR)
September 18 , 2025
Hiroshi Harada, Vice chair of 802.15.4ad (Kyoto University)

## Slide 3: Background
The SUN OFDM HR (High Rate) proposed for 802.15.4ad in documents 15-25/0280r4 and 15-25/0392r0 has been organized.
Based on these documents, the Next Step following the Hawaii meeting was discussed.
At the Hawaii meeting, the proposal merging and the standard baseline were discussed among the proposers.
This document is a summary of the discussion on SUN OFDM HR among these proposers.

## Slide 4: Current 802.15.4-2024 SUN-OFDM
 |  | Option1 | Option2 | Option3 | Option4
Channel spacing |  | 1200 kHz | 800 kHz | 400 kHz | 200 kHz
OFDM symbol duration |  | 120 μs |  |  | 
Subcarrier spacing |  | 31.25/3 kHz |  |  | 
DFT size |  | 128 | 64 | 32 | 16
Number of subcarriers |  | 104 | 52 | 26 | 14
Num. of data-subcarriers |  | 96 | 48 | 24 | 12
Primary modulation scheme |  | BPSK(MCS 0-1), QPSK(MCS 2-4), 16QAM(MCS5-6) |  |  | 
Coding Scheme and rate |  | Convolutional code (Constraint length: 7) Coding rate1/2 (MCS 0-3, 5), 3/4 (MCS 4,6) |  |  | 
Spreading factor |  | 4 (MCS 0), 2 (MCS1-2), 1(MCS 3-6) |  |  | 
Data rate for PSDU (kb/s) | MCS 0 | 100 | 50 | 25 | 12.5
 | MCS 1 | 200 | 100 | 50 | 25
 | MCS 2 | 400 | 200 | 100 | 50
 | MCS 3 | 800 | 400 | 200 | 100
 | MCS 4 | 1200 | 600 | 300 | 150
 | MCS 5 | 1600 | 800 | 400 | 200
 | MCS 6 | 2400 | 1200 | 600 | 300

## Slide 5: Two proposals
Proposal 1: Based on current OFDM, shorten the OFDM symbol period to one-third (40 us) .(TI and Kyoto Univ. 15-25/228r1 )
  Triple the OFDM subcarrier spacing
  Realize High definition video Transmission-based IoT
  Easy to implement from the existence chip (All MCSs except for subcarrier spacing are same)
Proposal 2: Add one MCS in the existence of SUN OFDM (Silab 15-25/479r0 and 15-23/389/r3)
  Add three options and one MCS (64QAM, R=3/4)
  Shorten the OFDM symbol period (80 us).

## Slide 6: Proposal 1: 802.15.4-2024 SUN-OFDM High Rate (HR) PHY(15-25/228r1)
 |  | Option1 | Option2 | Option3
Channel spacing |  | 4000 kHz | 2000 kHz | 1000 kHz
OFDM symbol duration |  | 40 μs | 40 | 
Subcarrier spacing |  | 31.25 kHz |  | 
DFT size |  | 128 | 64 | 32
Number of subcarriers |  | 104 | 52 | 26
Num. of data-subcarriers |  | 96 | 48 | 24
Primary modulation scheme |  | BPSK(MCS 0-1), QPSK(MCS 2-4), 16QAM(MCS5-6) |  | 
Coding Scheme and rate |  | Convolutional code (Constraint length: 7) Coding rate1/2 (MCS 0-3, 5), 3/4 (MCS 4,6) |  | 
Spreading factor |  | 4 (MCS 0), 2 (MCS1-2), 1(MCS 3-6) |  | 
Data rate for PSDU (kb/s) | MCS 0 | 300 | 150 | 75
 | MCS 1 | 600 | 300 | 150
 | MCS 2 | 1200 | 600 | 300
 | MCS 3 | 2400 | 1200 | 600
 | MCS 4 | 3600 | 1800 | 900
 | MCS 5 | 4800 | 2400 | 1200
 | MCS 6 | 7200 | 3600 | 1800
Same as existing SUN- OFDM
Proposal parts

## Slide 7: Proposal 2: 802.15.4-2024 SUN-OFDM High Rate (HR) PHY(15-25/479r0)
Same as existing SUN- OFDM
Proposal
64 QAM
R=3/4

## Slide 8: Future direction
There are three proposals
  1. Proposal 1
  2. Proposal 2
  3. Current SUN OFDM+ MCS7 (64QAM: R=3/4)
Which proposals we will take as baseline?
  Group agreed to take 1 and 3 as baseline.
Proposal 1 and Current SUN OFDM+ MCS7 (64QAM: R=3/4)
should be the baseline of the 802.15.4ad
Resolution