| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Clarification on FBIS initiation and termination in 16.1a Network |
| Date Submitted | 2012-01-17 |
| Source(s) | Anseok Lee, Eunkyung Kim, Sungcheol Chang, Sungkyung Kim, Won-Ik Kim, Miyoung Yun, Hyun Lee, Seokki Kim, Kwangjae Lim, Dongseung Kwon ETRI | E-mail: alee@etri.re.kr ekkim@etri.re.kr scchang@etri.re.kr |
| Re: | Call for Comments on the 802.16.1a Draft AWD, IEEE C802.16n-11/0033 |
| Abstract | This contribution provides modifications on FBIS initiation and termination for consistency with the MAC control messages in 16.1a network. |
| Purpose | To be discussed and adopted by 802.16 TGn |
| Copyright Policy | The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |
| Status | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |

# Clarification on FBIS initiation and termination in 16.1a Network

Anseok Lee, Eunkyung Kim, Sungcheol Chang, Sungkyung Kim, Won-Ik Kim, Miyoung Yun,

Hyun Lee, Seokki Kim, Kwangjae Lim, Dongseung Kwon

ETRI

# Introductions

This contribution provides modifications on FBIS initiation and termination for consistency with the MAC control messages in 16.1a network.

# Proposed Text for the 802.16.1a Amendment Working Document (AWD)

Note:

The text in BLACK color: the existing text in the 802.16.1a Amendment Draft Standard

The text in RED color: the removal of existing 802.16.1a Amendment Draft Standard Text

The text in BLUE color: the new text added to the 802.16.1a Amendment Draft Standard Text

[-------------------------------------------------Start of Text Proposal---------------------------------------------------]

## [Remedy1: Modify the following text of Section 6.12.7.3.1 in the 802.16.1a AWD]

##### 6.12.7.3.1 FBIS initiation

###### 6.12.7.3.1.1 Discovery of Designated FBIS HR-MS

The Degraded HR-BS which lost the wired backbone connection to the core network and does not have direct relay link to any of adjacent HR-BSs shall discover one or more HR-MSs which are able to establish Forwarding connections to an adjacent HR-BS. To initiate the scanning procedure, Degraded HR-BS shall transmit the unsolicited AAI-SCN-RSP message described in 6.2.3.15 to one or more sub-ordinate HR-MSs which have FBIS capability. The AAI-SCN-RSP message may contain ABS ID(s) of recommending HR-BS(s) if Degraded HR-BS has information of neighboring HR-BS(s).

The HR-MSs received the AAI-SCN-RSP message shall perform measurement of the neighboring HR-BSs for Designated FBIS HR-MS decision of the Degraded HR-BS. After completion of HR-MS scanning, HR-MSs shall and report the results to Degraded HR-BS by using AAI-SCN-REP message described in 6.2.3.16.

Based on the received measurement results in AAI-SCN-REP message transmitted by sub-ordinate HR-MSs, Degraded HR-BS shall select a Designated FBIS HR-MS among sub-ordinate HR-MSs which reported the measurement result using AAI-SCN-REP message and a Target HR-BS which is the Designated FBIS HR-MS having connectivity to.

###### 6.12.7.3.1.2 HO for FBIS

Degraded HR-BS shall command HO for FBIS by AAI-HO-CMD message described in 6.2.3.12 to Designated FBIS HR-MS. To command HO for FBIS, Degraded HR-BS shall set Mode to 0x100 and FBIS Mode to 0x00 of AAI-HO-CMD message. To command HO for FBIS, Degraded HR-BS shall set Mode to 0b11 and Extended HO Mode to 0b01 (FBIS Initiation) of AAI-HO-CMD message. The AAI-HO-CMD message may contain ABS ID of the Target HR-BS. Upon reception of AAI-HO-CMD message, Designated FBIS HR-MS shall perform the reentry procedure with the Target HR-BS.

In the reentry procedure, Designated FBIS HR-MS shall send AAI-RNG-REQ message with Ranging Purpose Indication = 0b1111 (Network reentry for FBIS operation). In the reentry procedure, Designated FBIS HR-MS shall send AAI-RNG-REQ message with Ranging Purpose Indication to 0b1110 and Extended Ranging Purpose Indication to 0b0001 (Network reentry for FBIS operation). In addition, Primary Serving ABS flag and Switched Access Mode shall also be included in the AAI-RNG-REQ message to Target HR-BS. The optimized HO may not be applied due to the failure of backbone connectivity at the Degraded HR-BS.

After completion of HO for FBIS, Designated FBIS HR-MS shall maintain the context of Degraded HR-BS and Degraded HR-BS shall also maintain the context of Designated FBIS HR-MS for data forwarding.

By the HO for FBIS, Designated FBIS HR-MS may have another serving HR-BS, Target HR-BS. The Primary Serving ABS flag indicates primary serving HR-BS which handle the services of Designated FBIS HR-MS. If the Primary Serving ABS flag is 0, Designated FBIS HR-MS sets Degraded HR-BS as its primary serving HR-BS. Otherwise, Designated FBIS HR-MS sets Target HR-BS as its primary serving HR-BS. In this case, the context related to the services of Designated FBIS HR-MS may be transferred to the Target HR-BS on the FBIS connection after FBIS connection is established. Another HR-BS other than primary serving HR-BS is secondary serving HR-BS for Designated FBIS HR-MS which is only for FBIS operation.

## [Remedy2: Modify the following text of Section 6.12.7.3.3 in the 802.16.1a AWD]

##### 6.12.7.3.3 FBIS termination

###### 6.12.7.3.3.1 FBIS termination initiated by Degraded HR-BS

FBIS operation may be terminated when the backbone connection of Degraded HR-BS is recovered or Degraded HR-BS has no connection to be forwarded by FBIS operation.

The backbone recovery of Degraded HR-BS may be notified to the Designated FBIS HR-MS by the AAI-MM-ADV message described in 6.2.3.65.1. When the Degraded HR-BS has no connection for its sub-ordinate stations, it may delete the FBIS connection by using DSD procedure. The Designated FBIS HR-MS which notified backbone recovery or performed DSD procedure with Degraded HR-BS shall start termination of connection with the secondary serving HR-BS (which does not handle the services for Designated FBIS HR-MS).

The termination of connection with the secondary serving HR-BS shall be initiated by transmitting AAI-HO-REQ message to the secondary serving HR-BS. Upon reception of AAI-HO-REQ message, the secondary serving HR-BS shall respond by AAI-HO-CMD message with Mode = 0b100 and FBIS Mode = 0b01 (FBIS termination). Upon reception of AAI-HO-REQ message, the secondary serving HR-BS shall respond by sending AAI-HO-CMD message with Mode = 0b11 and Extended HO Mode = 0b10 (FBIS termination). After sending AAI-HO-CMD message the secondary serving HR-BS shall start Resource Retain Time immediately and release connection information with the Designated FBIS HR-MS after Resource Retain Time expiration.

Designated FBIS HR-MS shall request Switched Access termination to its primary serving HR-BS by SAC signaling header with sub-type = 0b010. And the primary serving HR-BS shall respond Switched Access Termination Response by sending SAC signaling header with sub-type = 0b011. After transaction for termination of Switched Access, Designated FBIS HR-MS and the primary serving HR-BS shall stop the Switched Access and return to normal operation.

###### 6.12.7.3.3.2 FBIS termination by handover of Designated FBIS HR-MS

During the FBIS operation, any of two connections (connection with primary serving HR-BS or secondary serving HR-BS) may be lost due to the mobility of Designated FBIS HR-MS or other conditions. In this case, FBIS operation may need to be terminated and the Designated FBIS HR-MS may be served by another serving HR-BS.

Either two serving HR-BSs or Designated FBIS HR-MS may initiate handover during FBIS operation. If Designated FBIS HR-MS initiated HO, AAI-HO-REQ message described in 6.2.3.11 shall be transmitted to a serving HR-BS. In response to AAI-HO-REQ message from Designated FBIS HR-MS, the serving HR-BS transmits AAI-HO-CMD message with Mode = 0b100 and FBIS Mode = 0b01 (FBIS termination) to Designated FBIS HR-MS. If any of two serving HR-BS initiated HO, a serving HR-BS shall command HO by AAI-HO-CMD message with Mode = 0b100 and FBIS Mode = 0b01 (FBIS termination) to Designated FBIS HR-MS. In response to AAI-HO-REQ message from Designated FBIS HR-MS, the serving HR-BS transmits AAI-HO-CMD message with Mode = 0b11 and Extended HO Mode = 0b10 (FBIS termination) to Designated FBIS HR-MS. If any of two serving HR-BS initiated HO, a serving HR-BS shall command HO by AAI-HO-CMD message with Mode = 0b11 and Extended HO Mode = 0b10 (FBIS termination) to Designated FBIS HR-MS. In either case, a serving HR-BS shall start the Resource Retain Time immediately after sending AAI-HO-CMD message and release connection information with the Designated FBIS HR-MS after Resource Retain Time expiration.

Designated FBIS HR-MS shall request the FBIS termination to another serving HR-BS by SAC signaling header with sub-type = 0b010. In addition, and the another serving HR-BS shall respond Switched Access Termination Response by sending SAC signaling header with sub-type = 0b011. After transaction for termination of Switched Access, Designated FBIS HR-MS and the other serving HR-BS shall stop the Switched Access and return to normal operation.

[-------------------------------------------------End of Text Proposal----------------------------------------------------]

# References

[1] IEEE C802.16n-11/0186r3, “Forwarding Between Infrastructure Stations”

[2] IEEE C802.16n-11/0234r1, “Clarifications on FBIS in 16.1a Network”

[3] IEEE C802.16n-11/0235r2, “MAC Control Messages to support FBIS in 16.1a Network”

[4] IEEE 802.16n-11/0033, “WirelessMAN-Advanced Air Interface for Broadband Wireless Access Systems; Enhancements to Support Higher Reliability Operations.”

Title of Contribution

[Authors of Contribution]

[Affiliation of authors, per <http://standards.ieee.org/faqs/affiliationFAQ.html>]

# Template Instructions

This page provides instructions on using the template and submitting a contribution. Before submitting, delete these instructions or replace them with your text to be submitted.

# Document Format

Edit the cover page. Replace the square-bracketed sections with the correct text for your document. Eliminate the brackets. Leave the non-bracketed words on the cover page. Limit the cover page information to one page, shrinking the font if necessary.

Begin the main document with a page break after the cover page. Restate the document title and author name. You should use heading styles that support an outline view of the document.

# Header

The document number <http://ieee802.org/16/submit.html> goes in the upper right of the header. It takes the form “IEEE 802.16-YY-#####-RR-FFFF”, where:

• Every IEEE 802.16 document number begins with “IEEE 802.16-”.

• Following “IEEE 802.”, the remainder of the document number (“16-YY-#####-RR-FFFF”) is the Document Control Number (DCN), used by IEEE Mentor as the basis of the file name.

• “YY” represents the final two digits of the calendar year of original submission, as assigned by the IEEE Mentor documentation system.

• “####” represents the document serial number, as assigned by the IEEE Mentor documentation system. The serial number is uniquely assigned for each calendar year.

• “RR” represents the revision number, as assigned by the IEEE Mentor documentation system. The initial version of the document uses the revision number “00”.

• “FFFF” represents the Mentor “file code” <http://ieee802.org/16/submit.html>. It is selected by the submitter as the most appropriate identifier among the list of  IEEE 802.16 file codes in the IEEE Mentor documentation system.

# Fonts

Use only the fonts “Times” (or “Times New Roman”), “Arial” (or “Helvetica”),  and “Symbol,” since these fonts need not be embedded in PDF files. You may use other fonts only if necessary.

# Document Submission

To contribute a document to the IEEE 802.16 Working Group or a subgroup, create it using this template or another template at <http://ieee802.org/16/submit.html>. (If it cannot be put into one of the available formats, then create at least a cover page using an available template.) Submit the document following the instructions in the Call for Contributions or the IEEE 802.16 Document Submission Instructions <http://ieee802.org/16/submit.html>.