| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Clarification of AAI-MM-ADV message fields |
| Date Submitted | 2012-01-09 |
| Source(s) | Hyun Lee, Eunkyung Kim, Sungcheol Chang, Seokki Kim, Won-Ik Kim, Miyoung Yun, Sungkyung Kim, Chulsik Yoon, Kwangjae Lim ETRI | E-mail: hyunlee@etri.re.kr |
| Re: | “IEEE 802.16n-11/0033,” in response to the 802.16n (GRIDMAN) AWD Call for Comments |
| Abstract | Changes are provided to accommodate Correction on AAI-MM-ADV message fields |
| Purpose | To discuss and adopt the proposed text in the AWD of 802.16n |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Clarification of AAI-MM-ADV message fields

Hyun Lee, Eunkyung Kim, Sungcheol Chang, Seokki Kim, Won-Ik Kim, Miyoung Yun, Sungkyung Kim, Chulsik Yoon, Kwangjae Lim

ETRI

# Introductions

This contribution is intended to incorporate changes for correction on AAI-MM-ADV message fields. “Action Type == 0b1000” fields are duplicate. the duplicate fields should be deleted.

# References

- IEEE 802.16n-11/0033, “P802.16.1a Amendment Working Draft,” November 2011.

# Proposed Text for the 802.16n Amendment Working Document (AWD)

Note:

The text in BLACK color: the existing text in the 802.16n Amendment Draft Standard

The text in RED color: the removal of existing 802.16n Amendment Draft Standard Text

The text in BLUE color: the new text added to the 802.16n Amendment Draft Standard Text

[-------------------------------------------------Start of Text Proposal---------------------------------------------------]

[Remedy1: Modify the table in section 6.2.3.65.1 on page 59 of 802.16n AWD as follows.]

| Field | Size (bits) | Value/Description | Condition |
| --- | --- | --- | --- |
| } else if (Action Type == 0b0011) { |  |  | // power reduction |
| Tx Power Reduction | 10 | dB value of Tx power reduction | Mandatory |
| Expected time of power reduction | 8 | Expected resource adjustment time in units of frame |  |
| } else if (Action Type == 0b0100) { |  |  | // backhaul link down |
| Time of backhaul link down | 8 | Expected time when the backhaul link will be down in units of superframe | Optional |
| Expected time of backhaul link available | 8 | Expected time in unit of LSB of superframe when backhaul link will be available of HR-BS either itself or via neighbor HR-BS | Optional |
| } else if (Action Type == 0b0101) { |  |  | // backhaul link up |
| Expected time of backhaul link up | 8 | Expected time in unit of LSB of superframe when the HR-BS restarts service without any help of neighbor BS using relay link but the HR-BS’ backhaul link | Optional |
| }else if (Action Type == 0b0110){ |  |  | // FA change |
| FA index | 8 |  | Mandatory |
| Expected downtime of current FA | 8 | Expected current FA downtime in units of frame |  |
| Expected uptime of new FA | 8 | Expected uptime of new FA in units of superframe | Optional |
| } else if (Action Type == 0b0111) { |  |  | // multimode service end |
| Expected time of backhaul link up | 8 | Expected time in unit of LSB of superframe when the HR-MS release the multimode service and to allow subordinate MS to perform handover to other infrastructure | Optional |
| } |  |  |  |
| } else if (Action Type == 0b1000) { |  |  |  |
| Scan duration | 8 | Duration (in units of AAI subframe) of |  |

[Remedy2: Modify the table in section 6.2.3.65.1 on page 60 of 802.16n AWD as follows.]

| Field | Size (bits) | Value/Description | Condition |
| --- | --- | --- | --- |
|  |  | the requested scanning period. |  |
| Interleaving interval | 8 | The period of relay mode HR-MS’s active mode (in units of AAI subframes) that is interleaved between scan durations. |  |
| Start superframe index | 6 | Represents the 6 least significant bits of the absolute superframe index in which the first scanning interval starts. |  |
| Start frame index | 2 | Represents start frame number in the Start super frame number. 0b00: 1st frame in the super frame 0b01: 2nd frame in the super frame 0b10: 3rd frame in the super frame 0b11: 4th frame in the super frame |  |
| } |  |  |  |
| } else if (Action Type == 0b1000) { |  |  |  |
| Scan duration | 8 | Duration (in units of AAI subframe) of the requested scanning period. |  |
| Interleaving interval | 8 | The period of relay mode HR-MS’s active mode (in units of AAI subframes) that is interleaved between scan durations. |  |
| Start superframe index | 6 | Represents the 6 least significant bits of the absolute superframe index in which the first scanning interval starts. |  |
| Start frame index | 2 | Represents start frame number in the Start super frame number. 0b00: 1st frame in the super frame 0b01: 2nd frame in the super frame 0b10: 3rd frame in the super frame 0b11: 4th frame in the super frame |  |
| } |  |  |  |
| } else if (Action Type == 0b1001) { |  |  |  |

[-------------------------------------------------End of Text Proposal----------------------------------------------------]