## Slide 1: OFCOM Future Spectrum Requirements
Date: 2016-03-16
Authors:
Notes: July 2007

## Slide 2: Future spectrum requirements for mobile data, 5G and WRC-15/19: Where does IEEE 802 fit in? Presenter Andy Gowans input by F. Boccardi, M Paynter, S. Jones, S. Green

## Slide 3: Content Index
Future Mobile Data Use
Spectrum trends below 6GHz
Future studies in 5GHz
IEEE 802, 5G and above 6GHz use
Summary of Conclusions and points for future discussion
CONTENT

## Slide 4
Emerging services
Broadband++
high throughput, consistent QoE
M2M
low cost, low battery consumption
Critical
communications
low latency, high reliability
SPG
Technology
Source: modified from ITU
(1) Future Mobile Data Use
Notes: In this slides (inspired by a presentation given by Nokia) I summarised some of the services forecasted for the next 5-10 years. Some of the them are familiar (like broadband,…), some others are new. New emerging services include Car2X, Wireless factories and Robotics, M2M, Tactile Internet,…I divided them in three families.

## Slide 5
Technology trends
Broadband++
high throughput, consistent QoE
M2M
low cost, low battery consumption
Critical
communications
low latency, high reliability
SPG
Technology
5G
802.11p
LTE D2D / LTE-V
5G
/802.11ax
/LAA/LTE-U??
LTE /802.11ac
GSM/
LTE Cat 0/
GERAN/
5G/ Wi-Fi/Sigfox/
[…]
Bluetooth/ ZigBee/
satellites
(1) Future Mobile Data Use
Notes: For each family of services introduced in the previous slide, these are the related enabling technology standards. For broadband++ and critical communication it’s the usual battle between the two usual ecosystem (IEEE and 3GPPP). For M2M there is a lack of a dominant standard, and we will see in the next slides what this means in terms of technology adoption.
In the remaining part of this presentation I will spend a few slides on each of this families. Focus on questions rather than answers. And on the work needed to give good answers to those questions.

## Slide 6: Lack of spectrum should not inhibit the rapid rollout of new services
The approach….
Identify and prioritise potentially suitable bands
Monitor demand. market and technology developments, being ready to adapt our approach
Take a leading role in international harmonisation discussions
Take action resolving coexistence issues, awarding bands
The challenge: what will be the spectrum needs for mobile data in 10 years time?
(1) Future Mobile Data Use
Notes: What have we done to date:
Rapid growth in use of mobile broadband is set to continue
Network upgrades can help deal with growth, but spectrum is also needed

## Slide 7: Executive abstract
Future Mobile Data Use
Spectrum trends below 6GHz
  Licenced vs Unlicenced
  LAA/LTE-U vs WiFi
  Current and future Wi-Fi use
Future studies in 5GHz
IEEE 802, 5G and above 6GHz use
Conclusions and points for discussion
CONTENT

## Slide 8
700
>3.6GHz (harmonised)
2017-2022 Addition of 700 MHz, potentially 1427-1452 MHz, 3.6-3.8 GHz , 1492-1518 MHz
>2022 More uncertain potential addition of 3.8-4.2 GHz possibly tiered access ????
1.4GHz
2.3GHz
3.4GHz
2016 Addition of 1452-1492 MHz, 2.3 GHz, 3.4 GHz
1800
2.6GHz
800
900
2100
Today Existing mobile bands
Total downlink (scenarios)
Licenced spectrum availability in UK/Europe
(2) Spectrum trends below 6GHz
Notes: We have used our approach to identify potential new bands
We have considered:
Benefits-
Capacity
Coverage
Potential for international harmonisation
Costs and constraints of making available for sharing and re-purposing

## Slide 9: LE (802.11/15/16) spectrum available in UK
Frequency | Bandwidth | UK status | Indoor/Outdoor | Technical characteristics and capabilities
2.4 – 2.4835 GHz | 83.5 MHz | Licence Exempt | Indoor and outdoor | 100mW EIRP limit
5.15-5.35 GHz | 200 MHz | Licence Exempt | Indoor | 200mW EIRP limit DFS and TPC required in the upper half
5.470 – 5.725 GHz | 255 MHz | Licence Exempt | Indoor/Outdoor | 1W EIRP limit DFS and TPC required
5.825 – 5.875 GHz * | 150 MHz | Licence Exempt | Indoor/Outdoor | 25mW EIRP limit No DFS or TPC required
5.725 – 5850 GHz + | 105 MHz | Light licensed FWA use only | Outdoor | 4W EIRP limit DFS and TPC required
* Note: This is a generic SRD regulation not RLAN
+ Note: Not to use 20MHz between 5795 – 5815 MHz
(2) Spectrum trends below 6GHz

## Slide 10: In 2014 Wi-Fi traffic was 16 times cellular one
Chart: 
| 2014 Cisco VNI | 2014 IR
Wi-Fi | 1209 | 1440
Cellular | 74 | 44.3
UK Data carried in PB per month
Infrastructure Report, June 2014
Cisco VNI, 2014 average
602 MHz
available
602 MHz
available
538.5 MHz
available
538.5 MHz
available
(2) Spectrum trends below 6GHz
Notes: According to Cisco VNI, 3% of all IP traffic is carried by mobile, compared to 49% over Wi-Fi and 48% wired. This is despite Wi-Fi having access to less spectrum (538.5 MHz) compared to mobile (602 MHz).
Source: Cisco VNI, Office of National Statistics, Ofcom CMR 2014 and Ofcom Infrastructure Report 2014
Notes: Infrastructure Report data is based on June 2014 only and assumes 93% use wireless routers (CMR 2014).

## Slide 11: Wi-Fi vs cellular spectrum trends
One assumption that could be taken from this if we thought there was a need to keep the same proportion between licence and license-exempt spectrum in the future we should be adding approx. 600 MHz below 6GHz spectrum for Wi-Fi
Currently there is no evidence to back this assumption up or to quantify what the balance will be in the future. Do Wi-Fi alliance have similar info for other countries and do they think future studies are needed here!
Note: we don’t consider > 6 GHz spectrum
Chart: 
| 2015 | 2020 | 2025 | 2030
Cellular spectrum (MHz) | 770 | 1000 | 1261 | 1803
Wi-Fi spectrum (MHz) | 538 | 698.7013 | 881.0623 | 1259.7584
(2) Spectrum trends below 6GHz

## Slide 12
In previous studies and consultation in 2013/14 we looked at future wireless data uses including Wi-Fi.
  Responses indicated more contiguous channels with wide bandwidths (80 MHz and 160 MHz) mainly for indoor services
  need for more spectrum for lower bandwidth outdoor deployments with additional steps such as standardised protocols for coordination and restriction on use are needed
As a follow on we carried out a demand/supply study to assess the needs of further spectrum for Wi-Fi
  Varying results depending on assumptions used for demand and supply.
  Some scenarios showed a need of additional spectrum for all assumptions:
    Transport hubs
    Public event-type scenarios (e.g. stadium)
    To a lesser extent, terrace houses
We concluded that more work needs to be done on Wi-Fi spectrum requirements!
What about the other IEEE 802 standards and technologies spectrum requirements?
Wi-Fi demand trends
(2) Current Mobile Data Use in UK and possible spectrum trends.

## Slide 13
  Wi-Fi as standalone technology
    More effective MAC solutions (802.11ax) will allow a better performance in high-traffic conditions
    Wi-Fi features (e.g. Passpoint for cellular like experience, VoWiFi, etc.)
    Wi-Fi Direct (screen mirroring etc.)
    Low power/low data rate Wi-Fi for M2M and IoT (below 1GHz?)
  Wi-Fi LAA/LTE(U) as complementary technology
    Distributed SON algorithms will allow non-managed Wi-Fi deployments to have performance closer to managed ones
    Wi-Fi vs LAA
      will it increase traffic at 5GHz
      will it enable new opportunities for broadband Wi-Fi operators
        E.g.: mobility and wide-area support
    3G/4G/5G Interworking features?
      Yes for LAA, What about W-Fi?
  What are the implications of all these changes on future Wi-Fi spectrum needs?
Wi-Fi/LAA/LTE(U) technology trends
(2) Spectrum trends below 6GHz

## Slide 14
Ofcom initial views:
  Competition is a positive thing for consumers and LAA/LTE(U) could be good for the market.
  However, it is not clear what kind of effect the introduction of LAA/LTE(U) will have on current Wi-Fi users, that is why, in order to protect consumers, we support the work to develop fair and equitable sharing rules.
  In Europe the ETSI HS standard is right place to do this work and we are participating in ETSI BRAN.
  There needs to be studies to asses the impact of LAA/LTE-U use on future spectrum requirements and sharing with other services in 5GHz extension bands.
Some views on LAA/LTE-U vs Wi-Fi
(2) Spectrum trends below 6GHz
Notes: Questions for LAA/LTE-U
  Will LAA/LTE-U be disruptive to incumbent technologies and services?
  Will LAA/ULTE change the future usage profile (power and bandwidth) of the current bands Wi-Fi use? If Yes
    What effect will it have on sharing with incumbents?
    What effect will it have on the share of the markets?
    Which Wi-Fi markets will LAA/LTE-U address?

## Slide 15
BIG ?
What are the IEEE802 industry’s future spectrum needs?
(2) Current Mobile Data Use in UK and possible spectrum trends.

## Slide 16: Executive abstract
Future Mobile Data Use
Spectrum trends below 6GHz
Future studies in 5GHz
  UK/Europe vs US allocations in 5GHz
  Studies from WRC-15 & EU mandate process
  WRC-19 proposals and studies
IEEE802, 5G and above 6GHz use
Conclusions and points for discussion
CONTENT

## Slide 17: Previous Studies
Under WRC-15 AG 1.1 and EU Mandate candidate bands studied:
  5350 – 5470 MHz
    Current 5GHz RLAN mitigations do not make sharing feasible
    Studies on additional mitigation techniques not agreed
  5725 – 5850 MHz
    No conclusions to studies
    Some studies looking at enhanced DFS to protect Frequency Hopping radar.
    RLAN use already in each of the ITU-R Regions, regulations vary.
  5850 – 5925 MHz
    Already a primary mobile allocation in the band
    No studies carried out as part of WRC-15 period
Possible IMT allocation 5925 – 6425 MHz
  indicated that low power indoor use by IMT may be feasible (indoor 10mW?)
(3) Future studies in 5GHz

## Slide 18
 | Power |  | Indoor / Outdoor |  | Fixed / Mobile |  | DFS / TPC |  | EU/CEPT Regs | 
 | UK | USA | UK | USA | UK | USA | UK | USA | EU | CEPT
5150 to 5250 | Low | High | Indoor | Indoor & outdoor | Fixed & mobile | Fixed & mobile | No | No | Yes | Yes
5250 to 5350 | Low | Medium | Indoor | Indoor & outdoor | Fixed & mobile | Fixed & mobile | Yes | Yes | Yes | Yes
5470 to 5725 | Medium | Medium | Indoor & outdoor | Indoor & outdoor | Fixed & mobile | Fixed & mobile | Yes* | Yes† | Yes | Yes
5725 to 5850 | High (BFWA) | High | Indoor & outdoor | Indoor & outdoor | Fixed only | Fixed & mobile | Yes | No | No | Yes
* With longer initial start up time when co-channel with 5.6 to 5.65 GHz weather radars
† 5.6 to 5.65 GHz “to be avoided” whilst FCC is trying to introduce rules banning firmware mods
Summary current UK/EU/CEPT vs. USA Regs.
(3) Future studies in 5GHz

## Slide 19: WRC-19 proposals for Future Agenda item on RLANs
CITEL proposal
  Looking for RLAN studies and possible allocation in the 5350-5470 MHz band only
UK backed European MCP
  to study and assess the 5 GHz WAS (incl. RLAN) operational and spectrum requirements over the whole range 5 150-5 925 MHz
  to study the band 5 350-5 470 MHz and 5725 – 5850 MHz as potential frequency bands for WAS (incl. RLAN) operations.
  to study the bands 5150 – 5350 MHz and 5 850-5 925 MHz as potential frequency bands for outdoor WAS (incl. RLAN) operations
Possible Russian proposal to study above 5925 MHz
  To study mobile RLAN or IMT use in the 5925 – 6700MHz band
Outcome was a combination of the above.
(3) Future studies in 5GHz

## Slide 20: WRC-19 Agenda Item 1.16 on 5GHz RLANs What does it Cover?
Resolution 239 : invites ITU‑R to conduct and complete the following:
to study WAS/RLAN technical characteristics and operational requirements in the 5 GHz frequency range;
NOTE: not only looking at spectrum requirements and looks at whole 5GHz range!!!
b) to conduct studies with a view to identify potential WAS/RLAN mitigation techniques to facilitate sharing with incumbent systems in the frequency bands 5 150-5 350 MHz, 5 350-5 470 MHz, 5 725-5 850 MHz and 5 850- 5 925 MHz, while ensuring the protection of incumbent services including their current and planned use;
NOTE: This does not include the 5470 - 5725 MHz range!!!
to perform sharing and compatibility studies between WAS/RLAN applications and incumbent services in the frequency band 5 150-5 350 MHz with the possibility of enabling outdoor WAS/RLAN operations including possible associated conditions;
NOTE: This limits the scope of the studies to looking at possible outdoor use!!!
(3) Future studies in 5GHz

## Slide 21: WRC-19 Agenda Item 1.16 on 5GHz RLANs What does it Cover?
Resolution 239 : invites ITU‑R to conduct and complete the following:
to conduct further sharing and compatibility studies between WAS/RLAN applications and incumbent services addressing:
i) whether any additional mitigation techniques in the frequency band 5 350-5 470 MHz beyond those analysed in the studies referred to in recognizing a) would provide coexistence between WAS/RLAN systems and EESS (active) and SRS (active) systems;
NOTE: This is to concentrate studies on new mitigation techniques not existing ones!!!
ii) whether any mitigation techniques in the frequency band 5 350-5 470 MHz would provide compatibility between WAS/RLAN systems and radio determination systems;
NOTE: This enables existing mitigation techniques plus any new mitigation techniques to be studied!!!
iii) whether the results of studies under points i) and ii) would enable an allocation of the frequency band 5 350-5 470 MHz to the mobile service with a view to accommodating WAS/RLAN use;NOTE: There is currently no primary mobile allocation in this band.
(3) Future studies in 5GHz

## Slide 22
Resolution 239 covers the following: invites ITU‑R to conduct and complete the following in time for WRC‑19:
to also conduct detailed sharing and compatibility studies, including mitigation techniques, between WAS/RLAN and incumbent services in the frequency band 5 725- 5 850 MHz with a view to enabling a mobile service allocation to accommodate WAS/RLAN use;
NOTE: There is no current allocation for mobile, studies could use existing mitigation techniques from other bands and/or any new mitigation techniques to be studied!!!
to also conduct detailed sharing and compatibility studies, including mitigation techniques, between WAS/RLAN and incumbent services in the frequency band 5 850-5 925 MHz with a view to accommodating WAS/RLAN use under the existing primary mobile service allocation while not imposing any additional constraints on the existing services,
NOTE: This enables existing mitigation techniques plus any new mitigation techniques to be studied!!!
(3) Future studies in 5GHz
WRC-19 Agenda Item 1.16 on 5GHz RLANs What does it Cover?

## Slide 23: 5GHz spectrum allocation
5.0 | 5.025 | 5.05 | 5.075 | 5.1 | 5.125 | 5.15 | 5.175 | 5.2 | 5.225 | 5.25 | 5.275 | 5.3 | 5.325 | 5.35 | 5.375 | 5.4 | 5.425 | 5.45 | 5.475
 |  |  |  |  |  | Satellite |  |  |  | Earth Exploration Satellite Service and Space Research |  |  |  |  |  |  |  |  | 
Aeronautical Navigation Aid System |  |  |  |  |  |  |  |  |  |  |  |  |  | Aircraft |  |  |  |  | 
MOD |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | Wi-Fi indoor fixed and mobile |  |  |  |  |  |  |  |  |  |  |  |  | 
5.5 | 5.525 | 5.55 | 5.575 | 5.6 | 5.625 | 5.65 | 5.675 | 5.7 | 5.725 | 5.750 | 5.775 | 5.8 | 5.825 | 5.85 | 5.875 | 5.9 | 5.925 | 5.95 | 5.975
 |  |  | Amateur Radio |  |  |  |  |  |  |  | Road Tolling 5795 – 5815 MHz |  | A. R. |  | Intelligent Transport Services (30 MHz Safety Related 5875 – 5905 MHz) |  |  |  | 
 |  |  |  | MET Office |  | Space Research |  |  | Satellite E-S (Region 1 only up to 5850 MHz Worldwide up to 6700 MHz) |  |  |  |  |  |  |  |  |  | 
PMSE |  |  |  |  |  |  | PMSE |  |  |  | PMSE |  |  | PMSE |  |  | FIXED up to 6700 MHz |  | 
MOD |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Wi-Fi indoor and outdoor fixed and mobile |  |  |  |  |  |  |  |  | Wi-Fi indoor and outdoor fixed |  |  |  |  | PRIMARY MOBILE ALLOCATION UP TO 6700 MHz |  |  |  |  | 
Feeder links, N-GSO, used by Globalstar
SARs
(3) Future studies in 5GHz

## Slide 24: Opportunities/challenges 5150 – 5250 MHz:
RLAN vs MSS feeder links
Opportunities
Changing rules in 100 MHz of spectrum to allow for
  Outdoor mobile and fixed access
No DFS required in this band
Possibility for worldwide allocation with relaxed limits similar to US rules.
Globalstar are currently the only MSS operator in the band and does not appear to be plans for other operators in the band
Challenges
  There is a possible interference risk to MSS feeder links
  US Regulations based on acceptance of possible increased interference and monitoring of interference to satellites by Globalstar. It may not be possible to do this at international level.
  Original studies were conservative and assumed a max limit where interference was unlikely to occur, will using a less conservative limit allow higher powers and protect the actual satellite operations.
  Likely to be a big range (30dB) in the study results unless more evidence is provided to address the known unknowns in aggregate interference studies (e.g. building losses, activity factors, antenna discrimination etc.)
(3) Future studies in 5GHz

## Slide 25: Opportunities/challenges 5250 – 5350 MHz:
RLAN vs EESS/Radiolocation
Opportunities
Changing rules in 100 MHz of spectrum to allow higher power for
  Outdoor mobile and fixed access
No changes envisaged to current DFS rules already required in this band
Possibility for worldwide allocation with relaxed limits similar to US rules.
Reduced EESS operations (i.e. No SARs) in this band currently and does not appear to be any future plans for SAR operations in the band
Challenges
  There is a possibility that there is still an interference risk to other EESS (Altimeters/Scatterometers) operations in the band
  Not clear if EESS community is willing to give up on SAR operations in the band and likely to depend upon studies and protection in 5350 – 5470 MHz
  Likely to be a big range (30dB) in the study results for EESS unless more evidence is provided to address the known unknowns in aggregate interference studies (e.g. building losses, activity factors, antenna discrimination etc.)
  Not clear if radiolocation community will try to change DFS rules in the band to include FH radar.
(3) Future studies in 5GHz

## Slide 26: Opportunities/challenges 5350 – 5470 MHz:
RLAN vs EESS/Radiolocation (including Aero)
Opportunities
To allow new worldwide primary mobile allocation of 120 MHz of spectrum for RLANs
New additional mitigation techniques are already being studied within ITU such as geo-location, enhanced DFS, dedicated sensors etc..
Previous studies show may be possible to allow lower power with minimal mitigation techniques.
Challenges
  Previous studies showed that sharing is not feasible with EESS (SAR) and FH radar operations in the band without additional mitigation techniques being applied
  Changes envisaged to provide enhancements to current DFS rules used in other bands to detect FH radar are adding further complexity to DFS algorithms.
  All of the additional mitigation techniques being looked at to provide protection to incumbents from higher power Wi-Fi result in a certain percentage of Wi-Fi downtime.
  Not clear if EESS community is able to provide or be able to manage internationally all of the information required to minimise RLAN downtime.
  It will be significant challenge to provide protection for Aeronautical radar operating in this band.
  All of the additional mitigations being suggested for higher power Wi-Fi use are either new types of mitigation or not been used on an international basis for the protection of services.
(3) Future studies in 5GHz

## Slide 27: Opportunities/challenges 5725 – 5850 MHz:
RLAN vs FSS/Radiolocation/Road Tolling
Opportunities
To allow new worldwide primary mobile allocation of 125 MHz of spectrum with higher power for
  Outdoor mobile and fixed access
No DFS rules required in a number of countries due to ISM status of the band
Possibility for worldwide allocation with relaxed limits similar to current rules in a number of countries.
FSS operations in this band are only in Region 1 so no global FSS footprints in the band.
Road tolling only in Europe/Japan? in this band
Challenges
  There is a possibility that there is still an interference risk to FSS operations in the band. Likely to be a big range (30dB) in the study results unless more evidence is provided to address the known unknowns in aggregate interference studies (e.g. building losses, activity factors, antenna discrimination etc.)
  Not clear how radiolocation community will approach protection requirements for studies when taking account of ISM designation in the band.
  Currently different national regulations across the world and not clear if this will result in one set of global regulations.
  Will need additional mitigation techniques to protect road tolling in Europe.
(3) Future studies in 5GHz

## Slide 28: Opportunities/challenges 5850 – 5925 MHz:
RLAN vs FSS/ITS
Opportunities
To use existing worldwide primary mobile allocation of 75 MHz of spectrum with higher power for
  Outdoor mobile and fixed access
No sharing with radar so no DFS required in the band
ITS are using 802.11 technologies in the band.
Challenges
  There is a possibility that there is still an interference risk to FSS operations in the band. Likely to be a big range (30dB) in the study results unless more evidence is provided to address the known unknowns in aggregate interference studies (e.g. building losses, activity factors, antenna discrimination etc)
  FSS operations are worldwide in this band so there may be more stringent protection requirements
  Not clear how ITS community or regulators will approach protection requirements for studies.
  Also proposed ITS agenda item as currently different national regulations across the world for ITS and not clear if this will result in one set of global allocations for ITS.
(3) Future studies in 5GHz

## Slide 29: Opportunities/challenges 5850 – 5925 MHz:
RLAN vs FSS/ITS
Opportunities
To use existing worldwide primary mobile allocation of 75 MHz of spectrum with higher power for
  Outdoor mobile and fixed access
No sharing with radar so no DFS required in the band
ITS are using 802.11 technologies in the band.
Challenges
  There is a possibility that there is still an interference risk to FSS operations in the band. Likely to be a big range (30dB) in the study results unless more evidence is provided to address the known unknowns in aggregate interference studies (e.g. building losses, activity factors, antenna discrimination etc)
  FSS operations are worldwide in this band so there may be more stringent protection requirements
  Not clear how ITS community or regulators will approach protection requirements for studies.
  Also proposed ITS agenda item as currently different national regulations across the world for ITS and not clear if this will result in one set of global allocations for ITS.
(3) Future studies in 5GHz

## Slide 30: Opportunities/challenges general:
How do we address the Known/Unknowns?
Challenges
Large ranges in Aggregate interference studies
  Airborne Measurement programmes to compare the models being used with actual measurements. Needs to be comprehensive enough to cover different times of the day, geographic zones, different bands (including 2.4GHz)
  More appropriate indoor vs outdoor, small cell, building loss prorogation models towards satellites and other airborne uses could be developed but would probably need some measurement campaigns
  More information on busy hours (including bouncing busy hour across the globe) and likely activity factors for Home, Business and public access models for Urban, Sub-urban and rural environments.
  Additional mitigation techniques studies
  Look more at the real effect of interference on services at the protocol level and prove compatibility through simulations and real world testing.(e.g. ITS vs RLAN, RLAN vs RTTT etc)
  Look at simple mitigation techniques that could be employed today ( limitation on conducted power levels)
  Look at accepting lower power levels in line with what the vast majority of the market actually uses today and are likely to use in the future (see next slide).
  Look at the effect and possible regulatory constraints that could be applied with regards to use of smart antenna technologies (multi-mimo, beamforming etc).
(3) Future studies in 5GHz

## Slide 31: Opportunities/challenges 5925 – 64251 MHz: No support to be part of WRC-19 agenda item
RLAN vs FSS/FS
Opportunities
To use existing worldwide primary mobile allocation of up to 500 MHz of spectrum with higher power for
  Outdoor mobile and fixed access
No DFS anticipated in this band.
Fixed links in the band are using FDD duplexing so may be opportunities to use centre gaps
The larger the amount of spectrum available to Wi-FI the better the aggregate sharing environment will be across the whole 5-6 GHz range
Challenges
  Possibility of an interference risk to FS and FSS operations in the band. Likely to be a big range (30dB) in the study results unless more evidence is provided to address the known unknowns in aggregate interference studies (e.g. building losses, activity factors, antenna discrimination etc.)
  FSS operators are worldwide in this band and lobbied for countries to object strongly to include this band in the WRC-19 studies
  Currently used by Fixed Services across Europe, not clear what FS usage in other parts of the world is like.
  Recent ITU studies which looked at possible sharing between IMT and FSS and FS in the band proposed very conservative limits
(3) Future studies in 5GHz
1 - Ofcom is not proposing this band for future studies to look at RLAN /Incumbent sharing but it is included for completeness

## Slide 32: Wi-Fi topology/usage and spectrum studies?
Wi-Fi markets today and the future
  What’s the balance of indoor vs outdoor?
  What’s the balance of high power vs low power?
  What is the balance of bandwidth use in these categories?
  The table below shows powers from CEPT Work in 5GHz
Outdoor higher power Wi-Fi seems to be a niche market (around 1%) so should we look at future allocations based on mass market Wi-Fi use?
A picture of the different Wi-Fi market needs to built from the bottom up using realistic devices usage scenarios taking account of the bullets above.
Tx power e.i.r.p. | 1W (directional) | 1 W (omni) | 200mW (omni) | 80mW (omni) | 50mW (omni) | 25mW (omni) | all
indoor | 0% | 0% | 18% | 25.6% | 14.2% | 36.9% | 94.7%
outdoor | 0.10% | 0.20% | 0.95% | 1.35% | 0.75% | 1.95% | 5.3%
(3) Future studies in 5GHz

## Slide 33
BIG ?
How much industry support and resource will be available for the 5GHz studies?
(3) Future studies in 5GHz

## Slide 34: Executive abstract
Future Mobile Data Use
Spectrum trends below 6GHz
Future studies in 5GHz
Wi-Fi, 5G and above 6GHz use
  5G
  Possible future WRC-19 agenda item above 6GHz
  Wi-Fi in 5G and 60GHz
Conclusions and points for discussion
CONTENT

## Slide 35: 5G use cases: evolution of current and new use cases – Wireless access to more intelligent infrastructure
Source: NGMN 5G white paper, executive version
(4) Wi-Fi, 5G and above 6GHz use

## Slide 36: Wireless 5G technology: evolution of current standards and integration with new technologies
Wi-Fi
2000
2010
2020
2030
4G
mm-Wave
Low-cost wide area M2M
5G
Low-latency ultra-rel. M2M
(4) Wi-Fi, 5G and above 6GHz use

## Slide 37: Impact of emerging technologies on spectrum
Technology | Spectrum |  | 
 |  | Incremental | Disruptive
 | Evolutioanry |  | 
 | Radical |  | 
LAA
MMW
access
Low-latency/
high-reliability
M2M
Full duplex
access
Low-cost,
high volume
M2M
new
waveforms
Massive
MIMO
(<6GHz)

## Slide 38: Mm-Wave: technical assessment
6GHz
100GHz
Propagation loss (downlink) | 
Propagation loss (uplink) | 
Prop. loss (non-precoded channels) | 
Rain attenuation | 
Object blockage | 
Interference | 
Sharing possibilities (beamwidth) | 
Beamforming | 
Channel estimation | 
60GHz

## Slide 39: Wide area M2M: is there the need for a completely new design?
Extended from P. Popovski, “Ultra-Reliable communications in 5G Wireless Systems”, Arxiv, 2014.
# users
data
rate
R2: Ultra-dense
Networks (Mm-Wave)
R1: 4G extensions
Low cost M2M
R4: Low-lat.
ultra-rel M2M
R3: Low cost
Massive
M2M
Physically
impossible
Cellular systems have been traditionally designed to work in region R1 and R2, i.e. to maximise the throughput for a given amount of devices
Optimising the system for Regions R3 and R4 might lead to completely different designs
  E.g. coupling between data and control plane, new types of nodes, transmissions optimised for short data blocks, new waveforms,…

## Slide 40
2013
2014
2015
2016
2017
2018
2019
2020
NGMN white paper ready (Feb. – Mar.)
3GPP
Rel. 13
2021
2022
3GPP Rel. 14-15
3GPP Rel. 16 /
implementation and trials
First major deployments
expected
3GPP SA1 study item (Feb.)
Rel. 14 to start major works on 5G (Q4 2015 or Q1 2016)
Timeline
WRC 15
WRC 19

## Slide 41: Mm-Wave: WRC-19 future agenda item
Bands marked in red were proposed for studies by five regions
(4) Wi-Fi, 5G and above 6GHz use

## Slide 42
NGMN 5G is not only about mm-Wave or even wireless its about easy access to infrastructure for wireless devices
Frequencies below 6GHz are very important
  for coverage
  to provide a consistent QoS across time and space
  to support wide-area M2M
  to support ultra-reliable services
5G will be a network for communication and control
  can we use unlicensed spectrum for e.g. car-2-x?
  licensed but not dedicated?
What will be the role of wireless IEEE 802 standards be in 5G?
What about the fixed networks interface with the wireless networks (e.g. higher layer IEEE 802 standards?)
(4) Wi-Fi, 5G and above 6GHz use

## Slide 43
  Wi-Fi in 60GHz
    There is 9GHz (57 – 66GHz) available in Europe with various restrictions.
    Different amounts available in the band elsewhere in the world. What are the IEEE 802 plans for :
      use of the 60GHz band?
      Target markets for 60GHz products?
      Worldwide allocation of mmWave bands to be allocated in ITU under WRC-19 AI 1.13? Where do 802 fit into the picture?
  WRC -19 agenda item
    In support of 5G projects the possible agenda item will be targeting a number of bands. What do IEEE 802:
      do to engage with 5G projects?
      think the balance between LE vs licenced be in mmWave bands?
      about possible new allocations in the mmWave band for LE use?
Mm-Wave: Where does IEEE 802 fit in?
(4) Wi-Fi, 5G and above 6GHz use

## Slide 44
BIG ?
Where does IEEE 802 fit into 5G and mmWave use?
(4) Wi-Fi, 5G and above 6GHz use

## Slide 45: Executive abstract
Future Mobile Data Use
Spectrum trends below 6GHz
Future studies in 5GHz
Wi-Fi, 5G and above 6GHz use
Conclusions and points for discussion
CONTENT

## Slide 46: Conclusions on future mobile use and spectrum demand below 6GHz
Studies indicate the demand for wireless data services is only going to increase in the future, IEEE 802 technologies will play an important part in that future!
802/Wi-Fi sits alongside mobile networks as a way of delivering data to consumers and there will be a continued increasing demand for IEEE 802 services in the future.
It is not clear what the future balance of exempt vs licenced for wireless data traffic will be. Evidence is needed from IEEE802 to support spectrum estimates!
We support the introduction of LAA/LTE(U) assuming fair and equitable sharing protocols has been implemented in order to protect consumers.
BIG ?
What are the IEEE 802 industry’s future spectrum needs?
(5) Conclusions

## Slide 47: Conclusions on 5GHz studies
5 GHz bands will be an important factor in meeting the increasing data demand for LE services, but expansion into additional parts of the 5 GHz spectrum is not guaranteed. More evidence on future spectrum needs is needed from Wi-Fi industry!
Substantial Regulator and Wi-Fi community resources will be needed for studies in 5GHz bands.
Mitigation techniques to enable new Wi-Fi spectrum allocations are going to be difficult and time consuming to get approval for.
Spectrum requirement studies may have to be more focussed in the areas where the most beneficial future demand will be.
BIG ?
How much industry support and resource will be available for the 5GHz studies?
(5) Conclusions

## Slide 48: Conclusions on 5G and mmWave bands
5G is about integrating a number of services and technology into an overall network platform.
5G is not only about mm-wave bands, frequencies below 6GHz will be important for 5G use cases.
Future WRC-19 agenda (1.13) for mmWave bands is being driven by requirements for future LTE licenced spectrum requirements coming out of the 5G work. Where do IEEE802 fit into this?
It is not clear at this time what the plans of the IEEE 802 is for the 60GHz band and it is not clear where this fits into the 5G thinking.
It is not clear if there is a need to look for more LE spectrum in the mmWave bands beyond current 60GHz.
BIG ?
Where does IEEE 802 fit into 5G and mmWave use?
(5) Conclusions

## Slide 49
Thanks Any Questions!
Contact Details:
Andy Gowans OFCOM UK
Email : Andrew.gowans@ofcom.org.uk