## Slide 1: IEEE 802.18 Viewpoints on WRC-19 Agenda Items
Date: 01 May 2017
Revised: 05 April 2018
Authors:

## Slide 2: Introduction
IEEE 802 has been asked by regulators and other stakeholders for our views on certain WRC-19 Agenda Items (AI).
This document provides viewpoints for the Agenda Items that relate to current IEEE 802 standards activity.
This document represents the views of IEEE 802. It does not necessarily represent the views of the IEEE as a whole or the IEEE Standards Association as a whole.

## Slide 3: AI 1.12 ITS Harmonization
to consider possible global or regional harmonized frequency bands, to the maximum extent possible, for the implementation of evolving Intelligent Transport Systems (ITS) under existing mobile-service allocations, in accordance with Resolution COM6/13 (WRC-15);
IEEE 802.11 has provided the wireless standard (IEEE Std 802.11p-2010) that is the basis for much of the Intelligent Transport Systems (ITS) Vehicle-to-Vehicle (V2V) and Vehicle-to-Infrastructure (V2I) technologies. We believe that this technology is capable of sharing the 5850-5925 MHz band with other unlicensed applications. We also understand that global harmonization of the technology is a notable effort that would enable technology improvements and cost reductions to better address rapid adoption to meet the ITS safety goals, an effort we would support.

## Slide 4: AI 1.13 IMT
to consider identification of frequency bands for the future development of International Mobile Telecommunications (IMT), including possible additional allocations to the mobile service on a primary basis, in accordance with Resolution COM6/20 (WRC-15);
Due to the following developments, IEEE 802 recommends that WRC-19 not consider 66-76 GHz for IMT identification.
  On July 14, 2016, FCC published a Report and Order and Further Notice of Proposed Rulemaking (FCC 16-89) [https://apps.fcc.gov/edocs_public/attachmatch/FCC-16-89A1.pdf] to adopt 64-71 GHz band for License Exempt operation.
  In January 2018, the ITU-R published Recommendation M.2003-2 [https://www.itu.int/rec/R-REC-M.2003-2-201801-I/en] wherein this band was indicated for Multigigabit Wireless Systems. This facilitates the introduction of IEEE 802 technologies that are capable of supporting 5G use cases under the existing Mobile Allocation.
  In February 2018, the Radio Spectrum Policy Group of the European Union (RSPG) published their Second Opinion on 5G [http://rspg-spectrum.eu/2018/02/] in which they recommended making this band available on a general authorized access basis.
Given these facts, we believe that a wide variety of 5G services and use-cases will be deployed in this band globally without the need for an IMT identification. In fact, IMT identification could bar some key 5G technologies from operating in this band.

## Slide 5: AI 1.15 275 GHz
to consider identification of frequency bands for use by administrations for the land-mobile and fixed services applications operating in the frequency range 275-450 GHz, in accordance with Resolution COM6/14 (WRC-15);
The recently published Std. IEEE 802.15.3d-2017 targets point-to-point links in the frequency range of 252 to 325 GHz with data rates ranging from 1 to 100 Gb/s. The application scenarios comprise wireless backhaul and fronthaul links, kiosk downloading, reconfigurable wireless links for data centers in addition to fibers and intra-device communications. IEEE 802 especially supports the identification of the frequency bands 275 GHz to 325 GHz for license-exempt active services such as THz communications.
Higher frequency bands beyond 325 GHz, e. g. up to 450 GHz, are highly appreciated for future wireless communication applications. No activity toward a new standard at these higher frequencies has been formed yet, because the technology at 300 GHz seemed most promising in 2014 when the project for the first standard in the THz range was initiated. However this may change in the future.

## Slide 6: AI 1.16 5 GHz
to consider issues related to wireless access systems, including radio local area networks (WAS/RLAN), in the frequency bands between 5 150 MHz and 5 925 MHz, and take the appropriate regulatory actions, including additional spectrum allocations to the mobile service, in accordance with Resolution COM6/22 (WRC-15);
Since the 1990s, IEEE 802 has been actively developing standards for Wireless LAN technologies that operate in the 5 GHz bands. Among these is IEEE 802.11, which is the basis for Wi-Fi, the most successful, most used and most demanded 5 GHz wireless technology. IEEE 802.11 is carrying the vast majority of wireless internet traffic and is essential for commercial services, education, communications and social interactions, creating industries and providing jobs and economic growth around the world.
IEEE 802 recommends that any regulatory action should not disadvantage any IEEE 802 standard or add any additional regulatory burdens for its use of the 5 GHz bands.

## Slide 7: AI 9.1 Issue 9.1.5
to investigate the technical and regulatory impacts on the services referred to in Nos. 5.447F and 5.450A that would result from referencing Recommendation ITU-R M.1638-1 in place of Recommendation ITU-R M.1638-0 in those footnotes, while ensuring that no undue constraints are imposed on the services referenced in these footnotes;
to investigate the technical and regulatory impacts on the services referred to in Nos 5.447F and 5.450A that would result from adding a new reference to Recommendation ITU-R M.1849-1 to these footnotes, while ensuring that no undue constraints are imposed on the services referenced in these footnotes,
In preparation for WRC-15 and WRC-19, ITU-R carried out a significant amount of work to study coexistence between RLANs and new radar systems, such as bi-static and fast frequency-hopping radars. These studies confirm that the technical and regulatory impacts of requiring the mobile service to protect new radars types would impose undue constraints on RLAN operation in the 5250-5350 MHz and 5470-5725 MHz frequency ranges. The reference to ITU-R M.1638-0 should not be updated to ITU-R M.1638-1 in footnotes RR Nos. 5447F and 5.450A. Given that both ITU-R M.1638-0 and M.1849-1 Recommendations require essentially the same protection requirements, adding a new reference to ITU R M.1849-1 is redundant and unnecessary.

## Slide 8: AI 10 Consideration for WRC-23
There is an interest from regulators and other stake holders to provide cost-effective broadband connectivity to their masses. Problems are especially severe in Rural Areas.
TV WhiteSpaces based communications may be used to connect the un-connected due to their favorable propagation characteristics.
The TV WhiteSpace eco-system would like to initiate a study at the WRC-19 to investigate if the Radio Regulations can accommodate:
  55-88 MHz, 173-216 MHz, 470-585 MHz for terrestrial broadcast services with secondary operation by whitespace devices on a non-interfering basis
  OR Co-primary use of terrestrial TV Broadcast services with whitespace devices