## Slide 1: Update for IEEE 802
Andy Gowans – OFCOM (UK)
14 January 2018

## Slide 2: Contents
5.8 GHz UK release
WRC-19 agenda items
other issues
  6GHz
  66-71GHz
  802.11ah/15.4 co-ex
  5.8 GHz in car co-existence
  Future spectrum requirements (WRC – 23)

## Slide 3: Previous UK 5 GHz Band Consultation Responses
Drivers for future demand
  Almost everyone agreed the demand for data would increase …
Spectrum supply
  … but that a shortage of spectrum could occur in a diverse range of scenarios
  Most agreed that spectrum was needed alongside tech improvements and densification
  Spectrum particularly needed in scenarios where access points could not be coordinated
  60 GHz a compliment to other bands, but not a full substitute
Notes: The Cisco studies were the main ones cited, but Ericsson also pointed to its own mobility report. A growth factor of 10 times between 2015 and 2022 seemed to be a common view
We did note one common theme, though, and this was that spectrum was particularly needed where access points could not be coordinated. These areas might include blocks of flats and shopping centres where each shop had its own Wi-Fi network.
The Wi-Fi Alliance modelled a three-story block of flats and found that just over 1 GHz of spectrum would be necessary to deliver 1 Gbps to residents.
Microsoft’s response noted that 60 GHz might be good for very high data rate applications within a room, but not for coverage over a home.

## Slide 4: 5 GHz Consultation Responses
5725-5850 MHz
  Most agreed with us prioritising this band
  Already used by a diverse set of users
  We’ll talk about this some more on the next slide
Revisiting DFS
  Most agreed with our proposal to revisit DFS …
  … but it is still not clear which alternatives would be better
opening up 5850-5925 MHz; outdoor Wi-Fi use at 5150-5350 MHz; and opening up the ‘centre gap’ at 5350-5470.
  5850-5925 MHz will require cooperation with ITS
  5150-5350 MHz outdoor use more important for FWA than Wi-Fi
  5350-5470 MHz was support for Wi-Fi but also crucial for space science and military use

## Slide 5: Licence-exempt spectrum: UK said they would release more bands in 2017
5150 MHz
5350 MHz
5470 MHz
5725 MHz
5850 MHz
5925 MHz
Today: indoor.
ITU Studies for outdoor extension on-going. DFS required in the upper part.
Today: new release allowing indoor up to 200mW licence exempt
Still allow outdoor use :- SRD use (no DFS) up to 25mW licence exempt and BFWA up to 4W with a licence.
Today: in part available for ITS in line with EC Decision.
Today: not available.
Studies on-going.
Already available indoor and outdoor.
DFS required
Already used for WLAN
Not used for WLAN, studies agreed in WRC 15
Not used, no works in progress
new release in UK

## Slide 6: 5.8 GHz UK Release for Wi-Fi
5725 - 5850 MHz ISM band
UK made a statement releasing the band https://www.ofcom.org.uk/consultations-and-statements/category-1/5-GHz-Wi-Fi which closed in July 2017
Potential to become a global Wi-Fi band although UK regs. differ from US
Wi-Fi deployments in this band needed to coexist with different incumbents from US notably FSS (region 1 allocation only)
International work will continue on the band after UK release both in CEPT and the ITU
Some dispensations for channel use across the band edge boundary

## Slide 7: Closer view of the new regulations
Special dispensation for channels overlapping boundary at 5725 MHz to use 1W
DFS radar test signals slightly different in 5.8GHz from those used in other 5GHz bands.
To use DFS test procedures and requirements from EN301 893 but radar test signals from EN 302 502 for more detail see VNS 2030/8/3 https://www.ofcom.org.uk/__data/assets/pdf_file/0016/104416/vns-203083.pdf
Figure A1: Existing 5 GHz RLAN channels and the new channels we are making available

## Slide 8: WRC 19 and Wi-FI (UK perspective)
To allow outdoor use worldwide in existing bands
5150-5250 MHz
outdoor use seems more important for FWA than mass market Wi-Fi which seems to have less demand in UK, Ofcom are not proactive in presenting studies but are willing to be convinced by studies its possible to have outdoor use in the band similar to US/Canada regulations. France and Germany are pushing to allow low power use in cars in this band < = 25mW.
5250-5350 MHz
outdoor use more important for FWA than mass market Wi-Fi which seems to have less demand in UK, Ofcom are not proactive in presenting studies but are willing to be convinced by studies its possible to have outdoor use in the band similar to US/Canada regulations. Have not objected to a no change option being adopted by CEPT in their draft brief.

## Slide 9: WRC 19 and Wi-FI (UK perspective)
Proposed new allocations for Wi-Fi use worldwide
5350-5470 MHz was support for Wi-Fi use in UK consultation but the band is also crucial for space science and military use, Ofcom are not proactive in presenting studies but are willing to be convinced through more studies that sharing is possible with additional mitigation techniques. Have not objected to a no change option being adopted by CEPT in their draft brief.
5725–5850 MHz opened up by the UK recently and we have been proactive in promoting our studies and regulations in CEPT as a possible way forward for an primary mobile allocation for RLAN use in Region 1.
5850-5925 MHz will require cooperation with safety related ITS use in the band, Ofcom are not proactive in presenting studies but are willing to be convinced through more studies that sharing is possible with additional mitigation techniques. Have not objected to a no change option being adopted by CEPT in their draft brief.

## Slide 10: WRC 19 and Wi-FI (CEPT perspective)
5150-5250 MHz – no studies supporting outdoor use in CEPT so far but no strong incumbent representation. France and Germany looking to allow up to 25mW in Cars.
5250-5350 MHz - no studies supporting outdoor use in CEPT so far but quite strong incumbent representation on protecting EESS services. CPG recently adopted no change option for this band in draft CEPT brief.
5350-5470 MHz - no change option has been adopted in CEPT brief expect an ECP for this band next supporting no change.
5725–5850 MHz – some support for UK studies and regulations as a possible way forward but some CEPT countries looking for additional mitigation techniques to protect road tolling . Also still some issues around new FH radar for a few countries.
5850-5925 MHz - more studies on additional mitigation techniques required as a number of CEPT countries looking to give gold plated protection to safety related ITS use. CPG recently adopted no change option for this band in draft CEPT brief.

## Slide 11: RLAN technologies sharing spectrum in 5GHz
 | Type of spectrum access | Control | Level of interaction
WiFi/LTE integration | switching between licensed and licence-exempt | device with policies specified by the LTE operator | medium
LWA | hybrid | LTE operator | high
LWIP | hybrid | LTE operator | medium
LAA | hybrid | LTE operator | high
MulteFire | licence-exempt | - | -
The evolution of new technologies for licence-exempt spectrum has the potential to benefit consumers, but it is important these new technologies coexist nicely with Wi-Fi
In Europe politeness protocols are mandated by the EN 301 893 standard
We believe that the solution agreed in the new ETSI standard provides a higher degree of protection for UK consumers using Wi-Fi than the previous version of the standard
We will also participate in the next version of the ETSI standard where we would expect improvements in the standard regarding receiver parameters.
Notes: Wi-Fi dominates the 5 GHz space today, but there are other technologies looking to share as well
Most of the international work has been on coexistence with the various flavours of license exempt LTE, summarised here.
This work has been ongoing at ETSI BRAN
We are pursuing a technology neutral approach; room for all technologies if they share well
We believe the new standards provide protection for UK consumers by making sure these two families of technologies can share well

## Slide 12: Other Issues of note (1)
Possible RLAN use in 6GHz (5925 – 6425 MHz)
  CEPT only studying up to 6425 MHz
  SE45 studying co-ex with P to P Fixed links and FSS E to S
  FM57 working on questionnaire for CEPT countries on FS use and will receive EC mandate to study 5925 – 6425 MHz also.
66 - 71GHz - the band has been identified as possible candidate band for IMT under WRC-19 AI 1.13 in both the UK and the CEPT Roadmaps
  For UK see https://www.ofcom.org.uk/spectrum/spectrum-management
  For CEPT see https://cept.org/Documents/cpg/40566/temp08r1_information-on-cept-roadmap-for-5g

## Slide 13: Other Issues of note (2)
SRD use 800/900 MHz bands
  WGFM approved new rules in Rec 70-03 after public consultation
  See https://cept.org/ecc/groups/ecc/wg-fm/client/meeting-documents/?flid=6578 for more details
  Rules for generic SRDs is 70-03 Annex 1 see https://cept.org/Documents/wg-fm/39094/fm-17-177-annex-22_rec-70-03-annex-1-after-pc-finally-approved
  Rules for Tracking and data acquisition systems (sensors etc) is 70-03 Annex 2 see https://cept.org/Documents/wg-fm/39095/fm-17-177-annex-23_rec-70-03-annex-2-after-pc-finally-approved
  Rules for Wideband Data systems is 70-03 Annex 3 see https://cept.org/Documents/wg-fm/39096/fm-17-177-annex-24_rec-70-03-annex-3-after-pc-finally-approved
  Work is also continuing in WGSE and WGFM looking at recommendations and follow on activities from ECC Reports 246 and 261

## Slide 14: Other Issues of note (3)
5.8GHz band - CEPT are working on a draft ECC Report on SRD use in Cars, the work is in WGSE and looks at sharing between current SRD outdoor use up to 25mW RLAN (with no DFS) allowed and :-
    Road Tolling in 5795 – 5815 MHz
    Non safety ITS in 5850 – 5875 MHz
    See https://cept.org/Documents/wg-se/40548/se-18-006a3_draft-ecc-report-on-wi-57-srd-use-in-cars
WE NEED INPUT FROM THE RLAN INDUSTRY ON IN CAR SHARING STUDIES!
WRC-23 – WRC-19 Agenda Item 10 is to look at future agenda items for WRC-23
    In CEPT CPG PTA are the group responsible.
    Are any new frequencies that IEEE 802 would like to see harmonised at a global level for mobile use?
WE NEED INPUT FROM INDUSTRY ON FUTURE WRC STUDIES!
Any further questions contact : Email: Andrew.gowans@Ofcom.org.uk