## Slide 1: In-band interference effects on 802.15 UWB
Authors:

## Slide 2: INTRODUCTION
PURPOSE:
To present to IEEE 802.18 the results of testing carried out to examine how in-band interference affects the performance of 802.15 UWB
and thus
answer the question posed at a previous meeting
“how much separation is needed so that an in-band Wi-Fi type modulation does not affect the 802.15 UWB receiver”

## Slide 3: The testing
Testing was carried out in a wired setup using Decawave’s EVB1000 (an evaluation board for the DW1000 UWB transceiver IC)
The DW1000 IC implements the UWB PHY specified by the 802.15 amendment 4a (2007), now called the HRP UWB PHY in the 2015 revision of 802.15.4
The EVB1000 has an SMA antenna connection

## Slide 4: The test setup and procedure
The test setup is as shown. The Golden TX and DUT were configured to UWB Channel 5 (centred on 6.4896 GHz, with 499.2 MHz bandwidth) and to use the nominal 64 MHz PRF and the 6.81 Mb/s Data rate (the most popular configuration)
Levels at DUT were measured with a spectrum analyser
The power level from Golden TX was reduced until a 1% frame error rate was observed at the DUT
The power level was then increased by 3dB
The sig-gen was then used to generate a Wi-Fi like interference signal (at various bandwidths and centre frequencies for different tests) and its power level increased until a 1% frame error rate was again observed at the DUT
At this point the power level from the Golden TX was varied and frame error rates were recorded to generate the performance graph on the next sheet

## Slide 5: Results
Interferer power levels required to cause a 3dB drop in DW1000 RX sensitivity

## Slide 6: Results

## Slide 7: How far away would an in-band Wi-Fi device need to be to avoid degrading an 802.15.4 UWB receiver?
We see (from results) the signal needs to be < -78 dBm (about x10 thermal noise)
The proponents of Wi-Fi would like to use the same power levels in the 6 GHz band that they currently use in the U-NII bands, typically +20 dBm
Let’s use Friis transmission equation* to find out the distance, in deciBel form:
Assuming 0 dBi antennas and rearranging we get:
*https://en.wikipedia.org/wiki/Friis_transmission_equation

## Slide 8: What power level would avoid excessive interference?
Obviously Wi-Fi devices like mobile phones cannot be guaranteed to be further away than 291m from 802.15.4a UWB devices such as key-fobs.
If the power allowed for such devices in the 6 GHz band was limited to the same level as current UWB devices, i.e. -41.3 dBm/MHz then a typical device with 40 MHz bandwidth would transmit at -25 dBm.
The distance now becomes:
This separation is certainly a lot more achievable
This power level may limit data rates and range, but perhaps not excessively since UWB can achieve 27 MB/s data rate at 80 m

## Slide 9: Conclusion
The testing shows that in band interference has a big impact on UWB receiver performance.
This result backs up the concerns voiced at previous meetings, and in previous submissions:
    That there are major concerns for 802.15 UWB deployments operating in the 6 GHz to 7 GHz band if 802.11ax (or similar) radios be allowed transmit at typical existing Wi-Fi power levels in this band.

## Slide 10: THE END THANK YOU

## Slide 11: Backup info: Equations background