## Slide 1: Overview of recent 5GHz band rule changes in Japan
Authors:

## Slide 2: Background
MIC Japan was considering rule changes in 5 GHz band to allow next generation high efficiency wireless LANs
New rules
  Channel 144 is now available for low power data communication systems including wireless LANs.
  Requirements for the occupied channel bandwidth and spectrum mask are modified to allow 802.11ax signal.
  So called 4 ms rule is changed.
  Requirements for radar detection in the 5.3 GHz band are modified.
The new rule is announced on July 11th and is effective now.

## Slide 3: Channel 144
The channel 144 is now available for low power data communication system including WLANs.
  One additional channel for 20 MHz, 40 MHz and 80 MHz channels.
  Three additional combinations for the 80 + 80 MHz channelization.
5.15
5.35
5.47
5.73
36
40
44
48
52
56
60
64
5.2
5.3
100
104
108
112
116
120
124
128
132
136
140
144
38
46
54
62
102
110
118
126
134
142
42
58
106
122
138
50
114
20 MHz
channels
40 MHz
channels
80 MHz
channels
160 MHz
channels
5.5
5.6
5.7
GHz

## Slide 4: Occupied channel bandwidth
Requirements for the occupied channel bandwidths are relaxed to accommodate new OFDM signal of 802.11ax.

## Slide 5: Radio burst length/Effective duration of the carrier sense
There have been technical requirements for the length of radio burst and effective duration of carrier sense, so called 4 ms rule.
  The length of a radio burst must be less than of equal to 4 ms.
  A device has to do carrier sense if more than 4 ms had passed since previous carrier sense.
Now, 4 ms is relaxed to 8 ms.
CS
Radio Burst
Ack
CS
Radio Burst
Ack
Length <= 4 ms
This carrier sense can be omitted if 4 ms has not passed since previous CS

## Slide 6: Requirements for DFS in 5.3 GHz band
New pulse patterns for WLAN to detect are defined in terms of
  Minimum and maximum values of the pulse width (W), minimum and maximum values of pulse repetition frequency (PRF), number of pulses in a period, etc.
Future pulse pattern of the new weather radar is still under discussion.
The definition of traffic load during in service monitoring is changed similar to the requirement of ETSI (30% channel time).
There is mitigation period of 1 year to adopt new radar detection scheme.
W1
W2
T1
T2
1/PRF

## Slide 7: Reference
1. MIC Web site, Technical Requirements for the next generation high efficiency wireless LANs, http://www.soumu.go.jp/menu_news/s-news/02kiban12_04000251.html (in Japanese)