## Slide 1: Summary of the decisions of selected agenda items in WRC-19
Author:

## Slide 2: Background
This slide deck summarizes the decisions of selected agenda items on WRC-19 [1] that IEEE 802.18 is interested in.

## Slide 3: Item 1.12 (1)
To consider possible global or regional harmonized frequency bands, to the maximum extent possible, for the implementation of evolving Intelligent Transport Systems (ITS) under existing mobile-service allocations, in accordance with Resolution 237 (WRC-15).

## Slide 4: Item 1.12 (2)
From the CPM report [2]:
  1/1.12/4.1 Method A – No change to the Radio Regulations and suppress Resolution 237 (WRC-15).
  1/1.12/4.2 Method B – No change to the Table of Frequency Allocations in the Radio Regulations, and add a new WRC Resolution to encourage administrations to use 5 850-5 925 MHz, or parts thereof, as global harmonized evolving ITS frequency bands. Other harmonized frequency band(s) for evolving ITS applications refer to the most recent version of Recommendation ITU-R M.2121.
  1/1.12/4.3 Method C – No change to the RR Table of Frequency Allocations and to add a new WRC Resolution to encourage administrations to use globally and regionally harmonized frequency bands for ITS applications through reference to ITU-R Recommendation(s). Suppress Resolution 237 (WRC-15).

## Slide 5: Item 1.12 (3)
IEEE 802’s position [3]:
  IEEE 802.11 has provided the wireless standard (IEEE Std 802.11p-2010) that provides the basis for much of the Intelligent Transport Systems (ITS) Vehicle-to-Vehicle (V2V) and Vehicle-to-Infrastructure (V2I) technologies being deployed today. And now IEEE 802.11 is specifying an IEEE Next Generation V2X (NGV) amendment (the P802.11bd project) backward compatible to IEEE Std 802.11p-2010. We believe that these technologies are capable of sharing frequency bands, including the 5850-5925 MHz, with other unlicensed applications.
  We also understand that global harmonization of the technology is a notable effort that would enable technology improvements and cost reductions to better address rapid adoption to meet the ITS safety goals, an effort we would support.

## Slide 6: Item 1.12 (4)
WRC’s recommendation COM4/1 [1, pp. 555-557]:
  recommends
    that administrations consider using globally or regionally harmonized frequency bands, or parts thereof, as described in the most recent versions of Recommendations (e.g. ITU-R M.2121), when planning and deploying evolving ITS applications, taking into account recognizing b) above;
    that administrations take into account, if necessary, coexistence issues between ITS stations and stations of existing services (e.g. FSS earth stations), taking into account considering f),
  invites Member States and Sector Members
    to participate actively in and to contribute to ITU-R studies on aspects of ITS and evolving ITS (e.g. connected vehicles, autonomous vehicles, adaptive driver assistance systems), through the ITU-R study groups

## Slide 7: Item 1.12 (5)
WRC’s recommendation COM4/1 [1, pp. 555-557]:
  Author’s remarks on “recognizing b)”
    Recognizes that the use of frequency bands harmonized for evolving ITS, or parts thereof, does not preclude the use of these bands/frequencies by any other application of the services to which they are allocated and does not establish priority in the Radio Regulations
  Author’s remarks on “considering f)”
    Considers that some frequency bands harmonized for ITS are also allocated to the fixed-satellite service (FSS) (Earth-to-space), which under certain circumstances may cause potential interference to ITS stations while in close proximity

## Slide 8: Item 1.13 (1)
To consider identification of frequency bands for the future development of International Mobile Telecommunications (IMT), including possible additional allocations to the mobile service on a primary basis, in accordance with Resolution 238 (WRC‑15).

## Slide 9: Item 1.13 (2)
From the CPM report [2]:
  2/1.13/4.10 Item J: Frequency band 66-71 GHz
  2/1.13/4.10.1 Method J1: NOC
  2/1.13/4.10.2 Method J2: Identification of the frequency band 66-71 GHz for IMT in accordance with the following two alternatives (see [2]) and removal of the frequency band from RR No. 5.553
  2/1.13/4.10.3 Method J3: To continue studies on the possibility of identification in the frequency band 66-71 GHz for IMT with a WRC Resolution
  2/1.13/4.10.4 Method J4: Identification of the frequency band 66-71 GHz for IMT in accordance with the following two alternatives (see [2]) and retention of the frequency band in RR No. 5.553

## Slide 10: Item 1.13 (3)
IEEE 802’s position [3]:
  IEEE 802 strongly supports 66-71 GHz band for unlicensed operation.
  //
  We believe that a wide variety of 5G services and use-cases will be deployed in this band globally without the need for an IMT identification. Wi-Fi® plays an important role in and is an integral part of 5G. 5G will be driven by new IEEE 802 wireless technologies not only in the sub-6 GHz spectrum such as IEEE P802.11ax and IEEE P802.11be, but also others in the mmWave spectrum such as IEEE Std 802.11ad, IEEE P802.11ay and IEEE Std 802.15.3. In fact, we are concerned that IMT identification could bar some key 5G technologies like these from operating in this band.
  IEEE 802 recommends supporting CPM-19 Report Method J1 (Section 2/1.13/4.10.1) and would like to respectfully request MCMC to do the same.

## Slide 11: Item 1.13 (4)
WRC’s resolution COM4/7 [1, pp. 389-390]:
  resolves
    that administrations wishing to implement IMT make available the frequency band 66-71 GHz identified in No. 5.J113 for use by the terrestrial component of IMT;
    that administrations wishing to implement IMT in the frequency band 66-71 GHz, identified for IMT under the provisions in No. 5.J113, which are also wishing to implement other applications of the mobile service, including other wireless access systems in the same frequency band, consider coexistence between IMT and these applications

## Slide 12: Item 1.13 (5)
WRC’s resolution COM4/7 [1, pp. 389-390]:
  invites ITU-R
    to develop harmonized frequency arrangements for the implementation of the terrestrial component of IMT in the frequency band 66-71 GHz;
    to develop ITU-R Recommendations and/or Reports, as appropriate, to assist administrations in ensuring the efficient use of the frequency band through coexistence mechanisms between IMT and other applications of the mobile service, including other wireless access systems, as well as between the mobile service and other services;
    to regularly review, as appropriate, the impact of evolving technical and operational characteristics of IMT systems (including base-station density) and those of systems of space services on sharing and compatibility, and to take into account the results of these reviews in the development and/or revision of ITU-R Recommendations/Reports addressing, inter alia, if necessary, applicable measures to mitigate the risk of interference into space receivers.

## Slide 13: Item 1.13 (6)
WRC’s Article 5 Frequency Allocation [1, pp.58-59]:

## Slide 14: Item 1.15 (1)
To consider identification of frequency bands for use by administrations for the land-mobile and fixed services applications operating in the frequency range 275-450 GHz, in accordance with Resolution 767 (WRC-15).

## Slide 15: Item 1.15 (2)
From the CPM report [2]:
  1/1.15/4.1 Method A: No change to the Radio Regulations.
  1/1.15/4.2 Method B: Modifying the existing footnote RR No. 5.565 is proposed for FS/LMS applications in portions of the 275-450 GHz frequency range.
  1/1.15/4.3 Method C: This method suggests adding a new footnote to identify the 275-450 GHz frequency range for use by FS/LMS applications, while protecting EESS (passive) and RAS using the evolving guidance of ITU-R Recommendations and Reports, taking into account that there are no service allocations above 275 GHz.
  1/1.15/4.4 Method D: Adding a new footnote RR No. 5.D115 is proposed for land mobile and fixed service applications: 275-296 GHz, 306-313 GHz, 320-330 GHz and 356-450 GHz.

## Slide 16: Item 1.15 (3)
From the CPM report [2] (con’t):
  1/1.15/4.5 Method E: Adding a new footnote RR No. 5.E115 and modifying the existing footnote RR No. 5.565 are proposed for FS/LMS applications in portions of the 275-450 GHz band.
  1/1.15/4.6 Method F: Adding a new footnote RR No. 5.F115 is proposed for FS applications in portions of the 275-450 GHz band and for LMS applications in the entire 275-450 GHz frequency band.
  1/1.15/4.6 Method G: Adding a new footnote RR No. 5.G115 is proposed for FS/LMS applications in portions of the 275-450 GHz band.

## Slide 17: Item 1.15 (4)
IEEE 802’s position [3]:
  //
  We believe that the identification (by a new footnote or modification of the existing one RR No. 5.565) of at least the bands 275-296, 306-313, 320-330 and 356-450 GHz for LMS and FS will provide proper protection of the passive services. As an improvement to the current situation, this identification will provide clear guidance to manufacturers and administrations which bands should not be used in order to protect the passive services.
  We believe that the identification of these bands is very important today for backhaul and fronthaul links supporting 100+ Gbit/s for 5G and enables future applications such as kiosk downloading, reconfigurable wireless links for data centers in addition to fibers and intra-device communications.
  However, IEEE 802 has a process to will IEEE Std 802.15.3 according to the outcome of WRC-19 if necessary and may also develop a standard for bands above 325 GHz which were less promising in 2014 when the development of the standard was initiated.

## Slide 18: Item 1.15 (5)
WRC’s resolution 731 [1, pp. 334-335]:
  resolves
    to invite a future competent world radiocommunication conference to consider the results of ITU-R studies referred to in invites ITU-R below with a view to taking the necessary action, as appropriate, in order to accommodate the emerging requirements of active services, taking into account the requirements of the passive services, in bands above 71 GHz
  urges administrations
    to note the possibility of changes to Article 5 to accommodate emerging requirements for active services, as indicated in this Resolution, and to take this into account in the development of national policies and regulations

## Slide 19: Item 1.15 (6)
WRC’s resolution 731 [1, pp. 334-335]:
  invites ITU-R
    to continue its studies to determine if and under what conditions sharing is possible between active and passive services in the bands above 71 GHz, such as, but not limited to, 100-102 GHz, 116-122.25 GHz, 148.5-151.5 GHz, 174.8-191.8 GHz, 226-231.5 GHz and 235-238 GHz;
    to conduct studies to determine the specific conditions to be applied to the land mobile and fixed service applications to ensure the protection of Earth exploration-satellite service (passive) applications in the frequency bands 296-306 GHz, 313-318 GHz and 333-356 GHz;
    to study means of avoiding adjacent-band interference from space services (downlinks) into radio astronomy bands above 71 GHz;
    to take into account the principles of burden-sharing to the extent practicable in their studies;
    to complete the necessary studies when the technical characteristics of the active services in these bands are known;
    to develop Recommendations specifying sharing criteria for those bands where sharing is feasible

## Slide 20: Item 1.15 (7)
WRC’s Article 5 Frequency Allocation [1, pp.59-60]:

## Slide 21: Item 1.15 (8)
WRC’s Article 5 Frequency Allocation [1, pp.59-60]:

## Slide 22: Item 1.16 (1)
To consider issues related to wireless access systems, including radio local area networks (WAS/RLAN), in the frequency bands between 5 150 MHz and 5 925 MHz, and take the appropriate regulatory actions, including additional spectrum allocations to the mobile service, in accordance with Resolution 239 (WRC-15).

## Slide 23: Item 1.16 (2)
From the CPM report [2] on Frequency band A (5150-5250 MHz):
  2/1.16/4.1.1 Method A1: No change to the RR
  2/1.16/4.1.2 Method A2: Revision to Resolution 229 (Rev.WRC-12) to enable outdoor RLAN operations including possible associated conditions for new e.i.r.p. limits
  2/1.16/4.1.3 Method A3: Revision to Resolution 229 (Rev.WRC-12) to enable outdoor RLAN operations by applying the same conditions of use as defined for the 5250-5350 MHz frequency band in resolves 4 of Resolution 229 (Rev.WRC-12)
  2/1.16/4.1.4 Method A4: Revisions to Resolution 229 (Rev.WRC-12) to facilitate limited RLAN outdoor operation and RLAN in-vehicle (cars and trains) usage operation with associated e.i.r.p. levels
  2/1.16/4.1.5 Method A5: Revisions to Resolution 229 (Rev.WRC-12) to enable in-car use of RLAN operation with e.i.r.p. up to 40 mW
  2/1.16/4.1.6 Method A6: Revision to Resolution 229 (Rev.WRC-12) to enable outdoor RLAN operations including associated conditions for new e.i.r.p. limits and out-of-band emission limits

## Slide 24: Item 1.16 (3)
From the CPM report [2] on Frequency band B (5250-5350 MHz):
  2/1.16/4.2.1 Method B: No change to the RR
From the CPM report [2] on Frequency band C (5350-5470 MHz):
  2/1.16/4.3.1 Method C: No change to the RR

## Slide 25: Item 1.16 (4)
From the CPM report [2] on Frequency band D (5725-5850 MHz):
  2/1.16/4.4.1 Method D1: No change to the RR
  2/1.16/4.4.2 Method D2: A new Regional primary MS allocation
  2/1.16/4.4.3 Method D3: Accommodate WAS/RLAN in a new footnote
From the CPM report [2] on Frequency band E (5850-5925 MHz):
  2/1.16/4.5.1 Method E: No change to the RR

## Slide 26: Item 1.16 (5)
IEEE 802’s position [3]
  Since the 1990s, IEEE 802 has been actively developing standards for Wireless LAN technologies that operate in the 5 GHz bands. Among these is IEEE 802.11, which is the basis for Wi-Fi, the most successful, most used and most demanded 5 GHz wireless technology. IEEE 802.11 is carrying the vast majority of wireless internet traffic and is essential for commercial services, education, communications and social interactions, creating industries and providing jobs and economic growth around the world.
  IEEE 802 recommends that any regulatory action should not disadvantage any IEEE 802 standard or add any additional regulatory burdens for its use of the 5 GHz bands. More specifically, for 5725-5850 MHz, any actions should not impose additional constraints such as DFS, Tx Power restriction or Indoor restrictions.
  Moreover, IEEE 802 would like to have expanded access in 5150-5250 MHz through higher Tx Power and outdoor operations.

## Slide 27: Item 1.16 (6)
WRC’s resolution 229 [1, pp. 273-277] on 5150-5250 MHz, 5250-5350 MHz, and 5470-5725 MHz:
  resolves
    that the use of these bands by the mobile service is for the implementation of WAS, including RLANs, as described in the most recent version of Recommendation ITU-R M.1450;
    that in the band 5150-5250 MHz, stations in the mobile service shall be restricted to indoor use, including inside trains, with a maximum mean e.i.r.p. of 200 mW and a maximum mean e.i.r.p. density of 10 mW/MHz in any 1 MHz band or equivalently 0.25 mW/25 kHz in any 25 kHz band. Mobile stations inside automobiles shall operate with a maximum e.i.r.p. of 40 mW;

## Slide 28: Item 1.16 (7)
    that in the frequency band 5150-5250 MHz, administrations may exercise some flexibility by taking appropriate measures that would allow controlled and/or limited outdoor usage with a maximum mean e.i.r.p. of 200 mW. Administrations have a further option to permit stations in the mobile service, for indoor or controlled outdoor use, to operate up to a maximum mean e.i.r.p of 30 dBm. In the case of indoor or controlled outdoor use, administrations are requested to either ensure that the maximum e.i.r.p. at any elevation angle above 5 degrees as measured from the horizon shall not exceed 200 mW (23 dBm), or to ensure that the maximum e.i.r.p. at any elevation angle above 30 degrees as measured from the horizon shall not exceed 125 mW (21 dBm) or to apply the emission mask described in resolves 5 below to maintain protection to the incumbent services. In that case, administrations shall, take all appropriate measures, such as those described in recognizing k) to control the number of these higher power outdoor WAS/RLANs stations up to 2 per cent of the estimated total amount of WAS/RLAN stations. If the maximum e.i.r.p. is raised above 200 mW, unwanted emissions shall not increase above the existing levels already authorized within administrations for the existing systems that operate with an in-band e.i.r.p. of not greater than 200 mW. In all cases administrations are requested to maintain protection to the other primary services;

## Slide 29: Item 1.16 (8)
    that administrations may monitor whether the aggregate pfd levels given in Recommendation ITU-R S.14262 are exceeded as a consequence of a prolific growth in the number of WAS/RLAN;
    that in the frequency band 5250-5350 MHz, stations in the mobile service shall be limited to a maximum mean e.i.r.p. of 200 mW and a maximum mean e.i.r.p. density of 10 mW/MHz in any 1 MHz band. Administrations are requested to take appropriate measures that will result in the predominant number of stations in the mobile service being operated in an indoor environment. Furthermore, stations in the mobile service that are permitted to be used either indoors or outdoors may operate up to a maximum mean e.i.r.p. of 1 W and a maximum mean e.i.r.p. density of 50 mW/MHz in any 1 MHz band, and, when operating above a mean e.i.r.p. of 200 mW, these stations shall comply with the following e.i.r.p. elevation angle mask where θ is the angle above the local horizontal plane (of the Earth):

## Slide 30: Item 1.16 (9)
    that administrations may exercise some flexibility in adopting other mitigation techniques, provided that they develop national regulations to meet their obligations to achieve an equivalent level of protection to the EESS (active) and the SRS (active) based on their system characteristics and interference criteria as stated in Recommendation ITU-R RS.1632;
    that in the frequency band 5470-5725 MHz, stations in the mobile service shall be restricted to a maximum transmitter power of 250 mW with a maximum mean e.i.r.p. of 1 W and a maximum mean e.i.r.p. density of 50 mW/MHz in any 1 MHz band;
    that in the frequency bands 5250-5350 MHz and 5470-5725 MHz, systems in the mobile service shall either employ transmitter power control to provide, on average, a mitigation factor of at least 3 dB on the maximum average output power of the systems, or, if transmitter power control is not in use, then the maximum mean e.i.r.p. shall be reduced by 3 dB;

## Slide 31: Item 1.16 (10)
    that, in the frequency bands 5250-5350 MHz and 5470-5725 MHz, the mitigation measures for systems in the mobile service found in Annex 1 to Recommendation ITU-R M.1652-1 as well as the characteristics and interference criteria for systems in the radiolocation service stated in Annex 5 to Recommendation ITU-R M.1652-1 shall be used by systems in the mobile service to ensure compatible operation with radiodetermination systems
  invites administrations
    to consider appropriate measures when allowing the operation of stations in the mobile service using the e.i.r.p. elevation angle mask referred in resolves 5 above, to ensure the equipment is operated in compliance with this mask;
    to take appropriate measures, such as those examples in recognizing k), to control the number of outdoor stations in the frequency band 5150-5250 MHz, if implementing resolves 3 above, in order to ensure the protection of incumbent services

## Slide 32: Item 1.16 (11)
  invites ITU-R
    to consider appropriate measures to continue studies on mitigation techniques to provide protection of EESS from stations in the mobile service;
    to continue studies on suitable test methods and procedures for the implementation of dynamic frequency selection, taking into account practical experience.
  Author’s remarks on “recognizing k)”
    recognizes that measures to control the number of outdoor WAS/RLAN, in the frequency band 5150-5250 MHz, can include: authorization approach, registration procedures, domestic notification, limited application, limitation to fixed WAS/RLAN access points, etc.,

## Slide 33: Item 1.16 (12)
WRC’s Article 5 Frequency Allocation [1, pp. 37]:

## Slide 34: Item 9.1 issue 9.1.5 (1)
Resolution 764 (WRC-15) - Consideration of the technical and regulatory impacts of referencing Recommendations ITU-R M.1638-1 and ITU-R M.1849-1 in Nos. 5.447F and 5.450A of the Radio Regulations.

## Slide 35: Item 9.1 issue 9.1.5 (2)
From the CPM report [2]:
  Approach A updates both footnotes by removing the references and replacing them with the sentence “Resolution 229 (Rev.WRC-12) applies”.
  Approach B updates both footnotes by removing the references to the Recommendations and replacing them with a reference to RR No. 5.446A.

## Slide 36: Item 9.1 issue 9.1.5 (3)
IEEE 802’s position [3]:
  In preparation for WRC-15 and WRC-19, ITU-R carried out a significant amount of work to study coexistence between RLANs and new radar systems, such as bi-static and fast frequency-hopping radars. These studies confirm that the technical and regulatory impacts of requiring the mobile service to protect new radars types would impose undue constraints on RLAN operation in the 5250-5350 MHz and 5470-5725 MHz frequency ranges. The reference to ITU-R M.1638-0 should not be updated to ITU-R M.1638-1 in footnotes RR Nos. 5.447F and 5.450A. Given that both ITU-R M.1638-0 and M.1849-1 Recommendations require essentially the same protection requirements, adding a new reference to ITU-R M.1849-1 is redundant and unnecessary.
  IEEE 802 recommends supporting CPM-19 Report Approach B (Section 2/9.1.5/4.2).

## Slide 37: Item 9.1 issue 9.1.5 (4)
WRC’s Article 5 Frequency Allocation [1, pp. 38]:

## Slide 38: Item 10 (1)
To recommend to the Council items for inclusion in the agenda for the next WRC, and to give its views on the preliminary agenda for the subsequent conference and on possible agenda items for future conferences, taking into account Article 7 of Convention.

## Slide 39: Item 10 (2)
IEEE 802’s position [3]:
  //
  Extensive efforts are underway in Regions 1 and 2 in 6 GHz bands (5925-7125 MHz) to expand license-exempt device operation. More specifically, the European Commission has issued directives in form of an EC Mandate to CEPT to conduct the studies for co-existence and harmonized technical conditions for RLAN operation in the band. Please see recently published ECC Report 302 and draft CEPT Report 73. Similarly, U.S. Federal Communication Commission has issued a Notice of Proposed Rule Making for unlicensed use of the 6 GHz Band (NPRM). The 6 GHz Report and Order is expected to be issued by the end of 2019.
  Flexible sharing of the band facilitates growth and innovation globally and across the APT region.
  Consideration of an agenda item for WRC-23 for 6 GHz IMT designation, would be counterproductive as it may disrupt advancing growth and innovation globally and across Region 3 and cause unnecessary regulatory burden both at ITU and regionally in APT.

## Slide 40: Item 10 (3)
WRC’s resolution COM6/1 on Agenda for WRC-23 [1, pp. 470-474] :
  resolves to recommend to the Council that a world radiocommunication conference be held in 2023 for a maximum period of four weeks, with the following agenda:
    on the basis of proposals from administrations, taking account of the results of WRC-19 and the Report of the Conference Preparatory Meeting, and with due regard to the requirements of existing and future services in the frequency bands under consideration, to consider and take appropriate action in respect of the following items:
      1.1: to consider, based on the results of the ITU-R studies, possible measures to address, in the frequency band 4800-4990 MHz, protection of stations of the aeronautical and maritime mobile services located in international airspace and waters from other stations located within national territories, and to review the pfd criteria in No. 5.441B in accordance with Resolution 223 (Rev.WRC-19);

## Slide 41: Item 10 (4)
      1.2: to consider identification of the frequency bands 3300-3400 MHz, 3600-3800 MHz, 6425-7025 MHz, 7025-7125 MHz and 10.0-10.5 GHz for International Mobile Telecommunications (IMT), including possible additional allocations to the mobile service on a primary basis, in accordance with Resolution COM6/2 (WRC-19);
      1.3: to consider primary allocation of the band 3600-3800 MHz to mobile service within Region 1 and take appropriate regulatory actions, in accordance with Resolution COM6/3 (WRC-19);
      1.4: to consider, in accordance with Resolution COM6/4 (WRC-19), the use of high-altitude platform stations as IMT base stations (HIBS) in the mobile service in certain frequency bands below 2.7 GHz already identified for IMT, on a global or regional level;
      1.5: to review the spectrum use and spectrum needs of existing services in the frequency band 470-960 MHz in Region 1 and consider possible regulatory actions in the frequency band 470-694 MHz in Region 1 on the basis of the review in accordance with Resolution 235 (WRC-15);

## Slide 42: Item 10 (5)
      1.6: to consider, in accordance with Resolution COM6/5 (WRC-19), regulatory provisions to facilitate radiocommunications for sub-orbital vehicles;
      1.7: to consider a new aeronautical mobile-satellite (R) service (AMS(R)S) allocation in accordance with Resolution COM6/6 (WRC-19) for both the Earth-to-space and space-to-Earth directions of aeronautical VHF communications in all or part of the frequency band 117.975-137 MHz, while preventing any undue constraints on existing VHF systems operating in the AM(R)S, the ARNS, and in adjacent frequency bands;
      1.8: to consider, on the basis of ITU-R studies in accordance with Resolution COM6/7 (WRC-19), appropriate regulatory actions, with a view to reviewing and, if necessary, revising Resolution 155 (Rev.WRC-19) and No. 5.484B to accommodate the use of fixed-satellite service (FSS) networks by control and non-payload communications of unmanned aircraft systems;

## Slide 43: Item 10 (6)
      1.9: to review Appendix 27 of the Radio Regulations and consider appropriate regulatory actions and updates based on ITU-R studies, in order to accommodate digital technologies for commercial aviation safety-of-life applications in existing HF bands allocated to the aeronautical mobile (route) service and ensure coexistence of current HF systems alongside modernized HF systems, in accordance with Resolution COM6/8 (WRC-19);
      1.10: to conduct studies on spectrum needs, coexistence with radiocommunication services and regulatory measures for possible new allocations for the aeronautical mobile service for the use of non-safety aeronautical mobile applications, in accordance with Resolution COM6/9 (WRC-19);
      1.11: to consider possible regulatory actions to support the modernization of the Global Maritime Distress and Safety System and the implementation of e-navigation, in accordance with Resolution 361 (Rev.WRC-19);

## Slide 44: Item 10 (7)
      1.12: to conduct, and complete in time for WRC-23, studies for a possible new secondary allocation to the Earth exploration-satellite (active) service for space-borne radar sounders within the range of frequencies around 45 MHz, taking into account the protection of incumbent services, including in adjacent bands, in accordance with Resolution 656 (Rev.WRC-19);
      1.13: to consider a possible upgrade of the allocation of the frequency band 14.8-15.35 GHz to the space research service, in accordance with Resolution COM6/10 (WRC-19);
      1.14: to review and consider possible adjustments of the existing or possible new primary frequency allocations to EESS (passive) in the frequency range 231.5-252 GHz, to ensure alignment with more up-to-date remote-sensing observation requirements, in accordance with Resolution COM6/11 (WRC-19);
      1.15: to harmonize the use of the frequency band 12.75-13.25 GHz (Earth-to-space) by earth stations on aircraft and vessels communicating with geostationary space stations in the fixed satellite service globally, in accordance with Resolution COM6/12 (WRC-19);

## Slide 45: Item 10 (8)
      1.16: to study and develop technical, operational and regulatory measures, as appropriate, to facilitate the use of the frequency bands 17.7-18.6 GHz and 18.8-19.3 GHz and 19.7-20.2 GHz (space-to-Earth) and 27.5-29.1 GHz and 29.5-30 GHz (Earth-to-space) by non-GSO FSS earth stations in motion, while ensuring due protection of existing services in those frequency bands, in accordance with Resolution COM6/13 (WRC-19);
      1.17: to determine and carry out, on the basis of the ITU-R studies in accordance with Resolution COM6/14 (WRC-19), the appropriate regulatory actions for the provision of inter-satellite links in specific frequency bands, or portions thereof, by adding an inter-satellite service allocation where appropriate;
      1.18: to consider studies relating to spectrum needs and potential new allocations to the mobile-satellite service for future development of narrowband mobile-satellite systems, in accordance with Resolution COM6/15 (WRC-19);

## Slide 46: Item 10 (9)
      1.19: to consider a new primary allocation to the fixed-satellite service in the space-to-Earth direction in the frequency band 17.3-17.7 GHz in Region 2, while protecting existing primary services in the band, in accordance with Resolution COM6/16 (WRC-19);
    to examine the revised ITU-R Recommendations incorporated by reference in the Radio Regulations communicated by the Radiocommunication Assembly, in accordance with further resolves of Resolution 27 (Rev.WRC-19), and to decide whether or not to update the corresponding references in the Radio Regulations, in accordance with the principles contained in resolves of that Resolution;
    to consider such consequential changes and amendments to the Radio Regulations as may be necessitated by the decisions of the conference;
    in accordance with Resolution 95 (Rev.WRC-19), to review the Resolutions and Recommendations of previous conferences with a view to their possible revision, replacement or abrogation;
    to review, and take appropriate action on, the Report from the Radiocommunication Assembly submitted in accordance with Nos. 135 and 136 of the Convention;

## Slide 47: Item 10 (10)
    to identify those items requiring urgent action by the radiocommunication study groups in preparation for the next world radiocommunication conference;
    to consider possible changes, in response to Resolution 86 (Rev. Marrakesh, 2002) of the Plenipotentiary Conference, on advance publication, coordination, notification and recording procedures for frequency assignments pertaining to satellite networks, in accordance with Resolution 86 (Rev.WRC-07), in order to facilitate the rational, efficient and economical use of radio frequencies and any associated orbits, including the geostationary-satellite orbit;
    to consider and take appropriate action on requests from administrations to delete their country footnotes or to have their country name deleted from footnotes, if no longer required, taking into account Resolution 26 (Rev.WRC-19);

## Slide 48: Item 10 (11)
    to consider and approve the Report of the Director of the Radiocommunication Bureau, in accordance with Article 7 of the Convention;
      9.1: on the activities of the Radiocommunication Sector since WRC-19:
        In accordance with Resolution 657 (Rev.WRC-19), review the results of studies relating to the technical and operational characteristics, spectrum requirements and appropriate radio service designations for space weather sensors with a view to describing appropriate recognition and protection in the Radio Regulations without placing additional constraints on incumbent services;
        Review of the amateur service and the amateur-satellite service allocations in the frequency band 1240-1300 MHz to determine if additional measures are required to ensure protection of the radio navigation-satellite (space-to-Earth) service operating in the same band in accordance with Resolution COM6/17 (WRC-19);
        Study the use of International Mobile Telecommunication system for fixed wireless broadband in the frequency bands allocated to the fixed services on primary basis, in accordance with Resolution COM6/18 (WRC-19).

## Slide 49: Item 10 (12)
      9.2: on any difficulties or inconsistencies encountered in the application of the Radio Regulations; and
      9.3 on action in response to Resolution 80 (Rev.WRC-07);
    to recommend to the Council items for inclusion in the agenda for the next WRC, and items for the preliminary agenda of future conferences, in accordance with Article 7 of the Convention and Resolution 804 (Rev.WRC-19)

## Slide 50: Item 10: 6 GHz (1)
WRC’s resolution COM6/2 [1, pp. 475-476] :
  resolves to invite ITU-R
    to conduct and complete in time for WRC-23 the appropriate studies of technical, operational and regulatory issues pertaining to the possible use of the terrestrial component of IMT in the frequency bands in resolves to invite ITU-R 2, taking into account:
      evolving needs to meet emerging demands for IMT;
      technical and operational characteristics of terrestrial IMT systems that would operate in these specific frequency bands, including the evolution of IMT through advances in technology and spectrally efficient techniques;
      the deployment scenarios envisaged for IMT systems and the related requirements of balanced coverage and capacity;
      the needs of developing countries;
      the time-frame in which spectrum would be needed;

## Slide 51: Item 10: 6 GHz (2)
    to conduct and complete in time for WRC-23 the sharing and compatibility studies, with a view to ensuring the protection of services to which the frequency band is allocated on a primary basis, without imposing additional regulatory or technical constraints on those services, and also, as appropriate, on services in adjacent bands, for the frequency bands:
      3600-3800 MHz and 3300-3400 MHz (Region 2);
      3300-3400 MHz (amend footnote in Region 1);
      7025-7125 MHz (globally);
      6425-7025 MHz (Region 1);
      10 000-10 500 MHz (Region 2),

## Slide 52: Item 10: 6 GHz (3)
  resolves
    to invite CPM23-1 to define the date by which technical and operational characteristics needed for sharing and compatibility studies are to be available, to ensure that studies referred to in resolves to invite ITU-R can be completed in time for consideration at WRC-23;
    to invite WRC-23 to consider, based on the results of the above studies, additional spectrum allocations to the mobile service on a primary basis and to consider identification of frequency bands for the terrestrial component of IMT; the frequency bands to be considered being limited to part or all of the bands listed in resolves to invite ITU-R 2,
  invites administrations
    to participate actively in these studies by submitting contributions to ITU-R.

## Slide 53: Reference
[1] World Radiocommunication Conference 2019 (WRC-19) Provisional Final Acts, Available at https://www.itu.int/en/ITU-R/conferences/wrc/2019/Documents/PFA-WRC19-E.pdf
[2] Report of the CPM on technical, operational and regulatory/procedural matters to be considered by the World Radiocommunication Conference 2019, March 2019, Available at https://www.itu.int/md/R15-CPM19.02-R-0001/en
[3] IEEE 802’s submission to APG 19-5, Available at https://mentor.ieee.org/802.18/dcn/19/18-19-0094-05-0000-apt-wp1-wrc-19-ais-1-12-1-15-ieee-802-views.pdf; https://mentor.ieee.org/802.18/dcn/19/18-19-0095-05-0000-apt-wp2-wrc-19-ais-1-13-1-16-9-1-5-ieee-802-views.pdf; and https://mentor.ieee.org/802.18/dcn/19/18-19-0096-05-0000-apt-wp6-wrc-19-ais-10-ieee-802-views.pdf