## Slide 1: APAC update – January 2021
Author:

## Slide 2: Background
This slide deck provides a high-level overview of the activities in APAC (related to Wi-Fi and WPAN) between November 2020 and January 2021.

## Slide 3: Australia ACMA (1)
RECAP: New arrangements for low interference potential devices
  Information:
    https://www.acma.gov.au/sites/default/files/2020-09/Variation-to-the-LIPD-Class-Licence-consultation-paper.docx
    https://www.acma.gov.au/sites/default/files/2020-09/Draft-Radiocommunications-Low-Interference-Potential-devices-Class-Licence-Variation-Notice-2020-No-1.docx
    https://www.acma.gov.au/sites/default/files/2020-09/Notice-under-subsection-136-of-Radiocommunications-Act-1992-of-proposed-variation-of-LIPD-Class-Licence-2015.docx
    Consultation closes on October 26, 2020

## Slide 4: Australia ACMA (2)
RECAP: New arrangements for low interference potential devices (Cont’d)
  Abstract
    ACMA plans to introduce new arrangements to support 5G, the IoT and other new technologies related to the following spectrum bands by updating the Radiocommunications (Low Interference Potential Devices) Class Licence 2015 (a.k.a. LIPD Class License):
      Wireless broadband in the 24.25–25.10 GHz band
      IoT devices in the 928–935 MHz band and VHF high bands
      Radiodetermination devices in the 10.50–10.55 GHz band.

## Slide 5: Australia ACMA (2)
New arrangements for low interference potential devices (Cont’d)
  Decision is made on December 17, 2020
    https://www.acma.gov.au/sites/default/files/2020-12/Variation-to-LIPD-Class-Licence_Summary-and-response-to-submissions.docx
    Of interests to us are:
      Proposed arrangements for the 928–935 MHz band will proceed in line with the draft LIPD Class Licence variation provided in the consultation process.
      The inclusion of a definition of ‘indoor’ that would apply to the whole LIPD Class Licence in the next update to this instrument is under investigation:
        Indoor operation is limited to an area enclosed by permanent walls on all sides and having a permanent roof

## Slide 6: China MIIT (1)
Consultation: Notice on Matters Related to Radio Management in the 2400MHz, 5100MHz and 5800MHz Bands
  Information:
    https://www.miit.gov.cn/gzcy/yjzj/art/2021/art_35e50edb407b4063a366372f2394a4c5.html
    Consultation closes on February 28, 2021
  Objective
    To strengthen and standardize the 2400-2483.5 MHz, 5150-5350 MHz and 5725-5850 MHz frequency bands, promote the development of related radio services, and maintain the order of air waves.

## Slide 7: China MIIT (2)
  The followings are my own draft translation. Please refer to the official version in simplified Chinese for the exact proposed wordings.
  Proposed provisions
    2400-2483.5 MHz, 5150-5350 MHz, and 5725-5850 MHz frequency bands (abbreviated as 2400 MHz, 5100 MHz, and 5800 MHz, respectively) are allocated to fixed, mobile, radio localization, fixed satellite, satellite earth exploration, satellite radio measurement, space research, etc. 2400 MHz and 5800 MHz frequency bands are used for ISM applications and other non-wireless radio equipment radiating radio waves. Any wireless radio station or equipment shall be used these frequency bands exclusively.

## Slide 8: China MIIT (3)
  Proposed provisions (Cont’d)
    The 2400 MHz frequency band can be used for broadband wireless access (including wireless LAN), Bluetooth, point-to-point transmission and other radio communication systems. The 5100 MHz frequency band can be used for broadband wireless access (including wireless LAN) systems, and is limited to indoors (vehicles, train carriages, aircraft cabins, etc., are excluded). The 5800 MHz band can be used for broadband wireless access (including wireless LAN), point-to-point transmission, electronic non-stop toll collection systems, and other radio communication systems.

## Slide 9: China MIIT (4)
  Proposed provisions (Cont’d)
    For the wireless communications equipment operating in the 2400 MHz, 5100 MHz, and 5800 MHz frequency bands, the radio frequency unit and antenna must be designed in accordance with the integrated design and manufacturing; prohibited from changing the configurations of other antennas and installing additional RF power amplifiers without authorization; meeting the technical requirements listed in the Appendix 1 and Appendix 2; and obtaining the radio transmission equipment type approval certificate according to applicable laws.

## Slide 10: China MIIT (5)
  Proposed provisions (Cont’d)
    In order to be compatible with other services such as radiolocation, broadband wireless access (including wireless LAN) system operating in the 5250-5350MHz frequency band should adopt TPC and DFS interference suppression technology, and prohibited from creating a capability that allows turning off the DFS setting. TPC is not less than 6 dB. If there is no TPC function, the equivalent omnidirectional radiation and the maximum EIPR limits should be reduced by 3 dB.
    To ensure the compatible coexistence with different radio services, wireless communications systems operating in the 2400 MHz, 5100 MHz, and 5800 MHz frequency bands shall comply with one of the listed interference avoidance technical requirements in Appendix 2.

## Slide 11: China MIIT (6)
  Proposed provisions (Cont’d point 4)
    Wireless LAN equipment with IP address allocation function should support the IPv6 protocol, and enable IPv6 address allocation function by default.
    Security capabilities of the air interface access control should be complied with the GB 15629 Wireless LAN security series standards.
    In order to install and use wireless LAN access points, central station of broadband wireless access systems, and the radio stations of point-to-point transmission, a radio station license at a province level is required if the following conditions are met:
      Outdoor operation
      EIRP of a radio transmitting equipment operating in the 2400 MHz frequency is greater than 20 dBm; EIRP of a radio transmitting equipment operating in the 5800 MHz frequency band is greater than 30 dBm.

## Slide 12: China MIIT (7)
  Proposed provisions (Cont’d point 5)
    Except the abovementioned conditions, other wireless communications system and radio stations operating in the 2400 MHz, 5100 MHz, and 5800 MHz frequency bands are not required to obtain a frequency use permit and a radio station license.
    Radio management agencies of all provinces, autonomous regions, and municipalities shall promote online application of the radio station licenses for equipment operating in the 2400 MHz, 5100 MHz, and 5800 MHz frequency bands.
    The radio communication system station operating in the 5100 MHz frequency band should be located more than 3 km away from the earth station of the same frequency band for satellite radiodetermination (space-to-ground) and fixed satellite (space-to-ground). Sign posts on the prohibition of the installation and use of the radio communications systems shall be set up at road junctions within 3 km.

## Slide 13: China MIIT (8)
  Proposed provisions (Cont’d)
    For a radio station operating in the 2400 MHz, 5100 MHz, and 5800 MHz frequency bands with a valid radio station license, the station owner should report to the local radio regulatory agency and ask the agency for coordination. if the station is subject to harmful radio interference.
    For a radio station operating in the 2400 MHz, 5100 MHz, and 5800 MHz frequency bands with a valid radio station license, the protection requirement from any harmful interference cannot be in principle exempted. When the radio station produces harmful interference to other stations in the same or adjacent frequency bands, it shall stop immediately and resume operation only after eliminating harmful interference.
    Radio communication services operating in the 2400 MHz and 5800 MHz frequency bands should also withstand interference from ISM applications.

## Slide 14: China MIIT (9)
  Proposed provisions (Cont’d)
    In case of major national missions or national implementation of radio control, the installation and use of radio stations in the 2400 MHz, 5100 MHz, and 5800 MHz frequency bands shall be complied with the radio management regulations issued during major national missions, or obey the radio control instructions and radio regulations issued by the state.
    Micro-power short-range radio equipment operating in the 2400 MHz and 5800 MHz frequency bands shall be implemented in accordance with the Ministry of Industry and Information Technology Announcement No. 52 of 2019.
    The radio stations that operate in the 2400 MHz, 5100 MHz, and 5800 MHz frequency bands shall also be complied with the relevant regulations of other industry authorities.
    These provisions are effective from January 1, 2022.

## Slide 15: China MIIT (10)
  Proposed provisions (Cont’d)
    The former Ministry of Information Industry “Notice on Adjusting 2.4GHz Frequency Band Transmitting Power Limits and Related Issues” (Xinbuwu [2002] No. 353), “Notice on the Use of 5.8GHz Frequency Band Frequency” (Xinbu Wu [2002] No. 277), “About the 5.8GHz band intelligent traffic management dedicated wireless short-range communication system: Notice on Relevant Issues” (Xinbu Wuhan [2003] No. 225), and the Ministry of Industry and Information Technology “Regarding the release of 5150-5350MHz frequency band wireless access system frequency: The Notice on Use-related Matters” (Wuhan [2012] No. 620 of the Ministry of Industry and Information Technology) are repealed on January 1, 2022. If other previous documents are inconsistent with this article, this article shall prevail.

## Slide 16: Hong Kong OFCA (1)
Updated table of frequency allocation
  Published on January 4, 2021
    https://www.ofca.gov.hk/filemanager/ofca/common/Industry/broadcasting/hk_freq_table_en.pdf
  Compared with the April 2020 version, of interests to us are:
    The following footnote is updated from WRC-12 to WRC-19:
      The use of the bands 5150 - 5350 MHz and 5470 - 5725 MHz by the stations in the mobile except aeronautical mobile, service shall be in accordance with Resolution 229 (Rev.WRC-19) of the Radio Regulations

## Slide 17: Hong Kong OFCA (2)
Updated table of frequency allocation
  Of interests to us are (Cont’d):
    The following footnote is expanded with the outcome of WRC-19:
      In the band 5250 - 5350 MHz, stations in the mobile service shall not claim protection from the radiolocation service, the Earth exploration-satellite (active) and the space research (active) service. The radiolocation service, the Earth exploration-satellite service (active) and the space research service (active) shall not impose more stringent conditions upon the mobile service than those stipulated in Resolution 229 (Rev.WRC-19) of the Radio Regulations.

## Slide 18: Hong Kong OFCA (3)
Updated table of frequency allocation
  Of interests to us are (Cont’d):
    The following footnote is added with the outcome of WRC-19:
      In the frequency band 5470 - 5725 MHz, stations in the mobile service shall not claim protection from radiodetermination services. The radiodetermination services shall not impose more stringent conditions upon the mobile service than those stipulated in Resolution 229 (Rev.WRC-19) of the Radio Regulations.
    The status of the 66-71 GHz band allocation is updated from “TO BE PLANNED” to “mobile” with the addition of the following footnote:
      The frequency band 66 - 71 GHz is identified for use by administrations wishing to implement the terrestrial component of International Mobile Telecommunications (IMT).

## Slide 19: India DOT
Notice for seeking comments for Roadmap for use of Radio Frequency Spectrum in India during next 10 years
  Information:
    https://dot.gov.in/sites/default/files/DoT%20Website%20notice%20for%20Comments%20on%20Spectrum%20Roadmap.pdf?download=1Consultation closes on January 13, 2021
  Summary:
    What changes are required in current spectrum allocations?
    What frequency bands should be considered for IMT/5G and other uses?
    What spectrum allocations do you see in the next 10 years for India?
    Any other suggestion in this regard.

## Slide 20: Japan MIC (1)
Frequency reorganization action plan (second revision)
  Report is available for download at:
    https://www.soumu.go.jp/main_content/000716599.pdf
  Information:
    This second revision is published based on the feedback it received from its recent consultation that is closed in early October.
  Summary:
    It plans to release 150 MHz spectrum in 5.3 GHz and 5.8 GHz for WLAN
    It also plans to proceed with technical studies, e.g., sharing conditions, between WLAN with other wireless systems in the 5925 MHz – 7125 MHz band.
    It plans to allow UWB for outdoor use in 7584 MHz – 8400 MHz.

## Slide 21: Japan MIC (2)
Technical Conditions for Ultra Wideband Wireless Systems
  Information
    https://www.soumu.go.jp/menu_news/s-news/01kiban14_02000477.html
    Consultation closes on December 24, 2020.
  Summary:
    This report summarizes
      the trends in outdoor use of UWB systems (including a brief mention of 802.15.4a and its spectral mask) (c.f., Chapter 1)
      its forecasts in the deployment of UWB systems in Japan and other countries (c.f., Chapter 2)
      sharing conditions between UWB and other wireless systems (c.f., Chapter 3)
      the proposed technical requirements for operating UWB outdoors in 7250-9000 MHz band (c.f., Chapter 4).

## Slide 22: Japan MIC (3)
Technical Conditions for Ultra Wideband Wireless Systems
  General conditions
    The width between the outermost frequencies (fL, fH; fL < fH), which is 10 dB lower than the maximum radiation frequency (fM), is the bandwidth (B-10), and has a bandwidth of 450 MHz or more. A UWB radio system is one in which the bandwidth is divided by the center frequency (fC) and the bandwidth ratio (μ-10) is 0.2 or more.
    Regarding the method of changing the center frequency of the emitted radio waves such as frequency hopping and chirp, UWB radio has a bandwidth of 450 MHz or more that radiates power instantly or a bandwidth ratio of 0.2 or more.
      B-10 = fH - fL
      μ-10 = B-10/fC
      fC = (fH + fL )/2

## Slide 23: Japan MIC (4)
Technical Conditions for Ultra Wideband Wireless Systems
  General conditions (Cont’d)
    Use of frequency bands
      The frequency band used for outdoor UWB wireless systems is 7.250 GHz to 9.0 GHz.
      Regarding the operation of UWB radio systems in the relevant frequency band, harmful interference to other radio systems shall not be allowed, and interference from these radio systems shall be tolerated.
    Antenna power
      To be consistent with the system for indoor use and sharing with other wireless systems, the antenna power is -41.3 dBm/MHz or less for average power, and 0dBm/50 MHz or less for peak power as EIRP.

## Slide 24: Japan MIC (5)
Technical Conditions for Ultra Wideband Wireless Systems
  General conditions (Cont’d)
    Communication and modulation types
      The communication can be simplex, duplex, or semi-duplex based on the usage pattern.
      The modulation is not limited.
    Bandwidth spread
      The frequency bandwidth, which is 10 dB lower than the maximum power point, is 450 MHz or more.
      This value may be updated subject to other regulations worldwide.
    Transmission speed
      There is no applicable limit.

## Slide 25: Japan MIC (6)
Technical Conditions for Ultra Wideband Wireless Systems
  General conditions (Cont’d)
    Interference avoidance
      When transmitting data, it must have a function to automatically transmit or receive an identification code. In addition, when performing radio localization, the reflected wave of the radio wave transmitted by the own radio station and the radio wave transmitted by another radio station can be discriminated by identifying the modulation method and other characteristics of the received radio wave.

## Slide 26: Japan MIC (7)
Technical Conditions for Ultra Wideband Wireless Systems
  General conditions (Cont’d)
    Terminal equipment that uses radio waves in the terminal equipment
      Similar to the current regulations:
        Those that use radio waves between one part and the other part that make up the terminal equipment shall have an identification code of 48 bits or more.
        Except in specific cases, the availability of radio waves to be used shall be determined, and the communication path shall be set only when the radio waves are available.
    Operational restrictions
      Within the range necessary to protect the existing radio system from harmful interference.
      Not allowed for operations in the sky.

## Slide 27: Japan MIC (8)
Technical Conditions for Ultra Wideband Wireless Systems
  General conditions (Cont’d)
    Termination capability
      Have a function to stop the emission of radio waves.
    Housing conditions
      As a countermeasure against illegal modification, the housing should have a structure that cannot be easily opened.
    Compliance with radio wave protection guidelines
      The maximum transmission power is 0.22 mW even when assuming a 3 GHz width of 7.25 GHz to 10.25 GHz that can be used indoors, and if the distance from the transmission antenna is 2.7 mm or more.
      When the distance is within 20 cm from the human body, it is necessary to comply with the local absorption guideline in the radio wave protection guideline.

## Slide 28: Japan MIC (9)
Technical Conditions for Ultra Wideband Wireless Systems
  General conditions (Cont’d)
    Electromagnetic environment measures
      Sufficient consideration must be given to mutual electromagnetic interference between UWB wireless systems and medical electronic devices.
  Technical conditions for radio equipment
    Transmitter
      The occupied frequency bandwidth shall be within 1.75 GHz including the frequency tolerance.
      For unnecessary emission, the outside of the frequency band is the spurious region, and the permissible value of the intensity of unnecessary emission in the spurious region is as shown in Table 4-1.

## Slide 29: Japan MIC (10)
Frequency (MHz) | Average power | Peak power
< 1600 | < -90.0dBm/MHz | < -84.0dBm/MHz
1600~2700 | < -85.0dBm/MHz | < -79.0dBm/MHz
2700~7250 | < -70.0dBm/MHz | < -64.0dBm/MHz
7250~9000 | < -59.3dBm/MHz | < -35.0dBm/MHz
9000~10250 | < -60.0dBm/MHz | < -35.7dBm/MHz
10250~10600 | < -70.0dBm/MHz | < -64.0dBm/MHz
10600~10700 | < -85.0dBm/MHz | < -79.0dBm/MHz
10700~11700 | < -70.0dBm/MHz | < -64.0dBm/MHz
11700~12750 | < -85.0dBm/MHz | < -79.0dBm/MHz
> 12750 | < -70.0dBm/MHz | < -64.0dBm/MHz

## Slide 30: Japan MIC (11)
Technical Conditions for Ultra Wideband Wireless Systems
  Technical conditions for radio equipment (Cont’d)
    Transmitter (Cont’d)
      The reference bandwidth in the allowable value of the intensity of unwanted emission shall be 1 MHz.
      The EIRP is less than or equal to the permissible value of the intensity of unwanted emission.
    Receiver
      The equivalent isotropic radiated power is -54 dBm/MHz or less, and other frequencies shall be below the allowable value of the intensity of unnecessary emission.

## Slide 31: Malaysia MCMC (1)
Updated class assignment
  Information
    https://www.skmm.gov.my/skmmgovmy/media/General/pdf/CLASS-ASSIGNMENT-NO-1-OF-2020.pdf
  Of interest to us:
    Class assignment for Short Range Radiocommunications device
    Class assignment for Ultra Wide-Band communication device

## Slide 32: Malaysia MCMC (2)
  Of interest to us:
    Class assignment for short range radiocommunications device

## Slide 33: Malaysia MCMC (3)
  Of interest to us:
    Class assignment for Ultra Wide-Band communication device

## Slide 34: Vietnam MIC (1)
Draft Decision amending and supplementing the National plan on radio frequency spectrum
  Information
    https://mic.gov.vn/Upload_Moi/DuThaoVanBan/HO-SO-DANG-WEBSITE.ZIP
    Consultation closes on February 2, 2021.
  Abstract:
    Following the decision of WRC-19, the MIC proposes the followings:
      Consider, amend, supplement division for radio operations for 18 frequency bands;
      Revised 60 annotations;
      Added 26 new captions;
      Dropped 6 annotations.

## Slide 35: Vietnam MIC (2)
Draft Decision amending and supplementing the National plan on radio frequency spectrum (Cont’d)
  Of possible interest to us:
    Identify 66-71 GHz for IMT
      VTN24: The bands 24.25 to 27.5 GHz; 37-43.5 GHz; 45.5-47 GHz; 47.2-48.2 GHz, 66-71 GHz are intended for IMT mobile communication systems. The manufacture and import of radio equipment for use in Vietnam in these frequency bands must comply with this regulation and other relevant laws.

## Slide 36: Vietnam MIC (3)
Draft Decision amending and supplementing the National plan on radio frequency spectrum (Cont’d)
  Of possible interest to us:
    Revise conditions for Wi-Fi/RLAN devices to be operated in 5150-5250 MHz band such that the use of Wi-Fi/RLAN devices can be extended to use inside trains, cars, and outdoors.
      VTN14: Business Mobility in the 5150-5350 MHz bands; 5470-5725 MHz and 5725-5850 MHz are only limited to deploying radio access systems (WAS) including wireless LANs (WLANs). The use of the 5150-5250 MHz band for WiFi / RLAN inside trains, cars and outdoor use is subject to the provisions of Resolution 229 (WRC-19).