IEEE P802.18
Radio Regulatory Technical Advisory Group (RR-TAG)
Proposed response to EU RSPG’s questionnaire
Date: 2023-03-28
Author(s):
Name	Company	Address	Phone	email
Amelia Andersdotter	Sky Group/Comcast
Edward Au	Huawei
Dave Halasz	MorseMicro
Riku Pirhonen	NXP

Electronic filing	April 12, 2023

Re: Questionnaire on the Role of Radio Spectrum Policy to help combat Climate Change

Dear RSPG,

IEEE 802 LAN/MAN Standards Committee (LMSC) thanks the Radio Spectrum Policy Group (RSPG) for issuing the questionnaire on the role of radio spectrum policy to help combat climate change and for the opportunity to provide feedback on this topic.

IEEE 802 LMSC is a leading consensus-based industry standards body, producing standards for wireless networking devices, including wireless local area networks (“WLANs”), wireless specialty networks (“WSNs”), wireless metropolitan area networks (“Wireless MANs”), and wireless regional area networks (“WRANs”). We also produce standards for wired Ethernet networks, and technologies produced by implementers of our standards are critical for all networked applications today.

IEEE 802 LMSC is a committee of the IEEE Standards Association and Technical Activities, two of the Major Organizational Units of the Institute of Electrical and Electronics Engineers (IEEE). IEEE has about 400,000 members in over 160 countries. IEEE’s core purpose is to foster technological innovation and excellence for the benefit of humanity. In submitting this document, IEEE 802 LMSC acknowledges and respects that other components of IEEE Organizational Units may have perspectives that differ from, or compete with, those of IEEE 802 LMSC. Therefore, this submission should not be construed as representing the views of IEEE as a whole[1].
[1] This document solely represents the views of IEEE 802 LMSC and does not necessarily represent a position of either the IEEE or the IEEE Standards Association.

IEEE 802 LMSC supports RSPG’s ongoing activities on sustainability and climate change, and encourage RSPG to consider IEEE 802 technologies as playing an important role in providing energy-efficient wireless broadband connectivity to EU citizens. Please find below the responses of IEEE 802 LMSC to selected questions of this questionnaire.

Introduction: the lesson IEEE 802 wireless technologies learned from Ethernet

IEEE 802 wireless technologies use, for most part, license-exempt spectrum to operate. The technologies specified by the IEEE 802 LMSC are used in a range of scenarios where energy efficiency is of utmost important. For instance, the IEEE 802.15 family of standards provide specifications for technologies that are often energy constrained or have "bursty" transmission patterns (e.g., a need to transmit or receive data only rarely, but over a long total product life-span), such as sensor or IoT networks. The IEEE 802.11 standard [1] is incorporated in a large set of battery-driven devices (such as laptops and smartphones) used by individuals on a daily basis in professional and private settings that require a high level of energy efficiency to maximize utility of the devices for users, and also contains features to support bursty transmissions. In particular, the IEEE 802.11ah-2016 amendment [2] optimizes for energy efficiency over data rate for devices needing longer range or lower power consumption with extended battery life. Examples of these devices include video cameras and sensors.

This contribution focuses on mechanisms for energy efficiency that have been guiding the development of IEEE 802 wireless technologies in the last 15 years. First we introduce an early contribution of the IEEE 802.3 Ethernet Working Group to energy efficiency in networking, and then we exemplify how learnings from that contribution progressed into wireless technologies, making them the highly efficient technologies they are today.

IEEE 802.3az-2010 [3] was an early network standard that considered energy efficiency parameters suitable for standardization. Low Power Idle feature has two components. The first is disabling the transmitter, except for necessary intermittent refresh signaling, during the Low Power Idle state. This provides an energy saving compared to a continuous idle signal that was used on most links until then. The second is a 'sleep' and 'wake' signal that is sent before the link enters and before the link exits the Low Power Idle state, respectively.

The longer the wake time, the greater the potential energy savings in the receive device. This however comes at the cost of more buffering in the transmitting device, the transmitter must wait longer for the receiver to accept packets, and therefore greater latency. Since the latency a system can tolerate may vary over time, the IEEE 802.3az-2010 defines Link Layer Discovery Protocol (LLDP) messages that allow the default latency to be changed through negotiation between the two ends of the link, enabling the wake time to be changed dynamically. As an example, while a personal computer (PC) is running a voice application, the latency can be set low at the price of potentially lower energy savings. When use of the voice application is complete, and the PC is just web browsing, the latency and therefore the energy savings can potentially be increased.

Since there is both a latency and energy overhead in bringing a link out of the Low Power Idle state, at low utilization, it may be more energy efficient to bring a link out of the state once, rather than multiple times, to send multiple packets. It might even be possible that a constant low rate of packets will prevent a link from entering the Low Power Idle state. This is where the approach of buffering then bursting packets comes from, assuming that the resultant increase in latency can be tolerated.

The lesson from the research work that led to the IEEE 802.3az-2010 and that followed on real-world deployments of this standard in networks in different environments, is that there are energy gains to be made from being able to schedule traffic, being able to transmit large amount of data in bursts rather than smaller amounts of data continuously over a long time and being able to idle receivers. These lessons also apply for wireless technologies, and various features supporting such behavior are integrated in the IEEE 802 wireless technologies. For specific IEEE 802 wireless technology features that enable such energy conservation, see below under question 11.

Question 4. In your analyses related to energy consumption and/or energy efficiency, what are your reflections on the influence of parameters such as frequency band, type of radio access technology, coverage addressing different areas (urban, suburban, rural)?

Ubiquitous deployments of wireless communications based on IEEE 802 wireless technologies are essential to enable the EU’s sustainable development goals and achieve its Digital Decade vision. It has been remarked in several studies produced by or for European institutions that networks using IEEE 802 wireless technologies, in combination with wired backhaul over long distances, are the current leaders in terms of energy efficient networks [4][5].

As has been remarked by the RSPG’s opinion on Spectrum Policy in Climate Change published in November 2021 [6], access to large, contiguous frequency blocks reduces the consumption associated with the support of multiple carriers and carrier aggregation. IEEE Std 802.11ax-2021 [7] and IEEE P802.11be [8], for instance, introduce capability to operate in the entire 6 GHz band (i.e., 5925 MHz to 7250 MHz) with multiple concurrent 320 MHz channels. Drawing on the experiences of IEEE 802.3az-2010 cited above, having access to multiple concurrent 320 MHz channels and larger bandwidths is not only a question of maximizing through-put per time unit, but also enables more energy efficient transfer of data when needed with intermittent periods of idling. Extending the license-exempt operation to the upper 6 GHz band (specifically, 6425 MHz to 7125 MHz) in Europe is aligned with the RSPG’s opinion and makes the maximization of energy efficiency for the intended applications of Wi-Fi 6 (based on IEEE Std 802.11ax-2021) and Wi-Fi 7 (based on IEEE P802.11be) possible.

In addition, as the RSPG recognizes in its opinion that the current EU framework facilitates the roll-out of indoor networks, which in turn contributes to combat climate change, it is important for the RSPG to anticipate reflections on the future of the sub 1 GHz bands to enable wider deployment of IEEE 802 wireless technologies especially for indoor settings. For instance, IEEE 802.15.4 and IEEE 802.11ah technologies are often deployed in scenarios where a sensor device, usually battery-powered, might sporadically need to transmit or receive low volumes data. For these technologies, transmission can be scheduled and devices remain dormant between transmissions. A design goal of these devices is long life-span that lasts often tens of years.

Impulse radio based UWB  (Ultra Wideband) developed by IEEE802.15.4 uses very low power pulsed transmissions, limited by regulations to -41.3 dBm/1 MHz power spectral density, or in other terms, 37 nJ/ms. UWB is widely deployed in mobile phones and accessories for high integrity distance and direction measurement purposes, and will be used in car keys and other very low power consumption device to device use cases. Such solutions provide significant energy savings compared to approaches that rely on larger infrastructure.It is also worth mentioning that IEEE 802.11ah technologies can be deployed in scenarios where video is transmitted at a range farther than an IEEE 802.11 device operating in other frequency bands, such as video-enabled doorbells. For these technologies, the devices have higher transmission rates but may also sleep or doze for long periods of time.

Question 6. Taking into account the scope of the work of the RSPG above, do you wish to share other thoughts or ideas which could be helpful to the RSPG to identify the role radio spectrum policy can play to help combat climate change and mitigate other adverse environmental impacts?

IEEE 802 wireless technologies are typically designed in a way such that they can be either primary or secondary users of a frequency band. The majority of existing deployments of IEEE 802 wireless technologies operate in license-exempt bands or bands where an incumbent user has priority access to the band. This has the advantages of enabling IEEE 802 wireless technologies to be flexible over time, as well as allowing IEEE 802 wireless technologies to co-exist with pre-existing priority services in different bands. We would like to highlight the observation by the RSPG in its 2021 Opinion on Spectrum Policy in Climate Change [6] that spectrum needs and demands to help combat against climate change can change over time. License-exempt designations provide flexibility to the regulator and to technology developers in terms of changing and adapting features to the current needs of society and the economy.

Spectrum policy can facilitate and encourage use of low power technologies. While UWB radios cause very little or no interference to other users of the same spectrum, UWB radios themselves may become blocked by strong nearby signals. The UWB band is wide, in various parts of the world from 3.1 GHz to 10.6 GHz with variable amount of restrictions. While UWB radios are not protected from interference by regulations, spectrum policy can keep parts of the spectrum suitable for energy efficient low power device use.

Question 7. What information on energy consumption of the wireless ECNs does your company / the Members of your stakeholders' association collect? Which methodology/ methodologies are being used? Please name any standards that are being used.

IEEE 802 wireless standards specify mechanisms that can be incorporated by implementers in products in the way that the implementers prefer and choose. The specific set of mechanisms chosen by implementers for a product and the use of those implemented mechanisms has a large impact on the energy use of the product.

For this reason, the IEEE 802 LMSC do not consider any energy consumption benchmarking. Industry consortia that oversee particular uses of IEEE 802 wireless standards may, however, gather metrics on the energy consumption of implementations destined for those particular use-cases.

Question 11. Which actions is your company / the Members of your association taking to improve the energy efficient use of radio spectrum (e.g. switching to new technologies, advertisements to make energy efficient technologies more attractive, sleep mode for base stations, or other actions)?

IEEE 802 wireless standards already and continue to provide a rich toolbox of energy-saving features.

IEEE 802.11ah-2016 [2] is an amendment to the IEEE 802.11 standard [1] that specifies mechanisms for operation of wireless access system/radio LAN (WAS/RLAN) in sub-1 GHz bands. It was developed with sensor and IoT networks in mind, and contains an access point (AP) Power Save Mode. In this mode, the AP can signal to non-AP devices in the network that it is going to be in a "doze mode" for a period of time. By negotiating the length of the doze mode in advance, the AP and the non-AP devices can both conserve energy. This amendment introduced many features to increase energy efficiency. These include reducing overhead and relaxing timing for energy limited clients that typically operate from a coin cell. IEEE 802.11ah-2016 also introduced Target Wake Time (TWT), which allows long sleeping devices to negotiate a time for the device to be active. This enables optimizing power consumption per device.

The IEEE 802.11ax-2021 amendment [7] to the IEEE 802.11 standard specifies (broadcast) Target Wake Time, which is a scheduling mechanism for transmissions between an AP and a non-AP. It has the advantage of allowing larger throughput while lowering latency since both devices will not only be aware of when transmissions will be made, but also enable energy efficiency since the devices can be idle or quiet when transmissions do not need to be made.

The IEEE 802.11be project [8] specifies multi-link operation, which defines a way for multiple APs in a single device to coordinate traffic management over several bands. One mechanism provided for in multi-link operation is for the logical controlling entity of the multi-link device to quiet channels which are not necessary given the total data traffic load. In practice, if a multi-link device is capable of simultaneously sending traffic on 2.4 GHz, 5 GHz and 6 GHz links, but the current load on the network is such that only one or two of these links are necessary to provide a robust service level, the other one or two links can be quieted dynamically. The links can be un-quieted once the load on the network increases, with the result that the radios consume only the amount of energy they need for a given traffic load.

In the next major project of the IEEE 802.11 Working Group, namely the Ultra-High Reliability, the project description explicitly lists AP Power Save mechanisms as a target.

Question 12. What were the triggers for these actions (e.g. legal requirement, economic interests, consumer expectations, competitiveness, etc.)?

IEEE 802 wireless technologies are developed to satisfy market and society needs. Energy-efficient features are expected by consumers, enterprise and industrial users of IEEE 802 wireless technologies.

Question 13. Were there any difficulties when you attempted to introduce or perform these actions? Please specify.

No.

Question 14. What further actions would enable you to foster (a more) energy efficient spectrum use, if any? Should such an activity be done by national spectrum regulators / ministries / European entities? Please specify and explain.

Wider adoption of wide band data transmissions in the 915.8 MHz to 919.4 MHz band should be encouraged since this enables energy efficiency. Likewise, relaxation of occupied bandwidth to 2 MHz and relaxation of duty cycle restrictions will enable greater use of this band for video use cases. Relaxing the transmission power enables the video use case to reach a greater distance.

Avoiding allocation of spectrum for technologies that rely on high transmitter power especially in the range from 7.125 GHz to 9.5 GHz would allow low power technologies like UWB to achieve higher reliability. The more low power technologies are used, the less need there is for higher power, and the cumulative effect of this shift will have an environmental impact.

Question 15. Would some kind of spectrum regulation facilitate your motivation to use radio spectrum in a (more) energy efficient way?

See response to question 14.

Question 16. Taking into account the scope of the work of the RSPG above, do you wish to share other thoughts or ideas which could be helpful to the RSPG to identify the role radio spectrum policy can play to help combat climate change and mitigate other adverse environmental impacts?

License-exempt designations, whether accommodating license-exempt technologies as primary or secondary users of a frequency band, provide flexibility to the regulator and to technology developers in terms of changing and adapting features to the current needs of society and the economy. In addition, license-exempt technologies already have a good track-record of combining energy efficient spectrum use with higher capacity. We encourage global regulators and administrations to adopt policies that encourage technology neutrality and flexible shared spectrum usage to create social and economic benefit advantages for all.

The Wi-Fi Alliance, an industry consortium developing interoperability specifications and certifications for Wi-Fi technologies, has published a set of Sustainability information materials that further explain how implementations of IEEE 802.11 wireless technologies contribute to a more sustainable, green networking infrastructure [9][10].

The IEEE 802 LMSC provides wireless standards primarily designed for use of shared and license-exempt operation and enable an ecosystem in which many independent entities can contribute and enable an ever-expanding communications infrastructure, and we believe implementations of our technical standards already contribute to the RSPG's goals.

Conclusion

IEEE 802 LMSC thanks the RSPG for the opportunity to provide this submission and kindly requests the RSPG to take into account our responses in its decision towards the role of radio spectrum policy to combat climate change.

Respectfully submitted

By: /ss/.
Paul Nikolich
IEEE 802 LAN/MAN Standards Committee Chairman
em: p.nikolich@ieee.org

References:

[1]	IEEE Standard for Information Technology—Telecommunications and Information Exchange between Systems - Local and Metropolitan Area Networks—Specific Requirements - Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications, in IEEE Std 802.11-2020 (Revision of IEEE Std 802.11-2016) , vol., no., pp.1-4379, 26 Feb. 2021, doi: 10.1109/IEEESTD.2021.9363693.
[2]	IEEE Standard for Information technology—Telecommunications and information exchange between systems - Local and metropolitan area networks—Specific requirements - Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications Amendment 2: Sub 1 GHz License Exempt Operation, in IEEE Std 802.11ah-2016 (Amendment to IEEE Std 802.11-2016, as amended by IEEE Std 802.11ai-2016), vol., no., pp.1-594, 5 May 2017, doi: 10.1109/IEEESTD.2017.7920364.
[3]	IEEE Standard for Information technology—Local and metropolitan area networks— Specific requirements - Part 3: CSMA/CD Access Method and Physical Layer Specifications Amendment 5: Media Access Control Parameters, Physical Layers, and Management Parameters for Energy-Efficient Ethernet, in IEEE Std 802.3az-2010 (Amendment to IEEE Std 802.3-2008) , vol., no., pp.1-302, 27 Oct. 2010, doi: 10.1109/IEEESTD.2010.5621025.
[4]	WIK-Consult and Ramboll, Final Study Report for EU BEREC “External Sustainability Study on Environmental impact of electronic communications,” BoR (22) 34, 15 March 2022.
[5]	The digital environmental footprint in France: ADEME and Arcep submit their first report to the Government, 19 January 2022. Available online [accessed: 24 March 2023].
[6]	Radio Spectrum Policy Group RSPG21-0041-final, RSPG Opinion on the role of radio spectrum policy to help combat climate change. Available online [accessed: 24 March 2023]
[7]	IEEE Standard for Information Technology — Telecommunications and Information Exchange between Systems Local and Metropolitan Area Networks — Specific Requirements Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications Amendment 1: Enhancements for High-Efficiency WLAN, in IEEE Std 802.11ax-2021 (Amendment to IEEE Std 802.11-2020), vol., no., pp.1-767, 19 May 2021, doi: 10.1109/IEEESTD.2021.9442429.
[8]	IEEE Draft Standard for Information technology--Telecommunications and information exchange between systems Local and metropolitan area networks--Specific requirements - Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications Amendment: Enhancements for Extremely High Throughput (EHT)," in IEEE P802.11be/D3.0, January 2023 , vol., no., pp.1-999, 1 March 2023.
[9]	Wi-Fi Alliance, Wi-Fi: sustainable connectivity (highlights). Available online [accessed: 24 March 2023]
[10]	Wi-Fi Alliance, Wi-Fi: sustainability (complete information). Available online [accessed: 24 March 2023]