## Slide 1: IEEE 802.18 RR-TAG Public consultation of ECC Report 355 - OOB limits of 6GHz VLP RLAN -
Date: 11 March 2024
Authors:

## Slide 2: Introduction
CEPT: WI SE45_03:
  OOBE limits of 6 GHz VLP WAS/RLANs below 5935 MHz
Scope:
  To further study OOB emissions from Very Low Power (VLP) WAS/RLAN devices operating in the band 5945–6425 MHz to protect CBTC systems that operate in the band 5915-5935 MHz
Result:
  ECC Report in support of an update of the related RLAN regulation framework to be updated until 12/2024

## Slide 3: Draft ECC Report 355 in public consultation
The investigation results of SE45 are included in the draft ECC Report in public consultation until 02. April 2024:
  Public Consultation information
  ECC report 355 “Measurement-based compatibility studies assessing interference from Very Low Power (VLP) Wireless Access Systems including Radio Local Area Networks (WAS/RLAN) operating in 5945-6425 MHz to Communication Based Train Control (CBTC) systems
The ECC report 355 is the basis for the update of the regulation and a CEPT report:
  Draft CEPT Report 87  in PC until 19.April 2024
  Draft revision of ECC decision (20)01 in PC until 19.April 2024

## Slide 4: Issue
CBTC (Urban Rail) opponents asking for an OOB limit of -45dBm/MHz in the band below 5935MHz for VLB RLAN devices in the band above 5945MHz
ECC Report is interpreted by CBTC that this is required, or additional mitigation techniques are needed for VLP devices in the band 5945MHz
Most of the regulator are of the opinion that -37dBm/MHz is sufficient or even overprotective
If we can demonstrate based on the final ECC Report 355 that -37dBm/MHz is sufficient the related regulation action (CEPT Report and revised ECC decision) can be steered towards this value.

## Slide 5: Some point to be mentioned in relation to ECC Report 355
Main conclusions are based on simple MCL calculation under worst case conditions.
In the very final stage some simple statistical calculations have been included into the report missing out some effects
  Most CBTC systems are based on 802.11a technologies
  The repetition of messages based on the 11a protocol is not considered at all in this statistical evaluation (see ETSI TR 103 580 V1.1.1)
  The channel load of the systems is kept very low to reduce latency and hidden node effect (see ETSI TR 103 580 V1.1.1)

## Slide 6: Statements from ETSI TR 103 580 V1.1.1
ETSI TR 103 580 V1.1.1 (2019-08):
  Urban Rail ITS and Road ITS applications in the 5,9 GHz band; Investigations for the shared use of spectrum
ETSI TR 103 580 V1.1.1 further indicates that:
  „In order to balance the CSMA/CA drawbacks (in particular collisions due to the hidden node effect), the channel load during operation is kept well below the maximum limits possible in a CSMA/CA system.”
  "In addition, redundancy and several repetitions of each message are used to ensure the required level of transmission availability. With this system, application data are sent as unicast messages to/from each train."

## Slide 7: Conclusion
An updated regulatory framework in CEPT for VLB RLAN systems in the band 5945MHz could lead to a OOB requirement of -45dBm/MHz in the band below 5935MHz in Europe
Basis of this update is ECC Report 355 in Public Consultation
Conclusion in this Report will steer the further update process
Proposal:
  IEEE 802.18 should develop an input to this process in support of the OOB limit of -37dBm/MHz in the band below 5945MHz
  IEEE 802.18 should point out the additional redundancy capabilities and effects by message repetition based on the 11a protocol not considered yet in the draft Report
  IEEE 802.18 should point out optimization potential of the CBTC systems based on 802.11a
  IEEE 802.18 could also ask for more detailed investigations of the statistical effect based on network simulations