## Slide 1: ETSI TC BRAN updates, March 2025
Notice: This document has been prepared to assist IEEE 802.18. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2025-03-08
Authors:

## Slide 2: BRAN #128
In February, TC BRAN conducted its first plenary meeting for the year 2025
  BRAN(25)128004r4 provides an overview of the documents discussed during BRAN #128
TC BRAN discussed the status of several Harmonised Standards (HSs) older than five years
  TC BRAN declared that several HSs could be archived, see BRAN(24)127004
At present, TC BRAN has only one active Work Item
  Revision of EN 303 687

## Slide 3: EN 303 687—Major discussion topics
Coexistence between Narrowband Frequency Hopping (NB FH) and wideband transmissions
  TC BRAN reviewed a variety of documents related to Energy Detection Threshold levels, NB FH operation w/o Listen-before-Talk, and NB FH channelization
Client-to-Client communication (C2C) at Low Power Indoor (LPI) levels
  TC BRAN discussed if and how devices in range of an LPI Access Point (AP) could apply LPI levels for communication among them (C2C operation)

## Slide 4: EN 303 687—Updates
Version 1.1.1 of HS EN 303 687 defines two medium access mechanisms denoted as Load Based Equipment (LBE) and Frame Based Equipment (FBE)
  In addition, the HS defines a device category denoted as Narrowband Frequency Hopping Equipment (NBE)
For consistency, TC BRAN discussed to change these terms
  Channel access mechanisms to be called Frame Based channel Access (FBA), Load Based channel Access (LBA), and NarrowBand frequency hopping channel Access with Listen Before Talk (NBA-LBT)
  Usage of the term “equipment” to be limited to referring to physical instances that implement LBA, FBA, or NBA-LBT

## Slide 5: Official Journal of the EU (OJEU)
On 2025-01-30, the European Commission (EC) updated the part of the OJEU that relates to the Radio Equipment Directive (RED)
  There were no updates related to HSs developed by TC BRAN
On 2025-02-07, ETSI and EC had a meeting
  See related e-mail
  The next RED related update to the OJEU might occur at the end of March/beginning of April
  It might be that version 1.1.1 of HS EN 303 687 will be listed in the OJEU, then

## Slide 6: Upcoming TC BRAN meetings
TC BRAN changed the schedule of its next plenary meeting #129
  Will begin 2025‑03‑31T14:00+02:00
  Will end at latest 2025‑04‑02T18:00+02:00
  Might contain evening sessions from 18:30 until 20:00
BRAN #130
  2025‑06‑02T14:00+02:00 until 2025‑06‑06T14:00+02:00
BRAN #131
  2025‑09‑22T14:00+02:00 until 2025‑09‑26T14:00+02:00
BRAN #132
  2025‑11‑03T14:00+01:00 until 2025‑11‑07T14:00+01:00
BRAN #133
  2026‑01‑26T14:00+01:00 until 2026‑01‑30T14:00+01:00